## Slide 1: Addressing in Networks Last Update 2009.07.14 1.1.0

## Slide 2: Addressing in General
In any network of networks and devices attached to those networks a system of addresses in one form or the other is required to first deliver the data to the correct device and second to direct the data to the correct program or service on that device
The service address is the port number discussed earlier

## Slide 3: Addressing in General
We will now discuss how the data gets to the correct device
It is best when a communications system can supply a universal communication service that allows any host device to contact any other host device
To do so, such a system needs a globally accepted method of identifying each host that attaches to the internetwork

## Slide 4: Addressing in General
More importantly, not only each host, but each interface or entry point from the host to the internetwork must have such an address
Regardless of whether the interface points to an inside or outside network

## Slide 5: Addressing Levels in Networks
There are two levels of addressing that you must consider when creating a network
They are
  Within the network
  In the internetwork

## Slide 6: Within the Network
A local area network only operates at layers 1 and 2
To make this confusing you will see that we assign each end point in a local area network an IP address
However the LAN does not use that address to transfer data between devices attached to the local area network since the IP address is a layer 3 entity

## Slide 7: Within the Network
Since a LAN only operates at layers 1 and 2 the devices in a LAN must convert the layer 3 IP address to a layer 2 address
As we will see in the Host Addressing presentation this is done by the ARP protocol

## Slide 8: In the Internetwork
When two or more LANs are connected to each other we have an internetwork or a network of networks
These networks connect to each other using layer 3 devices such as routers and layer 3 switches
This interconnection between networks uses the layer 3 IP address

## Slide 9: Summary
In summary the transaction works this way
When a frame must go from one network to another network the transfer is done at layer 3 using a layer three device and a layer 3 IP address as a packet
Once this packet arrives at the receiving network the packet information is removed
It can no longer be used because the receiving network is a LAN

## Slide 10: Summary
Since the receiving network is a LAN the data can only be transferred between the devices connected to the LAN using a layer 2 MAC address

## Slide 11: Summary
The receiving device, the router or layer 3 switch, uses ARP to determine the MAC address of the device connected to the LAN that has been assigned the IP address contained inside the incoming packet

## Slide 12: Summary
The answer is used to create a frame with that MAC address as the destination MAC address
The source MAC address is that of the receiving device
In other words the router or layer 3 switch