## Slide 1: Network Layer
Last Update 2010.02.22
1.1.0

## Slide 2: The Network Layer
Several things happen at the network layer
In terms of the TCP/IP routed protocol stack what happens is the IP protocol provides a network level addressing scheme
Also at this level, and discussed separately, routing protocols live

## Slide 3: The Context for IP
Layer | Protocol
Application | FTP/SMTP and many others
 | Port
Transport | UDP/TCP
 | Protocol Number
Internet | IP
Network Interface | Ethernet handles these functions
Hardware | Ethernet handles these functions

## Slide 4: What is IP
IP – Internet Protocol is the only protocol that lives at this layer
This is the first protocol encountered as we enter the bottom of the TCP/IP protocol stack
Recall that the bottom two layers are part of the stack, but TCP/IP relies on an underlying system to provide those services

## Slide 5: What is IP
So the first protocol we encounter in the TCP/IP protocol stack is IP
It gets the data from one network to another
IP was first defined in January 1980 in RFC 760

## Slide 6: What is IP
As RFC 760 says
  The Internet Protocol is designed for use in interconnected systems of packet-switched computer communication networks.
  Such a system has been called a "catenet".
  The internet protocol provides for transmitting blocks of data called datagrams from sources to destinations, where sources and destinations are hosts identified by fixed length addresses.

## Slide 7: What is IP
  The internet protocol also provides for fragmentation and reassembly of long datagrams, if necessary, for transmission through "small packet" networks.
  The internet protocol is specifically limited in scope to provide the functions necessary to deliver a package of bits (an internet datagram) from a source to a destination over an interconnected system of networks.

## Slide 8: What is IP
  There are no mechanisms to promote data reliability, flow control, sequencing, or other services commonly found in host-to-host protocols.

## Slide 9: Operation
IP is a connectionless, unreliable, best effort packet delivery service
It is connectionless because each packet is independent of every other packet
  A sequence of packets may take entirely different paths to the same end point
It is unreliable because delivery is not guaranteed

## Slide 10: Operation
  The packet may be lost, arrive out of order, be delayed
  IP will not detect this
  So it will not let anyone know if any of this occurs
It is best effort because it treats all packets the same
  It attempts to deliver each and every packet

## Slide 11: IP Datagram
The thing that IP uses to carry stuff is the IP datagram
Like all such devices it has a header and a data area
HEADER | DATA

## Slide 12: IP Datagram Header
VERS
HLEN
SERVICE TYPE
TOTAL LENGTH
IDENTIFICATION
FLAG
FRAGMENT OFFSET
TTL
PROTOCOL
HEADER CHECKSUM
SOURCE IP ADDRESS
DESTINATION IP ADDRESS
IP OPTIONS

## Slide 13: IP Datagram Header
VERS
HLEN
SERVICE TYPE
TOTAL LENGTH
IDENTIFICATION
FLAG
FRAGMENT OFFSET
TTL
PROTOCOL
HEADER CHECKSUM
SOURCE IP ADDRESS
DESTINATION IP ADDRESS
IP OPTIONS

## Slide 14: IP Datagram Header
VERS or Version
  4 bits
  The version of IP
  Always 4 right now
  Shows as binary 0100
  To ensure everyone agrees on the format of the datagram

## Slide 15: IP Datagram Header
VERS
HLEN
SERVICE TYPE
TOTAL LENGTH
IDENTIFICATION
FLAG
FRAGMENT OFFSET
TTL
PROTOCOL
HEADER CHECKSUM
SOURCE IP ADDRESS
DESTINATION IP ADDRESS
IP OPTIONS

## Slide 16: IP Datagram Header
HLEN or Header Length
  4 bits
  Datagram header length in 32 bit words
  Used to indicate whether IP OPTIONS and PADDING fields are being used

## Slide 17: IP Datagram Header
VERS
HLEN
SERVICE TYPE
TOTAL LENGTH
IDENTIFICATION
FLAG
FRAGMENT OFFSET
TTL
PROTOCOL
HEADER CHECKSUM
SOURCE IP ADDRESS
DESTINATION IP ADDRESS
IP OPTIONS

## Slide 18: IP Datagram Header
SERVICE TYPE
  8 bits
  Specifies how the datagram should be handled
  QoS mechanism
The current name for this field is Differentiated Services Code Point or DSCP

## Slide 19: IP Datagram Header
VERS
HLEN
SERVICE TYPE
TOTAL LENGTH
IDENTIFICATION
FLAG
FRAGMENT OFFSET
TTL
PROTOCOL
HEADER CHECKSUM
SOURCE IP ADDRESS
DESTINATION IP ADDRESS
IP OPTIONS

## Slide 20: IP Datagram Header
TOTAL LENGTH
  16 bits
  The length of the datagram in octets including the header and data

## Slide 21: IP Datagram Header
VERS
HLEN
SERVICE TYPE
TOTAL LENGTH
IDENTIFICATION
FLAG
FRAGMENT OFFSET
TTL
PROTOCOL
HEADER CHECKSUM
SOURCE IP ADDRESS
DESTINATION IP ADDRESS
IP OPTIONS

## Slide 22: IP Datagram Header
IDENTIFICATION or Fragment Identifier
  16 bits
  Holds a unique integer that identifies which datagram a fragment belongs to if the packet has been fragmented, which most are

## Slide 23: IP Datagram Size
Minimum datagram size is 576 bytes
  With at least 552 bytes of data
Maximum size for an IP datagram is 65,535 bytes
  With at most 65,515 bytes of data
But Ethernet only handles 1500 bytes of data
So how is a 65,535 byte datagram to go into a 1500 byte data area
By fragmentation

## Slide 24: IP Datagram Size
It is then reassembled as seen above using the Fragment Offset part of the datagram header

## Slide 25: IP Datagram Header
VERS
HLEN
SERVICE TYPE
TOTAL LENGTH
IDENTIFICATION
FLAG
FRAGMENT OFFSET
TTL
PROTOCOL
HEADER CHECKSUM
SOURCE IP ADDRESS
DESTINATION IP ADDRESS
IP OPTIONS

## Slide 26: IP Datagram Header
FLAG or Fragmentation Flag
  3 bits, but part of the FRAGMENT OFFSET field
  Indicating that the datagram has been fragmented
  Bit 1 is not currently used
  Bit 2 is turned on to tell routers to not fragment a packet
    If the router must, but cannot, the packet is dropped and a message is sent to the receiver

## Slide 27: IP Datagram Header
  Bit 3 when on indicates more fragments are coming
    When set to 0 it indicates this is the last fragment
  All of this information is used to reassemble everything

## Slide 28: IP Datagram Header
VERS
HLEN
SERVICE TYPE
TOTAL LENGTH
IDENTIFICATION
FLAG
FRAGMENT OFFSET
TTL
PROTOCOL
HEADER CHECKSUM
SOURCE IP ADDRESS
DESTINATION IP ADDRESS
IP OPTIONS

## Slide 29: IP Datagram Header
FRAGMENT OFFSET
  13 bits
  This tells the receiver what piece of a datagram this packet is of a datagram that has been cut up due to the MTU of the underlying method being used to carry the datagram from point-to-point

## Slide 30: IP Datagram Header
  To distinguish fragments, each has its offset field set to the distance, measured in 8 byte units, between the beginning of the original datagram and the beginning of that particular fragment
  So the first fragment has an offset of 0, the second fragment has an offset value of the payload size of the first fragment, and so on

## Slide 31: IP Datagram Header
VERS
HLEN
SERVICE TYPE
TOTAL LENGTH
IDENTIFICATION
FLAG
FRAGMENT OFFSET
TTL
PROTOCOL
HEADER CHECKSUM
SOURCE IP ADDRESS
DESTINATION IP ADDRESS
IP OPTIONS

## Slide 32: IP Datagram Header
TTL or Time to Live
  8 bits
  Supposed to be in seconds, but things run so fast today it is normally hops
  Each router decrements the value by 1

## Slide 33: IP Datagram Header
VERS
HLEN
SERVICE TYPE
TOTAL LENGTH
IDENTIFICATION
FLAG
FRAGMENT OFFSET
TTL
PROTOCOL
HEADER CHECKSUM
SOURCE IP ADDRESS
DESTINATION IP ADDRESS
IP OPTIONS

## Slide 34: IP Datagram Header
PROTOCOL
  8 bits
  Indicates the higher level protocol used to create the datagram

## Slide 35: IP Datagram Header
VERS
HLEN
SERVICE TYPE
TOTAL LENGTH
IDENTIFICATION
FLAG
FRAGMENT OFFSET
TTL
PROTOCOL
HEADER CHECKSUM
SOURCE IP ADDRESS
DESTINATION IP ADDRESS
IP OPTIONS

## Slide 36: IP Datagram Header
HEADER CHECKSUM
  16 bits
  Checks the integrity of the header itself
  Not the data, the header

## Slide 37: IP Datagram Header
VERS
HLEN
SERVICE TYPE
TOTAL LENGTH
IDENTIFICATION
FLAG
FRAGMENT OFFSET
TTL
PROTOCOL
HEADER CHECKSUM
SOURCE IP ADDRESS
DESTINATION IP ADDRESS
IP OPTIONS

## Slide 38: IP Datagram Header
SOURCE IP ADDRESS
  32 bits
  Where it came from

## Slide 39: IP Datagram Header
VERS
HLEN
SERVICE TYPE
TOTAL LENGTH
IDENTIFICATION
FLAG
FRAGMENT OFFSET
TTL
PROTOCOL
HEADER CHECKSUM
SOURCE IP ADDRESS
DESTINATION IP ADDRESS
IP OPTIONS

## Slide 40: IP Datagram Header
DESTINATION IP ADDRESS
  32 bits
  Where its going

## Slide 41: IP Datagram Header
VERS
HLEN
SERVICE TYPE
TOTAL LENGTH
IDENTIFICATION
FLAG
FRAGMENT OFFSET
TTL
PROTOCOL
HEADER CHECKSUM
SOURCE IP ADDRESS
DESTINATION IP ADDRESS
IP OPTIONS

## Slide 42: IP Datagram Header
IP OPTIONS
  24 bits
  Not used except in testing

## Slide 43: IP Datagram Header
PADDING
  8 bits
  To bring the datagram up to a minimum size

## Slide 44: IP Datagram Header
DATA
  Size varies
  The important stuff

## Slide 45: Fragmentation
As I hope you noticed in the discussion of the fields in the IP header, fragmentation and reassembly is a major factor at the Internet layer
Fragmentation introduces quite a bit of processing, as such it is inefficient
As we will see later the manner in which fragmentation is handled is significantly changed in IPV6

## Slide 46: Fragmentation
IP views the things it sends from host to host as datagrams
When these datagrams are sent out over the internetwork they are called packets
Typically these packets are the fragmented subparts of the datagram

## Slide 47: Fragmentation
This is why the internetwork is called a packet switching network instead of a datagram switching network
Why is fragmentation required in IPv4
Let’s look at an example
The designers of IP could select any datagram size to use
They decided to use a datagram 65,535 bytes long

## Slide 48: Fragmentation
The designers of Ethernet decided 1,500 bytes was the best size for a frame on a Ethernet LAN
These various limits are called the MTU – Maximum Transfer Unit for a particular device
The MTU is the maximum size of a unit that can be handled by a link as defined by the hardware for that link
The best MTU is an efficient one

## Slide 49: Fragmentation
Efficiency in this case is where the packet is large enough that the amount of data versus the amount of overhead in terms of the headers required for the unit of information are in balance
In this case the larger the better
In IP that is 65,535 bytes
But efficiency also calls for no fragmentation of the unit of information by the routers along its path

## Slide 50: Fragmentation
Because this fragmentation is overhead, as in extra processing by the routers that fragment it and by the end station that must put it back together
This requirement calls for a small enough unit of information that no fragmentation is required
At present that is 576 bytes

## Slide 51: Fragmentation
Note the rather large discrepancy here between 576 and 65,535 bytes
How does this work
Say a full size IP datagram of 65,535 bytes arrives at the Ethernet interface of a router
Ethernet has a MTU of 1,500 bytes

## Slide 52: Fragmentation
To deal with this the router must divide the datagram into 44 fragments
The end point must then reassemble this mess back into the correct order
This is not such a big deal at the LAN end, but is more so if the fragmentation occurs at the router on the way out of the LAN into the WAN

## Slide 53: Fragmentation
A solution to this is to discover the smallest MTU, then set the upper layer protocols to use this value
IPV6 will discover this or a guaranteed default MTU can be used that all IPV6 devices will support

## Slide 54: Fragmentation
What methods can IPv4 use
There are two
  IP Router Segmentation
  Path MTU Discovery

## Slide 55: IP Router Segmentation
The simplest approach from the end system point of view is not to worry about the MTU size
In this approach the sender simply has to ensure that each packet is less than the MTU of the link on which it is sent
The network layer then has to arrange to cut packets up into fragments whenever a router encounters a link with an MTU smaller than the received packet size

## Slide 56: IP Router Segmentation
Recall that all the fragments of a packet carry the same identification in one of the IP header fields
The problem with this method is that it places a higher workload on the routers
It may also result in fragmentation of fragments as smaller and smaller MTUs are encountered along the way

## Slide 57: Path MTU Discovery
The second method is for the end system to discover how large of a datagram can be sent over the links that will be encountered without requiring fragmentation
The way in which the end system finds out this packet size, is to send a large packet, up to the MTU of the link to which it is connected

## Slide 58: Path MTU Discovery
This packet is sent with the DF – Do Not Fragment flag set in the IP header
If a router along the path finds that the MTU of the next link exceeds the packet size, the DF flag tells the router not to fragment the packet, but instead to discard the packet

## Slide 59: Path MTU Discovery
An ICMP message is returned by the router to the sender, with a code saying the packet has been discarded and stating the reason was the MTU was exceeded
This message also tells the end point what the MTU is
The end point may then divide the unit of information itself into chunks that match this MTU

## Slide 60: Path MTU Discovery
For multiple links the end point keeps a table of the MTU of the various IP addresses it is sending to
When there are a series of links along the path, each with smaller MTUs, the above process may take place a number of times, before the sender finally determines the minimum MTU

## Slide 61: Common MTUs
Ethernet | 1,492
Token Ring – 16 MBps | 17,914
Token Ring – 4 MBps | 4,464
IP | 65,535
PPP | 1,500

## Slide 62: Fragmentation
Fragmentation is only applied to the data portion of a datagram
All fragments carry the full header
Fragments are not reassembled until they reach the end point
Fragments are stored in memory until all of them arrive, then they are reassembled