## Slide 1: Fiber Optic Media Last Update 2014.08.09 1.18.0

## Slide 2: Objectives
Learn about the different types of fiber optic media

## Slide 3: Sending Data
Data can be sent over the media by
  Varying - modulating - an electrical signal as it passes over a copper wire
  Varying - modulating - the power of light as it is sent over a glass optical fiber
  Varying – modulating - the radio waves sent through space, which is commonly referred to as a wireless communications system

## Slide 4: What is Fiber Optic Cable
Fiber optics is a medium for carrying information from point to point using light as the transmission media
This is different from the more common copper cables that use electrical energy to carry the information

## Slide 5: Fiber Optic Interface

## Slide 6: Reasons to Use
There are four main reasons to use fiber instead of copper cables
  The long distances a fiber cable can run without loss of signal
  Resistance to interference
  Better security
  The carrying capacity of the fiber cable compared to a copper cable

## Slide 7: Fiber Compared to Copper

## Slide 8: Construction
Optical fiber for telecommunications consists of three components
They are the core, the cladding, and the coating

## Slide 9: Construction

## Slide 10: Construction

## Slide 11: Construction

## Slide 12: Construction
The core is the central region of an optical fiber through which light is transmitted
Glass is the common media for the core

## Slide 13: Construction
The cladding is manufactured together with the core as a single piece of silica glass with slightly different compositions, and they cannot be easily separated from one another
The glass does not have a hole in the core, but is completely solid throughout

## Slide 14: Construction
The lower refractive index of the cladding acts like a mirror reflecting the signal back into the core as it travels
The third section of an optical fiber is the outer protective coating called the buffer
This coating is typically made of plastic
It provides physical and environmental protection for the fiber

## Slide 15: Construction
The outer components of fiber optic cable differ depending on the purpose and application of the cable
Fiber optic cable that is used in telecommunications is typically made of glass
Plastic is used in some very limited cases
This plastic or POF – Polymer Optical Fiber is limited in bandwidth and distance

## Slide 16: Construction
Specifically around 100 Mbps and up to 50 meters
The core size of plastic fiber is also quite a bit larger at 490, 200, and 120 nm
Generally speaking fiber requires two cables, one to transmit and one to receive
These may be bonded side by side or inside another covering cable

## Slide 17: Lab
Pass around samples of different types of fiber optic cable

## Slide 18: Types of Fiber Optic Cable
In terms of the intended use of the cable there are two different types of fiber optic cable
  Tight Buffer
    For indoor use
  Loose Tube
    For outdoor use

## Slide 19: Types of Fiber Optic Cable

## Slide 20: Tight Buffer Fiber Construction
As stated the construction of the outer covering of the cable depends on how it will be used
Tight buffer construction is used for indoor applications

## Slide 21: Tight Buffer Fiber

## Slide 22: Loose Tube Fiber Construction
Loose tube design is used for most outdoor cables
In loose tube cable the fiber, with its covering, is contained inside of a gel, that is held inside of another cover
The gel combats the harmful effects of temperature, humidity, and mechanical loads

## Slide 23: Loose Tube Fiber Construction
Moisture will ruin the ability of the core to transmit a signal
Additional strength is provided by Kevlar yarn, armor sheaths, or steel messengers

## Slide 24: Loose Tube Fiber

## Slide 25: Loose Tube Fiber Construction
Some loose tube cables use a dry packing instead of a gel
In the dry packing type the packing is designed to fill in any nicks in the outer coating
The following photograph shows the gel type
The shiny substance on the inside of the orange cover is the gel

## Slide 26: Loose Tube Fiber
Gap between fiber and covering where gel goes

## Slide 27: Loose Tube Fiber Construction
The loose tube design also allows for stability in the cable when the temperature fluctuates
The buffer allows room for expansion and contraction

## Slide 28: Operation
The basic method of operation of a fiber optic system starts with a device on the network that takes the electrical energy that travels the normal computer network and translates it into light pulses
A transmitting device then places these signals onto a fiber cable by flashing the light source on and off in the pattern for the signal

## Slide 29: Operation
The cable carries the signal to the other end
At the far end a receiver accepts the light pulses
They are then converted back to an electrical signal for use in the computer

## Slide 30: Optical Media

## Slide 31: Operation
Optical fiber transmission utilizes wavelengths from above the visible light spectrum
The ITU – International Telecommunications Union has divided the mode wavelengths into bands as shown on the second chart

## Slide 32: Wavelength Chart
Cisco

## Slide 33: Wavelength Chart
Network Magazine
July 2001

## Slide 34: Wavelengths
As defined by the ITU the bands cover
  No label – 820 nm to 900 nm – for multimode cable
  O - 1260 nm to 1310 nm – for singlemode cable
  E – 1360 nm to 1460 nm – for singlemode cable
  S – 1460 nm to 1530 nm – for singlemode cable
  S+ - 1430 nm to 1480 nm - maybe
  C – 1530 nm to 1565 nm – for singlemode cable
  L – 1565 nm to 1625 nm – for singlemode cable
  U – 1625 nm to 1675 nm – for singlemode cable
nm = nanometer

## Slide 35: Wavelengths

## Slide 36: Operation
Typical optical transmission wavelengths are 850 nm, 1300 nm, 1310 nm, and 1550 nm
Both lasers and LEDs have been used to transmit light through optical fiber
Lasers are usually used for 1310 or 1550 nanometer, single-mode applications
LEDs are used for 850 or 1300 nanometer multi-mode applications

## Slide 37: VCSELs
In general at speeds at 1 Gigabit and above only lasers are used
For multimode cable VCSEL – Vertical Cavity Surface Emitting Lasers are used in place of LEDs
The reason for this is the slow signaling rate of LEDs

## Slide 38: VCSELs
They have a maximum rate of 622 Mbps as this is as fast as they can be turned on and off
This move toward VCSELs has also accelerated the move toward 50 micron fiber optic cable as the VCSELs do not work well with 62.5

## Slide 39: Caution
Never look into the end of a fiber which may have a laser coupled to it
Laser light is invisible and can damage the eyes
Viewing it directly does not cause pain
The iris of the eye will not close involuntarily as when viewing a bright light; consequently, serious damage to the retina of the eye is possible

## Slide 40: Caution

## Slide 41: Caution

## Slide 42: Caution
As the cabinets say

## Slide 43: Caution

## Slide 44: Caution

## Slide 45: Operation
Once light enters a fiber optic cable, it travels in a stable state called a mode
A mode is a ray of light, not the entire light beam - just a ray of that beam, that enters the fiber at a particular angle
There can be from one to hundreds of modes depending on the type of fiber

## Slide 46: Operation
Each mode carries a portion of the light from the input signal
Generally speaking, the number of modes in a fiber is a function of the relationship between core diameter, numerical aperture, and wavelength
In fiber optic cable it is desirable to have as few modes as possible

## Slide 47: Operation
Opposite of how it may seem the fewer modes the better
This is because single modes are more efficient
Think of it this way

## Slide 48: Beam Types
Laser | 
LED | 

## Slide 49: Operation
A single mode cable is just like the device used to send the signal, a laser
The beam is sharp and focused
It can travel a long distance before the strength weakens

## Slide 50: Operation
A multi-mode beam is like a cheap flashlight
The beam of light spreads out in all directions
As such, it soon plays out and things go dark just a few feet out from the end of the flashlight

## Slide 51: Fiber Optic Cable Issues
A fluke white paper on troubleshooting fiber optic cable pointed out these issues that are common to all types of fiber optic cable

## Slide 52: Attenuation
Attenuation in an optical fiber is caused by
  Absorption
  Scattering
  Bending
Attenuation is the loss of optical power as light travels along the fiber
Optical input power is the power injected into the fiber from an optical source

## Slide 53: Attenuation
Optical output power is the power received at the fiber end or optical detector

## Slide 54: Absorption
Absorption is a major cause of signal loss in an optical fiber
Absorption is defined as the portion of attenuation resulting from the conversion of optical power into another energy form, such as heat

## Slide 55: Scattering
Scattering losses are caused by the interaction of light with density fluctuations within a fiber
Density changes are produced when optical fibers are manufactured
During manufacturing, regions of higher and lower molecular density areas, relative to the average density of the fiber, are created

## Slide 56: Scattering
Light traveling through the fiber interacts with the density areas as shown in the figure below
Light is then partially scattered in all directions
This is primarily Rayleigh Scattering

## Slide 57: Bending
If the fiber cable were installed perfectly straight then the light that entered the cable at the suitable angles would easily reach the other end of the fiber without much degradation or loss in the cable
However there are small and large bends that affect fiber optic cable and its performance

## Slide 58: Bending
As light passes through these bends a certain amount of the light gets lost the more sharp the bend in the fiber becomes
If bends are numerous or severe, enough light may be lost so that the link fails
If the fiber is bent even further then the fiber is at risk of even breaking

## Slide 59: Bending
Two common types of bends in fiber are
  Micro
  Macro
Bending loss is classified according to the bend radius of curvature

## Slide 60: Bending
Micro bends are small microscopic bends of the fiber axis that occur mainly when a fiber is cabled, and in the manufacturing process
Macro bends are bends having a large radius of curvature relative to the fiber diameter
Micro bend and macro bend losses are very important loss mechanisms

## Slide 61: Bending
Fiber loss caused by micro bending can still occur even if the fiber is cabled correctly
Micro bend losses can be small discontinuities or imperfections in the fiber
Uneven coating applications and improper cabling procedures increase micro bend loss

## Slide 62: Bending
External forces are also a source of micro bends
An external force deforms the cabled jacket surrounding the fiber but causes only a small bend in the fiber
Micro bends change the path that propagating modes take

## Slide 63: Bending
Micro bend loss increases attenuation because low-order modes become coupled with high-order modes that naturally have more loss
Macro bend losses are observed when a fibers bend radius is larger than compared to the fiber diameter

## Slide 64: Bending
Practically speaking Macro bends are generally a result of the fiber being installed where it is bent to tightly either around a corner, as it enters the splice tray, patch panel
Micro bends can be a result of simply cinching a cable tie too tightly around the fiber cable or bundle

## Slide 65: Decibel to Power Table
Here is a table from Steenbergen that shows how this loss relates to dBs

## Slide 66: Decibel to Power Table

## Slide 67: Types of Fiber Optic Cable
In terms of how they carry the light there are two types of fiber optic cable
  Multi-mode
  Single-mode

## Slide 68: Types of Fiber Optic Cable

## Slide 69: Types of Fiber Optic Cable
In general, the telecommunications industry uses core sizes from 62.5 µm - micrometer down to 8.7 micrometers
  Multi-mode cable has a core diameter of 50 or 62.5 micrometers
  Single mode cable has a core diameter between 8 and 10 µm

## Slide 70: Types of Fiber Optic Cable
It is impossible to distinguish between multi-mode and single-mode cable by looking at it
The fibers are too small to accurately judge the size
The diameter of the cladding surrounding each of these cores is 125 µm, which is why they are labeled 62.5/125 or 8.7/125 for example

## Slide 71: Types of Fiber Optic Cable
A human hair is 70 µm or .003 inches thick

## Slide 72: Types of Fiber Optic Cable

## Slide 73: Types of Fiber Optic Cable

## Slide 74: Fiber Optic Cable
Fiber optic cable began to appear in the late 1970s into the early 1980s
Early fiber had a 50 micron diameter but this was soon changed to 62.5 due to the light emitting diode being based on an LED
The 62.5 cable allowed more of this dispersed light to be captured

## Slide 75: Fiber Optic Cable
As light sources moved from LEDs to VCSELs in the late 1990s there was no longer any need for this larger cable core
Current multimode cable is 50 micron

## Slide 76: Fiber Optic Cable

## Slide 77: Multi-Mode Fiber
Multi-mode fiber allows many modes, or paths, of light to propagate down the fiber optic path
Because these modes of light enter the fiber at different angles, they will arrive at the end of the fiber at different times
This characteristic is known as modal dispersion

## Slide 78: Multi-Mode Fiber
Modal dispersion limits the bandwidth and distances that can be traversed using multi-mode fibers
This is expressed as MBW

## Slide 79: MBW
For example 62.5 µm multimode fiber has a modal bandwidth equal to 160 MHz per km at 850 nm thus the maximum distance for Gigabit Ethernet is 220 meters
Whereas 62.5 µm multimode fiber with a modal bandwidth of 200 MHz per km at 850 nm has a maximum distance for Gigabit Ethernet of 275 meters

## Slide 80: MBW
If you are not sure what the MBW is for a cable, then the conservative case of a MBW of 160 should be used
Modal bandwidth is based on the individual pulses of light which make up a digital signal traveling along the fiber that will suffer some distortion

## Slide 81: MBW
This distortion is due to the energy traveling in different modes, so some of the light energy in a pulse travels along a longer path than other parts of the pulse
Graded Index fiber is used to overcome this problem
Steenbergen shows it this way

## Slide 82: MBW

## Slide 83: Multi-Mode Fiber
For this reason, multi-mode fiber is generally used for connectivity within a building such as a backbone cable
The relatively large core of a multi-mode fiber allows good coupling from inexpensive LEDs as light sources, and the use of inexpensive couplers and connectors

## Slide 84: Multi-Mode Fiber
This makes multi-mode most useful for short distance, low bandwidth applications
The 62.5 version of multimode cable is typically orange in color
The OM3 laser optimized multimode cable is commonly aqua in color
It is primarily used in LANs
Laser optimized cable can carry higher speeds using laser based equipment

## Slide 85: Multi-Mode Fiber
So be sure you know what size is being used for the fiber, the connectors, and the equipment
The primary advantage of multi-mode fiber over copper twisted pair cabling is that it supports longer segment lengths

## Slide 86: Multi-Mode Fiber
Multi-mode fiber can support segment lengths as long as 2,000 meters for 10 and 100 Mbps Ethernet, and 550 meters for 1 Gbps Ethernet

## Slide 87: Multi-Mode Fiber

## Slide 88: Types of Multi-Mode Fiber
As the textbook says
  Two types of multimode fiber exist, distinguished by the index profile of their cores and how light travels in them
  Step index multimode fiber has a core composed of one type of glass
  Light traveling in the fiber travels in straight lines, reflecting off the core/cladding interface

## Slide 89: Types of Multi-Mode Fiber
  The numerical aperture is determined by the differences in the indices of refraction of the core and cladding and can be calculated by Snell’s law
  Because each mode or angle of light travels a different path link, a pulse of light is dispersed while traveling through the fiber, limiting the bandwidth of step index fiber

## Slide 90: Types of Multi-Mode Fiber
  In graded index multimode fiber, the core is composed of many different layers of glass, chosen with indices of refraction to produce an index profile approximating a parabola
  Because the light travels faster in lower index of refraction glass, the light will travel faster as it approaches the outside of the core
  Likewise, the light traveling closest to the core center will travel the slowest

## Slide 91: Types of Multi-Mode Fiber
  A properly constructed index profile will compensate for the different path lengths of each mode, increasing the bandwidth capacity of the fiber by as much as one hundred times that of step index fiber
  Step index fiber is used where large core size and efficient coupling of source power is more important than low loss and high bandwidth
  It is commonly used in short, low-speed data links with LED sources

## Slide 92: Types of Multi-Mode Fiber

## Slide 93: Types of Multi-Mode Fiber
In the fiber optic cable industry multimode cable is also referred to using an OM nomenclature as in optical mode
This table from a webinar shows the different types of multimode cable from OM1 to OM4

## Slide 94: Types of Multi-Mode Fiber

## Slide 95: Types of Multi-Mode Fiber

## Slide 96: OM Types

## Slide 97: OM Types

## Slide 98: OM Types
OM1 and OM2 have been the only types commonly used with OM2 being by far the most common in building backbones
OM1 is basically obsolete
There is a shift to OM3 as it is laser optimized and therefore able to achieve higher data rates such as 10G

## Slide 99: OM Types
OM4 is for longer distances at 10G speeds as well as for short-range, high-speed backbones
As the shift is made from 62.5 to 50 the OM type purchased is also shifting from OM2 to OM3

## Slide 100: Single-Mode Fiber
Single-mode fiber has a core diameter that is so small, usually from 8 to 10 microns, that only a single mode of light is propagated
The exact size does not matter as long as it is in this range
This eliminates the main limitation to bandwidth, modal dispersion

## Slide 101: Single-Mode Fiber
Therefore, single-mode is capable of delivering considerably higher performance and over much larger distances, which is why it generally is used within environments that are more geographically dispersed

## Slide 102: Single-Mode Fiber
However, the small core of a single-mode fiber makes coupling light into the fiber more difficult, and thus expensive lasers must be used as light sources

## Slide 103: Single-Mode Fiber
Lasers produce higher bandwidth because their signaling rate is higher than an LED device
  That is the laser can turn on and off or cycle at a faster rate than an LED
  Therefore, more information can be placed on the channel in the same amount of time
For example

## Slide 104: Signaling Rate
Device | Time Span Zero to 1 Second |  |  |  | 
LED |  |  |  |  | 
Laser |  |  |  |  | 
It is how much is put into the pipe in a span of time Which is based on how fast the device can cycle on and off |  |  |  |  | 

## Slide 105: Single-Mode Fiber

## Slide 106: Single-Mode Fiber

## Slide 107: Single-Mode Fiber
This cable is usually yellow in color
It is used primarily outside of the LAN
Single mode is also referred to using the new nomenclature
  OS1
    This is basic single mode cable
  OS2
    This is the common low water peak single mode cable

## Slide 108: Multi-Mode v Single-Mode

## Slide 109: Multi-Mode v Single-Mode

## Slide 110: Types of Fiber Optic Cable
In terms of where the fiber optic cable can be used there are several types
  OFNP
    Plenum rated
  OFNR
    Riser rated
  OFNG
    General use

## Slide 111: Fiber Optic Cable Color Codes

## Slide 112: Fiber Optic Cable Colors
The approved colors for the outside cover of the various types of fiber optic cable is shown next on a slide from the Steenbergen presentation to NANOG 57 in 2013
Usually the short cables used inside use these color codes
A generic gray is commonly seen as well

## Slide 113: Fiber Optic Cable Colors

## Slide 114: Lab
Examine different type of fiber optic cable
Answer these questions about each one
  Type of cable
  Manufacturer
  Model number

## Slide 115: Transmission Distances
Using the standard methods multimode fiber optic cable can transmit data 2,000 meters without repeaters
Using common proprietary methods longer distances are possible
Singlemode cable can easily extend 80,000 meters
There is a formula to calculate the maximum transmission distance

## Slide 116: Transmission Distances
Link Length =
Available Power minus Link Loss
Divided By
Length Dependent Link Loss
Where
  Available Power in dB =
  Minimum Transmit Power in dBm minus Receive Sensitivity in dBm
  Link Loss in dB =
  Connector Loss in dB plus Fudge Factor in dB
  Link Dependent Link Loss =
  Maximum Attenuation in dB per km plus Splice Losses in dB per km

## Slide 117: Transmission Distances
These values are available from the equipment manufacturers
Here are some common figures for various fiber standards from Fluke

## Slide 118: Transmission Distances

## Slide 119: Use of Fiber

## Slide 120: Use of Fiber

## Slide 121: Use of Fiber
Fiber is widely used to interconnect long distances such as between cities and continents
Sometimes problems occur with these links
For example

## Slide 122: Use of Fiber

## Slide 123: Use of Fiber

## Slide 124: Use of Fiber

## Slide 125: Use of Fiber
Notice how long the fiber has been down

## Slide 126: Fiber Connectors
Several styles of connectors are used to terminate fiber optic cable
We will look at the more common ones

## Slide 127: ST Connector
ST - Straight Tip is a single tip connector similar to a BNC connector
This is the older style connector
It is still very widely used
It is sometimes referred to as a stick and twist as in ST

## Slide 128: ST Connector

## Slide 129: ST Connector

## Slide 130: SC Connector
SC - Subscriber Connector is a push on connector
It is also called a snap and click as in SC
This connector can be round, but is more commonly square
The square style has a latch that prevents the sections from coming apart

## Slide 131: SC Connector

## Slide 132: SC Connector

## Slide 133: Duplex or Simplex Connectors
ST and SC connectors can come in a duplex or simplex configuration
The difference is whether both the send and receive connectors are bonded or attached to each other or not
The duplex connector makes it easier to keep the send and receive straight
In any case they are color coded

## Slide 134: Duplex Connector

## Slide 135: Simplex Connector

## Slide 136: Small Form Factor Connector
The latest connector contains both connections inside of a single unit unlike most of the connectors discussed above
This connector puts both connections in a space of an RJ-45 connector
This allows manufacturers to pack more connectors in the same space

## Slide 137: LC Connector
The most common small form factor connector is the LC
It uses the common SC style but in a smaller size
This is seen in the next slide
  The connector at the top is a duplex SC
  The one at the bottom is a duplex LC

## Slide 138: LC Connector

## Slide 139: LC Connector

## Slide 140: MPO Connector
As 40G and 100G is deployed a connector that has more than two strands will be needed as these speeds use several at a time to achieve the speeds
A MPO connector can do this in a small form factor
Notice the multiple stands side by side here

## Slide 141: MPO Connector

## Slide 142: Who Uses What
As reported in an article by 3M a survey at a trade show from November 2013 suggested this is the amount of use of each type of connector

## Slide 143: Who Uses What

## Slide 144: Lab
Examined fiber optic cable connectors
Answer the following questions
  Type
  Simplex or duplex

## Slide 145: Differential Mode Delay
Another type of connector, which is actually a combination of connectors and cable, may be required when connecting singlemode and multimode equipment to each other

## Slide 146: Differential Mode Delay
When an unconditioned laser source that was designed for use with singlemode fiber cable is directly coupled to a multimode cable, an effect known as DMD - Differential Mode Delay may occur

## Slide 147: Mode Conditioning Cables
DMD can degrade the modal bandwidth of the fiber-optic cable, which causes a decrease in the link span, in other words the distance between the transmitter and the receiver
Mode Conditioning Cables, which as also known as Gigabit launch cables, are used when one of these singlemode devices is used with a multimode cable

## Slide 148: Mode Conditioning Cables
The function of the Mode Conditioning Cable is to provide an offset launch of the 8.3 µm singlemode core, into the 62.5 or 50 µm multimode core
Without this type of cable, multiple overlapping signals can occur when a singlemode signal is launched into the area of a multimode core

## Slide 149: Mode Conditioning Cables

## Slide 150: Equipment Modules
For the cable to be connected to the equipment, such as a switch or a router, it must have a port for the fiber optic cable
There are two ways to do this
  In some equipment the port is built-in to the equipment
  In other cases a module is plugged in

## Slide 151: Equipment Modules
Using a module allows the same box to handle different types of cable
There are two types of modules
  GBIC – Gigabit Interface Converters
  SFP – Small Form Pluggable
The GBIC is the older style

## Slide 152: Equipment Modules

## Slide 153: GBIC

## Slide 154: SFP

## Slide 155: Media Converter
Some times to save money fiber optic cable will be run from one point to another, but the devices at the ends, such as a switch, will have copper ports, since copper based boxes are cheaper than ones with fiber interfaces
To convert the copper port to the fiber optic cable a media converter is required
Such as

## Slide 156: Media Converter

## Slide 157: Sources
The slides with the blue top are from a presentation to NANOG 57 in February 2013 by Richard Steenbergen