## Slide 1: How to Use a Fluke DTX Cable Tester Last Update 2013.08.04 2.1.0

## Slide 2: Objectives
Learn how to use a Fluke DTX cable tester

## Slide 3: What is a Fluke DTX Test Unit
The Fluke DTX test unit is used to ensure copper and fiber optic cable and connections have been installed to the category or test level required for an installation

## Slide 4: Uses
This tester can be used to test
  Copper Cable
    UTP
    Coaxial
  Fiber Optic Cable
    Singlemode
    Multimode

## Slide 5: Tests That Can Be Done
A cable test regardless of the type of cable requires a test device on each end
For copper cable using this unit that is
  DTX CableAnalyzer
  DTX SmartRemote

## Slide 6: Tests That Can Be Done
For fiber optic cable using this unit that is
  DTX CableAnalyzer with the Fiber Module attached
  DTX SmartRemote with the Fiber Module attached
  or
  DTX CableAnalyzer with the Fiber Module attached
  SimpliFiber light source

## Slide 7: DTX CableAnalyzer
Here is what the CableAnalyzer looks like

## Slide 8: DTX CableAnalyzer

## Slide 9: Test Unit Setup
Regardless of the cable being tested the device must first be configured
This involves
  Telling the units what type of cable they will be testing
  Setting the reference level
The procedure for both copper and fiber optic cable will be discussed, beginning with copper UTP cable

## Slide 10: Setup for Copper Testing
Connect the two units to each other as shown here

## Slide 11: Setup for Copper Testing

## Slide 12: Setup for Copper Testing
To setup the CableAnalyzer to test UTP cable to a category’s requirements do the following
  Turn the unit’s selector to
    Setup
  On the screen select
    Twisted Pair
    Test Limit
      Whatever test limit you are testing

## Slide 13: Setup for Copper Testing
    Cable Type
      UTP
      Whatever cable type you are testing
    Outlet Configuration
      Whatever outlet configuration you are testing

## Slide 14: Set the Reference Level
Before testing copper cable the reference level should be set between the two CableAnalyzer and the SmartRemote
This sets a zero point to test from
First connect the two units to each other as shown below
Turn on both units
Turn the rotary switch to Special Functions

## Slide 15: Set the Reference Level
  Select Set Reference
  Press Enter
  Press Test

## Slide 16: Running the Test
Attach adapters appropriate for the job to the tester and the smart remote
Turn the rotary switch to AutoTest and turn on the smart remote
Connect to the installed cabling, as shown below depending on whether this is a permanent link or a channel

## Slide 17: Running the Test
Press Test
  To stop the test at any time, press Exit
The tester shows the AutoTest Summary screen when the test is complete
To view results for a specific parameter, use the Up and Down Arrow buttons to highlight the parameter, and then press Enter

## Slide 18: Running the Test
If the AutoTest failed, press F1 Fault Info for possible causes of the failure

## Slide 19: Permanent Link

## Slide 20: Channel

## Slide 21: UTP Test Results

## Slide 22: Failed UTP Test Results

## Slide 23: Testing Fiber Optic Cable
To test fiber optic cable a module is added to the CableAnalyzer and the SmartRemote
These two units when used together constitute an OLTS – Optical Loss Test Set
or
The unit at the remote end can be a SimpliFiber light source

## Slide 24: Fiber Module
The fiber module is used to allow the DTX to test fiber optic cable
This is attached to the back of the main and remote units

## Slide 25: Fiber Module

## Slide 26: SimpliFiber
In place of the fiber optic cable module attached to the SmartRemote of the DTX system a SimpliFiber end unit can be used
It looks like this

## Slide 27: SimpliFiber

## Slide 28: Fiber Testing
The fiber test example presented here is the test used for multimode cable as it is commonly used as a backbone cable inside of a building
This is a simple insertion loss test
The purpose of this test is to determine if any damage occurred during installation or termination

## Slide 29: Fiber Testing
For example, the cable itself may have micro or macro bends that will cause excessive loss
A connector may not have been properly installed
The cable end faces may be too dirty

## Slide 30: Steps in Fiber Testing
To perform a fiber optic multimode cable test
  Compute the allowable loss
  Setup the display unit
  Setup the remote light source unit
  Clean the connections
  Set the reference level
  Perform the test

## Slide 31: Compute the Allowable Loss
In most cases the expected loss must be calculated based on the number of connectors, splices, and length of the installed cable, then compared to the actual loss for a pass or fail of the link
The DTX CableAnalyzer will do this for you

## Slide 32: Compute the Allowable Loss
Even though it is calculated for us with these units let’s compute the expected loss just to see how it is done

## Slide 33: Compute the Allowable Loss
In this example, which is typical for a multimode fiber backbone cable we have
  Length of cable
    150 feet
    At 0.001067 dB of loss per foot
  Connectors
    One at each end using no polish connectors
    At 0.75 dB of loss per no polish connector

## Slide 34: Compute Allowable Loss
For this example of 150 feet of cable with a connector at each end
  (0.001067 X 150) + 0.75 + 0.75
  1.66 dB of loss in a perfect installation
Of course this number will vary depending on the characteristics of the actual installation in the field
These values for connector loss are also way to high

## Slide 35: Compute Allowable Loss
As most connectors these days have a typical loss of .1 dB and a maximum loss of .5 dB this allowable loss is going to be way high
Still .75 is considered to be the standard loss number used for these types of calculations
It provides an extra margin as well

## Slide 36: Compute Allowable Loss
If you wish to take the belt and suspenders approach you may add the commonly used fudge factor of 3 dB to the computed number to be sure the connection will still work as things deteriorate over time from slight damage and dirty connections
This would make the number to enter 4.66 in this example

## Slide 37: Compute Allowable Loss
Shown next are tables where the basic numbers are computed for common distances in feet for the two multimode test wavelengths
In our case the cable length is 150 feet
The value in the table for 100 feet is 1.6067
The value for 200 feet is 1.7134

## Slide 38: Compute Allowable Loss
So the table value for 150 feet is 1.66

## Slide 39: Compute Allowable Loss

## Slide 40: Compute Allowable Loss

## Slide 41: Setting the Fiber Test Settings
The next step is to setup the test units to do the type of test we want to do

## Slide 42: Setting the Fiber Test Settings
Turn on both units
On the CableAnalyzer turn the unit’s selector to
  Setup

## Slide 43: Setting the Fiber Test Settings
On the screen select
  Fiber Loss
    Test Limit
      Select or setup the test limit for the link to be tested
    Fiber Type
      Select the type of fiber being tested
        Multimode 62.5 in this example

## Slide 44: Setting the Fiber Test Settings
    Remote End Setup
      Smart Remote for the DTX SmartRemote
      or
      Far End Source for the SimpliFiber unit
    Bi-Directional
      No

## Slide 45: Cleaning Fiber Before Testing
Fiber connectors need to be clean before testing
To clean use 98% pure isopropyl alcohol or fiber cleaning fluid and optical grade wipes and swabs

## Slide 46: Cleaning Fiber Before Testing
To clean a connector in a patch panel
  Place a drop of cleaning solution on a fiber wipe
  Firmly touch the tip of a fiber optic cable cleaning swab to the damp spot to transfer the cleaning solution to the swab
  Insert the swab firmly against the end face inside the connector
  Pushing against the connector end face twist the swab round about 3 times

## Slide 47: Cleaning Fiber Before Testing
  Repeat this with a dry swab to remove any excess cleaning fluid

## Slide 48: Cleaning Fiber Before Testing
To clean a connector on a cable
  Place a drop of cleaning solution on a fiber wipe
  Wipe the tip of the connector to the damp spot
  Wipe the tip with a dry fiber wipe to remove any excess cleaning fluid

## Slide 49: Set the Reference Level
An accurate reference level must be set before any measurements are made in order for the CableAnalyzer to determine if the link passes or fails
It determines this by using the setup information to extract and use stored values for the characteristics selected during setup
Let’s set the reference level

## Slide 50: Set the Reference Level
Turn off both the DTX CableAnalyzer units
Setting the reference level requires two equal length patch cables with a connector at each end
One should be marked as cable 1 and the other as cable 2

## Slide 51: Set the Reference Level

## Slide 52: Set the Reference Level
Connect the black connector on either end of the patch cord labeled 1 to the input port on the CableAnalyzer
Leave the red end of this end of the cable loose

## Slide 53: Set the Reference Level
Connect the red connector at the other end of the patch cable labeled 1 to the output port of the remote unit
Leave the black connector of this end of the connector loose

## Slide 54: Set the Reference Level
Connect the red connector on either end of the patch cord labeled 2 to the output port on the CableAnalyzer
Leave the black end of this end of the cable loose

## Slide 55: Set the Reference Level
Connect the black connector at the other end of the patch cable labeled 2 to the input port of the remote unit
Leave the red connector of this end of the connector loose

## Slide 56: Set the Reference Level
If this is all done correctly the units will chirp

## Slide 57: Set the Reference Level
On the CableAnalyzer turn the unit’s selector to
  Special Functions
On the screen select
  Set Reference
The Set Reference screen is displayed

## Slide 58: Set the Reference Level
This screen shows a reference diagram
  Verify that the diagram matches your setup
  Press Test
After the test
  Press F2

## Slide 59: Set the Reference Level
Once the reference is set do not unplug the cable from either output port
Otherwise the reference will need to be reset

## Slide 60: Test the Link
Remove the inputs on each end
For cable 2 which is attached to the CableAnalyzer hook the black connector of the end of the cable where the red connector is already attached to the unit to the input port

## Slide 61: Test the Link
For cable 1 which is attached to the remote unit hook the black connector of the end of the cable where the red connector is already attached to the unit to the input port

## Slide 62: Test the Link
Connect cable 1 to cable 2 by using a dual sided connector to attach the remaining connectors this way
  Cable 1 red to one end of the cable to be tested red connector
  Cable 1 black to one end of the cable to be tested black connector

## Slide 63: Test the Link
For cable 2 which is attached to the CableAnalyzer hook the black connector of the end of the cable where the red connector is already attached to the unit to the input port

## Slide 64: Test the Link
Connect cable 1 to cable 2 by using a dual sided connector to attach the remaining connectors this way
  Cable 2 red to one end of the cable to be tested black connector
  Cable 2 black to one end of the cable to be tested red connector

## Slide 65: Test the Link
The unit should chirp

## Slide 66: Using Mandrels
There is a lot of back and forth about the need to use mandrels when testing fiber optic cable
As the cost of these is so small and the attachment of them to the patch cables is so easy, I fail to see why so much discussion revolves around this topic
Here is some of that discussion

## Slide 67: Using Mandrels
The reason the instructions call for this is if an LED light source is used at the far end of the link, then a mandrel should be used
The mandrel acts as a mode filter to remove the unwanted high order modes from the light source
This occurs as the less accurate LED overfills the fiber

## Slide 68: Using Mandrels

## Slide 69: Using Mandrels

## Slide 70: Using Mandrels
Mandrel wrapping is a technique used to create a defined mode power distribution
If the launch optical fiber is fully filled ahead of the mandrel wrap, the higher order modes will be stripped off, leaving only the lower order modes
This is required for the meter attached to the other end to properly measure the light received

## Slide 71: Using Mandrels

## Slide 72: Wrapping Mandrels
A patch cord is wrapped around the mandrel as show next

## Slide 73: Wrapping Mandrels

## Slide 74: Using Mandrels
Many argue against using these as they say in practice the large limits that are acceptable for these tests are sufficient that a mandrel need not be used
An article in a 2009 issue of BICSI News explained this very clearly
It says

## Slide 75: Using Mandrels
  The use of a mandrel, a smooth rod, is one additional practice specified by TIA standards to achieve the most accurate loss measurements during calibration and testing
  A multimode launch cord is wrapped five times - nonoverlapping around the mandrel before calibration

## Slide 76: Using Mandrels
  Consistency can be improved by taping the cord around the mandrel and then taping the entire assembly to the source to reduce undesirable movement of the launch cord in relation to the source
  The diameter of the mandrel is determined by the launch cord core size and construction, as shown in Table 3

## Slide 77: Using Mandrels
  The purpose of the mandrel in multimode testing is to remove the modes, or pathways, of light near the outer edge of the core, as shown in Figure 3
  Without a mandrel, these outer modes of light will make it through the short launch cord to the meter during calibration and ultimately be included in the reference measurement

## Slide 78: Using Mandrels
  When the link test is performed, the normal bends and connections of an installed link will cause these outer modes to be lost, and using a mandrel gives a more realistic measurement by removing these outer modes before calibration
  Most technicians do not use mandrels—in fact, many have never seen one

## Slide 79: Using Mandrels
  However, acceptable test results are typically still achieved since the acceptance values specified in the standards are relatively lax as noted previously
  If unexpected high loss is encountered in an installed link, using a mandrel may resolve that high loss

## Slide 80: Warm Up
Let the test and remote unit warm up for five minutes before testing a link

## Slide 81: Measure the Loss
To measure the loss
  Turn the selector to Auto Test
  Press Test
  Read the result
The unit will report a pass or a fail

## Slide 82: Viewing Test Results

## Slide 83: Viewing Test Results

## Slide 84: Visual Fault Locator
The CableAnalyzer includes a visual fault locator
This function is used to check fiber continuity, as well as to find faults
To use this function
  Connect the fiber to the VFL port
  Press the VFL button next to the connector
  Look for a red light from the fiber

## Slide 85: Visual Fault Locator