## Slide 1: Terminating Copper Media Last Update 2012.08.01 1.6.0

## Slide 2: Objectives
Learn how to attach connectors to copper cable

## Slide 3: UTP Wires
Before attaching a connector to a UTP cable be certain the correct type of cable is being used
UTP cable is made of solid or stranded wires
Solid wires are used to connect work areas to the LAN room as stranded wires attenuate faster

## Slide 4: UTP Wires
By solid I mean that each of the eight wires is a single piece
Stranded wire is used for patch cables, as it is easier to manage for this use only, where the cables are never very long
By stranded I mean that each of the eight wires is made up of several individual wires, but there are still only eight wires

## Slide 5: Use the Correct Connector
Also use the correct type of connector
As AMP says
  The conventional plug has in-line insulation displacement contacts that pierce the middle of the insulation and stranded wire when crimped
  RJ45 plugs designed for solid conductors have offsetting contacts that straddle and wedge the cable’s solid conductor

## Slide 6: Use the Correct Connector
  If a RJ45 plug designed for stranded conductors is crimped onto solid conductors, the blade’s piercing teeth will be deflected and bent by the cable’s center conductors resulting in an intermittent connection
  However, the newer tri-point plugs are designed for both stranded and solid conductors and will successfully terminate both types of conductors

## Slide 7: Use the Correct Connector
Fluke also discusses this issue
They say
  Using the wrong style of pin may cause intermittent connections after a period of time, though the cable usually works immediately after it is made

## Slide 8: UTP Termination Contacts

## Slide 9: UTP Termination Contacts

## Slide 10: UTP Connectors
In a LAN both ends of a UTP cable are terminated using RJ style connectors
Specifically the RJ-45 connector

## Slide 11: RJ-45 Jack

## Slide 12: RJ-45 Plug

## Slide 13: UTP Connection Method
Methods of connecting wires to their connectors include 110, BIX, and Krone
The 110 method is the most common
It uses the IDC – Insulation Displacement Method to attach the wires to the connector
This is done with a punch down tool or by crimping with pliers, depending on the style of connector being used

## Slide 14: UTP Connection Method
This either pierces the wire with a point on the connector’s contact as in a plug or pushes the wire down into a V groove in the connector in a jack
In a jack the restriction in the groove cuts through the insulation, thus making the connection
A wire with its cover is pushed down into a groove that narrows toward the bottom

## Slide 15: UTP Connection Method
As the cable goes down into this groove, the metal the groove is formed from, cuts through the cover, and makes contact with the copper wire inside

## Slide 16: IDC
Metal that forms the groove
Opening that forms the groove
Cable jacket
Wire

## Slide 17: IDC

## Slide 18: IDC

## Slide 19: UTP Wiring Schemes
Before beginning you must decide what wiring scheme to use
There are two schemes
  568A
  568B

## Slide 20: UTP Wiring Schemes
Keep in mind that UTP cabling uses an 8-wire modular connector called the RJ-45
The trick is in making sure that you connect the right colored wire to the right pin in the RJ-45 connector
568A, 568B, 258A, and USOC are all standards which describe which wire goes on which pin

## Slide 21: UTP Wiring Schemes
The first thing to remember is that the 8 wires are always thought of as 4 pairs
And no matter which cabling standard you follow, the pairs are always colored the same

## Slide 22: UTP Wiring Schemes
Pair 1
  Blue
    Blue
    Blue with White stripe
Pair 2
  Orange
    Orange
    Orange with White stripe

## Slide 23: UTP Wiring Schemes
Pair 3
  Green
    Green
    Green with White stripe
Pair 4
  Brown
    Brown
    Brown with White stripe

## Slide 24: UTP Wiring Schemes
Pin numbers are important to this discussion as well

## Slide 25: RJ-45 Jack Pin Locations
For a jack the pin locations are shown on the device
There is no standard for this so it may vary by manufacturer

## Slide 26: RJ-45 Jack Pin Locations

## Slide 27: RJ-45 Plug Pin Locations
For a plug when looking down at a plug from the top with the clip side down, pin 1 is on the left
Here is a great illustration of this from Wikipedia and another one from a presentation at Interop

## Slide 28: RJ-45 Plug Pin Locations

## Slide 29: RJ-45 Plug Pin Locations

## Slide 30: RJ-45 Pin Locations

## Slide 31: UTP Wiring Schemes
As you look at the diagrams below, note that
  The solid color wires and the striped wires always alternate
  Pin 1 is always a striped wire
  Pair 1, blue, is always in the middle on pins 4 and 5
  The orange and green pairs are interchanged

## Slide 32: UTP 568A Wiring Scheme

## Slide 33: UTP 568A Wiring Scheme
The 568A standard is supposed to be the preferred way of terminating cable
It is so because it matches the old USOC standard
However, keep reading as most do not use the 568A method
By the way it matches the method of terminating cable that Northern Telecom used for ISDN

## Slide 34: UTP 568B Wiring Scheme

## Slide 35: UTP 568B Wiring Scheme
Before the TIA ever met to begin creating the 568A standard for cable terminations, AT&T had a very similar standard for terminating their cable, called 258A
258A works just as well as 568A
In fact, the TIA committee decided to include AT&T's 258A standard, but they called it the 568B standard
258A and 568B are exactly the same

## Slide 36: UTP 568B Wiring Scheme
This is what happens when committees try to make everyone happy

## Slide 37: Wires Used

## Slide 38: UTP Crossover Wiring
Here are some great illustrations of the wiring for crossover cables
First 10 and 100 Mbps
The 1000 Mbps

## Slide 39: UTP Crossover Wiring Schemes

## Slide 40: UTP Crossover Wiring Schemes

## Slide 41: UTP Crossover Wiring Schemes

## Slide 42: Why These Pin Assignments
Why are the pin locations different
First, to confuse you
But the arrangement is somewhat logical, if you know the background
Ethernet was originally designed to run over the same cabling used by the phone system - AT&T deployed this as StarLAN - so this design left pins 4 and 5 available for a phone

## Slide 43: Why These Pin Assignments
If you plug an RJ-11 - 4 wire - into this, the middle two pins – 2 and 3 - of the RJ-11 would connect to the middle two pins – 4 and 5 - of the RJ-45, just perfect for a 1-line phone
If you plug an Ethernet cable into it, pins 1 and 2 will be used as one pair, and pins 3 and 6 will be used as another
So, no conflicts

## Slide 44: UTP Wiring Schemes
The bottom line is, use whichever scheme you wish
It makes no difference
Just be consistent throughout the network in which one you use
By far 568B is the most widely used in the industry in the US
Although the preferred standard is 568A

## Slide 45: UTP Wiring Schemes
The US government requires 568A, unless a waiver is granted
Most other countries use 568A
Again why is this, just to make it harder on you

## Slide 46: Terminate All the Wires
In some cases I have found that not all of the wires are terminated
The thinking seems to be that Ethernet as originally used only used four, so just terminate those four
This is bad practice do not do this
Also I understand, although I have never used it, that some Krone connectors only use four wires

## Slide 47: Attaching Wires to a Jack
Let’s see how to attach the wires to a jack
Here are some views from the L-com.com web site, these are also in their catalog, which I highly recommend

## Slide 48: Attaching Wires to a Jack

## Slide 49: Attaching Wires to a Jack

## Slide 50: Attaching Wires to a Jack
Here is another method also from L-com
Different manufacturers use different methods, but this is a good example of a common method using pliers to clamp down a cap that holds the wires in place

## Slide 51: Attaching Wires to a RJ-45 Jack
Remove approximately 2” of the outer jacket from the cable
Take care not to nick the wires

## Slide 52: Attaching Wires to a Jack
Secure the cable jacket to the strain relief slot in cover

## Slide 53: Attaching Wires to a Jack
Untwist pairs and insert into color coded slots for either T568A or T568B standard
Take care to maintain the twist to within .5” of IDC contact

## Slide 54: Attaching Wires to a Jack
Trim excess wires flush with the cover edge

## Slide 55: Attaching Wires to a Jack
Snap the prepared cover in place

## Slide 56: Attaching Wires to a Jack
Seat the cover with parallel action pliers

## Slide 57: Attaching Wires to a Jack
The termination at the patch panel end of the connection involves stripping away some of the jacketing material and untwisting the conductors
The jacketing material should not be removed any more than necessary to complete a termination

## Slide 58: Jack

## Slide 59: Jack

## Slide 60: Patch Panel Termination
As stated in the 568 standard, the pairs in a Category 5 cable should never be untwisted more than 1/2 inch from the point of termination
Any further untwisting of the pairs will increase crosstalk and susceptibility to EMI/RFI

## Slide 61: Patch Panel Termination

## Slide 62: Patch Panel Termination
The wire order for a patch panel is usually indicated on it
Typically the wires go for each color solid and then the white strip for the color
For example

## Slide 63: Patch Panel Termination

## Slide 64: Punch Down Tool
A tool is used to push the cable down into the groove so as to allow the groove to cut through the cover and make contact with the wire inside
This tool is called a Punch Down tool

## Slide 65: Punch Down Tool

## Slide 66: Terminating in the Work Space
The next step is to terminate the cable in each work space area
There are two main ways to attach the jack used to terminate the cable in the work area
  Flush Mount
  Surface Mount

## Slide 67: Flush Mount Termination
The procedures shown above are the same ones used in the work area for a flush mount
The only difference is the jack is clipped to a wall plate

## Slide 68: Wall Plate in Office

## Slide 69: Surface Mount Termination
The second main way to place the termination point in a work space is by using a box that mounts directly to the wall
This avoids the problem of cutting a exact size hole in the wall
In some cases this takes too long
In other cases the wall is not suitable for this type of cutting

## Slide 70: Surface Mount Box

## Slide 71: Surface Mount Wiring
All of the following is also from the L-com site at www.l-com.com
Different manufacturers use different methods, but this is a good example of a common method where a punch down tool is used instead of pliers
In this case for a surface mount box, but the technique is the same for a flush mount box or a patch panel connection

## Slide 72: Surface Mount Wiring
Remove the cover and attach the jack base assembly using the supplied screws or double stick tape

## Slide 73: Surface Mount Wiring
Remove approximately 3” of the outer jacket from the cable
Take care not to nick the wires

## Slide 74: Surface Mount Wiring
Secure the cable with a cable tie to the desired entry point

## Slide 75: Surface Mount Wiring
Insert the pairs to the color coded slots taking care to maintain the twist to within .5” of IDC contact
Punch down using a 110 style tool

## Slide 76: Surface Mount Wiring
Trim excess wire if your 110 tool doesn’t cut it off
Snap on the retainer caps

## Slide 77: Surface Mount Wiring
Notch the cover to match the cable entry and snap it in place

## Slide 78: Wiring a RJ-45 Plug
An installer terminated RJ-45 plug is not part of the structured cabling standard
As the BICSI manual says
  Field-constructed patch cords are not recommended for category 5e and higher systems, and they may not be allowed for systems above category 5e

## Slide 79: Wiring a RJ-45 Plug
  There may be circumstances in which field-constructed category 5e patch cords are requested (e.g., repair of an existing patch cord because a spare is not available and the circuit must be restored)
  If this is the case, the repaired cord should be replaced with a factory certified cord as soon as possible
  ANSI/TIA/EIA-568-B.1 states that patch cords should not be field terminated

## Slide 80: Wiring a RJ-45 Plug
The reason for this is you cannot do this as good as a machine
You will not be able to get the outer cover up under the locking section of the plug
This will let the wires pull out too easily
Often you will have trouble getting all of the wires all the way into the end of the plug

## Slide 81: Wiring a RJ-45 Plug
Then one or more of them will make an intermittent connection
Even if the connector works initially, it will fail over time as you unplug then plug it back in over and over

## Slide 82: Wiring a RJ-45 Plug
Further that left over wire you are using is solid wire, where plugs are designed for stranded wire
Solid wire when flexed will begin to crack and eventually fail

## Slide 83: Wiring a RJ-45 Plug
All in all this is a bad idea
Just buy patch cables instead of making them
The only time you must attach a plug to a UTP cable is for an outside wireless connection

## Slide 84: EZ-Plug
For this purpose or if you feel you must do this, then use an EZ-Plug

## Slide 85: EZ-Plug

## Slide 86: EZ-Plug
As you can see this plug has holes in the end
You untwist as much cable as you want
After putting the wires in the proper order, pull them through the connector until they are tight against the inside of the connector
The crimper sets the IDC connections as well as cutting off the excess

## Slide 87: EZ-Plug
Here are the instructions

## Slide 88: EZ-Plug Instructions

## Slide 89: EZ-Plug Instructions

## Slide 90: EZ-Plug Instructions

## Slide 91: EZ-Plug Instructions

## Slide 92: EZ-Plug Instructions

## Slide 93: EZ-Plug Instructions

## Slide 94: EZ-Plug Instructions

## Slide 95: EZ-Plug Instructions

## Slide 96: EZ-Plug Instructions

## Slide 97: EZ-Plug Instructions

## Slide 98: Crimping
As the EZ-Plug instructions show a crimping tool is how a plug is attached to the wires in the UTP cable
This is true regardless of whether the connector is a standard style or an EZ-Plug

## Slide 99: Crimping Tool

## Slide 100: Crimping

## Slide 101: Crimping

## Slide 102: Screw Terminal RJ-45 Jack
I have seen screw terminal RJ-45 jacks such as were once used for Category 3 cable
These are not suitable for data cabling
The connections are not reliable
They require too much untwisting of the wires

## Slide 103: Screw Terminal RJ-45 Jack

## Slide 104: Selecting Patch Cables
In an article for the January 2012 issue of Cabling Installation and Maintenance magazine Andy Work and Tom McAllister present further detailed reasons for only buying high quality patch cables and never building your own
You should read the entire article
Here is part of what they say

## Slide 105: Selecting Patch Cables
  Much has been written about the availability and abundance of substandard patch cords
  Recently the Communications Cable and Connectivity published findings that indicated extremely high failure rates in patch cords from sources other than the major national brands
  Substandard patch cords not only fail to perform; they can even damage physical hardware

## Slide 106: Selecting Patch Cables
  The first indicator of a substandard patch cord is price
  If you are paying less than $4 for a 3-foot Category 6 patch cord, then odds are it is substandard
  Quality, as well as code- and standard-compliance, has a price tag

## Slide 107: Selecting Patch Cables
  A high-priced patch cord does not mean it is standards based and will pass the performance requirements; however, price is the first indicator to help guide your decision
  The RJ-45 modular plug is a highly engineered connector
  The housing is molded from a fire-resistant plastic that meets the UL 94-V.O standard
  A simple test you can conduct is to put a lighter to the clip on the connector

## Slide 108: Selecting Patch Cables
  If it catches fire and does not self-extinguish, you have found a substandard connector that violates code requirements
  The cord could contain V.2 material, which is less expensive
  The pins should be made from phosphor bronze, a hardened alloy that allows the plug to be rated a minimum life cycle of 750 insertions

## Slide 109: Selecting Patch Cables
  Other conductive metals being used are too soft and cannot withstand the insertion cycles that are required
  The last step in manufacturing the contact is to apply a minimum of 50 p. of 24-karat gold (23.999 pure)
  Today gold costs approximately $1,700 per troy ounce

## Slide 110: Selecting Patch Cables
  Seventy percent of the cost of a Category 5e or Category 6 modular plug is in the gold
  The number-one area in which substandard manufacturers are skimping is the gold plating
  Substandard plugs can have a multitude of gold-related issues, one being a lower grade of gold, such as 14-k gold

## Slide 111: Selecting Patch Cables
  There are two different types of marks, issued by either Intertek (ETL) or UL
  The two types are safety and performance
  Usually when an item has passed the safety standard it is said to be "safety listed“
  When an item has passed a standards-based performance test it is called "verified"

## Slide 112: Selecting Patch Cables
  With patch cords, you are not just dealing with components that need to be both listed and verified; the entire assembly should be listed and verified
  To determine if your product has these markings, inspect the cable legend to see if there is a UL "E" number printed on the jacket
  If there is, go to UL's Online Certification Directory and run the E number to verify the manufacturer's authorization and standing

## Slide 113: Selecting Patch Cables
  If you cannot find the E number in the Online Certification Directory, odds are you have found a fraudulent use of UL's mark
  ETL has a similar guide on its website
  If you find the ETL mark printed on the jacket, check to see if the manufacturer's name and control number are also on the jacket
  That name is required on the ETL website, so you can check the manufacturer's authorization

## Slide 114: Selecting Patch Cables
  There are several reasons a patch cord with all the proper components will not pass a test
  It can be as simple as too much untwisting of pairs, not seating the cable to the very end of the connector, or using the improper crimp tool
  Often, patch cords that use molded boots will have a higher failure rate than assembled patch cords

## Slide 115: Selecting Patch Cables
  If your patch cord does not have strain relief, there is a high likelihood that it was not the only thing forgotten when your patch cord was made
  Here is a checklist for you to use when buying patch cords
    How much does it cost
    Who am I buying it from
    Is it a molded or assembled connector
    Does the plug burn

## Slide 116: Selecting Patch Cables
    What is the fitment like
      How easily does it plug and unplug
    Does it have an E number or a manufacturer's name for verification
    Is there strain relief
    Do the pins look good
    Does the manufacturer perform 100-percent patch-cord testing, not just channel testing which is less demanding

## Slide 117: Connectors for Shielded Cable
For shielded cables both jacks and plugs designed for shielded cable must be used to terminate this type of cable

## Slide 118: Shielded Jack

## Slide 119: Shielded Plug

## Slide 120: Terminating Shielded Cable
As shown next terminating shielded cable requires not only the wires be securely connected, but also the shielding

## Slide 121: Terminating Shielded Jack

## Slide 122: Terminating Shielded Jack

## Slide 123: Terminating Shielded Jack

## Slide 124: Terminating Shielded Plug

## Slide 125: Installing Shielded Cable
In order for the shielding in the cable to be effective its integrity must be maintained
Breaks in the shield will mitigate this, such as allowing excessive bending of the cable that allows breaks in the shield
In addition, all components must be properly grounded
As an article in Cabling & Maintenance states

## Slide 126: Installing Shielded Cable
  The shield must be kept intact over the entire length of the cable, and must fully surround the cable and connecting hardware
  If the shield is, for example, formed into a pigtail over the last inch of the cable, it will reduce the protection against EMI and alien crosstalk
  In addition, avoid splitting the shield at sharp bends in the cable

## Slide 127: Installing Shielded Cable
  The shield is typically a ribbon of aluminum foil that is wrapped around the cable
  If the cable is bent at too sharp of a radius, the shield may separate, thereby reducing the effectiveness of the shield and its ability to protect against alien crosstalk
  The shield must be grounded on both ends of the link
  It is often said that a shield is 90% effective when it is grounded at one end of the link

## Slide 128: Installing Shielded Cable
  Such a shield continues to protect the wire pairs against many external high-frequency disturbances, but an open-ended shield may allow resonances at certain frequencies
  A resonance creates the chance that the signals couple into the data wire pairs, creating a significant alien crosstalk disturbance at those individual frequencies

## Slide 129: Installing Shielded Cable
  Field certification may record very low margins for alien crosstalk at those frequencies
  Because the shield should be terminated to ground at both ends, it is critical that the ground potential at both ends is approximately the same to avoid any ground-loop currents

## Slide 130: Installing Shielded Cable
  The TIA-607 standard on grounding and bonding allows a maximum difference in ground potential of 1 Vrms (Volt root mean square) between the two ends

## Slide 131: Installing Shielded Cable
  This rule requires that the telecommunications system is grounded throughout in compliance with the TIA-607 standard and that the electrical system in the building is correctly grounded and fully complies with rules spelled out in the National Electrical Code and other codes enforced by local jurisdictions

## Slide 132: Installing Shielded Cable
  In the field, you can verify that the ground potential meets the difference requirement before you connect the other end
  Connect the shield at one end, then measure the alternating-current voltage between the shield and the ground connection at the other end using a digital voltmeter that covers a bandwidth of 100 kHz or better

## Slide 133: Grounding Shielded Cable
The article goes on to discuss the end to ensure proper grounding of this type of cable
  TIA and ISO standards provide one additional step for the grounding of screened and shielded cabling systems

## Slide 134: Grounding Shielded Cable
  Specifically, clause 4.6 of ANSI/TIA-568-B.1 and clause 11.3 of ISO/IEC 11801:2002 state that the cable shield shall be bonded to the TGB in the telecommunications room, and that grounding at the work area may be accomplished through the equipment power connection

## Slide 135: Grounding Shielded Cable
  This procedure is intended to support the optimum configuration of one ground connection to minimize the appearance of ground loops, but recognizes that multiple ground connections may be present along the cabling

## Slide 136: Grounding Shielded Cable
  When the grounding and bonding recommendations specified in ANSI-J-STD-607-A-2002 were developed, consideration was given to the possibility that grounding at the work area through the equipment cord may occur; therefore, there is no need to specifically avoid grounding the screened/ shielded system at the user’s PC or device
  The difference between a ground connection and a screen/shield connection is notable and important

## Slide 137: Grounding Shielded Cable
  A ground connection bonds the screened/shielded cabling system to the TGB or TMGB, while a screen/shield connection maintains electrical continuation of the cable screen/shield through the screened/shielded telecommunications connectors along the full length of cabling

## Slide 138: Grounding Shielded Cable
  Part of the function of the screen or shield is to provide a low-impedance ground path for noise currents that are induced on the shielded material

## Slide 139: Grounding Shielded Cable
  Compliance to the TIA and ISO specifications for the parameters of cable and connection hardware transfer impedance and coupling attenuation ensures the maintenance of a low-impedance path through all screened/shielded connection points in the cabling system

## Slide 140: Grounding Shielded Cable
  For optimum alien crosstalk and noise immunity performance, shield continuity should be maintained throughout the end-to-end cabling system
  UTP patch cords in screened/shielded cabling systems should be avoided
  Building end users should perform a validation to ensure that screened and shielded cabling systems are properly grounded to the TGB or TMGB

## Slide 141: Grounding Shielded Cable
Here’s a recommended inspection plan
  Visually inspect to verify that all equipment racks/cabinets/metallic pathways are bonded to the TGB or TGMB using a 6-AWG conductor
  Visually inspect to verify that all screened/shielded patch panels are bonded to the TGB or TMGB using a 6-AWG conductor

## Slide 142: Grounding Shielded Cable
  Perform a DC resistance test to ensure that each panel and rack/cabinet grounding connection exhibits a DC resistance measurement of <1 Ω between the bonding point of the panel/rack and the TGB or TMGB. (Note: Some local/ regional standards specify a maximum DC resistance of <5 Ω at this location)
  Document the visual inspection, DC test results, and all other applicable copper/fiber test results

## Slide 143: Grounding Shielded Cable
As the excerpts from this article discuss it is important to properly ground shielded cabling systems
Siemons, a cabling manufacturer, says this about the specific procedure to follow

## Slide 144: Grounding Shielded Cable
  While electrical services, telecommunications equipment, and all other low voltage systems are required to be bonded to ground per national and local electrical codes and industry standards for safety reasons; the specific need to ground screened and shielded network cabling systems is only a matter of performance

## Slide 145: Grounding Shielded Cable
  A properly bonded and grounded cabling system carries noise currents induced by electromagnetic interference (EMI) in the environment to ground along the screen or foil shield, thereby protecting the data-carrying conductors from external noise

## Slide 146: Grounding Shielded Cable
  The screen or foil shield also minimizes cabling emissions
  It is these functions that afford screened and shielded systems their superior immunity to alien crosstalk and other sources of conducted or radiated electromagnetic interference

## Slide 147: Grounding Shielded Cable
The general recommended grounding sequence is as follows
  The outlet self-grounds to the patch panel
  Then the panel is grounded to the equipment rack or adjacent metallic pathways
  The basic sequence is reflected in the diagram below

## Slide 148: Grounding Shielded Cable
More specifically
  F/UTP cable screen or the S/FTP shield is terminated by the outlet
  Outlet makes contact with patch panel's grounding strip as outlets are snapped into place
  Panel is grounded to equipment rack or adjacent metal pathways via 6 AWG wire attached to panel ground lug
  6 AWG ground wire connects rack to the TGB

## Slide 149: Grounding Shielded Cable

## Slide 150: Grounding Shielded Cable

## Slide 151: Grounding Shielded Cable
Panduit explains it this way for the patch panel end
  Bond all the shielding (foil and/or braid) of the data cable to the shielded jack module, which provides 360° shielding termination
  Snap the jack module into an all-metal patch panel to create a bond between the module and the unpainted tabs on the patch panel

## Slide 152: Grounding Shielded Cable

## Slide 153: Grounding Shielded Cable
  Attach the patch panel to the rack using thread-forming bonding screws; the thread on the screws removes paint from the thread holes on the rack, and the serrations on the head of the screws remove paint from the patch panel, creating a high-performance electrical bond between the patch panel and the rack

## Slide 154: Grounding Shielded Cable
  So long as electrical continuity exists throughout the rack, the last step is to bond the rack to the main busbar or MCBN located under the data center’s raised floor
  To ensure long-term integrity of the system, always use compression connectors (not mechanical) so the connection does not loosen with vibration

## Slide 155: Grounding Shielded Cable

## Slide 156: Grounding Shielded Cable
Panduit goes onto to say concerning the workstation end
  During installation, a frequently asked question is whether the installer should ground one or both ends of a shielded cable channel
  Generally, the cable shield is bonded to the grounded equipment chassis or rack at each access or patch location

## Slide 157: Grounding Shielded Cable
  In other words, if the IT equipment is grounded, then any shielded cables used to connect equipment to patch panels, or to other equipment, must be grounded
  A typical shielded structured cabling channel runs from a switch to the workstation and comprises two patch cord links and the shielded horizontal link

## Slide 158: Grounding Shielded Cable
  One end of the channel starts in the data center where the switch, patch panel, and shielded patch cord linking them must be properly bonded to the rack
  The rack is tied to the telecommunications grounding system, which in turn is bonded to the AC power system
  The other end of the channel terminates outside the data center at the workstation outlet

## Slide 159: Grounding Shielded Cable

## Slide 160: Grounding Shielded Cable
  An issue to consider is whether a shielded cabling link at this outlet location can be properly bonded to a grounding system without inducing a ground loop
  A cable shield that is terminated at the workstation may be bonded to the AC ground via connections within the workstation itself, but the outlet AC ground must be at the same potential as the telecommunications grounding system

## Slide 161: Grounding Shielded Cable
  Therefore, to reduce the magnitude of such ground currents, all serving AC power systems must be bonded together to the same grounding electrode system
  A building can have only one grounding electrode system, as required by the National Electrical Code

## Slide 162: Grounding Shielded Cable
  This approach will reduce any ground voltage differences that may exist either between differing AC power system grounds or between the AC power system ground and the telecommunications ground

## Slide 163: Grounding Shielded Cable
  An alternative industry practice is to use UTP patch cords between the outlet and the workstation, effectively grounding only one end of the shielded cable channel in the data center and leaving the cable link at the workstation area ungrounded

## Slide 164: Grounding Shielded Cable
  The advantage of this option is that the risk of establishing a substantial ground loop current is greatly reduced
  This option, however, lowers the level of protection against external noise, such as alien crosstalk, EMI, and RFI, across that link in the channel, thus lowering system performance

## Slide 165: Grounding Shielded Cable
  It commonly is used only when it is not possible to eliminate voltage differences between ground potentials
To facilitate inspection of the grounding system, install connectors, busbars, and conductors in such a way to allow visual verification of the bond

## Slide 166: Grounding Shielded Cable
There should be a logical flow as you follow the grounding busbar
If a potential difference exists between these two points, a ground loop will form and current may flow within the loop

## Slide 167: Grounding Shielded Cable

## Slide 168: Grounding Shielded Cable
A method for testing whether a ground loop potential exists at a workstation is to use a true RMS multimeter to measure the potential difference between the power outlet ground and the shielded module on the workstation outlet

## Slide 169: Grounding Shielded Cable
Position one multimeter probe on the face of the shielded module on the workstation and the other in the grounding prong of the electrical outlet, and check the voltage reading on the meter

## Slide 170: Grounding Shielded Cable
If the meter reads less than 1 volt of potential (as described in ANSI J-STD-607-A Annex D) between the module and the power outlet, the endpoint device is expected to operate properly during steady-state conditions
If the meter reads 1 volt or more, a ground loop problem exists that may cause data errors or equipment damage

## Slide 171: Grounding Shielded Cable

## Slide 172: Patch Panel

## Slide 173: Patch Panel

## Slide 174: Terminated in the Patch Panel

## Slide 175: Terminated in the Patch Panel

## Slide 176: Standard Patch Panel

## Slide 177: Angled Patch Panel

## Slide 178: Smart Patch Panel
Some vendors are producing patch panels with network management capabilities
These smart patch panels and their required cables can
  Map the network's physical connections
  Trace circuits so as to perform basic connectivity tests
  Monitor these connections for unauthorized changes

## Slide 179: Smart Patch Panels
Here are some examples of these

## Slide 180: Smart Patch Panels

## Slide 181: Smart Patch Panels

## Slide 182: Smart Patch Panels

## Slide 183: Transceiver
On occasion a cable has been terminated with one type of connector and the device only has another type of connector
To solve this problem in an Ethernet network a transceiver is used
For example

## Slide 184: Transceiver
AUI
BNC
AUI
RJ-45
BNC
RJ-45