## Slide 1: Terminating Wireless Media
Last Update 2012.04.23
1.3.0

## Slide 2: Objectives
Learn how wireless media is terminated

## Slide 3: Terminating Wireless Media
Terminating wireless media is much simpler than terminating either UTP or fiber optic cable
Wired or guided media consists of a cable onto which an end must be placed
This cable carries the signal
The end or connector allows the signal to enter and exit the media

## Slide 4: Terminating Wireless Media
For wireless or unguided media the signal is flying around in the air
Termination of wireless media requires that this signal be captured by a device that will convert it into an electrical or optical signal that is then placed onto one of the guided media

## Slide 5: Terminating Wireless Media
The devices used to launch then recapture the wireless media form the termination points for the wireless media
This is either a radio with an antenna or a photodiode

## Slide 6: Basic Radio Frequency Parts
When the wireless media is made up of radio frequency waves these are the parts that form the termination
  Antenna
  Radio
    Made up of
      Amplifier
      Filter
      Mixer
      Source

## Slide 7: Basic Radio Frequency Parts
These five parts are then put together to do one of two basic functions
  Transmit
  Receive
The name of the resulting device is a radio

## Slide 8: A Radio
The radio may also go by many other names based on marketing considerations or its specific role in the wireless network
A radio is used to send and receive a signal that flows through the air as a series of electromagnetic waves
Radios can take on many different forms, as such it is not always easy to identify them

## Slide 9: The Transmitter
When transmitting or receiving the goal is to produce a perfect sine wave, of the exact size required, at only one frequency
A block diagram of the basic parts looks like this
For a transmitter

## Slide 10: Transmitter Block Diagram

## Slide 11: The Receiver
A block diagram of the basic parts looks like this
For a receiver

## Slide 12: Receiver Block Diagram

## Slide 13: The Basic Parts
The main job of the manufacturers of these basic parts is to attempt to make them
  Smaller
  Lighter
  More energy efficient
  Lower in cost
Now on to some details on each of these parts

## Slide 14: What is an Antenna
Every radio frequency wireless system must have an antenna
You may not see it
You may not recognize it, if you do see it
But it must be there somewhere

## Slide 15: What is an Antenna
The antenna does only one thing, it converts electrical signals coming from a conductor into airborne waves or it converts airborne waves into electrical signals to be sent down a conductor
Just as the RJ-45 connector is the termination point for a wired UTP media so is the antenna for wireless radio wave media

## Slide 16: How an Antenna Works
Being a resonant device it operates efficiently over a narrow frequency band
The real way an antenna does its work is somewhat complex
But for this level of discussion lets say it this way

## Slide 17: How an Antenna Works
An antenna begins to radiate energy, in the form of radio frequency waves, whenever the length of the antenna becomes close to the wavelength of the signal
When an alternating electric current flows through a conductor, electric and magnetic fields are created around the conductor

## Slide 18: How an Antenna Works
If the length of the conductor is very short compared to a wavelength, the electric and magnetic fields will generally fade out within one or two wavelengths
But as the conductor is lengthened, the intensity of the fields around it grow bigger
As such, an ever increasing amount of energy escapes into space

## Slide 19: Antenna Radiation Pattern
When selecting an antenna the width of the area to be covered and the distance of each link must be considered
These considerations will then determine the type of antenna to use based on each antenna’s signal pattern
Every antenna has a pattern to the signal
This pattern applies to both sending and receiving

## Slide 20: Antenna Radiation Pattern
By convention the radiation line used to draw this pattern is drawn wherever the power radiating out drops to one half the power at the antenna surface
For example, for a dipole antenna

## Slide 21: Antenna Radiation Pattern

## Slide 22: Antenna Radiation Pattern
As opposed to a directional antenna

## Slide 23: Antenna Radiation Pattern

## Slide 24: Antenna Radiation Pattern
Note in the diagram above that the radiation pattern does not have an even outline
In that there is a large main lobe, which is desired, and one or more side lobes, which are undesirable
These side lobes are also called the minor lobes

## Slide 25: Antenna Radiation Pattern
Antennas also have a front to back ratio that is measured in dBs
The forward gain is the peak gain on the main lobe of the antenna
The rear gain is measured as either the gain at exactly 180 degrees from the main lobe, or from 90 degrees to 270 degrees from the main lobe

## Slide 26: Antenna Radiation Pattern
Using the wider sector is the better way to measure this
These back lobes are also undesirable
A front to back ratio of 10-15 dB is considered fair to poor, 15-20 dB is good, 20-30 dB is very good, and above 30 dB is excellent

## Slide 27: Antenna Radiation Pattern
The regions in between the main and minor lobes are areas of weak signals called nulls

## Slide 28: Antenna Radiation Pattern
Main or Major Front Lobe
Side or Minor Lobe
Null
Back Lobe

## Slide 29: Antenna Radiation Pattern
The pattern provided by the manufacturer can be a rectangular grid or the more popular polar coordinate system just shown
The plotting scales used range from linear to linear logarithmic to modified logarithmic
The linear logarithmic and modified logarithmic are the ones most commonly used

## Slide 30: Antenna Radiation Pattern
These scales show the side and back lobes as well as the main lobe
For antennas in the frequencies of interest here these patterns are for the far field of the antenna
The far field region is the area in which wave propagation occurs
This field starts basically 10 wavelengths from the antenna

## Slide 31: Antenna Radiation Pattern
The radiation pattern of an antenna is adjusted in most cases by adding reflectors and directors
The reflector adds gain to the antenna, in relation to the isotropic antenna, by redirecting the signal
The director then concentrates the beam into an even tighter pattern

## Slide 32: Amplifier
Things often need to get bigger
In radio frequency systems an amplifier does this

## Slide 33: What is a Filter
A filter filters signals
Such as a bunch of signals all at different frequencies coming in and just one, the desired one, going back out
In essence a filter is the door bouncer at a trendy club
Some get in and some are kept out

## Slide 34: What is a Filter
Filters are used at the receive side as the antenna will pick up signals at and near the desired frequency
The filter removes the undesired ones
Governmental regulatory authorities say you may only transmit on the authorized frequency
The filter is designed to ensure this is the case

## Slide 35: What is a Mixer
A mixer seeks to change the frequency of a signal while keeping everything else about the signal the same
But why would you want to do this
One reason would be that your voice creates sound in the area of 2,000 Hertz, but a cell phone operates at 900,000,000 Hertz

## Slide 36: What is a Source
The source or oscillator is what generates the radio frequency
The desire is to produce a perfect sine wave at the desired frequency
Of course this never happens

## Slide 37: Using a Radio in a LAN
In a local area network the typical use of a radio is to create an access point at one end of a link in order for wireless clients to access the wired network
In other words the access point is the on-ramp to the wired network
Then on the other end, a radio is used in a network interface card to connect a client computer to the access point

## Slide 38: Access Point
Access points come in many forms
Here is an example from Cisco

## Slide 39: Access Point

## Slide 40: NIC
Wireless NICs are commonly built-in to computers these days
In this case they are just small circuit boards
An easier to see form is a wireless NIC as a PCMCIA card such as this Cisco card

## Slide 41: NIC

## Slide 42: Using a Radio in a CAN
When used to create a link for a campus area network radios are used to create a bridge
In this use two identical radios are set to talk to each other, and only each other
For example

## Slide 43: Bridge

## Slide 44: Free Space Optics
FSO or Free Space Optics is a laser based system used to create a wireless link with light, instead of using a radio frequency
FSO systems operate very much like a fiber optic connection using a cable
The main difference being the attenuation in a cable is known and controllable

## Slide 45: Free Space Optics
Whereas in a FSO link that uses the atmosphere as the media, the exact attenuation of the link can vary by the second and is unknowable

## Slide 46: Method of Operation
To make this type of system work a device known as a laser diode is used to produce a signal in the first part of the near infrared range, which is just above visible light at 700 nanometers or nm
The most common wavelengths used are 780 nm to 900 nm and 1500 to 1600 nm

## Slide 47: Method of Operation
The laser diode differs from the traditional laser in that it is simpler, smaller, and lower powered
The device on the other end that receives the signal is a photodiode
A transceiver has both devices so that the units can send and receive
For example

## Slide 48: Method of Operation

## Slide 49: Free Space Optics
Here is an example of such a link

## Slide 50: Using FSO in a CAN

## Slide 51: Lab
Setup a RF CAN
Setup a FSO CAN