## Slide 1: Testing Copper Media Last Update 2012.01.10 1.7.0

## Slide 2: Objectives
Learn how to test copper media

## Slide 3: Important Parameters
There are three basic parameters that need to be tested when checking copper media such as UTP cable
These are
  Signal Loss
  Crosstalk
  Wire Mapping

## Slide 4: Signal Loss
There are two types of signal loss
  Attenuation
    The loss due to the length of the cable of a certain construction
  Insertion
    The loss due to devices connected to the cable such as connectors

## Slide 5: Signal Loss

## Slide 6: Crosstalk
Crosstalk is the leakage of the signal from one wire onto another wire
This most often occurs at the ends of the cable where connectors are attached
At that point the signal being sent out is at its strongest, while the signal being received is at its weakest
The usual cause is improper installation of the connectors

## Slide 7: Sources of Crosstalk

## Slide 8: Sources of Crosstalk

## Slide 9: Types of Crosstalk
There are two major types of crosstalk that are measured
  NEXT
    Near end
  FEXT
    Far end

## Slide 10: NEXT

## Slide 11: FEXT

## Slide 12: Wire Map
The wire map test is to be certain the correct pins are connected to each other

## Slide 13: Wire Maps

## Slide 14: Wire Maps

## Slide 15: Wire Maps

## Slide 16: Cable Testing
The last thing to do is to test every cable
This is what says a cable is rated to some category as discussed above
The device that does this testing is a cable tester
Such as

## Slide 17: Multifunction Cable Tester

## Slide 18: Multifunction Cable Tester
This device can test any kind of cable with the proper modules
Such as
  Coax
  UTP
  Fiber Optic

## Slide 19: Multifunction Cable Tester
There are two parts to these testers
  It does not matter which part is at which end of the connection
  The results are read on the tester
  The other part, the injector, provides a means to turn the information back to the tester

## Slide 20: Tester

## Slide 21: Injector

## Slide 22: Multifunction Cable Tester
The common type of cable tested is UTP cable
Each cable must pass a series of tests at a specified level
The nice thing about these cable testers is their ease of use
Notice the button labeled Autotest

## Slide 23: Common Problems
The most common problems with cables come from
  NEXT
  FEXT
In other words crosstalk
Crosstalk measures signal coupling from one wire pair to another within a twisted-pair cabling link

## Slide 24: Common Problems
This kind of coupling is undesirable because it creates a noise disturbance in the wire pair
The effect of crosstalk is similar to a noisy transmission line
A receiver may not be able to distinguish the signal sent by the transmitter at the other end of the link from the noise induced by crosstalk

## Slide 25: Common Problems
In data communications, crosstalk is a critical performance parameter

## Slide 26: NEXT
NEXT measures the crosstalk signal that appears at the same end of the line from the test signal

## Slide 27: FEXT
FEXT measures crosstalk at the other end

## Slide 28: NEXT
NEXT measures the crosstalk induced by signal A to B in pair 2 that returns to the receiver side and competes with signal B to A arriving at the same receiver as pair 2
Meanwhile, ELFEXT measures the crosstalk induced in wire pair 4 that travels the length of the cable in the direction of the transmitted signal and competes with the clarity of signal 4 arriving at receiver 4

## Slide 29: NEXT and ELEXT

## Slide 30: Testing Requirements
Each category of cabling has a set of parameters that it must meet in order to be certified
Every part that carries the signal must conform to the relevant parameters
You cannot mix categories
If you do, then even if the cabling is rated Cat 6, but the patch panel is Cat 5, then the cabling installation is Cat 5

## Slide 31: Testing Requirements
The testing parameters are shown next
The nice part is you need not worry about these as the cable tester takes care of this

## Slide 32: Testing Requirements
Test Value | Cat 5 | Cat 5E | Cat 6
Frequency Range | 1-100 MHz | 1-100 MHz | 1-250 MHz
Attenuation | 22.0 dB | 22.0 dB | 19.8 dB
NEXT | 32.3 dB | 35.3 dB | 44.3 dB
PSNEXT | Not Used | 32.3 dB | 42.3 dB
ACR | 10.3 dB | 13.3 dB | 24.5 dB
PSACR | Not Used | 10.3 dB | 22.5 dB
ELFFEXT | Not Used | 23.8 dB | 27.8 dB
PSELFEXT | Not Used | 20.8 dB | 24.8 dB
Return Loss | 16.0 dB | 20.1 dB | 20.1 dB
Delay Skew | 45 ns | 45 ns | 45 ns

## Slide 33: Testing Requirements
Test Value | Cat 6 | Cat 6A | Cat 7
Frequency Range | 1-250 MHz | 1-500 MHz | 1-250 MHz
Attenuation | 19.8 dB | ----- | 20.8 dB
NEXT | 44.3 dB | 27.9 dB | 62.1 dB
PSNEXT | 42.3 dB | ----- | 59.1 dB
ACR | 24.5 dB | ----- | -----
PSACR | 22.5 dB | ----- | -----
ELFFEXT | 27.8 dB | 9.3 dB | -----
PSELFEXT | 24.8 dB | 20.8 dB | 24.8 dB
Return Loss | 20.1 dB | 8.0 dB | 14.1 dB
Delay Skew | 45 ns | ----- | 20 ns

## Slide 34: Testing Requirements

## Slide 35: Testing Requirements
Nice set of numbers
So what do all of these mean
The cabletesting.com website says the following about each one

## Slide 36: Testing Requirements
Attenuation or Insertion Loss
  What Is It
    Electrical signals lose some of their energy as they travel along the cable from one end to the other
    Insertion loss measures the amount of energy that is lost
    The insertion loss measurement quantifies the effect of the resistance the cabling link offers to the transmission of the electrical signals
  Results Interpretation
    The attenuation in a cable is largely dependent upon the gauge of wire used in constructing the pairs, with larger wires being better
    Also, stranded cabling will have 20-50% more attenuation than solid copper conductors
  Troubleshooting
    Excessive length is the most common reason for failing attenuation
    It can also be caused by poorly terminated connectors or plugs
    Your clue to this cause is to compare the attenuation on the four pairs
    If only one or two pairs have high attenuation, this suggests an installation issue
    Temperature also affects attenuation in some cables
    Temperature increases exacerbate the problem

## Slide 37: Testing Requirements
NEXT
  What Is It
    When a current flows through a wire, an electromagnetic field is created which can interfere with signals on adjacent wires
    Each pair is twisted because this allows opposing fields in the wire pair to cancel each other
    The tighter the twist, the more effective the cancellation
    Maintaining this twist ratio is the single most important factor for a successful installation
    If wires are not tightly twisted, the result is Near End Crosstalk
  Results Interpretation
    Since NEXT is a measure of difference in signal strength between a disturbing pair and a disturbed pair, a larger number - less crosstalk - is more desirable than a smaller number- more crosstalk
    If the NEXT curve crosses the pass/fail line at any point, then the link does not meet the stated requirement.
    Since NEXT characteristics are unique to each end of the link, six NEXT results should be obtained at each end
  Troubleshooting
    In many cases, excessive crosstalk is due to poorly twisted terminations at connection points
    All connections should be twisted to within 13 mm of the point of termination

## Slide 38: Testing Requirements
PSNEXT
  What Is It
    PSNEXT - Power Sum NEXT is a calculation, not a measurement
    PSNEXT is derived from the summation of the individual NEXT effects on each pair by the other three pairs
    PSNEXT is important measurements for qualifying cabling intended to support 4 pair transmission schemes such as Gigabit Ethernet
  Results Interpretation
    Since PSNEXT is a measure of difference in signal strength between disturbing pairs and a disturbed pair, a larger number - less crosstalk - is more desirable than a smaller number -more crosstalk
    If you look at the PSNEXT on a 50 meter segment of twisted pair cabling, it has a characteristic "roller coaster" shape
    That is, it varies up and down significantly, while generally increasing in magnitude
    This is because twisted pair coupling becomes less effective for higher frequencies
    Typically, PSNEXT results are around 3 dB lower than the worst-case NEXT result at each end of the link
  Troubleshooting
    Since PSNEXT is a calculation based on NEXT measurements, troubleshooting for PSNEXT failures reduces to troubleshooting for NEXT problems
    Once you have isolated and repaired the NEXT problem, PSNEXT will automatically improve

## Slide 39: Testing Requirements
ACR
  What Is It
    ACR - Attenuation to Crosstalk Ratio is the difference between NEXT and the attenuation for the pair in the link under test
    Due to the effects of attenuation, signals are at their weakest at the receiver end of the link
    But this is also where NEXT is the strongest
    Signals that survive attenuation must not get lost due to the effects of NEXT
    During signal transmission over twisted pair cable, both attenuation and crosstalk are active simultaneously
    The combined effect of these two parameters is a very good indicator of the real transmission quality of the link
  Results Interpretation
    ACR is an important figure of merit for twisted pair links
    It provides a measure of how much 'headroom' is available, or how much stronger the signal is than the background noise
    Thus, the greater the ACR, the better
  Troubleshooting
    ACR is derived from NEXT and attenuation data
    Any steps taken to improve either NEXT or attenuation performance will improve ACR performance
    This usually means troubleshooting for NEXT, because the only way to significantly improve attenuation is to shorten the length of the cable

## Slide 40: Testing Requirements
PSACR - Power Sum Attenuation to Crosstalk Ratio
  What Is It
    Power Sum Attenuation to Crosstalk Ratio is actually a calculation, not a measurement made by the cable tester
    PSACR is derived from an algebraic summation of the individual ACR effects
    There are four PSACR results at each end of the link per link tested
  Results Interpretation
    Since PSACR is a measure of signal to noise ratio, a larger number - more signal and less noise - is more desirable than a smaller number - more noise and less signal
    Typically PSACR results are around 3 dB lower than the worst-case ACR result at each end of the link
  Troubleshooting
    Since PSACR is a calculation based on ACR measurements, troubleshooting for PSACR failures is really troubleshooting for ACR problems
    Troubleshooting for ACR becomes troubleshooting for NEXT and attenuation
    So concentrate on NEXT and attenuation as is often the case in cable troubleshooting
    Once you have isolated and repaired the ACR problem, the PSACR will automatically improve

## Slide 41: Testing Requirements
ELFFEXT
  What Is It
    ELFEXT is a calculated result, rather than a measurement
    It is derived by subtracting the attenuation of the disturbing pair from the Far End Crosstalk this pair induces in an adjacent pair
    This normalizes the results for length
  Results Interpretation
    Compare the results of measurements made from both ends of the link to the appropriate limits
    ELFEXT that is too high is indicative of either excessive attenuation, higher than expected FEXT, or both
  Troubleshooting
    The same factors that contribute to NEXT problems contribute to FEXT problems
    Troubleshooting for ELFEXT means troubleshooting NEXT and attenuation problems, just as you would for ACR problems

## Slide 42: Testing Requirements
PSELFFEXT
  What Is It
    PSELFEXT - Power Sum ELFEXT is actually a calculation, not a measurement
    PSELEXT is derived from an algebraic summation of the individual ELFEXT effects on each pair by the other three pairs
  Results Interpretation
    Typically PSELFEXT results are around 3 dB lower than the worst-case ELFEXT result at each end of the link
  Troubleshooting
    The same factors that contribute to NEXT problems contribute to PSELFEXT problems
    Troubleshooting for PSELFEXT means troubleshooting NEXT and attenuation problems, just as you would for ACR problems

## Slide 43: Testing Requirements
Return Loss
  What Is It
    Return Loss is a measure of all reflections that are caused by the impedance mismatches at all locations along the link and is expressed in decibels
    Return Loss is of particular concern in the implementation of Gigabit Ethernet
    The value of impedances at the ends of the link must be equal to the characteristic impedance of the link
    Frequently, this impedance is imbedded in the interface of equipment to be connected to the LAN
  Results Interpretation
    All standards define the formulae to calculate the allowable return loss for each cabling link model over the frequency range
    A field test instrument may report a passing return loss test result in one of two ways
      The worst case return loss margin
      The worst case return loss value
  Troubleshooting
    Installation practices are more important on Category 5e and 6 than they were for Category 5
    Additional unnecessary untwist or unjacketing in terminations can add several dB of return loss in some cases

## Slide 44: Testing Requirements
Delay Skew
  What Is It
    Delay Skew is the difference between the propagation delay on the fastest and slowest pairs in a UTP cable
    Some cable construction employ different types of insulation materials on different pairs
    This effect contributes to unique twist ratios per pair and to skew
    Skew is important because several high-speed networking technologies, notably Gigabit Ethernet, use all four pairs in the cable
    If the delay on one or more pairs is significantly different from any other, then signals sent at the same time from one end of the cable may arrive at significantly different times at the receiver
    A large skew will make it impossible to recombine the original signal
  Results Interpretation
    Well-constructed and properly installed cabling should have a skew less than 50 nanoseconds
    Lower skew is better
    Anything under 25 ns is excellent, skew between 45 and 50 nanoseconds is marginally acceptable
  Troubleshooting
    If one pair is much higher or lower in delay than the others, very high skew may result
    If one pair exhibits uncharacteristically high or low delay, re-examine the installation
    If the skew is high, it will still work in low speed environments

## Slide 45: What Does This Mean
In general the only thing that needs to be done while testing cables is to hookup the cable tester, then press the autotest button
The unit then tells you if the cable passed or failed
It really does not matter why the cable failed if it did
The unit will tell you if you wish to know

## Slide 46: What To Do
When a test fails what do you do
Unless you did a really bad job of pulling the cable through the walls and ceiling the most likely problem is a bad connection
So reterminate the cable
Then test again

## Slide 47: Testing Patch Cables
Until recently there was no way to test patch cables, but Annex J to TIA/EIA-568-B.2-1 specified a method
With the publication of this amendment, people started testing patch cables
One industry publications has reported that their tests on Cat5E and Cat6 patch cables show a failure rate for them on these tests from 70 to 80 percent

## Slide 48: Testing Patch Cables
This tells us one of three things
  The test is faulty
  There are a bunch of systems out there that are not working properly
  It really does not matter how good or bad a patch cable is
I expect to hear more research on this subject in the future, so pay attention to the trade press

## Slide 49: Testing Patch Cables
Sure enough in the January 2012 issue of Cabling Installation and Maintenance magazine there was an article on this problem of certifying patch cables
It argues that only expensive and tested by the manufacturer patch cables should be used
It also mentions an adaptor from Fluke that can now allow patch cable testing

## Slide 50: Testing Patch Cables
There will be more to come on this issue I am sure

## Slide 51: Communication While Testing
It is common that in a building where cabling is being installed there will be no telephones
So, to communicate from one end of the cable to the other
A radio or cell phone is often used

## Slide 52: Toner
A toner is not used to test cabling
It only is used to trace wiring
At one end a device is attached to the wiring
This device sends an electrical signal down the wires
The other part of the toner set is used at the far end to find the remote end of the wires

## Slide 53: Toner
This is accomplished by moving the remote end device past the wires at the remote end until a tone is heard from the remote end device

## Slide 54: Toner