## Slide 1: Wireless Media
Last Update 2011.07.15
2.0.0

## Slide 2: Objectives
Learn about wireless media

## Slide 3: Sending Data
Data can be sent over the media by
  Varying - modulating - an electrical signal as it passes over a copper wire
  Varying – modulating - the power of light as it is sent over a glass optical fiber
  Varying – modulating - the radio waves sent through space, which is commonly referred to as wireless communications

## Slide 4: Wireless Media
The air is the media used for wireless links
Across this media we send
  Radio frequencies
  Light waves
These methods can be used in various combinations
Here is an illustration from Tessco that shows some of the options

## Slide 5: Wireless Media

## Slide 6: Radio Waves
Radio waves are electromagnetic radiations
These can be characterized by both frequency and wavelength
For the frequencies of interest here, the ones used to create wireless data networks, the range is in or near the gigahertz frequencies

## Slide 7: Radio Waves
This is just under 1 GHz to just under 100 GHz, specifically 700 MHz to 95 GHz
Frequency being the number of complete oscillations per second of energy in the form of waves
In terms of the length of these waves, they range from 428.6 mm to 3.2 mm
The wavelength is the distance a radio wave will travel during one cycle

## Slide 8: Radio Waves
That is the distance between identical points in the adjacent cycles of a waveform
There are formulas to compute wavelength or frequency
  Note
    The actual speed of radio waves is the speed of light, which is 299,792,458 meters per second, but rounding to 300,000,000 is sufficient for this purpose

## Slide 9: Wavelength
Wavelength

## Slide 10: Radio Wave Formulas
  For frequency in megahertz
    f = frequency in megahertz
    v = velocity of the radio wave, which is the speed of light in meters per second, in this case divided by 1000
    w = wavelength in mm

## Slide 11: Radio Wave Formulas
  For frequency in gigahertz
    f = frequency in gigahertz
    v = velocity of the radio wave, which is the speed of light in meters per second, in this case divided by 100
    w = wavelength in mm

## Slide 12: Radio Wave Formulas
  For wavelength in mm for megahertz frequencies
    w = wavelength in mm
    v = velocity of the radio wave, which is the speed of light in meters per second, in this case divided by 1000
    f = frequency in megahertz

## Slide 13: Radio Wave Formulas
  For wavelength in mm for gigahertz frequencies
    w = wavelength in mm
    v = velocity of the radio wave, which is the speed of light in meters per second, in this case divided by 100
    f = frequency in gigahertz

## Slide 14: Radio Wave Propagation Speed
Since radio waves move really fast, their speed of propagation is not an issue when discussing wireless data networks such as these
It is safe to ignore the effect of the speed of the radio wave

## Slide 15: Signals
A signal in a RF or radio frequency system is produced by an electrical current flowing through a conductor
The antenna turns this current into invisible waves moving through the air from the transmitting end
Then at the receiving end the invisible waves are turned back into electrical current on a conductor

## Slide 16: Signals
The invisible airborne waves are signals
Signals can be
  Analog
  Digital

## Slide 17: Analog Signal
An analog signal is one that varies continuously from one value to another in the form of a sine wave, which is a waveform that represents periodic oscillations in which the amplitude of displacement at each point is proportional to the sine of the phase angle of the displacement

## Slide 18: Analog Signal
Sine itself being the trigonometric function that for an acute angle is the ratio between the leg opposite the angle when it is considered part of a right triangle and the hypotenuse
In other words, the current or voltage varies with the sine of the elapsed time

## Slide 19: Analog Signal

## Slide 20: Digital Signal
A digital signal in contrast goes instantly from one value to another

## Slide 21: Carrier and Information Signals
In radio frequency systems an analog signal is always used as the main airborne signal
This is the carrier signal
On top of this signal another signal, analog or digital, is added that carries the information
This is the information signal

## Slide 22: Carrier and Information Signals
This combination of signals is called the modulation

## Slide 23: Modulation
Modulation is how an information signal is added to a carrier signal
This is the superimposing of the information onto the carrier
In an RF system a modulator generates this information signal
Then it is passed to the transmitter and out the antenna

## Slide 24: Modulation
In other words it is modulated
Then at the other end the signal is demodulated
The way to think of this is like a letter
  The envelope is the carrier and the letter is the information
  The envelope is only needed during transmission

## Slide 25: Modulation
Modulation is why a perfect sine wave is desired
Modulators superimpose the information onto the sine wave by making tiny modifications to the sine wave
If the sine wave is not perfect, these small changes may be lost by the time the signal gets to the other end of the link

## Slide 26: Types of Modulation
There are three forms of modulation
  AM – Amplitude Modulation
  FM – Frequency Modulation
  PM – Phase Modulation

## Slide 27: AM
AM changes the height of the sine wave as time goes by
For example

## Slide 28: FM
FM changes the frequency of the sine wave as time goes by, without changing the height
For example

## Slide 29: PM
PM changes the phase of successive sine waves
A LEADS B BY 30 DEGREES
B LEADS C BY 30 DEGREES
A LEADS C BY 60 DEGREES
A
B
C

## Slide 30: PM
In general when you see phase modulation schemes explained B stands for binary, which is only 2 points
Q stands for quadrature, which is 4 points and 16 and 64 represent the higher number of points in the modulation schemes

## Slide 31: PM
Every time the number of points is increased the speed is increased, but interference tolerance is reduced
This is one of the reasons for automatic speed reduction in the face of interference
Going from binary - 2 to 64 requires a really clean signal

## Slide 32: PM Types

## Slide 33: PM Types
Some encoding methods used with phase modulation methods are
  MSK – Minimum Shift Keying
  BPSK – Bi-Phase Shift Keying
  QPSK – Quadrature Phase Shift Keying
  DQPSK – Differential OPSK
  GMSK – Gaussian Minimum Shift Keying

## Slide 34: Signal to Noise Ratio
All communication systems generate noise and pickup noise that is naturally occurring
The signal to noise ratio is a ratio of the signal power divided by the noise power
It is measured in decibels

## Slide 35: Sources of Noise
Noise consists of all undesired radio signals, whether manmade or natural
Noise makes the reception of useful information difficult
The radio signal’s strength is of little use, if the noise power is greater than the received signal power
This is why the signal to noise ratio is important

## Slide 36: Sources of Noise
Increasing receiver amplification cannot improve the signal to noise ratio since both signal and noise will be amplified equally and the ratio will remain the same

## Slide 37: Natural Noise
Naturally occurring noise has two main sources
  Atmospheric noise, such as thunderstorms, from 0 to 5 MHz
  Galactic noise, such as stars, at all higher frequencies
Both of these sources generate sharp pulses of electromagnetic energy over all frequencies

## Slide 38: Natural Noise
The pulses are propagated according to the same laws as the desirable signals being generated by the radio frequency equipment
The receiving systems must accept them along with the desired signal

## Slide 39: Manmade Noise
Manmade noise is part of modern life
It is generated almost anywhere that there is electrical activity, such as automobile ignition systems, power lines, motors, arc welders, fluorescent lights, and so on
Each occurrence is small, but there are so many that together they can completely hide a weak signal that would be above the natural noise in a less populated area

## Slide 40: Manmade Noise
The most common sources of noise in the urban environment are automotive noise, power generating noise, and industrial noise
  A Comparative Investigation on Urban Radio Noise…
  Ming-Hui Chang and Ken-Huang Lin
  IEEE Transactions on Broadcasting Vol. 50 Number 3 9-2004

## Slide 41: Lab
Measure Noise Level

## Slide 42: Environmental Factors
These things that have an effect include
  Free Space Loss
  Absorption
  Reflection
  Refraction
  Diffraction
  Scattering

## Slide 43: Free Space Optics
FSO or Free Space Optics is a laser based system used to create a wireless link with light, instead of using a radio frequency
FSO systems operate very much like a fiber optic connection using a cable
The main difference being the attenuation in a cable is known and controllable

## Slide 44: Free Space Optics
Whereas in a FSO link that uses the atmosphere as the media, the exact attenuation of the link can vary by the second and is unknowable

## Slide 45: Method of Operation
To make this type of system work a device known as a laser diode is used to produce a signal in the first part of the near infrared range, which is just above visible light at 700 nanometers or nm
The most common wavelengths used are 780 nm to 900 nm and 1500 to 1600 nm

## Slide 46: Lab
Go to http://www.systemsupportsolutions.com/
Look at some of the available units