## Slide 1: Capturing VLAN Tags Last Update 2012.04.10 1.0.0

## Slide 2: Objectives
Learn how to capture VLAN tags for analysis using a network analyzer

## Slide 3: The Problem
I do not believe there is anything harder than figuring out how to capture VLAN tags using a network analyzer such as Wireshark or Omnipeek
This is mostly due to the lack of clear detailed instructions for specific equipment operating system sets as well as the failure of NIC manufacturers to build this capability into their device drivers

## Slide 4: The Problem
Further most of the examples only work on certain models of hardware and certain versions of software
The specifics as to these are often missing
Therefore, here I will provide several examples of exactly how to do this with defined equipment sets that I have access to

## Slide 5: The Problem
If you have some other type of hardware or software, well tough luck I cannot help you as I have wasted enough time getting this to work
Once you get it working, let me know the details
I will add it here

## Slide 6: The Problem
There are three main areas of failure that will keep you from capturing the VLAN tags
First, the driver for your NIC is stripping off the VLAN fields added to the Ethernet II header when the port this computer is attached to is added to a VLAN

## Slide 7: The Problem
Second, the configuration of the switch is not providing frames with this information to the port that the computer running the network analyzer is attached
Third, the configuration of everything is correct, but the switch wants a partner to connect to before providing the information to the port that the computer running the network analyzer is attached to

## Slide 8: The Problem
All of this makes figuring out exactly where the problem is a little tricky
Let’s deal with these problems one at a time

## Slide 9: NIC Driver Problem
Wireshark has some guidance on this subject which is both right and wrong
It is right when it says some NICs do not strip the tags
It is right when it says some NICs can be adjusted in the Windows registry to no longer strip the tags

## Slide 10: NIC Driver Problem
It is wrong when it says
  If the OS or the network adapter driver won't allow the VLAN tags to be captured, set up port mirroring (or "port spanning", as Cisco calls it) on the VLAN switch and connect an independent system, such as a laptop, to the mirror port, and don't configure the interface attached to that port as a member of a VLAN

## Slide 11: NIC Driver Problem
  You'll definitely see the VLAN tags, regardless of what OS the independent system is running or what type of network adapter you're using
This does not work

## Slide 12: NICs That Work
The NICs I have verified that retain and allow the display of the VLAN tags
  No modification required
    Trendnet TE100-PCIWN Version 2.21
      This is the Realtek RTL8139/810x chipset
      Wireshark says this should work and it does work without any modification required
      The driver is
        Microsoft
        5/30/2008
        6.111.530.2008

## Slide 13: NICs That Work
  Modification required
    Intel 82567LM Gigabit NIC
      This is a Intel chipset in a Dell laptop
    Wireshark says this should work with a registry change
    It does work once the registry is changed
    The driver is
      Microsoft
      8/18/2008
      10.0.22

## Slide 14: NICs That Do Not Work
The NICs I have verified do not work no matter what you do to them are
  Intel 82579V Gigabit NIC built into an Asus P8Z68-V Pro
  The driver is
    Intel
    3/15/2012
    11.16.96.0
  Intel does not explicitly say whether this one should work after the registry value is added

## Slide 15: NICs That Do Not Work
  Intel PRO/1000 GT PCI NIC
  The driver is
    Microsoft
    5/28/2008
    8.4.1.0
  Intel says this NIC should work after the registry value is added
  You are thinking the driver is the problem since it is from Microsoft, but Intel claims they have no Windows 7 64 bit driver for this NIC

## Slide 16: NICs That Do Not Work
As there are some reports that Intel server NICs will work without modification I tested one of these
  Intel PRO/1000 PT Dual Port Server Adapter
  The driver is
    Intel
    3/23/2012
    17
  It does not work out of the box

## Slide 17: NICs That Do Not Work
  Intel says this NIC should work after the registry value is added
  In this case MonitorMode as this is a PCI Express card
  On these types of cards there are three possible values 0, 1, and 2
  None of these values work

## Slide 18: NICs That Do Not Work
Therefore I conclude that just like Wireshark Intel’s information is not to be trusted
Does no one test this stuff
How hard does this need to be

## Slide 19: NIC Modification Required
The modification required to the Intel NIC chipsets to pass the required data is described in
  http://www.intel.com/support/network/sb/CS-005897.htm
Regedit is used to do what is described
Keep in mind that this may work, and then again it may not

## Slide 20: NIC Modification Required
This document says
  Allow tagged frames to be passed to your packet capture software by going into the registry and either add a registry DWORD and value or change the value of the registry key

## Slide 21: NIC Modification Required
  The bus type of your network adapter you dictate the keyword used, either "MonitorModeEnabled" for PCI/PCI-X Network Adapters, or "MonitorMode" for PCI-e based Network Adapters The new key (DWORD) should be placed at:
    HKEY_LOCAL_MACHINE\SYSTEM\ControlSet001\Control\Class\{4D36E972-E325-11CE-BFC1-08002BE10318}\00nn

## Slide 22: NIC Modification Required
This part of the instructions are clear as far as they go
But then it further says
  ControlSet001 may need to be CurrentControlSet or another 00x number
In most cases there are two of these 001 and 002
See

## Slide 23: NIC Modification Required

## Slide 24: NIC Modification Required
So which one is it
  ControlSet001
  or
  ControlSet002
In the one I changed that then worked I made the change to ControlSet001
In the one I changed that did not work I tried it in 001 only, 002 only, both 001 and 002

## Slide 25: NIC Modification Required
Intel goes on to say
  The registry DWORD for a PCI or PCI-X Network Adapter is
    MonitorModeEnabled
      Set the DWORD value to one of the following options:
        0 - disabled (Do not store bad packets, Do not store CRCs, Strip 802.1Q VLAN tags)
        1 - enabled (Store bad packets. Store CRCs. Do not strip 802.1Q VLAN tags)

## Slide 26: NIC Modification Required
  The registry DWORD for a PCI-Express Network Adapter the registry DWORD is
    MonitorMode
      Set the DWORD value to one of the following options:
        0 - disabled (Do not store bad packets, Do not store CRCs, Strip 802.1Q VLAN tags)
        1 - enabled (Receive bad/runt/invalid CRC packets. Leave CRCs attached to the packets. Strip VLAN tags and ignore packets sent to other VLANs as per normal operation.)

## Slide 27: NIC Modification Required
        2 - enabled strip VLAN (Receive bad/runt/invalid CRC packets. Leave CRCs attached to the packets. Pass all VLAN packets to the host, even those sent to other VLANs. Leave VLAN tags attached to the packets. This mode is likely to break VLAN)
Intel just does not bother to say exactly where under this ControlSet this new DWORD goes
It says it goes right under
  {4D36E972-E325-11CE-BFC1-08002BE10318}\00nn

## Slide 28: NIC Modification Required
Where nn is the NIC
Huh
As you can see there are quite a few lines with this exact same heading

## Slide 29: NIC Modification Required

## Slide 30: NIC Modification Required
You first have to look over in the right panel to see which one of these identical heading lines defines the NICs
As you work your way down the lines you find a little ways down several with the name network in them
The one you want is named
  Network adapters

## Slide 31: NIC Modification Required

## Slide 32: NIC Modification Required
One might think the DWORD goes here
Oh no, expand the lines under this
This where the elusive 00nn referred to above lives
Once we do this we see

## Slide 33: NIC Modification Required

## Slide 34: NIC Modification Required
Now scroll down that list from 0000 until you find the line for the NIC of interest
Here is mine
In this case the 00nn is 0016
You can tell this by seeing the name of the NIC in the right panel
In this case
  Intel PRO/1000 GT Desktop Adaptor

## Slide 35: NIC Modification Required
To add the required DWORD right click in the right panel
This appears

## Slide 36: NIC Modification Required

## Slide 37: NIC Modification Required
Select DWORD (32 bit) Value

## Slide 38: NIC Modification Required
A new line appears at the bottom

## Slide 39: NIC Modification Required

## Slide 40: NIC Modification Required
Change the name of the line to MonitorModeEnabled or MonitorMode as directed above
The value by default is 00000000 in hex or 0 in decimal
Right click on this line and select Modify

## Slide 41: NIC Modification Required

## Slide 42: NIC Modification Required
Change the value to 1
Intel does not bother to say whether this change should be Hexadecimal or Decimal or whether it really makes a difference
I used Decimal

## Slide 43: NIC Modification Required

## Slide 44: NIC Modification Required
Click OK
Exit out of Regedit

## Slide 45: Switch Configuration
The only equipment I deal with is Cisco so this discussion of equipment sets and configurations will be limited to Cisco stuff
As is often the case with Cisco the configuration to use depends on the model and the IOS version
Some that should work, do not

## Slide 46: Switch Configuration
In some places you will find statements that a certain model will work, but only later will you find an obscure note that says it really does not, but then on testing you find it really does after all
This is the case with the very common 2950 line of switches
Let’s see what does work and does not work based on actual testing

## Slide 47: Using 2960 Switches
This setup is based on a discussion of this problem by an unidentified person here
  http://dot1x.blogspot.com/2010/03/sniffing-dot1q-tags-with-wireshark.html
The first set I got to work was two Cisco 2960 switches with these characteristics
  WS-C2960-24TT-L 12.2(44)SE6 C2960-LANBASE9-M

## Slide 48: Using 2960 Switches
The physical setup is next with the switches shown vertically just to make the lines easier to see

## Slide 49
Laptop One
Connected to FA0/1
In VLAN 2
On SwitchOneWireshark
Laptop Two
Connected to FA0/1
In VLAN 2
On SwitchTwo
Laptop Three
Connected to FA0/24
On SwitchOneWireshark
Switch
Cisco 2960
Named
SwitchOneWireshark
Switch
Cisco 2960
Named
SwitchTwo
On Each Switch
FA0/23
is Connected to
FA0/23

## Slide 50: Using 2960 Switches
Here is the configuration for the switches

## Slide 51: Switch One Wireshark
!Switch One Wireshark Connected
enable
config t
hostname SwitchOneWireshark
vlan 2
int fa0/1
switchport mode access
switchport access vlan 2

## Slide 52: Switch One Wireshark
interface fa0/23
switchport mode trunk
switchport trunk allowed vlan all
monitor session 1 source interface fa0/23
monitor session 1 destination interface fa0/24 encap replicate
end

## Slide 53: Switch Two
!Switch Two
enable
config t
hostname SwitchTwo
vlan 20
int fa0/1
switchport mode access
switchport access vlan 2

## Slide 54: Switch Two
interface fa0/23
switchport mode trunk
switchport trunk allowed vlan all
end

## Slide 55: Laptop One
Laptop One is connected to the switch named SwitchOneWireshark at port Fa0/1
IP Address 10.0.0.1
Subnet Mask 255.255.255.0

## Slide 56: Laptop Two
Laptop Two is connected to the switch named SwitchTwo at port Fa0/1
IP address 10.0.0.2
Subnet mask 255.255.255.0

## Slide 57: Laptop Three
Laptop Three is connected to the switch named SwitchOneWireshark at port Fa0/24
IP Address 10.0.0.3
Subnet Mask 255.255.255.0
This computer is running Wireshark 1.6.5

## Slide 58: Use of IP Addresses
The IP addresses were assigned to the computers in order to check connectivity before the VLANs were created and then the lack of connectivity once the VLANs were created

## Slide 59: Use of IP Addresses
In addition a continuous ping was run from Laptop One to Laptop Two to provide some traffic over the trunk link from port Fa0/23 on switch SwitchOneWireshark to Fa0/23 on switch SwitchTwo
Laptop Three was attached to port Fa0/24 on switch SwitchOneWireshark
This is the span or monitor port

## Slide 60: The Result
The result was

## Slide 61: The Result

## Slide 62: The Result

## Slide 63: The Result
Now we have VLAN tagged frames caught in the wild to use to illustrate such things

## Slide 64: Using One 2960 Switch
The monitor port in SwitchOneWireshark does not receive many frames at all when the trunk cable is disconnected from the second switch named SwitchTwo
There is definitely no sign of ICMP traffic
Of course the computer at 10.0.0.2 could not answer as it is attached to the now isolated switch since the cable between the two switches is disconnected

## Slide 65: Using One 2960 Switch
What if the computer at 10.0.0.2 is moved to the switch named SwitchOneWireshark to a port in the same VLAN as the computer at 10.0.0.1 with the other switch disconnected
This does not work
Very little traffic is seen at the monitoring port

## Slide 66: Using One 2960 Switch
What if we get rid of the trunking and switch the monitoring source to the port in VLAN 2 that is the target of the pings
Using this configuration
  monitor session 1 source interface fa0/2
  monitor session 1 destination interface fa0/24 encapsulation replicate
The pings work, but no VLAN data is seen

## Slide 67: Using One 2960 Switch
What if we eliminate the monitoring session as well
Then place the computer with Wireshark installed into the same VLAN as the other two computers
The pings work, but no VLAN data is seen

## Slide 68: Using Two 2950 Switches
The procedure detailed above for the 2960 switches will work using 2950 switches instead with the following changes
  The cable connecting the two switches to each other, the trunk cable from Fa0/23 to Fa0/23, must be a crossover cable as the 2950 is unable to change a port to handle a straight through cable

## Slide 69: Using Two 2950 Switches
  The configuration line that reads
    monitor session 1 destination interface fa0/24 encapsulation replicate
  Must be changed to say
    monitor session 1 destination interface fa0/24 encapsulation dot1q
Everything else stays as described in the 2960 section of this presentation

## Slide 70: Router on a Stick
Instead of two switches VLAN captures can be done with one switch and a router with the router acting as a Router On A Stick as seen in this example

## Slide 71
Laptop One
Connected to FA0/1
In VLAN 2
On SwitchWireshark
Laptop Two
Connected to FA0/2
In VLAN 3
On SwitchWireshark
Laptop Three
Connected to FA0/24
Switch
Cisco 2960
Named
SwitchWireshark
Router
Cisco 2600
Named
RouterOnStick
On The Switch
FA0/23
is Connected to
FA0/0
On The Router

## Slide 72: The Configurations
Here is the configurations for each device
Notice that a default gateway is added to Laptop One and Laptop Two

## Slide 73: Switch
!Switch Wireshark Connected
enable
config t
hostname SwitchWireshark
vlan 2
vlan 3

## Slide 74: Switch
int fa0/1
switchport mode access
switchport access vlan 2
int fa0/2
switchport mode access
switchport access vlan 3

## Slide 75: Switch
interface fa0/23
switchport mode trunk
switchport trunk allowed vlan all
monitor session 1 source interface fa0/23
monitor session 1 destination interface fa0/24 encapsulation replicate
end

## Slide 76: Router
!Router On A Stick
enable
config t
hostname RouterOnStick
int fa0/0.2
encapsulation dot1q 2
ip address 192.168.1.1 255.255.255.0

## Slide 77: Router
int fa0/0.3
encapsulation dot1q 3
ip address 192.168.2.1 255.255.255.0
int fa0/0
no shutdown
exit
ip route 0.0.0.0 0.0.0.0 fa0/0
end

## Slide 78: Laptop One
Laptop One is connected to the switch named SwitchWireshark at port Fa0/1
IP Address 192.168.1.2
Subnet Mask 255.255.255.0
Default Gateway 192.168.1.1

## Slide 79: Laptop Two
Laptop Two is connected to the switch named SwitchWireshark at port Fa0/2
IP address 192.168.2.2
Subnet mask 255.255.255.0
Default Gateway 192.168.2.1

## Slide 80: Laptop Three
Laptop Three is connected to the switch named SwitchWireshark at port Fa0/24
This computer is running Wireshark 1.6.5

## Slide 81: Configuration Oddities
There are some confusing configurations that one will run across while researching this topic
One is the configuration line that says in part
  encapsulation 8021q
This relates back to older equipment that supported the Cisco propriety protocol ISL

## Slide 82: Configuration Oddities
The newer IOSs do not have that command as there are no options anymore
Everyone already uses 8021q