## Slide 1: How to Use SNMP to Collect Network Data Last Update 2013.04.18 1.1.0

## Slide 2: Objectives
Learn how to collect data with SNMP to use in baselining and troubleshooting a network

## Slide 3: What is SNMP
SNMP is the Simple Network Management Protocol
It is used to collect and then report information on devices such as routers and switches attached to the network
To accomplish this an SNMP agent must be running on the device that will be monitored

## Slide 4: What is SNMP
Then a program called a NMS – Network Management System must be installed to access and display this information on another device
SNMP is defined by several RFCs including these

## Slide 5: SNMP RFCs
1155 - Structure and identification of management information for TCP/IP−based internets
1156 - Management information base for network management of TCP/IP−based internets (MIB I)
1157 - Simple network management protocol

## Slide 6: SNMP RFCs
1213 - Management information base for network management of TCP/IP−based internets (MIB II)
1441 - Introduction to version 2 of internet−standard network management framework
1452 - Coexistence between version 1 and version 2 of the internet−standard network management framework

## Slide 7: SNMP RFCs
2578 - Structure of Management Information Version 2
3414 - User−based Security Model for version 3 of the Simple Network Management Protocol
3584 - Coexistence between Version 1, Version 2, and Version 3 of the internet−standard network management protocol

## Slide 8: Enable SNMP on the Device
The device to be examined must have SNMP enabled and configured
In this example SNMP will be enabled and configured on Windows
The exact sequence will depend on the version of Windows
For example to do this on Windows 7 follow these steps

## Slide 9: Enable SNMP on the Device
From the Control Panel select
  Programs and Features
Select
  Turn Windows features on and off
Scroll down to
  Simple Network Management Protocol (SNMP)
Select the checkbox to activate it

## Slide 10: Enable SNMP on the Device
Click Ok
Close out the Control Panel

## Slide 11: Configure SNMP on the Device
Most defaults will work in the typical installation
In the real world the community string – password – should be changed as everyone knows the default password
In the example here – Windows 7 – there is no community string so one will be entered

## Slide 12: Configure SNMP on the Device
To do this from the Control Panel select
  Administrative Tools
Then select
  Services
Scroll down to SNMP Service
Double click it
Select the Security tab
Select Add under the Community box

## Slide 13: Configure SNMP on the Device
Put in a password
Click
  Accept SNMP packets from any host
Close out all dialog boxes

## Slide 14: Install an SNMP NMS
There are a large number of NMS programs
In this example PRTG Traffic Grapher from Paessler will be used
Download the program
Install the program using the defaults and the free version

## Slide 15: Setup the Sensor
After the program is installed a sensor must be added to access the information available form the device to be monitored
In this case we will look at the bandwidth used by the NIC card in the computer
Click
  Add
The following dialog boxes appear

## Slide 16: Setup the Sensor
Accept the defaults and click next for both

## Slide 17: Setup the Sensor

## Slide 18: Setup the Sensor

## Slide 19: Setup the Sensor
In the next dialog box
  Enter a name for the device
  Enter the password
  Click
    Next

## Slide 20: Setup the Sensor

## Slide 21: Setup the Sensor
On the Sensor Selection list select the
  Local Area Connection Ethernet Connected
at the bottom of the list of these
Click
  Next

## Slide 22: Setup the Sensor

## Slide 23: Setup the Sensor
In the next dialog box change the Scanning Interval to 1 second Click
  Finish

## Slide 24: Setup the Sensor

## Slide 25: Display the Data
On the next screen a set of graphs will appear

## Slide 26: Display the Data

## Slide 27: Display the Data
To see something here surf the web
Then switch back
Something like this will appear

## Slide 28: Display the Data