## Slide 1: How to Use the Wireshark Protocol Analyzer
Last Update 2013.03.11 1.12.0

## Slide 2: What is a Protocol Analyzer
A protocol analyzer, such as Wireshark, is used to copy frames off of an active network
These frames are like the cars on the highway
They are the reason for the highway or network
These frames carry the information in the case of a network

## Slide 3: What is a Protocol Analyzer
They carry the people and cargo in the case of a highway
By capturing and examining these frames we can see exactly what is happening on the network
Then when the network stops working as we expect, we can use this same tool to determine why it is not working

## Slide 4: Let’s Look at Wireshark
Wireshark, once called Ethereal, is an open source network analyzer
It looks like this

## Slide 5: Wireshark

## Slide 6: Wireshark
Not very interesting is it
It is of more interest after it has captured a frame or two
For example

## Slide 7: Wireshark

## Slide 8: Wireshark
What are we seeing here

## Slide 9: Wireshark
The frames that were captured
The layers in the currently selected frame
The contents of the current layer in hex and ASCII

## Slide 10: The Layers
As you will recall from the OSI model there are several layers that each do different functions that are part of the captured frame
This is also true of the TCP/IP model which all current networks use
It is divided up into these layers

## Slide 11: TCP/IP Model

## Slide 12: The Layers
Let’s look more closely at the layers in one of the frames shown above

## Slide 13: The Layers
The frame shown in detail below
All the layers in this frame
The contents of the selected layer
The contents in hex
The contents in ASCII

## Slide 14: The Network Access Layer
Recall that the Network Access layer is two layers in the OSI model
  Physical
  Data Link
Wireshark cannot show the physical layer
For that an oscilloscope is required
On such a device the physical layer for an Ethernet based network looks like this

## Slide 15: The Physical Layer

## Slide 16: The Data Link Layer
The first layer that Wireshark can display is the top of the Network Access layer
This is the Data Link layer as shown next
Then after it the Network layer, the Transport layer, and the Application layer

## Slide 17: The Data Link Layer

## Slide 18: The Network Layer

## Slide 19: The Transport Layer

## Slide 20: The Application Layer

## Slide 21: To Capture Frames
Let’s capture some frames now
Select
  Capture
  Interfaces
  Click Start beside the interface that is showing activity

## Slide 22: To Capture Frames

## Slide 23: To Capture Frames

## Slide 24: To Capture Frames

## Slide 25: To Capture Frames

## Slide 26: To Capture Frames

## Slide 27: Statistics
Wireshark can also show some statistics about the network
For example to see the packets per second select
  Statistics – IO Graphs

## Slide 28: Packets per Second

## Slide 29: Statistics
The data rate can be shown
  Statistics – Summary
    Average Mbit per second for example

## Slide 30: Data Rate

## Slide 31: Protocol Hierarchy
A list of the protocols in use can be created by selecting
  Statistics – Protocol Hierarchy
This should be examined for unexpected protocols or the excessive use of a protocol

## Slide 32: Protocol Hierarchy

## Slide 33: Who is Talking
A list of the top talkers as well as who is talking to whom can be created
  Statistics – Conversations
Along with a list of MAC addresses and IP addresses

## Slide 34: Who is Talking

## Slide 35: Who is Talking

## Slide 36: IP Addresses
To se all of the IP addresses select
  Statistics – IP Addresses

## Slide 37: IP Destinations
To see the destinations select
  Statistics – IP Destinations

## Slide 38: Ports Used
To see the ports used select
  Statistics – IP Protocol Types

## Slide 39: Packet Length
The distribution of packet lengths can be shown

## Slide 40: Packet Length

## Slide 41: Flow Graph
A graph of the flow of a conversation can be created by selecting
  Statistics – Flow Graph

## Slide 42: Flow Graph

## Slide 43: TCP Trace Graph
As Laura Chappell who provides training on network analysis discusses in one of her labs a TCP Trace Graph is used to locate any problem in the flow of data
This graph should proceed upward from the bottom left corner to the top right corner at a steady pace
The sequence numbers are on the left which should constantly increase

## Slide 44: TCP Trace Graph
Time is along the bottom axis
There are two lines
The lower darker line is the data flow
The upper lighter line is the window size

## Slide 45: TCP Trace Graph

## Slide 46: TCP Trace Graph
In most cases a flat area indicates a problem

## Slide 47: TCP Trace Graph

## Slide 48: TCP Trace Graph
These flat areas occur when the two lines intersect
This means the window size has gone to zero
This is never good as it slows the traffic way down
The reason could be a transmission problem or just that the server is waiting for the user to type something

## Slide 49: TCP Trace Graph
The gray line is the Window Size

## Slide 50: TCP Trace Graph

## Slide 51: TCP Trace Graph
As you zoom in very closely the I bars that appear represent the data crossing the link
Each one is a segment
The vertical gray line beside them represents the ACK
The gap in the vertical I bars is a lost segment
The flat line to the side are duplicate ACKs

## Slide 52: TCP Trace Graph

## Slide 53: TCP Trace Graph
Bumps or rat's nests on the data line are also bad
These indicate data loss
This can be seen more clearly by zooming in on that section of the line

## Slide 54: Capture and Decode Process
Wireshark can bring frames in from a live capture or from a capture file stored on a drive
Let’s see how these two processes work

## Slide 55: Live Capture

## Slide 56: Live Capture
During a live capture off of a network the frames are feed by the NIC driver to one of the Wireshark entry points
  WinPcap
    Wired Windows based connection
  AirPcap
    Wireless Windows based connection
  libpcap
    Wired or wireless Linux and some other OSs

## Slide 57: Live Capture
A capture filter can be applied at this point to limit what reaches Wireshark
This is to be avoided if possible as whatever this filter drops cannot be recovered
The last step is the frames being feed to the capture engine to be sent on to the decoding section

## Slide 58: Capture Filter
In Laura Chappell’s view the most useful capture filters are

## Slide 59: Capture Filters

## Slide 60: Capture Filters
Here are some other useful ones from the Wireshark mailing list
These all go on one line so ignore the line wrapping
  To divide up a capture file too large to read into Wireshark
    “c:\Program Files\Wireshark\tshark.exe" -r 500MB_capture_file.cap -R "ip.addr==127.0.0.1" -w output_file_name.cap

## Slide 61: Capture Filters
  For multiple VLAN capture assuming you can see the traffic for multiple VLANs
    vlan and (ether[14:2]&0x0fff = 102 or ether[14:2]&0x0fff = 103)

## Slide 62: Capture File

## Slide 63: Capture File
If an existing capture file is used the frames are feed straight into the library for presentation to the decoding process
In this case a live capture driver is not required

## Slide 64: Connecting to the Network
For the capture from the network to be effective the network analyzer must be properly connected to the network
Regardless of the method used to make the connection in general connect as near to the user experiencing the problem as possible

## Slide 65: Connecting to a Network
The type of network from which the frames need to be captured affects how Wireshark should be attached to that network
The two basic types are
  Wired
  Wireless
Then within wired networks are those at layer 1 v layer 2

## Slide 66: Connecting to a Wired Network
Connecting to a hub based wired network that lives solely at layer 1 is easy
Just plug into an unused hub port
Connecting to a switch based layer 2 network is much more difficult
In fact there is no easy, low cost solution to this problem
Here are some possibilities

## Slide 67: Connect to the Network
Keep in mind that once a switch learns a MAC address on a port, it forwards traffic for this MAC address directly to the corresponding port
On a switch, after host B's MAC address is learned, unicast traffic from A to B is only forwarded to B's port, and therefore not seen by the analyzer

## Slide 68: Connect to the Network

## Slide 69: Insert a Hub
A hub may be inserted between the switch port and the device under study
However, one still only sees the traffic back and forth to that device, not all the traffic
Hubs are no longer produced
Those that are available are limited to 10 or 100 mbps

## Slide 70: Insert a Hub
Three common problems take place when a hub is inserted into the link
  If the link was originally forced to full-duplex, then a new problem has been introduced into the link, as the hub will be operating in half duplex
  If the hub used is actually a partial or full bridge and not a true hub as was common as hubs were being phased out nothing is gained

## Slide 71: Insert a Hub
  The link already had one or more hubs and the Ethernet architecture is now illegal, which causes late collisions

## Slide 72: Span or Mirror a Port
To watch traffic on a switch based network, plug the cable from the computer running the analyzer software into any standard port on the switch
Then set the switch port to span or monitor mode

## Slide 73: Span or Mirror a Port
In such a mode instead of the port just seeing the traffic directed to the MAC address of the computer on that port, the broadcast traffic, and the multicast traffic it will see all of the traffic on the local network
As in

## Slide 74: Span or Mirror a Port

## Slide 75: Span or Mirror a Port
To do this on the Cisco Catalyst 2950 switch for example the Switched Port Analyzer or SPAN feature, also called port mirroring or port monitoring, selects network traffic for analysis by a network analyzer
This is called creating a Span port

## Slide 76: Span or Mirror a Port
The Catalyst 2950 Switches can have only one SPAN session active at a time and can monitor only source ports, it can not monitor VLANs

## Slide 77: Span or Mirror a Port
To create such a port, access the command line interface for the operating system then enter
  C2950#config t
  C2950(config)#monitor session 1 source interface fastEthernet 0/2
  !-- Interface fa 0/2 is configured as source port

## Slide 78: Span or Mirror a Port
  C2950(config)#monitor session 1 destination interface fastEthernet 0/3
  !-- Interface fa0/3 is configured as destination port
  C2950(config)#Ctrl Z
To check this enter
  C2950#show monitor session 1
  Session 1
  ---------

## Slide 79: Span or Mirror a Port
  Source Ports:
  RX Only: None
  TX Only: None
  Both: Fa0/2
  Destination Ports: Fa0/3
To clear this
  C2950#config t
  C2950#no monitor session session 1

## Slide 80: Span or Mirror a Port
Catalyst 2950 Switches are able to span source port traffic in the
  Receive direction only - Rx span or ingress span
  Transmit direction only - Tx span or egress span
  Both directions

## Slide 81: Span or Mirror a Port
Keep in mind the way most switches work these days in that if the switch receives a corrupted packet, the ingress port usually drops it, so you won't see it on the egress port
It is then true that a switch is not completely transparent when it is a matter of capturing traffic

## Slide 82: Span or Mirror a Port
So when you see a corrupted packet, the errors where generated on the egress segment

## Slide 83: Insert a Tap
In copper based UTP cable networks a tap is similar to a hub
There are two types of UTP taps, standard and aggregating

## Slide 84: Standard Tap
Using standard taps means that the monitoring tool either sees the request or the response, but not both
In order to see both the request and the response the monitoring tool needs two analysis input ports, one for the TX path and one for the RX path

## Slide 85: Standard Tap
A standard tap provides a copy of all traffic on the link, including any errors that may be present
A standard tap does not experience oversubscription because it has a separate output for each direction

## Slide 86: Standard Tap
This permits the monitoring tool to have access on par with a hub in series without the drawback of forcing the link to half-duplex or creating a duplex mismatch
However, to see both streams of traffic two analyzers are required
Then the two capture files must be synchronized and combined

## Slide 87: Aggregating Tap
Aggregating taps provide both the request and response by design
Aggregating taps often also provide configurable ingress capability
The monitoring tool can send and receive through the tap output port
Aggregating taps may also offer more than one output port, so that two or more test tools can receive the same output traffic

## Slide 88: Aggregating Tap
The latest generation of aggregating taps uses a bridging function to combine the data streams from the RX and TX data paths

## Slide 89: Aggregating Tap

## Slide 90: Aggregating Tap
As a modified bridge link aggregating taps are subject to the oversubscription problem
Bursty traffic, which is common to networking, may or may not exceed the buffer inside the aggregating tap
The presence of the buffer may obscure some data loss, and would be a very significant concern for forensic analysis

## Slide 91: Aggregating Tap
Most reactive troubleshooting would not be affected greatly by data loss through oversubscription or by having a burst exceed the buffer, as the cause of a reactive troubleshooting problem is usually related to the majority of the traffic present
Filtering applied by the aggregating tap may be discarding the traffic of interest

## Slide 92: Aggregating Tap
A filter applied for a prior event may still be active, which would affect both troubleshooting and forensic activities
In addition, the act of filtering may cause the aggregating tap to drop additional frames due to CPU overhead in the tap
MAC Layer errors are dropped because bridges do not forward errors

## Slide 93: Aggregating Tap
Everything else is flooded to the monitor port
This is perceived as a significant drawback by the industry since standard taps forward errors, and aggregating tap vendors are working hard to correcting this limitation

## Slide 94: Aggregating Tap
Typically, only aggregation taps that support injection - ingress traffic from the monitoring tool - have support for Power over Ethernet, so inserting a standard tap will often turn off a PoE powered station
This is most noticeable when troubleshooting VoIP and wireless access points, which are likely to rely on PoE

## Slide 95: Fiber Optic Cable Tap
When the cabling being used in the network is fiber optic cable then a different construction must be used for the tap
A fiber optic cable tap takes a single input of light and splits between the intended destination port and the tap
These taps have a split ratio of either 70/30 or 50/50

## Slide 96: Fiber Optic Cable Tap
Where either 30 percent or 50 percent of the single goes to the tap
This light splitting can be done in one of two ways
  Fused bionic taper splitter
    The most common method
  Reflective splitter
These look like this

## Slide 97: Fiber Optic Cable Tap

## Slide 98: Span Port or Tap
Fluke performed a test to see which was the better method to use to connect to a network for analysis
Should one use a span port or invest in a tap
They ran the test on a Cisco Catalyst switch using one port for the tap and another port set to spanning

## Slide 99: Span Port or Tap
Using iPerf to fully load each port one at a time they achieved a data rate of 93.1 Mbps for 10 seconds
On the span port 125,221 frames were captured
But on the tap 133,126 frames were captured

## Slide 100: Span Port or Tap
Clearly a tap is a better method to use to connect to a heavily loaded network
Fluke recommends that if the data stream will load the span port to 50 percent or more of its capacity, then use a tap instead

## Slide 101: Connecting to the Network
There are ways to collect information from switch based networks other than using a protocol analyzer that will be covered elsewhere

## Slide 102: Connecting From Both Sides
Another connection problem occurs when data must be captured at both sides of a link such as both sides of a WAN
Two analyzers are required
Then the two capture files must be synchronized and combined
A NTP server is one way to do this

## Slide 103: Connecting From Both Sides

## Slide 104: Wireless Network Connections
For wireless networks unless a hardware device such as an AirPcap adaptor from Cace Technologies is used there will be a significant limit to the wireless traffic seen
As the Wireshark FAQ points out this is because the driver for the wireless NIC must be placed in promiscuous mode just like a NIC on a wired network in order to capture wireless traffic

## Slide 105: Wireless Network Connections
To see traffic on networks other than the one the device is attached to the NIC must also be placed in monitor or RF Mon mode
Even with these settings non data frames may be ignored
There are a large number of non data frames on a wireless network
When in RF Mon mode it stops acting like a normal NIC

## Slide 106: Wireless Network Connections
Therefore some default settings for Wireshark must be changed to avoid problems when capturing wireless frames, such as name resolution settings
This means that you should disable name resolution when capturing in monitor mode

## Slide 107: Wireless Network Connections
Otherwise, when Wireshark tries to display IP addresses as host names, it will probably block for a long time trying to resolve the name because it will not be able to communicate with any DNS or NIS servers

## Slide 108: Wireless Network Connections
Wireshark will only see some if any wireless frames without a special adapter from Cace Technology
Their AirPcap USB adapter looks like this

## Slide 109: AirPcap Adapter

## Slide 110: AirPcap Adapter
A capture of wireless frames in Wireshark using the AirPcap device looks like this

## Slide 111: Wireless Frames

## Slide 112: AirPcap Adapter
To use the AirPcap adapter with Wireshark it must be set based on the network under study
Here are the common elements to set as illustrated by Laura Chappell

## Slide 113: AirPcap Adapter Setup

## Slide 114: AirPcap Adapter Setup
And a closer look at the main things to set

## Slide 115: AirPcap Adapter Setup

## Slide 116: AirPcap Adapter Setup
The first thing to do is to select the adapter as there can be up to three installed at one time
This is done in the dropdown section under Interface
Next the selected adapter is set to a channel in the dropdown section under Basic Configuration – Channel

## Slide 117: AirPcap Adapter Setup
If channel bonding is being used the Extension Channel dropdown can select the channel just before the one specified above by using -1 or the one just after by using +1
The Capture Type dropdown selection tells the adapter what types of frames to capture
These include as the documentation says

## Slide 118: AirPcap Adapter Setup
Capture Type
  802.11 frames only
  802.11 frames plus radio information by using radiotap
  802.11 frames plus the Per-Packet Information (PPI) header

## Slide 119: AirPcap Adapter Setup
PPI and radio information includes additional information not contained in the 802.11 frame, such as transmit rate, signal power, signal quality, channel, and (for PPI) multiple antenna information
The radio information comes from the radiotap addition
It is defined as

## Slide 120: AirPcap Adapter Setup
  The ieee80211_radiotap definitions provide a device-independent bpf(4) attachment for the capture of information about 802.11 traffic which is not part of the 802.11 frame structure
For example as mentioned above
  Transmit rate, signal power, signal quality, channel
The PPI information is defined as

## Slide 121: AirPcap Adapter Setup
  When capturing live network data, it is often useful to collect out-of-band information and provide it along with in-band packet data
  The traditional method of doing this is to prefix each PDU with a meta-information header (often called a pseudoheader)
  Current implementations include such information as 802.11 radio information, access server user IDs, and point-to-point link direction

## Slide 122: AirPcap Adapter Setup
  The Per-Packet Information (PPI) Header is a general and extensible meta-information header format originally developed to provide 802.11n radio information, but can handle other information as well
  PPI is intended to supplement individual packets received from a hardware or software engine with interesting data in a light-weight fashion

## Slide 123: AirPcap Adapter Setup
  Often such data of interest pertains to the PHY layer, but this need not always be the case
  Whatever the carried information may be, the intent is that the information contained is only added to data captured in real-time, not stored packets

## Slide 124: AirPcap Adapter Setup
The last main setting is whether to capture the FCS or not
This is done by selecting
  Include 802.11 FCS Frames
And then the types to capture under the FCS Filter dropdown selection
The possibilities include

## Slide 125: AirPcap Adapter Setup
  All Frames: the adapter will capture all the frames regardless of whether the FCS is valid or not
  Valid Frames: the adapter will only capture frames that have a valid FCS
  Invalid Frames: the adapter will only capture frames that have an invalid FCS

## Slide 126: AirPcap Adapter Setup
If required the next step is to enter a WEP key if you want to do this in AirPcap
This key along with WPA and WPA2 settings can also be done directly in Wireshark if they are needed

## Slide 127: AirPcap Adapter Setup

## Slide 128: Wireless Toolbar
Wireshark has a toolbar specific for wireless networks
This is off by default
To turn it on select
  View – Wireless Toolbar

## Slide 129: Wireless Toolbar
The AirPcap says this about the setup of the wireless toolbar

## Slide 130: Wireless Toolbar

## Slide 131: Wireless Toolbar
Most of the settings are the same as described above
But if decrypting traffic keep this in mind about the possible settings
  None
    No decryption is performed, neither at the driver level nor in Wireshark

## Slide 132: Wireless Toolbar
  Wireshark
    The driver doesn’t perform any decryption of the captured packets, and they are decrypted by Wireshark while displaying them
    This has the advantage of minimizing the CPU load during the capture process
    Moreover, the driver doesn’t manipulate the packets, so the captured data is a precise picture of the network traffic
    However, capture filters (also known as BPF filters) on TCP/IP fields or packet payloads will not work

## Slide 133: Wireless Toolbar
    Since this kind of decryption is done by the analyzer, when you turn it on or off, you will see the changes immediately reflected in the Wireshark window
  Driver
    The packets are decrypted by the driver before reaching Wireshark
    This option has two advantages: capture filters on TCP/IP fields or packet payloads will work; when logging the network traffic to disk, it will be unencrypted

## Slide 134: Wireless Toolbar
    This will make it easier for third party applications to understand them
    Since this kind of decoding is done during the capture, the changes you make will be effective starting with the next capture

## Slide 135: Wireless Setup
Laura Chappell suggests these additional steps when working with a wireless network

## Slide 136: Wireless Setup

## Slide 137: Decoding
Once the frames are acquired one way or the other the information must be decoded

## Slide 138: Decoding

## Slide 139: Decoding
This part of the process consists of
  Core Engine
  Dissectors
  Plugins if any
  Display Filters if any
The dissectors do the work of interpreting what is seen in the frames
The result is sent to the GUI, GTK in this case

## Slide 140: Expert Composite Info
Wireshark has a basic expert analysis function
These are just indications, not absolutes
The expert system is activated by Wireshark when it notices errors
This is accessed by either of two ways
  From the Analyze – Expert Info Composite
  By clicking the button in the lower left corner

## Slide 141: Expert Composite Info

## Slide 142: Expert Composite Button

## Slide 143: Expert Composite Button
The color of the button tells us something about what has been detected
  Red
    Errors were found
  Yellow
    Warnings are noted
  Light Blue
    Notes are shown

## Slide 144: Expert Composite Button
  Blue
    Chats are shown
  Gray
    Nothing was detected

## Slide 145: Expert Composite Info
More specifically these levels indicate
  Errors are packet or dissector errors
  Warnings are unusual responses from the application or transport layers
  Notes are unusual responses from the application or transport layers or they maybe a recovery process from a Warning
  Chats are information about the workflow

## Slide 146: Expert Composite Info
These can be filtered on to display them
  expert.severity==error
  expert.severity==warn
  expert.severity==note
  expert.severity==chat
The Notes and Warnings for TCP traffic can be displayed by filtering on
  tcp.analysis.flags
This will show TCP related problems

## Slide 147: Expert Composite Info
Warnings and Notes are related but different
A Warning is a problem with a communication, such as a lost packet
A Note is normal reaction traffic, such as a retransmission
The note maybe indicate a problem, but is still an expected activity due to something else happening first

## Slide 148: Expert Composite Info
Wireshark will report retransmissions and fast retransmissions
These are the same thing
Ignore the difference
Treat them the same

## Slide 149: While Using Wireshark
When using Wireshark some aspects of it should be kept in mind
Such as
  Hiding Wireshark
  Colorization of Frames
  Display Filters
  Not Me Capture Filter

## Slide 150: Hiding Wireshark
Any protocol analyzer should be invisible on the network
This is both good and bad
Good because we do not want extraneous data flowing on the network that will make analysis more difficult
Bad because pesky users can place these on the network as well

## Slide 151: Hiding Wireshark
Wireshark does not need an IP address assigned to the device on which it is running

## Slide 152: Hiding Wireshark
To keep Wireshark from sending data out on the network turn off all name resolution
  Edit – Preferences – Name Resolution
    Enable MAC name resolution
    Enable network name resolution
    Enable transport name resolution
The only one that is likely to send anything out is network name resolution

## Slide 153: Hiding Wireshark

## Slide 154: Colorization
Wireshark makes extensive use of color to identify different types of frames and the parts of those frames
Some or all of the colorization rules can be turned off
However, the colorization notes inside the frame decode cannot
Here is an example of this type of note

## Slide 155: Colorization

## Slide 156: Colorization
The first coloring rule that is true is the only one applied
To be sure a rule of interest is used move it up the list of coloring rules

## Slide 157: Colorization
An individual conversation can be colorized by
  Right Click – Colorize Conversation

## Slide 158: Colorization

## Slide 159: Colorization
To turn this off
  View – Colorize Packet List

## Slide 160: Colorization

## Slide 161: Display Filters
If only a certain type of traffic is of interest it is generally best to capture all traffic then use a display filter to view the traffic of interest
For example to see only DNS traffic
  Enter dns is the capture filter box
  Click Apply

## Slide 162: Display Filters

## Slide 163: Display Filters

## Slide 164: Not Me Capture Filter
Create a Not Me capture filter to filter out traffic back and forth from your own PC
The syntax is
  not ether host XX:XX:XX:XX:XX:XX
    Where the Xs are your PC’s MAC address

## Slide 165: Problems With Wireshark
When using Wireshark some common problems seen include
  Dropping Frames
  Checksum Errors
  Decrypting Wireless Frames
  Showing Errors in Frames

## Slide 166: Dropping Frames
If there are a large number of frames across the link on which Wireshark is capturing traffic it can be overwhelmed
This results in it dropping frames
This could be due to a number of issues including the limitations of the device on which Wireshark is running
To alleviate this try the following

## Slide 167: Increase Buffer Size
Increase the buffer size by selecting
  Capture – Options
  Buffer size

## Slide 168: Increase Buffer Size

## Slide 169: Increase Buffer Size

## Slide 170: Packets in Real Time
Turn off update packets in real time
  Capture – Options
  Update list of packets in real time

## Slide 171: Packets in Real Time

## Slide 172: Name Resolution
Turn off enable name resolution
  Capture – Options
  Enable network name resolution

## Slide 173: Name Resolution

## Slide 174: TCP Checksum Validation
Turn off TCP checksum validation
  Edit – Preferences – Protocols – TCP
  Validate the TCP checksum if possible

## Slide 175: TCP Checksum Validation

## Slide 176: TCP Checksum Validation

## Slide 177: TCP Checksum Validation

## Slide 178: Remove Unneeded Columns
Remove any columns that do not provide currently useful information
  Edit – Preferences – Protocols – TCP
  Columns

## Slide 179: Remove Unneeded Columns

## Slide 180: Remove Unneeded Columns

## Slide 181: Use Tshark Instead
If the GUI version of Wireshark is overwhelmed, then try capturing from the command line using Tshark
The capture file can be opened in Wireshark for analysis

## Slide 182: Use Tshark Instead

## Slide 183: Odd Results Seen in Wireshark
There some common results seen in Wireshark that appear to be problems but are not, such as checksum errors

## Slide 184: Checksum Errors
Wireshark will commonly report many checksum errors that are not really checksum errors
The reason they might be invalid is when Wireshark is being run on the device reporting the bad checksums the problem is likely not bad checksums, but checksum offloading

## Slide 185: Checksum Errors
This occurs when Wireshark captures the frames before the checksum has been computed
These look like this

## Slide 186: Checksum Errors

## Slide 187: Checksum Errors
If responses to these packets are seen, then the checksum is likely good
Wireshark says this concerning this problem
  If the packets that have incorrect TCP checksums are all being sent by the machine on which Wireshark is running, this is probably because the network interface on which you're capturing does TCP checksum offloading

## Slide 188: Checksum Errors
  That means that the TCP checksum is added to the packet by the network interface, not by the OS's TCP/IP stack
  When capturing on an interface, packets being sent by the host on which you're capturing are directly handed to the capture interface by the OS, which means that they are handed to the capture interface without a TCP checksum being added to them

## Slide 189: Checksum Errors
  The only way to prevent this from happening would be to disable TCP checksum offloading, but that might not even be possible on some OSs
  However, you can disable the check that Wireshark does of the TCP checksum, so that it won't report any packets as having TCP checksum errors, and so that it won't refuse to do TCP reassembly due to a packet having an incorrect TCP checksum

## Slide 190: Checksum Errors
  That can be set as an Wireshark preference by selecting "Preferences" from the "Edit" menu, opening up the "Protocols" list in the left-hand pane of the "Preferences" dialog box, selecting "TCP", from that list, turning off the "Check the validity of the TCP checksum when possible" option, clicking "Save" if you want to save that setting in your preference file, and clicking "OK"

## Slide 191: Checksum Errors
Both Wireshark and the information on the NIC from the operating system will show this

## Slide 192: Checksum Errors
To look at this in Wireshark select Details under the Capture menu
  Capture – Interfaces – Details – Task Offload

## Slide 193: Checksum Errors

## Slide 194: Checksum Errors

## Slide 195: Checksum Errors

## Slide 196: Checksum Errors
In the OS, Windows for example, look at
  Device Manager
  Network Adaptor
  Properties
  IPv4 Checksum Offload

## Slide 197: Checksum Errors

## Slide 198: Checksum Errors
This coloring rule can be turned off, but the text in the capture file cannot be removed
To turn off the coloring rule
  View – Coloring Rules
  Checksum Errors
  Disable

## Slide 199: Checksum Errors

## Slide 200: Checksum Errors

## Slide 201: Decrypting Wireless Frames
Wireshark can only decrypt WEP, WPA, WPA2 in pre-shared key mode
The enterprise version that uses a RADIUS server is not supported

## Slide 202: Showing Errors in Frames
Unlike hardware based analyzers Wireshark is limited in several areas especially as related to showing errors on the network
Lacking a set of drivers designed for the NICs out there Wireshark can only read in the frames the standard NIC driver presents to it
Standard NIC drivers do not read in errors

## Slide 203: Showing Errors in Frames
Here is what the Wireshark FAQ says about this issue
  Unless the OS always supplies packets with errors such as invalid CRCs to the raw packet capture mechanism, or can be configured to do so, Wireshark - and other programs that capture raw packets, such as tcpdump - cannot capture those packets
  Most OSs probably do not support capturing packets with invalid CRCs on Ethernet

## Slide 204: Showing Errors in Frames
This is also true of invalid FCS fields at the end of the frame
To which the Wireshark FAQ says
  Unless the OS supplies the FCS of a frame as part of the frame, or can be configured to do so, Wireshark - and other programs that capture raw packets, such as tcpdump - cannot capture the FCS of a frame
  Most OSs do not support capturing the FCS of a frame on Ethernet

## Slide 205: Showing Errors in Frames
This means the network will appear to be error free at the physical and data link layers when it may not be
This is a significant limitation of Wireshark
Other than using a hardware based analyzer, the only way to see these errors is to check the error counters in each switch

## Slide 206: Command Line Tools
As mentioned above Wireshark has several command line non-GUI tools, such as
  tshark
  capinfos
  editcap
  mergecap
  text2pcap
These do the following

## Slide 207: Command Line Tools
Tshark captures files without the added burden on the hardware of a GUI interface
Capinfos prints information about capture files
Editcap edits capture files
Mergecap merges capture files
Text2pcap converts raw hex dumps into pcap files

## Slide 208: Detecting Wireshark
There is no absolutely certain way to detect a protocol analyzer running on a network as these are passive devices
This is a major problem with this sort of tool, which is free to anyone
The best thing to do is to search the web using a phrase such as
  detecting sniffers
then try what they say

## Slide 209: Detecting Wireshark
The basic technique is to attempt to discover NICs set to promiscuous mode as there is no reason for a NIC to be set to this unless the device is running a network analyzer of some sort
However, this does not work when one of these is attached to a spanned or rspanned port

## Slide 210: Detecting Wireshark
But if someone has this level of physical access to the network, you have bigger problems than a network analyzer

## Slide 211: Sources
A considerable amount of this is based on various articles and training material produced by Laura Chappell
If you want to learn abut Wireshark or network analysis she is the place to go

## Slide 212: Sources
The discussion of fiber optic cable taps is from an article in Cabling Installation and Maintenance magaine by Kozischek and Iery of Corning Cable Systems March 2013