## Slide 1: Using a Network Analyzer To Examine a Network
Last Update 2014.06.01 1.10.0

## Slide 2: Objective
Learn what problems commonly occur on networks as well as how to discover if they are occurring on your network

## Slide 3: Sources
Most of this is copied or adapted from a series of seminars and labs by Laura Chappell or a white paper from Fluke Networks
The retransmission filter is from Network Analysis Using Wireshark Cookbook by Yoram Orzach

## Slide 4: Basic Steps
There are certain basic analysis tasks that need to be done on any network
Some of these are done when the network is working correctly and some when it is not
These include
  Baselining the network for troubleshooting
  Isolating the source of a problem
  Identifying security scans and breaches

## Slide 5: Baselining the Network
A baseline is a record of the normal operation
In this case the normal operation of a network
With the baseline record a reported problem can be compared to it to assist in determining the cause of the problem

## Slide 6: Baselining the Network
The elements of a network baseline for troubleshooting purposes include recording and being familiar with the normal operation of each of these
  Broadcast and Multicast Types and Rates
  Bootup Sequence
  Login Sequence
  Protocols and Applications in Use
  Launch and Use of Common Applications

## Slide 7: Baselining the Network
  Web Browsing
  Throughput
  Idle Time Traffic
  Connectivity Tests Through the Network
  Logoff Sequence
Let’s list each of these in more detail as suggested by Laura Chappell

## Slide 8: Broadcast and Multicast Traffic
Who is broadcasting
What applications are broadcasting
What is the rate in packets per second
Who is multicasting
What applications are multicasting
What is the rate in packets per second

## Slide 9: Bootup Sequence
Examine the DHCP process
See what applications are started automatically

## Slide 10: Login Sequence
What discovery process takes place
What server is contacted
What login processes take place
How many packets are required

## Slide 11: Protocols and Applications
What applications are running
What protocols are being used
What ports are in use
What routing protocols are being used
What does the routing update process look like
What ICMP traffic is seen

## Slide 12: Launch and Use of Applications
What discovery process does the application use
Does the application use UDP or TCP
What ports are used
What devices are contacted
How many packets are required
How long does it take
Is cleartext used

## Slide 13: Web Browsing
What DNS servers are used
How long does DNS take
What is the round trip time to the server
What is the application response time to the page request
What servers are contacted
Are any HTTP errors produced

## Slide 14: Throughput
What application is being used for the test
What are the configurations of the test devices
What packet sized is being used
What is the Mbps both ways
What is the packet loss both ways

## Slide 15: Idle Time Traffic
What protocols and applications are seen
What hosts are contacted

## Slide 16: Connectivity
Record ping times between devices

## Slide 17: Logoff Sequence
What logoff processes take place
How many packets are required

## Slide 18: Isolating the Problem Domain
The first step in solving any problem is to isolate the problem domain
That is ignore extraneous matters, identify the specific area in which the problem is occurring, and then fix that problem
Let’s see where problems are most likely to occur and how we isolate the exact source of the problem

## Slide 19: Common Sources of Problems
In a 2008 white paper titled Application Troubleshooting Guide Fluke Networks presented a useful procedure for determining the source of a problem
In their view network problems are due to one of three possible problems with Laura Chappell who does training on network analysis suggesting two more

## Slide 20: Common Sources of Problems
The common problem areas are
  Network
  Server
  Application
  Client
  User

## Slide 21: Causes of Poor Performance
Regardless of the exact location of the problem Laura Chappell lists these as the top causes of poor performance
  High latency times
  Misconfiguration of a device
  Slow processing by a device
  Packet loss
  Traffic redirection
  Small payload sizes

## Slide 22: Causes of Poor Performance
  Congestion
  Application faults

## Slide 23: Common Sources of Problems
Let’s look at each of these five common sources of problems one at a time

## Slide 24: The Network as the Problem
The network can be the source of the problem for several reasons including
  Network Design
  Improper Media Installation
  The Protocols Used
  The Equipment Used
Let’s look at each one of these

## Slide 25: Network Design
Network design in detail is the topic of another course
It is also not related directly to troubleshooting as we are discussing here
However there are some design issues that would cause delay in the network including

## Slide 26: Network Design
  Too many hops between end points
  Improper routing
  Under powered devices

## Slide 27: Improper Media Installation
Structured cabling in detail is also the topic for another course even though we will discuss it in this course to some extent as a troubleshooting issue
Basically if cabling or whatever type of media such as wireless is used is installed incorrectly it may cause delays on the network due to the frames being dropped causing retransmissions

## Slide 28: The Protocols Used
The nature of the protocols commonly used on networks these days can cause numerous problems on the network
The protocols in question include
  TCP
  Protocols Involved in Application Flow

## Slide 29: TCP
Recalling the functions of the four layers of the TCP/IP model, TCP is the main protocol that creates and maintains the data flow across the network
At the transport layer TCP carries about 90% of the traffic on a network and UDP most of the rest
For example as Fluke says

## Slide 30: TCP
  If you segment the traffic on a corporate network into categories determined by the purpose of that traffic, you would probably find a break down something like this: email (10%), transaction processing (25%), http web traffic (35%), broadcast and control (10%) and other traffic (20%)
  The only part of the mix that is based primarily on UDP is in the “other” category
  The remainder use mostly TCP

## Slide 31: TCP
TCP is an adaptive protocol in that it adjusts to changes in throughput
Unfortunately these changes in throughout can be due to network, server, or application problems that produce undesirable results in TCP’s reactions
As TCP adjusts due to these problems it will mask the underlying source of the problem

## Slide 32: TCP
Why is this
Let’s look at how frames move back and forth when utilizing TCP at the transport layer
In this example data is being sent from a client to a server

## Slide 33: TCP
  Laura Chappell explains the process this way
    At the client computer
      To begin the TCP protocol that is part of the TCP/IP stack on the client computer first determines how much data it can send
      This is usually 1460 bytes
      This segment created by the TCP protocol is delivered to the IP protocol at the Network layer where the IP addresses of the sender and receiver are added

## Slide 34: TCP
      Then the IP software contacts the operating system to say an outgoing message is ready to be sent
      When the operating system gives the okay, the outgoing packet is moved to the NIC by handing it off to the Data Link layer
      In this entire process, the performance of the client’s processor is critical to how fast this all can take place
      Slow computer – slow transfer

## Slide 35: TCP
    Across the network
      Packets can follow a short, fast route, a slow, long route or any combination of links
      It is common for a packet to traverse 10-20 individual network links when going over an Internet connection
      Like the adage about the strength of a chain depending on the weakest link, the speed through the network depends on the slowest link
      More often than not, the slowest link is the access link into the network and the egress link out of the network

## Slide 36: TCP
    At the server
      Just like the client end how fast the server processes the request impacts the round trip time of the transaction
      Slow server – slow transfer

## Slide 37: TCP Flags
The flag field in the TCP header can provide some useful troubleshooting information
Let’s look at the eight flags used by TCP as discussed by Chris Greer in a series of articles from Fluke Networks
They are

## Slide 38: TCP Flags

## Slide 39: TCP Flags
  Congestion Window Reduced
  ECN-Echo
  Urgent
  Acknowledgment
  Push
  Reset
  Syn
  Fin

## Slide 40: TCP Flags
Congestion Window Reduced and ECN-Echo
  These two flags are used together when used, but then they are very rarely seen in practice
  They were meant to indicate congestion
Urgent
  As it seems, process this data now

## Slide 41: TCP Flags
Acknowledgment
  This field indicates that the data has been successfully received
  It is also used when establishing and tearing down TCP connections
  Often every packet in a TCP connection has the ACKs flag after the initial SYN

## Slide 42: TCP Flags
Push
  Sometimes set at the end of a block of data to tell the receiver to process the block now
Reset
  This tells the receiver that the sender has unexpectedly terminated the connection
  Although some applications will due this on purpose

## Slide 43: TCP Flags
Syn
  Used as part of the three way TCP handshake to open the connection
Fin
  Used to properly terminate the TCP connection

## Slide 44: TCP Flags
Lets see what the Fluke white paper has to say about how these flags can be used to troubleshoot the network
If using Wireshark, applying the display filter tcp.analysis.flags will display only symptomatic packets
This is a great filter to use when looking at these issues

## Slide 45: TCP Flags
SYN Attack
  This is a type of denial of service attack where a host sends repeated SYN packets to a server, often on the same port
  If the server responds to all these SYNs with a TCP handshake, eventually the server resources will be taken up and it will no longer respond to further SYNs

## Slide 46: TCP Flags
Duplicate ACKs
  When there is packet loss in a TCP Stream, it is possible to see several duplicate ACKs
  When selective acknowledgements are used, the sender of the ACKS (the receiver of the data) will send these to indicate which packet was lost, while acknowledging subsequent packets

## Slide 47: TCP Flags
Window Update and Zero Window
  These are ACK packets sent to indicate the size of the receive buffer of the host who sent it
  If a TCP window is at zero, this informs the other side of the connection that no more room is available in the TCP buffer, and data should stop until further notice
  If a station has window problems, data transfer will be slow

## Slide 48: TCP Flags
Abrupt Resets
  If users are being disconnected from an application, check for RST packets
  We have seen these sent by incorrectly configured load balancers, as well as applications that are mishandling their TCP stacks

## Slide 49: TCP Inefficiency
All in all TCP is an inefficient protocol as it imposes considerable overhead on each transaction
The assumption being that a lengthy stream of conversation will ensue whenever TCP is used
Overhead of up to 50% is common
Further, TCP reacts very aggressively to lost packets

## Slide 50: Application Flow
Next let’s look at the protocols used at the other layers in the overall flow of data when a client requests data from a server
In this example the request is to a web based application
The overall process is
  DNS lookup
  ARP resolution
  Route to the Server

## Slide 51: Application Flow
  Establishing the TCP connection
  Flow of Data
  Closing the TCP connection

## Slide 52: DNS Lookup
Problems that can occur when the server request is made to a web site based application begins with the DNS lookup
Application servers are specified by name, not IP address
Computers connect to each other using IP addresses
Therefore the IP address of the server must be determined

## Slide 53: DNS Lookup
This requires a private or public DNS server be asked for the IP address of the application server
If the DNS server addresses listed for the primary and secondary DNS servers are incorrect or point to hard to reach servers the whole process will begin slowly as the client seeks a DNS server that can respond to its query

## Slide 54: DNS Lookup
Being hard to reach could be due to the use of incorrect or poorly configured routes that would not even be evident when examining the problem from a purely local level

## Slide 55: ARP Resolution
Once again we see the need to translate an IP address when the data is sent around in a frame on a local area network
In this case the device has the IP address of the device it needs to talk to
But an IP address cannot be used on a LAN
So ARP is used to find the MAC address of the device

## Slide 56: Route to the Server
Just as the route to the DNS server may be slow and inefficient or even fail, so might this be true of the route to the server itself
This might be due to a route traveling over slow links or a route that traverses too many hops
This may be due to the network design or the routing protocol used

## Slide 57: TCP Connection
Before data can be transferred over the connection, certain parameters of operation must be agreed upon by the sending and receiving TCP software modules
Recall that TCP is responsible for flow control, reliable delivery, and error control

## Slide 58: TCP Connection
In order to agree on how this will be handled, each TCP stack exchanges certain information during this three-way handshake
For example, in order to establish the maximum number of bytes that will be permitted in each packet, the sender includes a statement of the intended MTU

## Slide 59: TCP Connection
While this is normally 1460 bytes, it isn’t mandatory that value be used
If the other TCP module receives this indication and doesn’t like the value and thinks it should be lower, it simply doesn’t acknowledge that it received it
The sender must take the hint and lower the value

## Slide 60: TCP Connection
A second thing that must be established is how many bytes the receiver can receive in total in its receive buffer
This value, called the window advertisement, is also indicated in the first packet exchanged in the handshake

## Slide 61: TCP Connection
Another value that must be established is the point at which each end will begin to count bytes of data
This is a random value called the initial sequence number and each announces their value in the first two steps of the handshake

## Slide 62: Sequence and Acknowledgment
There are two numbers used to monitor the flow of data back and forth
These are the sequence and acknowledgment numbers
These 32 bit numbers are used to track data that has been sent, received, and still outstanding

## Slide 63: Sequence and Acknowledgment
TCP tracks the data by assigning a sequence number to each byte sent, then it uses an acknowledgement number to determine if any data was lost in transit
When the TCP connection is established each side will use an Initial Sequence Number computed from a unique clock value from 0 to 4,294,967,295

## Slide 64: Lab
Let’s look at the normal TCP connection process called the handshake sequence
Start Wireshark
Open trace05.pcap
Filter for the TCP traffic

## Slide 65: Lab

## Slide 66: Lab
Recall that the handshake sequence is
  SYN
  SYN-ACK
  ACK
Let’s look at each one
Expand the TCP header in each one

## Slide 67: Lab

## Slide 68: Lab

## Slide 69: Lab

## Slide 70: Connection Quality
A common metric of performance of the network application is the round trip time
This is the time from when the SYN is sent and the SYN/ACK is returned
This value is one of the things the sending TCP stack uses to determine how much data should be offered to the network
If the RTT is low, the network appears to be fast

## Slide 71: Connection Quality
If the RTT is high, the network or the server appears to be slow and the TCP stack will adjust accordingly

## Slide 72: Measure RTT
One way to examine this is to use the Round Trip Time graph in Wireshark
This graph created by Wireshark gives a good overall view of the time for a client request to reach the server
If there is a delay it does not say where the delay occurred
But it does show whether further investigation is called for

## Slide 73: Lab
Start Wireshark
Let’s do this lab developed by Laura Chappell
Open download-good.pcap
Pick a server to client packet
Select
  Statistics – TCP Stream Graph – Round Trip Time Graph

## Slide 74: Lab
In this example there is a delay that causes the axis to set itself to 200 milliseconds
There is a set of packets at 130 milliseconds
The majority are at the bottom

## Slide 75: Lab

## Slide 76: Lab

## Slide 77: Lab

## Slide 78: Lab
Vertical strips in a graph like this are another indication of a problem
This is due to packet loss and a high number of duplicate ACKs
This also occurs when data is held by a router, then released

## Slide 79: Lab
Start Wireshark
Open download-bad.pcap
Create the same type of graph
A one second Y axis is very bad

## Slide 80: Flow of Data
TCP has a long list of rules that the sending and receiving protocol software must follow
The method used in the complete implementation of the protocol is beyond the scope of this document

## Slide 81: Flow of Data
However, here are a few of the rules that help in understanding the relationship between how TCP behaves and the network performance
  Delayed acknowledgements occur when packets are received out of order, the last segment isn’t acknowledged until the missing segments are received

## Slide 82: Flow of Data
  If a sender doesn’t receive an acknowledgement of a segment, it doesn’t immediately resend the segment as it could still be in transit
    It waits until it receives three duplicate acknowledgements of the previously received segment
    At that point it assumes the next segment was lost and proceeds with the retransmission

## Slide 83: Flow of Data
  To do this it uses a technique called slow start
  In this procedure one or two segments are sent and the acknowledgements are awaited
  If they return quickly, the sender increases the block size - the number of segments it sends simultaneously

## Slide 84: Flow of Data
  It will continue to increase the block size until one of two things happens: either there is a time out because an acknowledgement isn’t received, such as when a segment has been discarded, or the total data sent is one-half the receiver’s advertised window value

## Slide 85: Flow of Data
This example points out several important features of applications that are using TCP
First, they will appear to adapt to the speed of the network
If the response of the server and the speed of the network are both good, TCP sends more and more data until either the link or the recipient has been saturated with information

## Slide 86: Flow of Data
TCP reacts very aggressively when data is lost in that it slows way down
Now this slowing may be due to only a single bit being damaged
Yet if even one bit is damaged the entire frame is discarded
Therefore TCP is a poor choice for high error environments such as wireless links and poorly cabled networks

## Slide 87: Flow of Data
Yet we have no other choice than to use it, even there
This slow down could also be due to a slow application or slow server rather than a slow network
For example in the last lab you could see that

## Slide 88: Flow of Data
  If the server was quickly processing the incoming data, it would respond on or before the 200 ms wait time
  Instead, the server uses 230 ms to acknowledge that it received the two segments
  Then it sends ACK3
  In step three, the client’s calculation of round trip time (RTT) tells TCP that this situation involves either a slow network or slow server

## Slide 89: Flow of Data
  One of the two is not operating optimally
  So, rather than increase its outgoing number of segments as it did in the other examples, the client sends two segments again, segments four and five
  In step 3, the server is still operating sub optimally, so it takes it 280 ms to determine that it received two more segments
  Then the server sends ACK5

## Slide 90: Flow of Data
  In the final step illustrated, step 4, the client still realizes the RTT is high, so it proceeds to send only two segments again
  After these segments are delivered, if the server would happen to increase its performance, the RTT would be a lower value
  The client’s calculation would indicate that it can increase the number of simultaneous segments it is sending

## Slide 91: Flow of Data
This example points out an additional important point
A subtle point is illustrated by the fact that the client never aggressively increased the number of segments being simultaneously sent
This indicated slowness somewhere
The turn-around time at the server was high

## Slide 92: Flow of Data
This indicated an inability to keep up with the rate at which it was receiving data
It is obvious that the server is the issue here

## Slide 93: Lab
Let’s look at this flow of data process and what it looks like when it goes wrong
Start Wireshark
Open download-bad.pcap
The information in the Expert Composite Info window provides areas to examine to narrow down the problem

## Slide 94: Lab
To see the expert analysis click on the yellow circle at the lower left corner of Wireshark
The expert window pops up

## Slide 95: Lab

## Slide 96: Lab

## Slide 97: Lab
Look at what it say under the Notes tabs, duplicate ACKs are sent when an expected packet is not received
The receiver asks for it again by acknowledging the packet prior to the missing packet

## Slide 98: Lab

## Slide 99: Lab
Keep Alive packets keep the connection up when the window size is zero
Expand one of these
Click on it to go to the packet in Wireshark

## Slide 100: Lab

## Slide 101: Closing the Connection
The last step is to close the TCP connection
This usually works without problem

## Slide 102: Isolating the Problem Domain
If the problem appears to be in part of the network the next question is in what part
In other words the exact problem domain needs to be isolated
Let’s see this procedure in operation

## Slide 103: Lab
Start Wireshark
Open the trace02.pcap file
In this lab an example of how to determine where a problem exists in the network is illustrated
Isolating the problem domain using Wireshark on a full duplex network can be difficult as only one side of the conversation is seen

## Slide 104: Lab
An aggregating tap is a better way to collect the data for this type of analysis
If one is not available this method can be substituted
The indication being looked for is when a retransmission is seen, was the original frame also seen

## Slide 105: Lab
If it is, then packet loss has not yet occurred
The problem is downstream from where the analyzer is currently connected to the network
Upstream is toward the sender of the data
Downstream is the receiver direction

## Slide 106: Lab
To isolate the device or link causing the problem move the analyzer from section to section from the sender end down toward the receiver end until you no longer see both the original packet and the retransmission
When you only see the retransmission this is the area of the problem

## Slide 107: Lab
As you are now downstream from the packet loss
To do this go to the expert composite window
Under the Notes tab select a retransmission warning packet
Highlight the sequence number in the TCP header

## Slide 108: Lab
Use this to create a filter by selecting the sequence number line, then right click and select Apply as Filter - Selected
If any other packets show then we have seen both the original and the retransmitted segments in this section
Therefore we are upstream from the problem area

## Slide 109: Lab
If we do not, then we are downstream
In that case we need to move upstream toward the sender end

## Slide 110: Lab

## Slide 111: Filtering for Retransmissions
Another way to look for retransmissions is to use a display filter
  tcp.analysis.retransmissions
For the trace02.pcap file this display filter shows this

## Slide 112: Filtering for Retransmissions

## Slide 113: Filtering for Retransmissions
The area of interest is seen when the fields under TCP and [SEQ/ACK analysis] is expanded
This shows the following

## Slide 114: Filtering for Retransmissions

## Slide 115: Filtering for Retransmissions
Look at the lines under TCP Analysis Flags
  The time since the original frame is retransmitted is .006 in this example
  Below this is the frame that was retransmitted is shown
  It is 12 here

## Slide 116: Filtering for Retransmissions
Typically the Retransmission Time Out (RTO) timer will be around 0.2 seconds for local connections, and up to 0.3 to 0.4 seconds for international connections

## Slide 117: How Applications Fail
As mentioned above applications can fail due to several factors such as
  DNS Failures
  ARP Failures
  Routing Problems
  Problems Creating a Connection
  Slow Responses

## Slide 118: DNS Failures
When a client application needs the address of a server, its DNS software called the resolver creates a query and forwards it to the local DNS server
The local DNS server is normally listed in its IP configuration

## Slide 119: DNS Failures
If the local DNS server knows the address corresponding to the name, the server returns it and we say the name has been resolved
If the local DNS server does not know the name, it has two choices: forward the query up the tree to the next DNS server or ask each server successively going up the tree to resolve the name on its behalf

## Slide 120: DNS Failures
Either way this takes time and slows the connection attempt
As discussed above improper listing of the DNS server IP addresses will slow this process

## Slide 121: Lab
Let’s look at normal DNS traffic
Start Wireshark
Open trace03.pcap
Filter for just DNS traffic

## Slide 122: Lab

## Slide 123: Lab
Let's look at the first packet
This is a standard recursive query asking for the IP address of www.espn.com
At the bottom of this section are the four main DNS questions

## Slide 124: Lab
These are
  Questions
  Answer Resource Records
  Authority Resource Records
  Additional Resource Records
Next is a response packet
  Note Questions is set to 1 and Answers is set to 1

## Slide 125: Lab

## Slide 126: Lab

## Slide 127: Lab
In packet 54 we can see a conical name response
This is where the DNS query asks for a site, but the site says no, go here instead
In other words it redirects it to another web server for what it wants

## Slide 128: Lab
This is common for sites where the data is placed on distributed servers nearer to the user, such as on the Akamai network

## Slide 129: Lab

## Slide 130: Lab
Next we will examine abnormal DNS traffic
Start Wireshark
Open trace12.pcap
In this example the client tries all three DNS servers it has received an IP address for from the DHCP server
As you can see none of them respond

## Slide 131: Lab
In this specific case the problem was a misconfigured router

## Slide 132: Lab

## Slide 133: ARP Failures
When ARP fails it is commonly due to duplicate IP addresses or the wrong IP address for the default gateway listed in the configuration

## Slide 134: Routing Failures
Routing failures can be due to several factors such as
  Poor route selection over unreliable or slow links
  Poor selection of the routing protocol used
  Routers discarding packets
    A router might discard a packet due to corruption in the packet or more insidiously due to the router being overloaded

## Slide 135: Connection Creation
The most common problem here is the client asking for a service the server does not provide
When this occurs the client specifies a port for a service, the server ignores the request as that port is not open on the server

## Slide 136: Looking for Causes
What tools and procedures do we use then to determine why we are seeing these sorts of errors
The first thing to do is to eliminate the network as the cause of the problem
Doing this involves looking for the problems discussed above
Let’s see how we do this

## Slide 137: TCP/IP Stack Configuration
First check to see if the values the client has are correct
  IP address
  Subnet mask
  Default gateway
  DHCP server
  DHCP lease time
  DNS server addresses

## Slide 138: TCP/IP Stack Configuration
  These values are checked from the command line with
    ipconfig /all

## Slide 139: Lab
If these values are incorrect then perhaps the DHCP process needs to be examined
In this lab we will look at a normal DHCP process
Start Wireshark
Open the trace04.pcap
Here is a normal DHCP exchange

## Slide 140: Lab

## Slide 141: Lab
If the device has never received an IP address or if it is outside of the lease time then all four of the frames shown above will exist
If the device is still inside of the lease time when it boots up, then only the Request and ACK will be seen
The same Transaction ID number is used for the entire process

## Slide 142: Lab

## Slide 143: Lab
Here are the details of the DHCP Request
The Parameter Request is the additional information the device wants from the server if the server can supply it

## Slide 144: Lab

## Slide 145: Lab
Here is the initial response Offer
The IP address in this Offer is the address being offered to the client in this case 10.0.99.2
The hops field shows how far away the DHCP server is and the address of the relay agent if one is needed
In this case the server is on the same network as the hop count is 0

## Slide 146: Lab

## Slide 147: Lab
The device says fine, let me have that address

## Slide 148: Lab

## Slide 149: Lab
The server says ok here it is
The only thing provided in the Offer is the IP address
Now the rest of the information the client wanted that the server can provide is given to it in the ACK

## Slide 150: Lab

## Slide 151: Lab
A clue that the DHCP server or the connection to it is experiencing some problem would be the appearance of more than one Discover from the client
Each Discover would have a different process ID
Typically any eventual answer to the first Discover that timed out would be ignored by the client

## Slide 152: Lab

## Slide 153: Lab
If the device is within its lease time a Discover is not sent, just a Request

## Slide 154: Lab

## Slide 155: Lab
Start Wireshark
Open dhcp-renewtorebind.pcap
When the lease is about to expire the client attempts to renew the lease
After 50 percent of the lease time has expired the client sends a Request
If the server is going to renew the lease it returns an ACK

## Slide 156: Lab
If the client does not receive an ACK at 50 percent, then at 87.5 percent it attempts rebinding
This is where the client looks for another DHCP server
The client makes two requests to the original DHCP server
Then it broadcasts four requests for the same server

## Slide 157: Lab
Finally to starts the process again with a Discover frame

## Slide 158: Lab

## Slide 159: Lab
Start Wireshark
Open arp-bootup.pcap
After receiving the address the client will use a series of Gratuitous ARP requests to see if anyone else is already using that address

## Slide 160: Lab

## Slide 161: Lab
Notice that the sender and target IP addresses are the same
This is a gratuitous ARP

## Slide 162: Lab

## Slide 163: Finding Rogue DHCP Servers
Wireshark can be used to find rogue DHCP servers by capturing the stream of frames back and forth from the client with the problem to the rogue DHCP server
Within this capture the MAC address of the rogue server can be seen
The MAC address tables of the switches can be queried to see what switch and port the rogue DHCP server is attached to

## Slide 164: DNS Resolution
To see if DNS queries are being resolved properly use a command line tool
The command line tool for this is
  nslookup
This is not always useful as nslookup is used by hackers so many servers ignore it

## Slide 165: Isolating the Problem Domain
When the network is slow the cause might be the network, the server, the application running on the server, or the client
Here is an illustration from Laura Chappell showing this

## Slide 166: Isolating the Problem Domain

## Slide 167: Isolating the Problem Domain
Let’s look at these causes as well as application causes in more detail

## Slide 168: Is the Network the Problem
The basic way to see if the network is the problem is to measure the Round Trip Time from end to end
This is the latency in the network
More than 40 milliseconds is too slow for most users
The worst they can tolerate is 100 milliseconds

## Slide 169: Latency
To further examine why this Round Trip Time would be high let’s look at an example from a Laura Chappell presentation
The first six packets in this screenshot show the latency
The time from 1 to 2 show that there is network latency

## Slide 170: Latency
See the difference from 1 to 2 is 167 milliseconds
The server is not the problem as after the ACK in 5 to the data flowing in 6 is very short at .002 milliseconds

## Slide 171: Latency

## Slide 172: Latency
Another indicator of latency would be a high number of duplicate ACKs indicating packet loss and high round trip latency

## Slide 173: Latency
Changing the time setting through
  View – Time Display Format
To Seconds Since Previously Displayed Packet can be useful to show high latency
Then sort this column to identify frames with large delays between them

## Slide 174: The Equipment Used
If the equipment such as the routers and switches used in the network cannot handle the load of the packets and frames flying around the media, then drops will be common
Further, misconfigurations and poorly chosen routing protocols can also cause delays

## Slide 175: The Server as the Problem
If the slowness is not in the network, then the cause may be the server
The time from the initial GET to the server’s ACK is an indication of the server response time
In this example, there is a .15554 second delay before the GET is responded to with an ACK from the server

## Slide 176: The Server as the Problem

## Slide 177: The Server as the Problem
So any delay is not due to the server being slow to fulfill the client request

## Slide 178: The Server as the Problem
Another indication of the server being the problem is a large delay between the ACK after the GET and the initial flow of data
A delay here may be due to processor latency
As Chappell shows

## Slide 179: The Server as the Problem

## Slide 180: The Server as the Problem
In this example the data begins flowing within .001938 seconds as seen in packet 6

## Slide 181: The Server as the Problem

## Slide 182: Lab
Let’s look at some normal server responses to a request
We will look at normal traffic for
  HTTP
  POP
  SMTP

## Slide 183: Lab
Start Wireshark
Open trace06.pcap
After the usual TCP handshake process seen in the first three packets the client issues a GET for the HTTP data it wants
Then the details of the GET are shown

## Slide 184: Lab
Next the server says the information has been moved, which does not always happen, but is also not unusual
Finally the server says, here is the data
The last step is the signoff, the details of which can vary

## Slide 185: Lab

## Slide 186: Lab

## Slide 187: Lab

## Slide 188: Lab

## Slide 189: Lab

## Slide 190: Lab
Now for normal POP traffic
We will use a function of Wireshark called Follow Stream to make seeing the entire process easier
Start Wireshark
Open trace08.pcap
The connection is made
Here is the start of the process

## Slide 191: Lab

## Slide 192: Lab
Select the top packet
Right click and select Follow TCP Stream to see the entire process POP uses

## Slide 193: Lab

## Slide 194: Lab

## Slide 195: Lab
Now for normal SMTP traffic
We will use the same Follow Stream function to make seeing the entire process
Start Wireshark
Open trace09.pcap
The connection is made
Here is the start of the process
Then data flows

## Slide 196: Lab

## Slide 197: Lab

## Slide 198: Lab

## Slide 199: The Server as the Problem
Common statistics to examine on a server to see if it is causing the slow response include
  Dropped frames
  CPU utilization

## Slide 200: The Application as the Problem
A problem with an application running on a server is seen in
  Small data sizes sent and received
  High CPU utilization
  Excessive redirections
  Excessive use of multiple servers for the same application

## Slide 201: Lab
The user says the network is slow
Let’s look at an example where the network is not the problem, rather the way the application is designed is
In this case it is illustrated by a web site access that requires the client receive responses from multiple servers

## Slide 202: Lab
Start Wireshark
Open http-espn.pcap
With this capture file open select
  Statistics – HTTP – Load Distribution
  Click the Create Stat button

## Slide 203: Lab
Examine the result
  How many HTTP servers did the client end up talking to
  Are the IP addresses of these servers all near to each other
    In other words are these servers all at the same place or on different, perhaps widely distributed networks
  Look at the server names are all of them controlled by the same organization

## Slide 204: Lab
Select
  Statistics – HTTP – Packet Counter
  Click the Create Stat button
  Expand the HTTP Response Packets section
    What does it show any problems in terms of
      ??? Broken
      1xx Informational
      2xx Success
      3xx Redirection
      4xx Client Error
      5xx Server Error

## Slide 205: HTTP Stream
To more clearly see the HTTP GET requests and the corresponding response codes in the Packet List pane disable the TCP preference
  Allow subdissector to reassemble TCP streams

## Slide 206: Graph HTTP Traffic Flows
To troubleshoot slow web browsing sessions create a flow graph by selecting
  Statistics – Flow Graph
This shows each target host on a column and every packet in a row

## Slide 207: Graph HTTP Traffic Flows

## Slide 208: Graph HTTP Traffic Flows

## Slide 209: HTTP Requests
The HTTP Requests statistic is also useful to examine the flow
To produce this select
  Statistics – HTTP - Requests

## Slide 210: HTTP Requests

## Slide 211: The Client as the Problem
The first indication that the client might be the problem is after the handshake how long did it take for the client to issue a GET request to the server for data in whatever form that GET request might be
If the GET is not immediately issued, then examine the client as the cause of the delay

## Slide 212: An Example of This
Here is an perfect example of this type of problem and why being abele to do this type of analysis is so important
This is from Jeremy Stretch of PacketLife.net
He wrote in a post titled The Importance of Watching the Wire on April 3, 2013

## Slide 213: An Example of This
  I came across an interesting problem today that I think serves as an excellent example of why packet analysis is such a critical skill for network engineers
  A few days ago, the internal network belonging to one of my employer's customers was compromised by a malicious party

## Slide 214: An Example of This
  Since the customer had connectivity into our network by way of a VPN tunnel and we didn't want to knowingly expose ourselves or other customers to the threat, we saw fit to temporarily sever the VPN while the breach was tended to by another party
  We also upgraded the site's core switch to better support a feature useful in the analysis of the breach

## Slide 215: An Example of This
  Shortly thereafter, we began receiving reports of problems with Internet connectivity from the site
  Everything was reachable, it was just... Slow
  And worse, the issue seemed not to have any uniform effect
  One person experiencing the issue might sit next to someone else who was completely immune and who noticed no difference from the day before

## Slide 216: An Example of This
  This of course made troubleshooting frustrating, to say the least
  First we tried reversing the firmware upgrade on the core switch, as it was reasonable to suspect we may have encountered some obscure bug, but this was quickly revealed to be a red herring as the issue persisted

## Slide 217: An Example of This
  On-site engineers verified that they could still reach everything excluding of course our internal resources which were no longer reachable as a result of severing the VPN and speed tests showed mostly normal results
  There was no correlation between affected users and any access switch, VLAN, or IP subnet

## Slide 218: An Example of This
  We also confirmed about seventeen times that Internet traffic was in fact traveling from end hosts through the firewall directly to the Internet, with no proxy or caching servers in between
  Frustrated with the lack of progress in isolating the issue, I asked for a packet capture to be performed at the site

## Slide 219: An Example of This
  The testing procedure was as follows:
    Open a web browser
    Navigate to about:blank
    This ensures that the test begins with a clean slate and guards against any rogue HTTP requests resulting from leaving the prior page
    Start a promiscuous packet capture in Wireshark
    Navigate to packetlife.net and wait for the page to completely load
    Stop and save the capture

## Slide 220: An Example of This
  My motivation for choosing packetlife.net as the test target was more than mere vanity
  When you load a major web site like yahoo.com or cnn.com, you're actually generating a huge number of HTTP requests under the hood for content from a dozen or so sources such as content delivery networks, embedded advertisements

## Slide 221: An Example of This
  By using a simple, familiar site I knew what sort and number of HTTP requests to expect, which makes the job of analyzing each packet in the capture a good deal easier
  After quickly sanity-checking the packet capture to ensure that the test was completed as designed, my first step was to isolate the initial TCP session triggered by the web request

## Slide 222: An Example of This
  A quick way to do this if you know the IP address of the remote server is to apply a display filter showing only traffic to or from that IP:
    ip.addr==174.143.213.184
  Then, right-click on the first TCP packet (the one with only the SYN flag set) and select "Follow TCP Stream“

## Slide 223: An Example of This
  This will apply a new display filter showing only packets which belong to that TCP session
  It will also generate a new dialog showing the contents of the HTTP request, which in many cases can be quite handy but wasn't of interest at this time
  I reviewed the TCP exchange and everything appeared normal, until I noticed the packet timestamps

## Slide 224: An Example of This
  After the initial three-way TCP handshake SYN, SYN/ACK, ACK completed, there was a delay of about five seconds before the HTTP GET request was transmitted between packets #32 and #101 in the figure below
  Under normal conditions, there should be practically zero delay between the handshake completion and the initial HTTP request, so I knew I was on to something

## Slide 225: An Example of This

## Slide 226: An Example of This
  The delta time column in the screenshot was added to the default column set to show the difference in seconds between each packet and the one displayed immediately before it
  One important clue to note is that the delay here is almost exactly five seconds; a round number to us humans

## Slide 227: An Example of This
  This suggests that some process triggered by or in parallel with the TCP connection is intelligently timing out at five seconds, at which point the HTTP request proceeds
  I cleared the display filter and begin sifting through the packets which were captured between the establishment of the TCP session and the first HTTP request
  Most of it is ambient noise

## Slide 228: An Example of This
  There's nothing terribly interesting except for a few unanswered TCP requests from the local host to a remote server that used to be accessible via the VPN tunnel we disconnected earlier
  The requests were destined for port 5274; a quick google of the port number yielded no clues

## Slide 229: An Example of This
  But the answer finally clicked when I looked up the destination IP address: It was a Trend Micro antivirus server
  What does an antivirus application have to do with Internet connectivity
  One of the services provided by Trend Micro and countless other AV products is the ability to filter URLs and block access from the local machine to questionable web sites

## Slide 230: An Example of This
  As I understand it and I could be wrong, as we're well outside my area of expertise now, the client software hijacks the web browser's HTTP request and sends the URL to a central server which compares it against a blacklist
  In this scenario, that server is no longer accessible, and the connection attempt times out after - you guessed it - five seconds

## Slide 231: An Example of This
  The client then "fails open," meaning that the HTTP request is allowed to continue despite receiving no response from the filtering server
  In hindsight, a big red error page complaining about AV software issues would have all but eliminated our time spent troubleshooting

## Slide 232: An Example of This
  Five seconds may not seem like a substantial amount of time, but remember how I mentioned earlier that large sites tend to pull content from myriad sources just to render a single page
  If several of those request are being hijacked and delayed one after another, the cumulative delay can quickly grow to the point where angry phone calls are placed

## Slide 233: An Example of This
  This explanation also reveals why some users were immune to the issue: They were using an alternate antivirus product, or didn't have the URL filtering feature enabled
  Fortunately, the resolution for this issue ended up being trivial to implement

## Slide 234: An Example of This
  But how long do you suppose troubleshooting might have gone on had we not taken the time to inspect the wire directly
  Hone your packet analysis skills well, as the investment will quickly pay off

## Slide 235: The Client as the Problem
A good indication that the client is the source of the problem is a large number of packets with the window size set to zero
This means the client is overloaded
It cannot currently accept any more data
Watch for this as this will slow the data flow by watching the TCP ACK packets of the receiver

## Slide 236: The Client as the Problem
As the client does not respond to the server the server sends keep alive packets to maintain the TCP connection

## Slide 237: The Client as the Problem

## Slide 238: The Client as the Problem

## Slide 239: Receiver Congestion
This window size zero issue can occur at either the client or the server end
Let’s see how this happens
In this example the receiver, a server in this example, has buffer space for four segments
As the server receives segments the buffers are filled

## Slide 240: Receiver Congestion
At some point if the application cannot pull the segments from the buffers eventually they will all fill up
The receiver will respond to this by sending a Window Size of 0

## Slide 241: Receiver Congestion

## Slide 242: Receiver Congestion
Here comes the first segment of 1460 bytes
It takes up buffer space

## Slide 243: Receiver Congestion

## Slide 244: Receiver Congestion
An ACK goes back

## Slide 245: Receiver Congestion

## Slide 246: Receiver Congestion
Here comes more data
More buffer space is gone

## Slide 247: Receiver Congestion

## Slide 248: Receiver Congestion
More data and less buffer space

## Slide 249: Receiver Congestion

## Slide 250: Receiver Congestion
Now all the buffer space is gone

## Slide 251: Receiver Congestion

## Slide 252: Receiver Congestion
As the ACKs go back for each segment the Window Size is also sent
It drops as the buffer space is used up until finally there is no buffer space and the Window Size is set to zero telling the sender to stop sending

## Slide 253: Receiver Congestion

## Slide 254: Receiver Congestion
It is not just window size zero that is a problem
You must watch for small window sizes as well these have the same effect
For example this client says it has only 576
This causes a 2.75 second delay until the client says here is a larger window size

## Slide 255: Receiver Congestion

## Slide 256: Receiver Congestion
In this example either the server cannot process fast enough or the application is too slow in processing the data it receives

## Slide 257: Lab
Let’s look at an example of the problem a window size of zero creates by examining a capture that also shows how when this occurs the backoff timer that is part of TCP increases exponentially with each window zero packet arrives
Start Wireshark
Open trace21.pcap

## Slide 258: Lab
Scroll down to packet 30
Look at the time column for 30 through 39
Notice the constant increase

## Slide 259: Lab

## Slide 260: Display Host Protocols
Examining the protocols and applications in use by a host can be useful to identify possible causes of slow reactions by the host
To do this
  Apply a display filter, such as by IP address, to limit the display to a single host
  The select Statistics – Protocol Hierarchy

## Slide 261: Display Host Protocols

## Slide 262: Display Host Protocols

## Slide 263: Display Host Protocols

## Slide 264: The User as the Problem
Pesky users are a common problem
If we could just get rid of them, but I believe we are stuck with them
Here is Laura Chappell’s list of common user related problems

## Slide 265: The User as the Problem

## Slide 266: Security Scans and Breaches
The process of guarding a network from simple scanning for holes to plugging security breaches is beyond the scope of this presentation focusing on troubleshooting
The details of this important topic are covered elsewhere

## Slide 267: Another View of Response Time
Wild Packets in a 2010 webinar presented a similar view of application response time
In their view application response time is made-up of
  network response time + transaction response time

## Slide 268: Network Response Time
Wild Packets sees network response time as being composed of
  payload divided by bandwidth + application turns times round trip response time
These parts are defined as
  Payload – bytes of information in the typical frame going back and forth
  Bandwidth – minimal link speed

## Slide 269: Network Response Time
  Application Turns – Number of back and forth frames needed to complete an action the user sees
  Round Trip Response Time – The time from the client to the server

## Slide 270: Transaction Response Time
Wild Packets says the transaction response time is
  Server Response Time plus Client Response Time
These two are
  Server Response Time – Processing time required by the server
  Client Response Time – Processing time required by the client

## Slide 271: Server Response Time
Server Response Time consists of
  Server Latency – Time needed for the server to process a request which is dependent on the memory, disk system, CPU, and load on the server
  Application Latency – Time for the application to perform its job, which is mostly dependent on the software design

## Slide 272: Server Response Time
  Database Latency – Database aspects such as layout and the software design of the program
  Browser Workstation Latency – The client processing ability
  Protocol Latency – Some protocols work better than others, such as the TCP problems detailed above

## Slide 273: Summary
As you can see there are a large number of areas where problems may arise in a network
Using these procedures the first step is to isolate the problem to one area
Then seek the solution to the problem