## Slide 1: NETW-250 PSTN Telephony Applications Last Update 2012.08.08 1.0.0

## Slide 2: Applications
What a telephone can do goes by many names such as actions, routes, forwarding plans, or as in the textbook applications
These are the most common ones
  Basic call handling
  Administration
  Messaging
  Advanced call handling
  CTI

## Slide 3: Applications
Applications themselves are invented out of necessity and driven by market forces
Sometimes the solution is submitted to the ITU, ANSI, or IETF for recommendation as a standard
Most PBX vendors deliver a majority of features using their own proprietary methods
Let’s look at each of these applications

## Slide 4: Basic Call Handling
Most call handling features resemble the services available to a POTS subscriber
  Connecting, disconnecting, and call transfer
The ones we will look at in more detail include
  Intercom Calling
  Mute Hold Transfer Multiparty Calls
  Conferencing
  Call ID

## Slide 5: Intercom Call
Intercom calling is the oldest of all telephony applications
It was the intercom calling application that lead to the invention of the telephone
An intercom call is merely a conversation between two private endpoints
Most intercom calls are two-way conversations, meaning both parties can talk and hear each other talk

## Slide 6: Intercom Calls
In PBX terms, intercom calls are calls between extensions

## Slide 7: Mute
Mute allows the local party to temporarily stop sending sound to the remote party

## Slide 8: Hold
Hold is a form of mute that allows the local party to leave the phone set for an extended period of time, unattended, and then return

## Slide 9: Transfer
Call transfer allows the local party to hand the call in progress off to another extension

## Slide 10: Multiparty
Multiparty conference allows the local party to set up conference calls from their phone
A blind call transfer is one in which the transferring party hangs up immediately following the transfer, having no knowledge of the availability of the party to whom the call was transferred

## Slide 11: Multiparty
A consultative transfer allows the transferring party to speak with the receiving party prior to making the transfer or merely verify the receiver's availability before completing the transfer

## Slide 12: Conferencing
Conferencing allows more than two parties to have a call, all able to hear one another at the same time
Meet-me conferences are ad hoc conferences in which users can voluntarily join a conference in progress by dialing a code on their phones

## Slide 13: Caller ID
Caller identification, also called calling party identification, allows the recipient of a phone call to know which endpoint is calling both before and after answering
Caller ID signals can be sent using in-band or out-of-band signaling

## Slide 14: Administration
Common administrative functions include
  Call accounting
  Console
  Call Logging
  Paging
  Voice Mail
  Call Notification

## Slide 15: Call Accounting
Call accounting includes gauging to whom, when, and to where calls were placed so that utilization of the PBX can be fairly accounted for within the enterprise
Call accounting allows system managers to enforce voluntary system policies, too: abuse of telephone privileges can be documented, etc.

## Slide 16: Console
A console application can
  Monitor the status of calls in progress throughout the PBX or within a certain scope of users
  Tell who's on the phone and who's not
  On some systems keep track of who's in the office and who's out of the office in one of these manners

## Slide 17: Console
    In-Out
      The endpoint can be used to alert the console when an office occupant is in or out of their office
    Do Not Disturb
      An endpoint function that allows each user to silence the ringer on their phone
    Call Forward
      Gives PBX endpoints the ability to temporarily relay all incoming calls to another endpoint

## Slide 18: Call Logging
Call logging is the process of collecting phone call data, analysing this data, and then reporting on the telephone network's cost, performance, capacity and quality of service

## Slide 19: Paging
Overhead paging is when an endpoint broadcasts the voice of the caller over a large group of endpoints simultaneously
Barging is similar to overhead paging, but instead of broadcasting the caller's voice over a large group of endpoints, the caller can send his voice to a single extension
  It's called barging because this feature tends to allow callers to interrupt calls in progress

## Slide 20: Voice Mail
Voice mail records voice messages on behalf of people who aren't available to answer their calls
Some switches have voice mail built in, but most offload the voice mail functions to a dedicated server

## Slide 21: Message Notification
Message notification is the ability to notify each user when they have messages waiting such as a signal from the PBX to light or message an indication lamp on that user's phone
Some network-aware voice mail servers can send an email in the form of a WAV file

## Slide 22: Advanced Call-Handling
Advanced call handling applications include
  Call Parking and Orbiting
  Automatic Call Return
  Hunt and Ring Groups
  Hold Queues
  Directories
  Presence
  Bridging

## Slide 23: Call Parking and Orbit
Call parking allows calls to be placed on hold at virtual extensions until the intended recipient of the transfer can be located
Orbit adds a bit of functionality to call parking by causing the holding call to eventually ring back at the phone where it was parked to begin with

## Slide 24: Automatic Call Return
With automatic call return dialing a DTMF code on the phone, *69 in many areas, causes a PSTN subscriber to automatically return the call of the last person to have called the line

## Slide 25: Hunt Groups and Ring Groups
Hunt groups are logical, sequential groups of endpoints that ring individually when the phone before them in the sequence is busy or unavailable
Ring groups, conversely, are groups of phones that ring simultaneously until one of them is answered, connecting the call

## Slide 26: Hold Queues
The hold queue is a call-ordering application that keeps people waiting in line in the same order in which the phone system originally fielded their calls
Most common in call centers where lots of people are answering a very high volume of calls simultaneously

## Slide 27: Directories
The directory provides subscribers and inbound callers alike with information about how to reach people on the phone system
Information is presented
  On an endpoint's display
  In a web-based or PC application
  Through audible interactive voice response prompts

## Slide 28: Presence
Presence is a genre of applications designed to make it easier to find a particular phone user
It may ring their desk phone and cell phone simultaneously or sequentially
It may mean publishing information about their availability, or presence, in a directory application

## Slide 29: Presence
This information might be the user's current location or possibly a list of people from whom he is willing to receive phone calls at the moment

## Slide 30: Bridging
Bridging is the simultaneous connection to more than one endpoint, such as an office phone and a cell phone

## Slide 31: CTI
CTI - Computer Telephony Integration applications combine the telephony functions of a PBX with database or personal productivity functions on a personal computer or web site
Accessing your bank account from the telephone is an example of this type of application

## Slide 32: CTI
Some common examples of this type of computer assisted application are
  Automated Attendants and IVR
  Privacy Management
  Call Centers

## Slide 33: Automated Attendants
Automated attendants are applications that answer calls using a recorded voice and then respond to caller commands that have been issued through DTMF tones
Interactive Voice Response is an example of an autoattendant

## Slide 34: Privacy Management
Privacy management is used to recognize and attend to certain kinds of incoming calls automatically, based on the caller ID information
For example, it might have the application greet the caller, record the caller's name, and then ring an internal phone to ask the local party whether she wishes to speak with the person

## Slide 35: Privacy Management
If the local party indicates no, the call is disconnected, but if she indicates yes, the call is allowed to proceed as normal with both parties connected

## Slide 36: Call Centers
A call center is a high concentration of application resources dedicated to a concentration of users
One or more PBX systems and special-purpose IVR servers running customized software that has been built for specific customer-service or knowledge-processing applications