## Slide 1: NETW-250 Cisco Voice Solutions Last Update 2014.02.12 1.1.1

## Slide 2: Cisco Voice Solutions
Cisco’s approach to carrying voice traffic naturally reflects their background in designing solutions for data traffic
They eschew the PSTN as best they can for a VOIP only solution
For marketing purposes they call this combination of data, voice, and video traveling over the same network Unified Communications

## Slide 3: Cisco Voice Solutions
Cisco offers three solutions to manage carrying voice over a data network based on the size of the organization
From small to large
  Cisco Unified Communications Manager Express
  Cisco Business Edition
  Cisco Unified Communications Manager

## Slide 4: Cisco Voice Solutions
Two others can be added for greater capability
  Cisco Unity Connection
  Cisco Unity Presence
All of these have gone by one or more other names
Let’s look at these in more detail beginning with Cisco Unified Communications Manager Express

## Slide 5: What is CME
Cisco Unified Communications Manager Express commonly called CME, which was named in the past Cisco Unified Call Manager Express and Cisco Call Manager Express, is a Cisco IOS based IP-PBX for small to medium sized organizations and branch offices of any size organization
The endpoint limit is 450 with 34 appearances per phone

## Slide 6: What is CME
The advantage to CME is that it runs on a regular router
When the proper IOS version when using a 12 and before IOS or the proper license when using a version 15 IOS is acquired for a router then the CME functions are available

## Slide 7: What is CME
CME supports Cisco IP phones using the SCCP - Skinny Client Control Protocol and SIP - Session Initiation Protocol
Cisco likes SCCP a lot, but it is going away
SIP is the one for the future
CME can connect to TDM lines such as a PRI or to any type of packet based digital line

## Slide 8: What is CME
Here are some diagrams from a Cisco brochure on CME that shows how it would be used

## Slide 9: What is CME

## Slide 10: What is CME

## Slide 11: What is Cisco Business Edition
The Cisco Business Edition 300 and 6000 fails in between the Express version the full size CUCM
For example Cisco Business Edition 600 supports up to 1,000 users across 50 sites

## Slide 12: What is CUCM
CUCM - Cisco Unified Communications Manager is the enterprise level solution from Cisco
When the organization size becomes too large for one of the other two, migration to CUCM is required
It scales up to 80,000 users

## Slide 13: Cisco Unity Express
For some bizarre reason known only to Cisco voicemail is not included on either the low end CME or even the high end CUCM
Cisco Unity Express is an add-on that adds voicemail and automated attendant capabilities

## Slide 14: Cisco Unity Connection
Here is what Cisco says about the Cisco Unity Connection add-on
  Enhance Voice Messaging and Collaboration
    Access Voicemail Anytime, Anywhere
      Access your Cisco Unity Connection voice messages the way you prefer – whether from an IP phone, mobile phone, web browser, email client, or a desktop client like Cisco Jabber
      You can also use Cisco SpeechView to have your voice messages transcribed and delivered to your email inbox

## Slide 15: Cisco Unity Connection
    Accelerate Collaboration
      Respond quickly to colleagues and partners by using speech-activated tools
      Easily prioritize and manage messages, access meetings on your calendar, and connect to colleagues by simply saying their names
    Reduce TCO
      Simplify your deployment efforts with the Cisco Unity Connection solution on a Linux appliance
      Enjoy the flexibility to deliver unified messaging, integrated messaging, or simply voicemail
      Cisco Unity Connection works in a variety of messaging environments using standard protocols

## Slide 16: Cisco Unity Connection
    Deploy a Reliable Solution
      With years of successful deployments, Cisco Unity Connection is a tested, reliable solution
      Take advantage of redundancy and voicemail survivability to make sure you never miss a voicemail
    Secure Your Messages
      Security is a concern for most organizations, and mandatory for others
      Cisco Unity Connection keeps your messages highly secure so they cannot be played by someone outside your organization

## Slide 17: Cisco Unified Presence
As Cioara and Valentine explain Cisco Unified Presence promotes an awareness of the VOIP and data networks
Many folks commonly use Instant Messenger (IM) clients to communicate
In these applications, you are able to see the status of a user, gauging whether they are available, busy, or offline before you begin to chat with them

## Slide 18: Cisco Unified Presence
Cisco Unified Presence stretches this capability to the voice network, allowing you to see the status of a user (are they on the phone, off the phone, not available, and so on) before you pick up the phone to dial
In addition to this core functionality, Cisco Unified Presence adds the following capabilities to your voice network

## Slide 19: Cisco Unified Presence
  Enterprise instant messaging
    Unified Presence incorporates the Jabber Extensible Communication Platform (XCP), which is an industry standard method of communicating between different IM clients
  Message compliance
    Many industries require strict compliance guidelines on instant messenger communication
    Cisco Presence supports logging functionality for all types of IM communication

## Slide 20: Cisco Unified Presence
  lnterdomain federation
    Unfortunately, this feature has nothing to do with Star Trek; however, it has everything to do with connectivity
    Using Interdomain federation connections from Unified Presence, you can connect your organization to other domains, such as Google Talk or Web Ex Connect, thus giving you worldwide reach

## Slide 21: Cisco Unified Presence
  Jabber XCP extensibility
    XCP allows you to extend Unified Presence into virtually any area of the data or voice network
    XCP can allow features such as peer-to-peer file sharing, application sharing, video-conference systems, and so on
    XCP integrates with nearly any infrastructure
  Secure messaging
    Applications integrating into Unified Presence can use IPSec or TLS standards to encrypt and secure all communications

## Slide 22: Creating a VOIP Solution
We will focus here on CME as it shows very clearly the type of hardware and the configuration required to make one of these call manager solutions from Cisco work
First the hardware required

## Slide 23: ISR Routers
CME runs on the ISR line of routers such as the 1800, 2800, 2900, 3800, and 3900 series routers
When using CME the number of users determines which router will be needed
Here is a table from Cisco showing the limits by router

## Slide 24: ISR Routers

## Slide 25: Cisco IP Phones Supported
The endpoints are what you use to communicate over this VOIP connection
Typically this will be a hard phone
Cisco IP Phones are divided into four types based on the functions they support
This table from Cisco shows these types

## Slide 26: Cisco IP Phones Supported

## Slide 27: Cisco IP Phone
Let’s look at a typical Cisco IP phone
First the front

## Slide 28: Cisco IP Phone

## Slide 29: Cisco IP Phone
And the back

## Slide 30: Cisco IP Phone

## Slide 31: Cisco IP Phone
Here is what the ports do
  RS232
    This port connects to an expansion module if needed
  10/100 SW
    This port connects the IP phone to the network
  10/100 PC
    This allows another device with a NIC to be attached to the network without running an additional cable

## Slide 32: Cisco IP Phone
Cisco IP Phones have a small switch built into the unit, thus the two RJ-45 ports
This allows it to handle traffic for two VLANs at the same time
Electrical power to the phone can be provided by POE or a power brick plugged into an outlet
POE is by far the best way

## Slide 33: Cisco IP Phone
When power is applied the phone boots up
Let’s see what it does at this point
  The phone is connected to a switch port
  If the IP phone and switch support POE, the IP phone receives power through POE
  As the phone powers on, the switch delivers the voice VLAN information to the IP phone using CDP as the delivery mechanism

## Slide 34: Cisco IP Phone
  The phone sends a DHCP request asking for an IP address on its voice VLAN
  The DHCP server responds with an IP address offer
  When the phone accepts the offer, it receives all the DHCP options that go along with the DHCP request
  DHCP options include items such as default gateway, DNS server information, domain name information, and so on

## Slide 35: Cisco IP Phone
  In the case of Cisco IP phones, a unique DHCP option is included, known as option 150
  This option directs the IP phone to a TFTP server
  After the phone has the IP address of the TFTP server, it contacts the TFTP server and downloads its configuration file

## Slide 36: Cisco IP Phone
  Included in the configuration file is a list of valid call processing agents such as CME routers
  The Cisco IP phone attempts to contact the first call processing server listed in its configuration file to register
  If this fails, the IP phone moves to the next server in the configuration file

## Slide 37: Cisco IP Phone
  This process continues until the phone successfully registers or it runs out of servers to look for

## Slide 38: Licensing CME
CME requires three licenses
  The IOS license for the router’s IOS
  The CME license for the number of users
  A license for each phone
The IOS license comes with the IOS bin file
The phone license is included with the phone

## Slide 39: Load on the Router
Cioara and Valentine in their book from Cisco Press on preparing for the CCNA Voice test make these important points about the router processing load VOIP adds to the basic routing functions
  Cisco designed its routers with one primary purpose in mind: routing

## Slide 40: Load on the Router
  Moving packets between one location and another is not a processor-intensive task, thus Cisco routers are not equipped with the kind of memory and processing resources typical PCs are equipped with
  For example, from a router's perspective, having 256 MB of RAM is quite a bit
  From a PC's perspective, 256MB will barely help you survive the Microsoft Windows boot process

## Slide 41: Load on the Router
  Moving into the realm of VOIP, the network now requires the router to convert loads of voice into digitized, packetized transmissions
  This task would easily overwhelm the resources you have on the router
  This is where DSPs come into play
  DSPs offload the processing responsibility for voice-related tasks from the processor of the router

## Slide 42: Load on the Router
  This is similar to the idea of purchasing an expensive video card for a PC to offload the video processing responsibility from the PC's processor
  Specifically, a DSP is a chip that performs all the sampling, encoding, and compression functions on audio coming into your router

## Slide 43: Load on the Router
  If you were to equip your router with voice interface cards (VIC), allowing it to connect to the PSTN or analog devices, but did not equip your router with DSPs, the interfaces would be worthless
  The interfaces would be able to actively connect to the legacy voice networks, but would not have the power to convert any voice into packetized form

## Slide 44: Load on the Router
  DSPs typically come in chips to install in your Cisco router that look like old memory SIMMs
  Some Cisco routers can also have DSPs embedded on the motherboard or added in riser cards
  Above all, it is important for you to add the necessary number of DSPs to your router to support the number of active voice call, conferencing, and transcoding sessions you plan to support

## Slide 45: Load on the Router
  Cisco provides a DSP calculator that provides the number of DSP chips you need to purchase based on the voice network you are supporting
  A growing network will always require more DSP resources
  It is usually best to pack the router full with as many DSP resources as you can fit in it; you're going to need them

## Slide 46: CME Configuration
Let’s next look at a typical configuration and installation of a CME based VOIP system using Cisco IP phones
The basic steps are

## Slide 47: CME Configuration
  On the switch
    Create a VLAN for data traffic and voice traffic
  On the router
    Activate and configure CME
    Setup DHCP
    Setup NTP

## Slide 48: Create VLANs
The voice traffic needs to be on its own VLAN so it can be given a higher QoS setting
Here is what it looks like

## Slide 49: Create VLANs

## Slide 50: Create VLANs

## Slide 51: Create VLANs
Notice that each port is in two VLANs at the same time

## Slide 52: Activate and Configure CME
To activate and perform just basic configuration of CME this is required
  Activation command
  IP source address specification
  Max-ephones setting
  Max-dn setting
  Specifications for each phone
  Associating ephones and ephone-dns

## Slide 53: Activate and Configure CME
For example
  telephony-service
  ip source address 192.168.1.1
  max-ephones 5
  max-dn 5
  ephone-dn 1
  number 101
  button 1:2

## Slide 54: Activate and Configure CME
We will see more of this and explain all of the commands in more detail in the CME configuration lab

## Slide 55: Setup DHCP

## Slide 56: Setup NTP

## Slide 57: IP Phone Configuration Files
The DHCP option 150 and the TFTP server IP address work together to manage the configuration file each IP phone must receive from CME for the phone to function
The TFTP server holds the configuration files for the phones

## Slide 58: IP Phone Configuration Files
When you configure a Cisco IP Phone in either CME or CUCM a XML configuration file is generated and stored on a TFTP server
These XML configuration files have a filename format of SEPdP Phone MAC Address>.cnf.xm1 and contain a base configuration for the IP phone, such as language settings, URLs, and so on

## Slide 59: IP Phone Configuration Files
These XML files also contain a list of up to three CUCM server or CME IP addresses the Cisco IP Phone uses for registration
After the IP phone receives the XML file, it attempts to register with the first CUCM or CME server listed in the file

## Slide 60: IP Phone Configuration Files
If it is unable to reach that server, it moves down to the next until the list is exhausted at which point the IP phone reboots and tries it all over again
If the Cisco IP Phone has not yet been configured in CUCM or CME no SEP<MAC>.cnf.xml file exists on the TFTP server

## Slide 61: IP Phone Configuration Files
So the phone requests a file named XMLDefault.cnf.xml
This is a base configuration file typically used for a feature called Auto-Registration
That is allowing phones to register without being configured
Many people often wonder the meaning of SEP at the beginning of the configuration filename

## Slide 62: IP Phone Configuration Files
SEP stands for Selsius Ethernet Phone
Selsius was the name of the company Cisco bought in order to get into the VOIP market

## Slide 63: IP Phone Registration
Once the phone finishes the boot up process it must register with the call manager, CME in this case
The phone use either SCCP or SIP for this
The process it follows is
  Contact the call processing server
  Identify itself by its MAC address

## Slide 64: IP Phone Registration
  The call processing server looks at its database and sends the operating configuration to the phone
  The operating configuration is different than the settings found in the configuration XML file located on the TFTP server
  The TFTP server configuration is base level settings, including items such as device language, firmware version, call processing server IP addresses, port numbers, and so on

## Slide 65: IP Phone Registration
  The operating configuration contains items such as directory and line numbers, ring tones, softkey layout, and so on
  Although the TFTP server configuration is sent using the TFTP protocol, the operating configuration is sent using SCCP or SIP

## Slide 66: Dial Peers
The above is all that is required when the calls stay in one location
If the calls need to cross a link between routers, then dial peers must be configured at both ends so calls can travel both ways

## Slide 67: Dial Peers
The commands look like this
  dial-peer voice 1100 voip
  destination pattern 110.
  session target ipv4:192.168.1.2
Again more detail on this in the lab

## Slide 68: QoS
QoS is very important for VOIP
There are numerous ways to do this
Books have been written on the subject
There is still no complete agreement or simple way to do this
In the Cisco world by far the easiest way is to use the AutoQoS command

## Slide 69: Sources
Much of the above was copied from the CCNA Voice certification test guide by Cioara and Valentine from Cisco Press