## Slide 1: NETW-250 PSTN How It Works Last Update 2012.09.03 1.0.0

## Slide 2: Mesh Versus Switched
Telephones can be connected with three approaches
  As a mesh network where every phone is connected to every other phone
  As a switched network where links are established and removed as needed
  As a stateless packet based network
Let’s look at how the PSTN developed from its earliest days to today

## Slide 3: Mesh
In the beginning around 1877 each site that wanted to talk to another site had to be connected to it with dedicated wires
This is a mesh network layout

## Slide 4: Mesh

## Slide 5: Mesh
In a mesh network a ring-down circuit is used
In a ring-down circuit there is no dialing of numbers
Instead, a physical wire connects the two devices
One for the connection and the other one attached to ground

## Slide 6: Mesh
One person picks up the phone and the other person is on the other end
Moving the voices across the wire requires a carbon microphone, a battery, an electromagnet, and an iron diaphragm
Mesh networks do not scale well as they require too many wires from each site

## Slide 7: Mesh

## Slide 8: Exchanges
It became obvious very quickly that this would not work on a large scale
The solution was to run all wires to a central point called an exchange
The first Bell system exchange went into operation in 1878 in New Haven Connecticut

## Slide 9: Exchanges
By 1878 most major urban areas had a telephone exchange that operated under a license from the Bell System

## Slide 10: Operators
These exchanges required operators and switchboards in order to create the end to end connection
The operators at first wrote down the number the person wanted to call, and then called back the originator of the call once the connection was ready
The route of the call was built from office to office operator by operator

## Slide 11: Switching
Operator assisted calls began to be automated in 1926 with the Combined Line and Recording method
With it the first operator the customer spoke to was the one who built up the circuit and placed the call
For the first time, most calls were completed while the customer stayed on the line

## Slide 12: Switching
The average call completion time dropped to 2.1 minutes
In 1929 the Bell system put the national General Toll Switching Plan into operation
This plan established a hierarchical, national circuit switching network

## Slide 13: Switching
A call went to the local office where it was connected to one of more than 2,000 toll offices or 140 primary centers, and then up to 8 interconnected regional centers
Sectional centers were added in the 1950s
Here is what it looked like

## Slide 14: Switching

## Slide 15: Switching
Automated switching began in 1943 when the first No. 4 Crossbar Switch was added to the system in Philadelphia
These switches were able to automatically route operator-dialed routing codes or customer-dialed numbers

## Slide 16: Switching
With it a single operator built up the needed circuit by dialing a series of routing codes to instruct this automatic electromechanical switch
Dialed routing codes soon gave way to the familiar area codes, which the switch itself could translate into the needed routing information

## Slide 17: Switching
AT&T soon modified the switch to handle customer-dialed long distance calls
The modified design became the No. 4A crossbar switch
No. 4A crossbar switches and direct-distance dialing spread to subscribers across the country during the 1950s

## Slide 18: Switching
Call-completion time dropped to 10-20 seconds
In 1976, the first electronic switch was introduced as the 4ESS in Chicago
The 4ESS was in essence a special purpose computer
Call completion dropped to 1 to 2 seconds

## Slide 19: Switching
The hierarchical call structure where a call went from office to office up a chain and then back down could now be bypassed as the 4ESS was capable of selecting the best route across the network

## Slide 20: Transmission
In addition to the developments in switching the transmission system underwent a course of development as well
The original system was copper wires of various sizes connecting the end users and the telephone office, and then one telephone office to the next all around the world

## Slide 21: Copper Cabling
Copper is a flexible, resilient material that is highly conductive of electricity
It has excellent transmission characteristics over short-distances
Over long distant runs it suffers from attenuation

## Slide 22: Transmission
In order to carry the increasing number of calls outside of local areas the Bell system began to introduce new methods in the 1940s to replace and supplement the copper lines
Copper cables over long distances were replaced by microwave radio links through the AT&T Long Lines system

## Slide 23: AT&T Long Lines Network
The towers used still exist in some areas
You have probably seen the signs of this wireless WAN when traveling down the highway, especially outside of a major city
The sign to look for to identify the remains of this network is

## Slide 24: AT&T Long Lines Network

## Slide 25: AT&T Long Lines Network
AT&T used these towers from 1947 to the late 1990’s
This was the long distance network you used whenever you called someone in another city
It connected the central offices throughout the country to each other, and to other provider’s networks

## Slide 26: AT&T Long Lines Network
This network used microwave radio frequency links
Each link went from tower to tower

## Slide 27: Fiber Optic Cabling
In the 1960s the copper analog transmission system was switched to a digital fiber optic cable based system
Switching the light source on and off or changing intensity allows you to transmit a digital bit stream over the fiber

## Slide 28: Fiber Optic Cabling
Fiber optic cabling is a good choice for longer runs because of its lower attenuation characteristics
Between the mid 1980s and the early 1990s the entire long distance network became an all digital, fiber optic cable based network with the radio links going away and all but the last mile being fiber optic cabling

## Slide 29: Circuits
Over these transmission lines circuits of various types carried the traffic
The most common voice circuit is the PRI – Primary Rate Interface version of a T1 line

## Slide 30: Circuits
A PRI circuit is a digital signal carried across 23 digitally encoded voice channels, called DS0s, to be carried across a T1 circuit between the central office and an enterprise PBX
The 24th channel is the carrier channel or the signaling channel

## Slide 31: Circuits
The basic PRI circuit is grouped with others to create larger circuits
SONET - Synchronous optical network STS-1s and DS3 - 44.736 Mbps also called T3 lines carry several T1s providing high-bandwidth-signaling pathways between switches on the PSTN

## Slide 32: Circuits
The transmission system circuit hierarchy looks like this
  T1/E1
    T1 is a 1.544-Mbps digital transmission link normally used in North America and Japan
    E1 is a 2.048-Mbps digital transmission link normally used in Europe

## Slide 33: Circuits
  T3/E3, T4 over coaxial cable
    T3 carries 28 T1s or 672 64-kbps connections and is 44.736 Mbps
    E3 carries 16 E1s or 512 64-kbps connections and is 34.368 Mbps
  T4 handles 168 T1 circuits or 4032 4-kbps connections and is 274.176 Mbps

## Slide 34: Circuits
  SONET is normally deployed in OC-3, OC-12, and OC-48 rates, which are 155.52 Mbps, 622.08 Mbps, and 2.488 Gbps, respectively
    OC-1 = 51.85 Mbps
    OC-3 = 155.52 Mbps
    OC-12 = 622.08 Mbps
    OC-24 = 1.244 Gbps
    OC-48 = 2.488 Gbps
    OC-192 = 9.952 Gbps
    OC-255 = 13.21 Gbps

## Slide 35: Circuit
Another circuit that has been used for voice calls is an ISDN BRI circuit
It uses two channels of voice called B channels, each using 64 kbps of bandwidth, while the third channel called the D channel uses 16 kbps for call signaling

## Slide 36: Channel Banks
A channel bank is used to multiplex, that is combine, separate digital voice signals into a single T1 circuit and demux or split it back into its individual signals again at the other end
A channel bank combines up to 24 separate phone lines into a single digital link

## Slide 37: Channel Banks
One purpose of a channel bank might be connecting a group of digital phones to a PBX through that PBX's T1 interface

## Slide 38: The Network
All of these transmission lines and circuits are laid out in a network where they are used to connect the end user to the various offices of the phone company so as to enable communication around the world

## Slide 39: The Network
This network consists of
  From the customer site to the nearest central office
  From the central office to a higher level office
  Across the PSTN
  From the higher level office to the central office
  From the central office to the customer site

## Slide 40: The Network
For connections from the central office to a residence customer an analog phone line is used
  There is usually only one conversation on each one of these
For connections from the central office to a business a PBX trunk is used
  Usually several simultaneous conversations can be carried on these

## Slide 41: The Network
Connections between PBXs at a customer site are trunks
Connections between central office switches are trunks

## Slide 42: The Network
The telephone infrastructure starts with a simple pair of copper wires running to your home
This physical cabling is known as a local loop
The local loop physically connects the end user telephone to the central office switch also known as a Class 5 switch or end office switch

## Slide 43: The Network
The communication path between several central office switches is known as a trunk
Just as it is not cost-effective to place a physical wire between your house and every other house you want to call, it is also not cost-effective to place a physical wire between every central office switch

## Slide 44: The Network
End office switches or central office switches interconnect through trunks to tandem switches also referred to as Class 4 switches
Higher layer tandem switches connect local tandem switches
For example

## Slide 45: The Network

## Slide 46: Trunks
Trunk lines are use for several purposes

## Slide 47: Switch-to-Switch Trunks
A switch-to-switch trunk is one that carries calls between two switches in the PSTN
Trunks that connect a PBX to the local phone company are also considered switch-to-switch trunks

## Slide 48: Switch-to-Switch Trunks

## Slide 49: Point-to-Point Trunking
High-density copper cables used to interconnect PBXs that are within a few hundred meters of each other are called point-to-point trunks or private trunks
These interconnect PBXs at a site without going back through the PSTN

## Slide 50: POTS
The result of all of these transmission lines, circuits, and networks is the POTS – Plain Old Telephone Service
This is the traditional wired telephone connected by a two wire circuit that is installed between your home or business and the central office of the local phone company

## Slide 51: POTS
All power to the phone comes from the central office
Ringing, dial tone, and busy signals come from the central office
Any other feature that you may have all come from the central office
Simplicity and reliability have been key reasons for its longevity

## Slide 52: Analog Telephone
An analog phone is composed of five parts
  Ringer
  Dial Pad
  Hybrid
  Hook Switch
  Handset
These all work together in this manner

## Slide 53: Ringer
To activate the ringer when the central office wants to signal an incoming call, it will connect an alternating current signal of roughly 90 volts to the circuit
This will cause the bell in the telephone to produce a ringing sound
This current is different from the PSTN supplied DC current that powers the phone

## Slide 54: Dial Pad
The dial pad in the telephone sends a tone to the central office to tell it who it wants to call, as well as to respond to prompts
Today these are DTMF tones
For example

## Slide 55: Dial Pad

## Slide 56: Hybrid
The hybrid also called the network is a type of transformer that combines the signals transmitted and received across a single pair of wires and the two pairs of wires in the handset
One of the functions the hybrid performs is regulating sidetone, which is the amount of your transmitted signal that is returned to your earpiece

## Slide 57: Hybrid
Its purpose is to provide a more natural-sounding conversation
Too much sidetone, and your voice will sound too loud, too little, and you’ll think the line has gone dead

## Slide 58: Hook Switch
This device signals the state of the telephone circuit to the central office
When you pick up the telephone, the hook switch closes the loop between you and the central office, which is seen as a request for a dial tone
When you hang up, the hook switch opens the circuit, which indicates that the call has ended

## Slide 59: Hook Switch
The hook switch can also be used for signaling purposes as a flash

## Slide 60: Handset
The handset or telephone consists of a transmitter and receiver
It performs the conversion between the sound energy humans use and the electrical energy the telephone network uses

## Slide 61: Tip and Ring
In an analog telephone circuit, there are two wires
In North America, these wires are referred to as Tip and Ring
This terminology comes from the days when telephone calls were connected by live operators sitting at cord boards

## Slide 62: Tip and Ring
The plugs that they used had two contacts, one located at the tip of the plug and the other connected to the ring around the middle
For example

## Slide 63: Tip and Ring

## Slide 64: Tip and Ring
The Tip lead is the positive polarity wire
In North America, this wire is typically green and provides the return path
The Ring wire is the negative polarity wire
In North America, this wire is normally red
For modern Cat 5 and 6 cables, the Tip is usually the white wire, and Ring is the coloured wire

## Slide 65: Tip and Ring
When your telephone is on-hook, this wire will have a potential of –48V DC with respect to Tip
Off-hook, this voltage drops to roughly –7V DC

## Slide 66: Signals
To make the POTS work over these circuits carried by the transmission lines various types of signals have been and are carried over these
Let’s look at these

## Slide 67: Analog Signals
Everything you hear, including human speech, is in analog form
In the beginning the PSTN was based on an analog infrastructure
Analog communication is ideal for human interaction, but it does not work well over long distances due to line noise

## Slide 68: Analog Signals
In the early telephony network, analog transmission was passed through amplifiers to boost the signal
But, this practice amplified not just the voice, but the line noise as well
This line noise resulted in an often unusable connection

## Slide 69: Analog Signals
The reason for this is analog communication is a mix of time and amplitude
Here is what it looks like in a view from a Cisco book

## Slide 70: Analog Signals

## Slide 71: Analog Signals
If you were far away from the end office switch, an amplifier might be required to boost the analog transmission
Analog signals that receive line noise can distort the analog waveform and cause garbled reception
This is more obvious to the listener if many amplifiers are located between your home and the end office switch

## Slide 72: Analog Signals
As this figure shows an amplifier does not clean the signal as it amplifies, but simply amplifies the distorted signal

## Slide 73: Analog Signals

## Slide 74: Analog Signals
This process of going through several amplifiers with one voice signal is called accumulated noise

## Slide 75: Sound Range
Humans can hear in the range of 20 to 20,000 Hz
However, human speech is mostly in the 250 to 3,000 Hz range
So the PSTN was designed to carry signals in the 300 to 3,500 Hz range

## Slide 76: Digital Signals
In digital networks, line noise is less of an issue because repeaters not only amplify the signal, but clean it to its original condition
This is possible with digital communication because such communication is based on 1s and 0s

## Slide 77: Digital Signals
So, as shown in this figure a repeater, which is a digital amplifier, only has to decide whether to regenerate a 1 or a 0

## Slide 78: Digital Signals

## Slide 79: PCM
PCM – Pulse Code Modulation is the most common method of encoding an analog voice signal into a digital stream of 1s and 0s
All sampling techniques use the Nyquist theorem, which basically states that if you sample at twice the highest frequency on a voice line, you achieve good-quality voice transmission

## Slide 80: PCM
The PCM process is as follows
  Analog waveforms are put through a voice frequency filter to filter out anything greater than 4,000 Hz
  These frequencies are filtered to 4,000 Hz to limit the amount of crosstalk in the voice network
  Using the Nyquist theorem, the signal is sampled at 8,000 samples per second to achieve good quality voice transmission

## Slide 81: PCM
  After the waveform is sampled, it is converted into a discrete digital form
  This sample is represented by a code that indicates the amplitude of the waveform at the instant the sample was taken
  The telephony form of PCM uses eight bits for the code and a logarithm compression method that assigns more bits to lower amplitude signals

## Slide 82: PCM
For PCM if you multiply the eight-bit words by 8,000 times per second, you get 64,000 bits per second
The basis for the telephone infrastructure is 64,000 bps or 64 kbps

## Slide 83: Digital Signals
Two basic variations of 64 kbps PCM are commonly used
  μ-law, the standard used in North America
  a-law, the standard used in Europe
The methods are similar in that both use logarithmic compression to achieve from 12 to 13 bits of linear PCM quality in only eight-bit words, but they differ in relatively minor details

## Slide 84: Signaling System
To manage these signals as they transit the transmission lines a signaling system is required to setup, maintain, and teardown the calls

## Slide 85: Signaling System
Generally, two types of signaling methods run over these various transmission media
The signaling methods are broken into the following groups
  User-to-network signaling
    How an end user communicates with the PSTN
  Network-to-network signaling
    How the switches in the PSTN intercommunicate

## Slide 86: User-to-Network Signaling
The most common signaling method for user-to-network analog communication is DTMF - Dual Tone Multi-Frequency
DTMF is known as in-band signaling because the tones are carried through the voice path
Tones consist of two pitches
Here is how DTMF tones are derived

## Slide 87: User-to-Network Signaling

## Slide 88: User-to-Network Signaling
When you pick up your telephone handset and press the digits, the tone that passes from your phone to the central office switch to which you are connected tells the switch what number you want to call
DTMF is defined by the ITU Q.23 and Q.24 specifications

## Slide 89: Standard Tones
The other tones used in the network are called standard tones
These are the dial tone, the ringback tone - the ringing the caller hears while waiting for his call to be connected, and the busy tone
These tones are also defined by the ITU, in specifications E.180 and Q.35

## Slide 90: Standard Tones

## Slide 91: Network-to-Network Signaling
To manage the PSTN itself a network-to-network signaling system is required
Network-to-network signaling types include in-band signaling methods such as MF - Multi-Frequency and RBS - Robbed Bit Signaling and out of band signaling such as the common Signaling System 7

## Slide 92: SS7
SS7 is the PSTN’s network-to-network signaling system
It coordinates communication between switches, telephone company databases, and billing systems
SS7 was developed by the ITU Telecommunications Standardization Sector

## Slide 93: SS7
It is called C7 in Europe
SS7 is a separate network whose duties are setting up, tearing down, monitoring, and routing calls on the PSTN
Like TCP/IP, SS7 is packet-based

## Slide 94: SS7
SS7 is an out-of-band signaling standard because, it doesn't use the same frequency band, or the same transport, as the voice transmission

## Slide 95: SS7

## Slide 96: Numbering Systems
To keep all of this straight a worldwide numbering system is used as well as the interior extension numbers

## Slide 97: Geographic Codes
An area code is a geographic code grouped into logical, compact geographic areas large enough to support from five or six million phone numbers each
These area codes, are used to help the PSTN and SS7 route calls between subscribers in remote areas of the network

## Slide 98: Geographic Codes
Country codes are similar prefixes, but for calls between different national PSTN designations
These codes are defined in the ITU recommendation E.164

## Slide 99: PSTN Numbering Plans
One feature that slowly changed over time is the dial plan
The addition of second lines for Internet access, cell phones, and fax machines has created a relative shortage of phone numbers
In some places in the United States, it is necessary to dial 10 digits for even a local call

## Slide 100: PSTN Numbering Plans
This will become more and more prevalent as more devices require telephone numbers
The need to dial 10 digits for a local number is normally due to an overlay
An overlay can result in next-door neighbors having different area codes

## Slide 101: PSTN Numbering Plans
An overlay is when a region within an existing area code has another area code overlaid
This offers the existing customers the benefits of not having to switch area codes, but forces everyone in that region to dial 10 digits to call anywhere

## Slide 102: PSTN Numbering Plans
NANP is an 10-digit dialing plan that contains three parts
  The NPA - Numbering Plan Area also referring to as area code)
  The NXX Central Office Code
  The Station Number
This plan is often referred to as NPA-NXX-XXXX

## Slide 103: PSTN Numbering Plans
NPA codes use the following format
  NXX, where N is a value between 2–9 and X is a value between 0–9
  NANP is also referred to as 1+10
  This means that when a 1 is the first number dialed, and then the 10-digit NPA-NXX-XXXX number

## Slide 104: PSTN Numbering Plans
This enables the end office switch to determine whether it should expect a 7 or 10 digit telephone number

## Slide 105: Applications
As with almost every industry, it is usually better and easier to acquire additional business from current customers than it is to go out and get new customers
The PSTN is no different
To grow the system the Local Exchange Carriers have been increasing the features they offer to create a higher revenue stream per consumer

## Slide 106: Applications
Numerous services are now available, for example, which were not available just a few years ago
These services come in two common flavors
  Custom calling features
  CLASS features

## Slide 107: Applications
Custom calling features rely upon the end office switch, not the entire PSTN, to carry information from circuit-switch to circuit-switch
CLASS features, however, require SS7 connectivity to carry these features from end to end in the PSTN

## Slide 108: Applications
A few of the popular custom calling features commonly available are
  Call waiting
    This notifies customers who already placed a call that they are receiving an incoming call
  Call forwarding
    This enables a subscriber to forward incoming calls to a different destination
  Three-way calling
    This enables conference calling

## Slide 109: Applications
Some of the CLASS features are
  Display
    Displays the calling party’s directory number, or Automatic Number Identification
  Call blocking
    Blocks specific incoming numbers so that callers are greeted with a message saying the call is not accepted

## Slide 110: Applications
  Calling line ID blocking
    Blocks the outgoing directory number from being shown on someone else’s display
  Automatic callback
    Enables you to put a hold on the last number dialed if a busy signal is received, and then place the call after the line is free
  Call return
    Enables users to quickly reply to missed calls

## Slide 111: Applications
Many interexchange carriers also offer business features, such as
  Circuit-switched long distance
    Basic long-distance services at a discounted rate

## Slide 112: Applications
  Calling cards
    Pre-paid and post-paid calling cards
    You dial a number, enter a password, and then call your destination
  800/888/877 numbers
    The calling party is not charged for the call
    Instead the party called is charged

## Slide 113: Service Providers
The telecommunications network in the US is made up of ILECs, CLECs, and IXCs
The ILECs are the original telephone network providers such as
  AT&T
  Century Link
  Frontier

## Slide 114: ILECs
The only significant ones left are
  AT&T
  Verizon
  Qwest

## Slide 115: CLECs
The CLECs are newer companies that compete against them in one or more of the ILEC’s market areas
Such as
  Cbeyond
  Earthlink
  Level 3 Communications
  Windstream
  XO Communications

## Slide 116: IXCs
IXCs are network operators that provide connections between PSTN network carriers

## Slide 117: ISPs
ISPs are not a part of the PSTN
They are often operated by the same companies that provide PSTN services

## Slide 118: LATAs
As part of the 1984 breakup of Ma Bell the country was divided into LATAs - Local Access Transport Areas
160 of these cover the US

## Slide 119: Texas LATAs

## Slide 120: Customer Premises Equipment
At the end of all of this and the area we will be working in is the customer premises
Any equipment installed by the telephone company for use in terminating voice calls or other connections is called CPE - Customer Premises Equipment
Things found at the CPE include

## Slide 121: Customer Premises Equipment
The Demarc
  The point at which telephone company-owned facilities terminate
Inside Wiring and the Cable Plant
  The privately owned network of communications cabling and wiring terminals located on the customer side of the demarc
Switches
  Usually a PBX or a KSU

## Slide 122: Customer Premises Equipment
CP Distribution Frames
  Cross-connect blocks, terminals, or patch panels where endpoint locations are aggregated and centralized
Let’s look at this equipment in more detail

## Slide 123: Demarc
A demarc is a demarcation point
It is where you stop and the phone company starts
This means that whatever does not work on your side is your problem
Whatever does not work on their side is also your problem, but you’ll have to call them to get it fixed

## Slide 124: Demarc
The demarc can be called several things
For example, I use demarc as short for demarcation point
Others write demark
BICSI, who certifies cable installers, calls it the RDP – Rate Demarcation Point

## Slide 125: Demarc
The phone company calls it several different things
  Network Interface
  NID – Network Interface Device
  Network Interface Unit

## Slide 126: Demarc at a House

## Slide 127: Demarc at a Small Business

## Slide 128: Demarc at a Small Business

## Slide 129: Demarc at a Large Business

## Slide 130: Demarc at a Large Business

## Slide 131: Inside Wiring

## Slide 132: Telephone

## Slide 133: Telephone
In conventional telephony, every endpoint - telephone - is an analog transducer set with a touch tone dial-pad or a rotary-dial pulse wheel in the old days
Both touch-tone and rotary phones share support for some variant of FXS signaling

## Slide 134: CPE Signaling Methods
FXS and FXO Signaling
  FXS - Foreign Exchange Station refers to the signaling used by switch interfaces that serve analog telephones
  An FXS interface is on the switch, with a phone connected to it
  FXO - Foreign Exchange Office refers to the signaling used by telephones or PBX systems
  An FXO interface is on a phone or PBX that is connected to a port at the central office

## Slide 135: CPE Signaling Methods
Loop Start Signaling is
  Used to initiate a call on an analog phone by lifting the handset thus closing the loop
  Current creates the sound of the dial-tone in the handset's transducer

## Slide 136: CPE Signaling Methods
Channel Associated Signaling is
  A digital cousin of FXS and FXO that uses an in-band or robbed-bit approach
  Also called channel associated signaling, or CAS robbed-bit means that a portion of the digital bit stream normally used for sound transmission is allocated for signaling
  Unless you use channel banks extensively, you're unlikely to encounter CAS

## Slide 137: Lines and Line Appearances
There are two ways to refer to voice channels on each phone
  A line is a physical connection to the PBX, a single voice circuit that is capable of carrying one concurrent phone call
  A line appearance, conversely, is the one concurrent phone call

## Slide 138: Lines and Line Appearances
For example from a PBX subscriber's phone, you may dial extension 101, put that call on hold, dial extension 102, put that call on hold, dial extension 103, put that call on hold, and then switch back and forth among them
Three line appearances, one phone, one line to that phone from the PBX

## Slide 139: FXS Analog Endpoints
The VOIP systems we will be working with require additional interfacing in order to use analog phones
SoftPBX vendors support analog endpoints with FXS signaling using an
  Analog telephone adapter
    ATAs usually have one RJ11 port, for the phone, and one RJ45 port, for the Ethernet switch
    These digitize and encode packets as needed to use the analog phone in a VOIP environment

## Slide 140: FXS Analog Endpoints
  Outboard analog media gateway
    This is a device that serves the same purpose as an ATA, but allows more than one analog phone to be used
    It may also have some built-in call-routing functionality
  Onboard analog media interface
    This is an interface port on the softPBX server itself that allows for direct connection of a single analog phone

## Slide 141: Digital Endpoints
Digital phones are functionally similar to analog phones
Their digital connection is carried on two pairs of copper instead of a single loop

## Slide 142: Managing Multiple Lines
When the end user needs more than one or two phone lines a device is needed to manage these lines
For a small concern a key system is used
For larger organizations a PBX is used

## Slide 143: Key System
This key system or KTS is used to share a group of telephone company POTS lines
  Each phone has several lines coming in to it
  Buttons are used to select a line
  It allows a single operator to place a call on hold while answering a call on another line

## Slide 144: PBX
PBX – Private Branch Exchange
  Used by large businesses
  It is a small version of a telephone company switch
  Phones connect to the PBX
  Internal calls don’t need access to external telephone lines
  Public lines connect to the PBX for external access

## Slide 145: Ring Groups Hunt Groups
PBXs whether PSTN based or VOIP based have features that make management of the premises easier
For example
  Ring groups allow two or more phones to ring simultaneously when a call is incoming
  Once answered on any phone in the ring group, the ringing stops

## Slide 146: Ring Groups Hunt Groups
  Private hunt groups are more advanced ring groups
  Sequential hunt groups seek the next available channel from a list

## Slide 147: Ring Groups Hunt Groups
  RNA - Ring No Answer hunt groups roll the call to the next channel when there's no answer on the first phone, in addition to when that first phone is in a call
  Simultaneous hunt groups may ring all phones simultaneously, like a ring group, but only when a lead phone is busy on a call

## Slide 148: Dial Plan
A dial plan is set of rules that governs the call-routing behavior of a PBX
Generally they describe
  How phones are uniquely identified on the network, usually through extension numbers
  How to connect calls based on the caller's DTMF digits
  How to connect or restrict calls based on their origin

## Slide 149: Dial Plan
  What effects the origin of a call has on its priority
  How to group phones together for common applications, such as group ring or hunt groups
While the principle of dial plan design and capabilities are more or less universal, the platform specific implementations of a dial plan can be vastly different in structure

## Slide 150: Dial Plan
With a traditional PBX, phones are called extensions
Connections to the phone company are called dial tone trunks
Connections to other private PBXs are called private trunks
Typically the terminology is applied the same way in a VOIP network

## Slide 151: Dial Plan
Many of the same considerations have to be made when creating a dial plan
  How many phones will there be in the network
  Does the extension number allow for enough digits for all of them
  Will phone users dial a special digit, such as 8 or 9, at the beginning of PSTN bound calls, or will the phone system just figure out how to route their calls

## Slide 152: Dial Plan
  Will calling between private switches be possible
  Will extension numbers be based on a mitigating or symbolic convention, such as the organizational location of the phone or a desire to match a particular user's DID phone number
  Will each user's voice mail box number match her extension number

## Slide 153: Dial Plan
  Will calls routed from a particular user to the PSTN always travel the same trunk, or will the trunks be selected randomly when calls are placed

## Slide 154: Centrex
All of this Key System and PBX work can be turned over to the service provider by signing up for a extra cost service such as Centrex
This offering was designed to curb the need for small businesses to invest in PBX equipment in order to get modern telephony features

## Slide 155: Erlang Traffic Engineering
Dial tone trunks are the PSTN pathways of a PBX
Outbound or PSTN bound traffic flows to the dial tone trunks
Inward traffic flows across them to the PBX
Traditional dial-tone trunks can be POTS, Centrex, BRI channels, or PRI DS0 channels

## Slide 156: Erlang Traffic Engineering
Having too few trunks means missed calls or busy signals
Having too many trunks means extra expense
In order to achieve a balance the Erlang calculation method is used
An Erlang is a unit of voice traffic

## Slide 157: Erlang Traffic Engineering
It is used to balance the cost of trunks against the system's capacity requirements
Each Erlang is equal to the average number of calls to a system in an hour times the average duration of the calls in seconds, divided by the number of seconds in an hour

## Slide 158: Erlang Traffic Engineering
For example
  For a system with 120 calls per hour at 250 seconds apiece, the formula is applied like this
  (120 cph x 250 seconds ) / 3,600 = 8.3 Erlangs
The Erlang is a unit of voice traffic, not a unit of physical capacity so, you need a conversion table to correlate the results

## Slide 159: Erlang Table
Trunks required | Blocking 1%, Erlangs | Blocking 5%, Erlangs
1 | .01 | .05
2 | .15 | .4
3 | .5 | .9
4 | .9 | 1.5
5 | 1.4 | 2.2
6 | 1.9 | 3.0
7 | 2.5 | 3.7
8 | 3 | 4.5
9 | 3.8 | 5.4
10 | 4.5 | 6.2
11 | 5.2 | 7.1
12 | 5.9 | 8.0
13 | 6.6 | 8.8
14 | 7.4 | 9.7
15 | 8.1 | 10.6
16 | 8.9 | 11.5
17 | 9.7 | 12.5
18 | 10.4 | 13.4
19 | 11.2 | 14.3

## Slide 160: DID
Direct inward dial service allows inbound PSTN calls to the PBX to be routed directly to certain private extensions based on the phone number that the caller dialed
Regular POTS lines have an assigned phone number that cannot be changed

## Slide 161: DID
DID channels on a PRI can have a different phone number every time they are used to connect an incoming call to the PBX

## Slide 162: Extension Numbering Plan
As part of the design process of the internal communication network an extension plan must be developed
It can be based on
  DID – Direct Inward Dialed numbers
    Where the numbers match the DID number given to each phone user
    For example, the DID phone number is 335-1464, then extension would be 1464

## Slide 163: Extension Numbering Plan
  Based on geography
    Where the extension number has a geographical significance
    For example
      Extensions 1100-1199 are the Detroit Sales Office
      Extensions 1200-1299 are the Southfield Sales Office
  Based on department
    For example
      Extensions 1000-1199 for Marketing
      Extensions 1200-1299 for Accounting

## Slide 164: Extension Numbering Plan
There's no right or wrong way to establish a call-routing scheme unless its complexity or economy make it unmanageable
VOIP networks can be eminently more programmable than the old PBX system

## Slide 165: An Example
Let’s look at an example of the PSTN POTS service from the user end to the central office

## Slide 166: PSTN

## Slide 167: The Last Mile
I am here
The service provider’s central office is here
34,000 wire feet away

## Slide 168: Demarc
All of the copper lines from the PSTN to the house come in here

## Slide 169: Copper Wire
The copper wires leave the house and cross the yard

## Slide 170: Copper Wire
The lines go across the yard underground

## Slide 171: Copper Wire
Down the side of the road

## Slide 172: Copper Wire
Across the hay field

## Slide 173: End User Pedestal
To the connection box

## Slide 174: End User Pedestal
The circuit is just a set of copper wires like all the others that serve the house

## Slide 175: Street Pedestal
The circuit goes across the road to another copper connection post for all the lines in this section of the street

## Slide 176: Street Circuit
The copper lines go down the road toward the highway

## Slide 177: Neighborhood Connection
To the neighborhood connection pedestal where all of the nearby street circuits interconnect

## Slide 178: Neighborhood Connection

## Slide 179: Neighborhood Connection
Here is what it looks like underground

## Slide 180: Neighborhood Connection

## Slide 181: Neighborhood Connection

## Slide 182: Neighborhood Connection

## Slide 183: Neighborhood Connection

## Slide 184: Copper Box
All of the copper lines from these neighborhood pedestals are terminated here in this box

## Slide 185: Fiber Box
The copper lines are combined and converted to fiber optic cables in this box

## Slide 186: PSTN
The fiber goes down the highway

## Slide 187: PSTN
In town the fiber leaves the highway and proceeds down the street

## Slide 188: Central Office
To the service provider’s central office

## Slide 189: Circuit Switching
The PSTN is based on circuit switching
Circuit switching is characterized by the reservation of bandwidth for the duration of a call
This reservation involves an initial call establishment or set-up phase using signaling messages, and the release of the bandwidth in a call termination or clearing phase at the end of a call

## Slide 190: Circuit Switching
In modern digital networks, reserved bandwidth means periodically repeating time slots in time division multiplexed type links
Circuit switching works well for voice calls, for which it is designed
All voice is basically at the same rate of 64 Kbps without compression

## Slide 191: Circuit Switching
TDM can easily handle bandwidth reservations of this amount
Also, voice calls require minimal delay between the two parties because excessive delays interfere with interactivity
Circuit switching imposes only propagation delay through the network which is dependent only on the distance

## Slide 192: Circuit Switching
Delay is considered one of the important quality of service metrics
There is also minimal information loss, another QoS metric, because the reserved bandwidth avoids interference from other calls

## Slide 193: Problems With Circuit Switching
A number of drawbacks to circuit switching are typically cited for data
The first drawback is inefficiency when data is bursty
The reserved bandwidth is wasted during the periods of inactivity
The inefficiency increases with the burstiness of traffic

## Slide 194: Problems With Circuit Switching
Another drawback cited for circuit switching is its inflexibility to accommodate data flows of different rates

## Slide 195: Packet Switching
IP is connectionless and works a little differently
Instead of carrying a virtual circuit number, IP packets carry a destination address and source address
An IP router examines the destination address and decides on the egress port after consulting a routing table

## Slide 196: Packet Switching
The routing table lists the preferred egress port calculated from a routing algorithm that usually selects the least cost route for each destination address
The great advantage of connectionless packet switching is the lack of state in the router

## Slide 197: Packet Switching
In connection-oriented packet switching, the switch must keep state or memory of every virtual circuit
A disruption of the switch will necessitate each virtual circuit to be reset, a process that will involve the hosts
In comparison, a disruption of an IP router will cause the dynamic routing protocol to adapt and find new routes

## Slide 198: Packet Switching
This will be done automatically within the network without involving the hosts
IP offers a flexible and relatively simple method to accommodate a wide variety of data applications
Whenever data is ready, it is packetized and transmitted into the network

## Slide 199: Packet Switching
Routers are easy to deploy and dynamically figure out routes through standard routing protocols
Routers are simple by design, and costs have fallen dramatically with the growth of the Internet

## Slide 200: Problems with Packet Switching
The main problem with a packet switched network is providing QoS

## Slide 201: Comparison
Circuit v Packet
Reserved v Statistical
Stateful v Stateless
Homogeneous v Heterogeneous
Specialized v Nonspecialized

## Slide 202: Sources
Some of the description of the PSTN is copied word for word from a chapter on the PSTN in a Cisco Press book on VOIP
Other parts are copied or based on the book Asterisk The Future of Telephony from O’Reilly by Meggelen, Madsen, and Smith