## Slide 1: NETW-250 QoS For VOIP Last Update 2012.09.29 1.0.0

## Slide 2: QoS Past and Present
In traditional telephony quality of service is guaranteed by the constant availability of dedicated bandwidth
Digitally encoded call paths on the PSTN use the same codec, G.711, so transcoding isn't necessary

## Slide 3: QoS Past and Present
If the PSTN and SS7 can't establish a full-bandwidth path through the network, the call just doesn't get connected and the caller hears a trouble tone
Packet networks work the other way where when bandwidth availability drops, as more packets are sent on the network, throughput slows

## Slide 4: QoS Past and Present
Slowness of transmission - latency - is the enemy of VOIP
The solution to the latency problem is QoS protocols and standards, such as 802.1p, 802.1q VLAN, DiffServ, RSVP, and MPLS

## Slide 5: Call Quality Scoring
Historically, the quality of a phone calls‘s audio has been measured using the MOS - Mean Opinion Score from a group of listeners
The sample's quality is judged on a scale of 1 to 5, with 5 being the best quality

## Slide 6: Call Quality Scoring
The quality of a sound sample is altered by the choice of codecs, transcoding combinations, packet interval, and packet loss rate

## Slide 7: Call Quality Scoring
Researchers have determined that, with no packet loss, G.711's highest perceived quality score is 4.4
G.729A's is only 3.6

## Slide 8: MOS
To measure the MOS place a series of test calls across each call path and then record the MOS opinions of each call
Do this before you replace your legacy links with VOIP
You can use the scores as a guide when selecting standards and equipment for the new VOIP system

## Slide 9: Noise
VOIP introduces new kinds of noise
Background noise and signal interference
Transcoding distortions that occur when the lossiness of a particular codec is compounded by the lossiness of a second codec
The resulting signal may sound robotic or machine-like

## Slide 10: Distortion
Distortion can be either additive or subtractive
Additive distortion sources are things like background noise and amplification
Subtractive distortion is caused by signal loss and attenuation
While noise cannot be entirely avoided, it should be minimized

## Slide 11: QoS is Two Things
QoS is made up of
  The network design concept
  A set of standards for bandwidth reservation on the network
The QoS concept deals with the fundamental detractors from quality
  Packet loss
  Latency
The cure is sound network design

## Slide 12: QoS is Two Things
Most network engineers, when faced with bottlenecks, instinctively seek to add more bandwidth
  It's not the most elegant or cost-effective way of dealing with the problem
  It's quality of service that's needed, not quantity of service

## Slide 13: Is QoS Really Needed
Some will argue that the solution to QoS is to design in so much capacity that quality problems are unlikely to occur
  This may work for web surfing and database applications, but it doesn't always work for voice
  Excess capacity increases the cost

## Slide 14: Is QoS Really Needed
QoS protocols approach this matter with an assumption of limited bandwidth resources
Their purpose is to increase the availability of the network for high-priority traffic
Sometimes, this means handling voice packets before handling other kinds of traffic called precedence

## Slide 15: Is QoS Really Needed
Other times, it means allocating a logical channel of dedicated bandwidth across the entire network from caller to receiver

## Slide 16: QoS
Some of the QoS methods work on a coarse, or single-link basis
Others work on a fine, or end-to-end basis

## Slide 17: QoS

## Slide 18: QoS

## Slide 19: Latency Packet Loss Jitter
Three factors are the chief cause of poor perceived call quality
  Latency
  Packet Loss
  Jitter
These are caused primarily by slow network links

## Slide 20: Latency
End-to-end latency is the time it takes from the instant the caller utters something until the time the receiver hears that utterance
Round-trip latency less than 150 ms is not immediately noticeable
Latency higher than 150 ms is discouraged

## Slide 21: Latency
Some state that latency higher than 300 ms is unacceptable
Cisco states that round-trip latency higher than just 150 ms is unacceptable

## Slide 22: Latency
Latency has the following effects on telephony applications
  It can slow down the human conversation
  It can result in caller and receiver unintentionally interrupting each other
  It can cause echo
  It can cause synchronization delays in conference-calling applications

## Slide 23: Latency
The best ways to beat latency are
  Use low-packet-interval codecs
  Maintain fast network links
QoS protocols alone cannot directly improve latency's impact
QoS protocols can not speed up the network

## Slide 24: Latency
Some codec-based solutions to packet loss and jitter add significant latency
Many things contribute to latency
  Framing and packetization
  Software processing
  Jitter buffering
  Routing and firewall traversal
  Transcoding
  Media access and network interfacing

## Slide 25: Latency
The biggest sources of latency are
  Framing or packetization
    Which can add up to 30 ms of latency
  Routing
    Which can add 5-50 ms per hop
  Transcoding

## Slide 26: Latency

## Slide 27: Packet Loss
Packet loss is very damaging to VOIP calls
The chief cause is network congestion
PLC - Packet Loss Concealment is a feature of some codecs that allows perceptions of a quality breakdown to be minimized through vectoring algorithms

## Slide 28: Packet Loss
They work by replacing the sound that would presumably have been produced by a packet that was lost with sound that is predicted based on the sequence of packets received before it and when extensive buffering is used after it
Packet loss rates on a VOIP network should be kept below 1%

## Slide 29: Packet Loss
A drawback of PLC is that it can increase latency

## Slide 30: Jitter
Jitter is a more complex problem than latency and packet loss
  Jitter is the variation in latency time from one packet to the next
  It can cause packets to arrive out of order
Jitter is at its worst when voice traffic must travel through several routers on the network

## Slide 31: Jitter
Different routers may be configured to queue and forward different kinds of traffic in different ways
A router may also be load-balancing, which can contribute to jitter
The primary objective of QoS protocols is to eliminate jitter

## Slide 32: Jitter
Jitter buffers, in endpoints and VOIP servers, can minimize the effect of jitter but, they do so by increasing latency
Jitter should be 30ms or less

## Slide 33: Echo
When you hear the words you've just spoken repeated back to you a split second later on the telephone, you're experiencing echo
If the echo occurs less than 150 ms from the time you actually said the words, then you won't notice it

## Slide 34: Echo
Echo is a by-product of the gateway electronics that bridge soft-based PBX systems to analog or TDM links
It is caused by three conditions, and it's at its worst when they exist together
  Interfacing between TDM and VOIP endpoints or analog and VOIP endpoints
    The more interface points in the network, the worse echo is likely to be

## Slide 35: Echo
  Long round-trip latency between caller and receiver
    The higher the latency, the more annoying echo is likely to be
  Interfacing of a call path between two-wire analog and TDM or four-wire analog devices
    In this case, echo is caused by an inability of the TDM or four-wire circuit to cancel the local side-tone signal on the two-wire device

## Slide 36: Echo
The keys to removing echo are minimizing the use of gateway devices that use hybrids, which, today, are quite hard to avoid, and reducing latency as much as possible

## Slide 37: Class of Service
COS – Class of Service systems work to prioritize traffic on a single data link
For example, an Ethernet switch providing CoS packet prioritization to and from a single host
Whereas QoS refers to the greater network, such as a group of routers participating in a more elaborate, end-to-end QoS solution

## Slide 38: Class of Service
Two key standards support CoS
  802.1p
  DiffServ

## Slide 39: 802.1p
802.1p uses a 3-bit portion of the Ethernet frame header to classify each packet into a particular level of precedence on the local data link
The ToS - Type of Service field is the portion of the frame’s header where precedence information is stored
802.1p and ToS tend to be used together when TCP/IP is the networking protocol

## Slide 40: 802.1p
Each hop along the path of the traffic would have to support the same per-hop precedence behavior in order to make the QoS policy consistent across a routed WAN

## Slide 41: 802.1p

## Slide 42: 802.1p Frame Tagging Method

## Slide 43: DiffServ
DiffServ is a CoS standard that uses ToS tags in a more elaborate manner than 802.1p
DiffServ is used to support routed point-to-point WANs

## Slide 44: DiffServ
The process is
  A packet reaches the edge of the network
  DiffServ tags that packet's ToS header based on the priority established for that packet by policy
  All subsequent router hops must enforce the priority set by the edge router that admitted the packet

## Slide 45: DiffServ
The majority of bottlenecks occur on the edge of the network rather than within the core network where there's usually considerable bandwidth
DiffServ may be the only Quality-of-Service standard necessary
Its policy decision points are always at the edge of the network

## Slide 46: Policy Servers
COPS - Common Open Policy Service is a centralized method of storing and querying centralized policy information on the network
It is used by DiffServ to determine how to handle traffic coming into the network
COPS is a product of the IETF Resource Allocation Protocol working group

## Slide 47: DiffServ Code Points Classes
Six bits in are defined in the IP header for this
They are used by DiffServ to assign different levels of importance
The remaining 3 bits are for future expansion

## Slide 48: DiffServ Code Points Classes
Per-hop behaviors break down into three basic groups
  AF - Assured Forwarding, is a highly expedient DSCP class, sometimes used to tag signaling packets such as H.245/H.225 and SIP packets
  EF - Expedited Forwarding, is the most expedient DSCP class, used to tag packets carrying actual sound data

## Slide 49: DiffServ Code Points Classes
  BE - Best Effort, is a nonexpedient DSCP class, used to tag non-voice packets
  Many DiffServ decision points don't use BE
If you use DiffServ, configure the routers or softPBX to use Expedited Forwarding for all voice traffic

## Slide 50: DiffServ CoS Process
DiffServ begins operation during call setup, when an RTP media session is being established
It proceeds this way
  While the calling party is transmitting its first packets of audio, a classification lookup is conducted against the COPS policy server in order to determine the priority of that RTP session

## Slide 51: DiffServ CoS Process
  The COPS server informs the edge router which of the three DSCP classes each packet should carry
  The edge router tags the packet with the DSCP
  The edge router then remembers the policy rule that applies to all subsequent packets in this particular RTP session

## Slide 52: DiffServ CoS Process
DSCP classes are backwardly compatible with ToS classes
Core routers are spared the task of having to look up the policy repeatedly because the RTP traffic has already been classified

## Slide 53: DiffServ CoS Process
DiffServ has several advantages including
  As an IP-only solution, it is usually managed with the same equipment used to manage the WAN link
  It can run transparently alongside other QoS solutions including 802.1p and RSVP
  It is easy to set up on small to mid-sized routed enterprise networks

## Slide 54: DiffServ CoS Process
  It can be optionally policy-based using COPS or LDAP
  It pushes QoS decisions to the edge of the network, resulting in less complexity
  It is compatible with IPv4 and IPv6
In networks with no centralized policy servers, the DiffServ router admitting the traffic into the edge can have policy rules programmed into its onboard memory

## Slide 55: CoS Over VLAN Trunks
VLAN traffic contains 802.1q tagging, which identifies which VLAN each frame belongs to and which user priority the frame has
This user priority field ranges from 0 to 7, with 7 being the highest priority

## Slide 56: CoS Over VLAN Trunks
Priority traffic is sent across the VLAN trunk first and, when received on the other end, is sent to the receiving switch's backplane first
Lower-priority traffic is queued and ultimately dropped if the switch runs out of buffer space

## Slide 57: CoS Over VLAN Trunks
VLANs accomplishes several things that can improve VOIP service
  It divides and partitions Ethernet broadcast domains
  It provides a best-effort CoS prioritization scheme for traffic on each switch's backplane
  It creates a standard for dividing traffic logically across large routed and switched networks using VLAN trunking

## Slide 58: Intserv and RSVP
Intserv - Integrated Services is an IETF recommendation for providing dedicated bandwidth to individual media channels on an IP network
Media channels are referred to by their socket numbers as they are in DiffServ

## Slide 59: Intserv and RSVP
All routers, whether at the edge or core of the network, play an active role in the policy decision process that results in dedicated bandwidth for each successful request
RSVP - Resource Reservation Protocol is the recommended signaling protocol for Intserv

## Slide 60: Intserv and RSVP
The purpose of RSVP is to ensure that the network has enough bandwidth to support each call, before any data is passed through the media channel
RSVP adds decision-making points to the core network, increasing the processing overhead requirement on core routers

## Slide 61: Intserv and RSVP
The increased overhead tends to discourage RSVP's use in networks with plenty of bandwidth
RSVP is the perfect solution for bandwidth allocation over slower links, because it guarantees availability for each RTP stream

## Slide 62: Intserv and RSVP
Voice systems can tell routers, at the edge and the core, to reserve dedicated bandwidth for the duration of each call
So RSVP is QoS, not CoS
It is an end-to-end solution that sets up a reservation across every hop that the call path crosses

## Slide 63: Intserv and RSVP
RSVP uses the session ID of the RTP stream in order to identify a bandwidth reservation request
RSVP isn't needed in small setups
If you have a two-office VOIP network with 50 endpoints at each office, RSVP is overkill

## Slide 64: Intserv and RSVP
Simplify the QoS approach by using 802.1p and, if you must, DiffServ on your routers and switches

## Slide 65: Controlled Loads
RSVP defines three service levels in RFC 2211
  Best Effort
    A class of service that has no QoS measures whatsoever, wherein RSVP ADSPECs and RMs can be used to collect data about network conditions but not actually enforce any bandwidth allocations
    On Cisco routers, the fair-queuing feature is used to enable Best Effort service

## Slide 66: Controlled Loads
  Controlled Load
    More like CoS, Controlled Load allows prioritization of traffic over multiple routers like DiffServ but includes core routers in the decision-making process
  Guaranteed
    The ultimate application for RSVP, Guaranteed means that no packets will be lost, bandwidth will be constant, and delay will be within the prescribed ranges set up in the traffic contract

## Slide 67: Controlled Loads
The decision of which level of service to enforce with RSVP is up to the administrator
If you aren't going to use Guaranteed, you may do just as well to use DiffServ

## Slide 68: Controlled Loads
RSVP has the following general characteristics
  It is enforced with routers like DiffServ
  It can run transparently alongside other QoS solutions especially 802.1p
  It is intended for networks with limited through bandwidth or networks with voice traffic typically greater than its non-voice traffic
  It can be optionally policy based

## Slide 69: Controlled Loads
  It keeps QoS decisions to the core of the network and therefore has more complex signaling than DiffServ
  It is compatible with IPv4 and IPv6

## Slide 70: MPLS
Multiprotocol Label Switching is the most advanced QoS measure available for enterprise VOIP networks
MPLS's role is in carrier-grade networks or extremely large enterprise networks with tens of thousands of nodes
MPLS can be supported by just about any modern topology

## Slide 71: MPLS
The purpose of MPLS labels is to identify the paths and priorities associated with each packet
  Paths correspond to the media channel of the VOIP call
  Priorities respond to the QoS level of service negotiated for those channels

## Slide 72: MPLS
MPLS can use a dumb network core
  If a packet is carrying a label, all a router has to do is send it along the labeled path, rather than making a redundant assessment of the packet's payload
MPLS has the following general characteristics
  Is usually managed with switches

## Slide 73: MPLS
  It can run transparently within other labeled switching solutions such as ATM
  It is intended for carrier-grade networks
  It mimics ATM in function, but can be used across a variety of non-ATM networks, such as TCP/IP
  It is the most flexible, and the most sophisticated, QoS mechanism for VOIP systems

## Slide 74: MPLS
For small- to mid-size VOIP networks with a few hundred endpoints, you can safely forego MPLS switching
MPLS is aimed at networks that operate with extremely high volumes of real-time traffic
Use MPLS switching in environments with carrier-grade requirements or thousands of endpoints

## Slide 75: Residential QoS
Providing reliable voice quality using VOIP in the home or small office is a challenge
Residential broadband connections aren't always operated by the same people operating the VOIP service
Most broadband Internet connections aren't supported by a backbone that has QoS measures

## Slide 76: Residential QoS
It is common for many ISPs to prioritize in the style of 802.1p
Almost none of them guarantee a service level
Residential broadband routers haven't historically supported any QoS measures internally, though this is changing
Experimenting with QoS measures doesn't require a pricey Cisco router

## Slide 77: Residential QoS
A Linux computer can configured as a gateway router to implement DiffServ

## Slide 78: Dial-Tone Providers and QoS
Some Internet service providers now offer telephone service via VOIP using broadband connections that they own
This service tends to be more expensive than that which comes from a third-party provider that doesn't own the last-mile data link
There's a greater likelihood that this type of service will have end-to-end QoS

## Slide 79: Dial-Tone Providers and QoS
IP-Centrex is a way the telephone company can deliver dial-tone services to a PBX system or a group of IP phones with a VOIP gateway router
Dial-tone services are trunked from the phone company to the subscriber using IP-based packet streams
IP-Centrex offerings tend to be equipped with QoS

## Slide 80: Best Practices for QoS
Best practice for QoS include
  Selecting the right standards
  Using multiple QoS standards that can complement one another, but don't overdo it
  If the network traffic is more than 70% data to voice, use a packet prioritization technique like DiffServ or 802.1p
  If the network is large, such as hundreds of voice nodes and relatively busy, use DiffServ

## Slide 81: Best Practices for QoS
  If the network is especially congested or very large use RSVP
Use the standards correctly
  In DiffServ setups, classify IP voice traffic as EF - Expedited Forwarding
  In 802.1p setups, classify IP voice traffic using IP precedence tag 5

## Slide 82: Best Practices for QoS
Build the network to favor VOIP
  Use 802.1q VLAN, and establish one or more separate VLANs for IP phones and VOIP servers
  To be on the safe side, assume every data link will need an additional 20 to 30 percent overhead bandwidth for call-signaling and routing protocols aside from that normally used by the voice traffic itself

## Slide 83: Best Practices for QoS
  If you are able to manage queuing on your IP routers, use low-latency queuing
  Use network links with faster speeds
  Adding capacity is an acceptable, albeit inelegant and sometimes noneconomical, way of solving QoS issues
  Don't use slow links at all
  Don't use wireless Ethernet for large workgroups of VOIP users

## Slide 84: Best Practices for QoS
  Avoid running VOIP sessions through a VPN unless absolutely necessary, as VPNs have a lot of overhead
  Use digital PRI circuits or IP based trunks rather than analog POTS or Centrex trunks to connect to the phone company as this can lessen the amount of digital/analog conversion and subsequent latency

## Slide 85: Best Practices for QoS
Use voice coding techniques that enhance QoS
  Use the G.711 codec as often as possible
  It is the most resilient waveform codec with a negligible packaging delay
  Some codecs offer packet loss concealment
  Use them to decrease perceived quality problems related to packet loss, but use them sparingly, as they can create latency

## Slide 86: Best Practices for QoS
  To minimize latency, decrease the packet interval
  Intervals can go as short as 10 ms, but 20 is typical
  Decrease the use of jitter buffers by avoiding features like PLC, if possible
  Avoid transcoding if possible
  If absolutely necessary, use IP endpoints and VOIP servers that support wireless codecs such as GSM

## Slide 87: Best Practices for QoS
  If echo is a problem, use codecs that support echo cancellation
Watch network utilization rates
  Keep total packet loss on each Ethernet segment below 1%
  Keep packet loss on T1s and other point-to-point connections at 0%

## Slide 88: Best Practices for QoS
  Keep packet loss and jitter on frame-relay connections, VPNs, and other network clouds as low as possible
  Negotiate an SLA with the service provider to enforce this

## Slide 89: Best Practices for QoS
Establish a service-level agreement
  Before building the VOIP system, determine the MOS rating of all call paths on the current system
  Use these scores as a minimum effort when selecting standards and equipment for your new VOIP system

## Slide 90: Best Practices for QoS
  After the implementation, particularly in large corporate or carrier-class networks, establish an SLA between you and your users that provides an MOS expectation for every call path
  Use this SLA and associated MOS scores as a metric to show your success