## Slide 1: NETW-250 Troubleshooting Last Update 2014.02.19 1.0.1

## Slide 2: VOIP Troubleshooting Tools
Some useful VOIP troubleshooting tools include
  A softphone, because softphones tend to be easier to configure than hardphones, as well as providing more useful logging output
  A network analyzer such as Wireshark

## Slide 3: VOIP Troubleshooting Problems
For troubleshooting from behind a firewall, access to an unfirewalled public IP address will be needed as SIP can be stymied by NAT firewalls

## Slide 4: Things to Watch
To assess a network carrying VOIP traffic the following must be examined
  Latency
  Jitter
  Signaling and interoperability problems

## Slide 5: Things To Watch
Latency
  On the Internet, the round-trip latency of a phone call can be relatively stable from one moment to the next, but vary heavily from one day to the next
  Use troubleshooting tools to find the sources of latency that can make VOIP call quality fluctuate

## Slide 6: Things To Watch
Jitter
  On the Internet, moment-to-moment changes in latency are called jitter
  Jitter is a huge problem
  Troubleshooting tools are used to identify the root causes of jitter

## Slide 7: Things To Watch
Signaling and interoperability problems
  Perhaps the most difficult to isolate, interoperability problems require a working knowledge of the signaling protocols that are used on the VOIP network
  Interoperability problems are avoided by sticking with a single standard, or even a single vendor

## Slide 8: SIP Packet Inspection
In packet telephony applications, capture tools aren't just the last resort they're a primary troubleshooting tool
Using a protocol analyzer, you can capture and dissect call setups, teardowns, and other signals

## Slide 9: SIP Packet Inspection
You can zero in on capabilities to figure out why two particular phones can't call each other while the rest of the network functions fine

## Slide 10: Inspect SIP Traffic
Let’s look an example from the book to see the overall process used
Here is what it says
  First set up a filter to capture SIP registration signals in two scenarios
    One for a successful SIP registration
    Another for a failed SIP registration

## Slide 11: Inspect SIP Traffic
  Next configure the SIP softphone
    Configure the softphone to register using a number and password to match what you've established in the dial-plan configuration on the SIP server
    If registration was successful, you'll see Logged-in as in the UI display

## Slide 12: Inspect SIP Traffic

## Slide 13: Inspect SIP Traffic
  In order to limit the kind of traffic that Wireshark will capture, you'll need to use a filter string
  Wireshark has a rather sophisticated syntax for this string, which instructs Wireshark what to capture and what to ignore

## Slide 14: Inspect SIP Traffic
  In this case, our SIP server is 10.1.1.10, and the standard port for SIP traffic is UDP 5060
  We want to capture traffic in both directions—that is, to the SIP server and to the softphone running on the same host as Wireshark
  The string that achieves this is
    host 10.1.1.10 and udp port 5060

## Slide 15: Observe SIP Registration
  Restart X-Lite
  It will attempt to register automatically with the SIP server upon startup
  Status of 200 Ok in Packet 6 indicates success

## Slide 16: Observe SIP Registration

## Slide 17: Observe Registration Failure
  In this example we alter the registration username of the SIP profile in X-Lite to one that doesn't match a SIP peer on the SIP server
  403 Forbidden indicates a name mismatch
  401 Unauthorized indicates a password failure

## Slide 18: Observe Registration Failure

## Slide 19: Inspect SDP Negotiation
  The SDP - Session Description Protocol is an essential part of SIP call signaling
    Its elements are text tokens sent in SIP packets with the SDP content-type header
    Tokens advertise the capabilities and requirements of each endpoint according to the parameters of the application, be it a telephone call, instant message, or something else

## Slide 20: Inspect SDP Negotiation
  During call setup, specifically during the SIP INVITE, the SDP payload is sent from one endpoint to the other
    A SIP 200 OK response indicates agreement with the SDP parameters, while a 4xx response indicates disagreement or incapability

## Slide 21: Inspect SDP Negotiation
  When you place the call on X-Lite, capture the SIP packets and zero in on the SDP content carried in the INVITE methods and 200 OK responses

## Slide 22: Inspect SDP Negotiation

## Slide 23: Inspect Failed Negotiation
  We will simulate a codec capabilities mismatch, so the SIP client won't be able to pass the SDP negotiation, and call setups will fail
  This packet contains the SDP with a list of supported codecs

## Slide 24: Inspect Failed Negotiation

## Slide 25: Inspect Failed Negotiation
  The 200 OK response sent by the receiver to the sender has an SDP payload that presents no audio codecs at all in its media attributes
  Without any matching SDP media attributes to establish the RTP media channel, the receiver selects attribute reference number 101 using SDP's M token

## Slide 26: Inspect Failed Negotiation
  101 means there’s no valid capabilities match

## Slide 27: Inspect Failed Negotiation

## Slide 28: Log Comparison
  Configure Asterisk to require an MD5 secret for a SIP peer, without informing the SIP client, X-Lite, what the MD5 secret is
  You can require an MD5 secret for any SIP peer by finding the section for the peer in /etc/asterisk/sip.conf and adding md5secret=whatever

## Slide 29: Log Comparison
  Using X-Lite's Diagnostic Log window, you can see the REGISTER method that the SIP client is sending to the Asterisk server notice the Call-ID generated by the SIP User Agent to uniquely identify this particular signal exchange

## Slide 30: Log Comparison
  SEND TIME: 158566682
  SEND >> 10.1.1.10:5060
  REGISTER sip:10.1.1.10 SIP/2.0
  Via: SIP/2.0/UDP 10.1.1.201: 5060;rport;branch=z9hG4bKA98898C43B1E11D99DF4000A958240F6
  From: Ted Wallingford <sip:203@10.1.1.10>;tag=1055640066 To: Ted Wallingford <sip:203@10.1.1.10>
  Contact: "Ted Wallingford" <sip:203@10.1.1.201:5060>
  Call-ID: 383F74D93AA611D99DF4000A958240F6@10.1.1.10 CSeq: 62767 REGISTER
  Expires: 1800
  Max-Forwards: 70
  User-Agent: X-Lite release 1103m
  Content-Length: 0

## Slide 31: Log Comparison
  Here is the failure response
  Notice the 403 Forbidden

## Slide 32: Log Comparison
  RECEIVE TIME: 158747423
  RECEIVE << 10.1.1.10:5060
  SIP/2.0 403 Forbidden
  Via: SIP/2.0/UDP 10.1.1.201:5060;branch=z9hG4bK15429F973B1F11D99DF4000A958240F6
  From: Ted Wallingford <sip:203@10.1.1.10>;tag=1055640066
  To: Ted Wallingford <sip:203@10.1.1.10>;tag=as0e35e19d
  Call-ID: 383F74D93AA611D99DF4000A958240F6@10.1.1.10 CSeq: 62774 REGISTER
  User-Agent: Asterisk PBX
  Allow: INVITE, ACK, CANCEL, OPTIONS, BYE, REFER
  Contact: <sip:203@10.1.1.10>
  Content-Length: 0

## Slide 33: Log Comparison
  Nothing obvious here
  Let’s check out the log files on the Server

## Slide 34: Log Comparison
  Assume that we've got a highly detailed Asterisk message log at /var/log/asterisk/full
  Issue the Unix (Linux) command
    # cd /var/log/asterisk
    # cat full | grep 383F74D93AA611D99DF4000A958240F6@10.1.1.10 | more

## Slide 35: Log Comparison
  And we receive an output of
    Nov 20 12:23:17 DEBUG[1090935488]: Auto destroying call '383F74D93AA611D99DF4000A958240F6@10.1.1.10' Nov 20 12:23:17 VERBOSE[1090935488]: Destroying call '383F74D93AA611D99DF4000A958240F6@10.1.1.10'

## Slide 36: Log Comparison
  Which provides us with the Linux Thread ID of:1090935488
  Now, examine all the output related to thread 1090935488 by issuing the command
    # cat full | grep 1090935488 | grep "Nov 20 12:2" | more
    The result in part is

## Slide 37: Log Comparison
      Nov 20 12:26:01 DEBUG[1090935488]: Setting NAT on RTP to 0 Nov 20 12:26:01 VERBOSE[1090935488]: Found user '203' Nov 20 12:26:01 NOTICE[1090935488]: Failed to authenticate user Ted Wallingford <sip:203@10.1.1.10>;tag=435868921

## Slide 38: Troubleshooting QoS
Sound issues are affected by many disciplines of networking such as switching, routing, QoS, and packetization
The way congestion on a routed link shows up is in dropouts, or in busy signals if you're using a QoS solution
As with signaling, good diagnostic logging is valuable for troubleshooting

## Slide 39: Troubleshooting QoS
Packet analysis is less useful when examining sound quality problems
To identify jitter across IP links, use tools like traceroute and pathping, which succinctly show the variances in round-trip latency on every hop of a route

## Slide 40: Packet Analysis Tools
If firewalls or other filters block ICMP or TCP traffic along the call path you're troubleshooting, then you may need to use a packet capture tool with advanced VOIP capabilities

## Slide 41: Packet Analysis Tools
Both permit analysis of signaling and media packets, readily understand the structure of RTP, can identify jitter, and can reveal sources of congestion on your network

## Slide 42: Use Pesky Users
The human ear is a great instrument for troubleshooting
Carry an IP phone from one server closet to the next, listening to calls to the same destination from different points along the call path

## Slide 43: Use Pesky Users
Ask users to make a call that you expect to traverse the call path you're looking at, and then ask them how it sounds or if they get a busy signal

## Slide 44: Simulating Loads
The bandwidth requirements of a VOIP call can be calculated by adding overhead factors such as RTP and IP headers and Ethernet framing to the size of the actual audio frame
That gives the packet size, which can be multiplied by the packet rate in order to figure out the bandwidth required for the call

## Slide 45: Simulating Loads
A great tool for adding load to a network is IPerf
  This package can create streams of UDP traffic that use up the amount of bandwidth specified

## Slide 46: Common Problem Situations
The people you call complain about echo
  Echo is at its worst when end-to-end latency is high
  If end-to-end latency is below 150 ms, echo should be nearly imperceptible
  Remove echo by removing latency
  Using bigger packet sizes, which are often used with low-bandwidth codecs, can increase latency

## Slide 47: Common Problem Situations
The phone rings, but callers cannot hear you
  This problem can occur when a NAT firewall exists between the caller and the recipient
  NAT cannot keep track of connectionless applications that use more than one socket pair, like a two-way phone conversation

## Slide 48: Common Problem Situations

## Slide 49: Common Problem Situations
The phone rings, but callers cannot hear you
  Solution 1
    To solve this problem, add a SIP proxy server between phone A and firewall B
    Configure the SIP phone so that it places all calls through the SIP proxy
    The SIP proxy knows how to handle the RTP data sent to, and received from, many SIP endpoints simultaneously

## Slide 50: Common Problem Situations
    The SIP proxy would need to reside on a DMZ between A and B, so that it can have a publicly routable IP address
    The SIP proxy could also reside on the same host as the firewall, if public IP addresses aren't abundant

## Slide 51: Common Problem Situations
The phone rings, but callers cannot hear you
  Solution 2
    Another way to approach the NAT problem is to use a STUN - Simple Traversal of UDP NAT server
    This server assists endpoint devices in figuring out what sockets to use in signaling a VOIP call setup, so that UDP NAT traversal can occur without a DMZ
    STUN is described in RFC 3489

## Slide 52: Common Problem Situations
The IP phone can't make any calls
  Is the phone's IP configuration correct
  This problem normally occurs when the phone is unable to register or log on to the SIP registrar or H.323 gatekeeper server
To resolve the failed registration, be certain the phone's user ID and password match those stored in the registrar or softPBX

## Slide 53: Common Problem Situations
If MD5 is being used, make sure that both ends support it and the they both have the correct key

## Slide 54: Common Problem Situations
Past a certain number of simultaneous calls, quality breaks down or calls are disconnected
Levels of utilization that result in a performance loss, or performance limits, are a result of improper planning or provisioning

## Slide 55: Common Problem Situations
This can mean a number of things
  The RAM and processor power of servers along the call path may be too low to handle a high number of simultaneous calls
  There's no hard and fast rule for provisioning these
  But the test lab is the best place to establish the specifications for your servers

## Slide 56: Common Problem Situations
  The bandwidth availability on a data link in the call path, such as an Ethernet segment or frame-relay virtual circuit may not be large enough
  An old-fashioned calculator will suffice for bandwidth projections
  Perhaps the wrong type of codecs are being used, resulting in unnecessary processing load

## Slide 57: Common Problem Situations
  For example, running G.729A over Ethernet isn't really necessary
You lose the dial-tone every few days or so, and you can't receive any calls from the PSTN
  This problem usually occurs if the access router that connects to the Internet service provider is configured for DHCP, and its IP address has changed because the router's DHCP lease expired

## Slide 58: Common Problem Situations
  The best way to eliminate this problem is to get a static IP address from the ISP
Dialed digits work to place calls but not to interact with IVR prompts
  The network can transmit dialed digits in two ways: in-band and out-of-band
  This problem occurs most often when in-band signaling of digits are used
  It is possible that the signals can be distorted during encoding, transport, and decoding

## Slide 59: Common Problem Situations
To avoid this issue, configure the SIP endpoints and ATAs to use an out-of-band DTMF signaling approach such as the SIP INFO method

## Slide 60: Common Problem Situations
Callers sound robotic, or they say you do
  The human voice can be distorted when many subsequent digital/analog conversions or encoding/decoding operations occur
  Unfortunately, most of the control over this issue resides with the service providers
  Most problems involve cell phone systems GSM codecs which use SS7, which is out of the reach of most enterprise VOIP users

## Slide 61: Dropouts in the Audio
Dropouts generally means that the latency or jitter on the call path's route is a problem
If the wide area link is used for voice and data, use routers that support IP precedence to promote VOIP over non-VOIP traffic

## Slide 62: Dropouts in the Audio
If the link is running at capacity, consider increasing its capacity or using a bandwidth-reservation QoS measure across the link
For call paths that have limited bandwidth, calls should be using a narrow band codec not G.711

## Slide 63: Stepping On Each Other
You start to talk while the other person is talking
This is often caused by latency in the path
  Decrease latency on this call path
    Use a small packet interval to reduce latency
    Use packet-loss concealment
    Use you jitter buffering
    Increase the link speed
    Do not use a VPN

## Slide 64: Can't Hear the First Word or So
When the first words cannot be heard often this problem is caused by poor silence suppression techniques
Silence suppression conserves bandwidth by not transmitting sound frames during periods of silence
Any cessation of sampling during silence-suppressed periods indicates poor design

## Slide 65: Can't Hear the First Word or So
Test phones that support silence suppression with, and without, that feature enabled

## Slide 66: No Power
Power provisioning is a common challenge with IP telephony
Use 802.3af to provide power to the IP phones with proper power backup