## Slide 1: NETW-250 The VOIP Concept Last Update 2013.03.07 1.1.0

## Slide 2: VOIP
There is an alternative way of sending calls over the PSTN using its ability to handle both voice and data traffic
This alternate way is to place the voice into a frame for conversion to a packet for transmission over the Internet
Thus it is called VOIP – Voice Over Internet Protocol

## Slide 3: VOIP
This can be used as a replacement for traditional telephony even though it runs over the PSTN
Using this method a PBX can be implemented on a PC

## Slide 4: VOIP Advantages
The CCNA Voice certification prep book by Cioara and Valentine provide this list of advantages to VOIP over the PSTN
  Reduced cost of communicating
    Instead of relying on expensive tie lines or toll charges to communicate between offices, VoiP allows you to forward calls over WAN connections

## Slide 5: VOIP Advantages
  Reduced cost of cabling
    VoiP deployments typically cut cabling costs in half by running a single Ethernet connection instead of both voice and data cables
  Seamless voice networks
    Because data networks connect offices, mobile workers, and telecommuters, VoiP naturally inherits this property
    The voice traffic is crossing "your network" (relatively speaking) rather than exiting to the PSTN

## Slide 6: VOIP Advantages
  Take your phone with you
    Cost estimates for moves, adds, and changes to a traditional PBX system range from $55 to $295 per MAC
    With VoiP phone systems, this cost is virtually eliminated

## Slide 7: VOIP Advantages
  IP SoftPhones
    SoftPhones represent an ideal example of the possibilities when combining voice and data networks
    Users can now plug a headset into their laptop or desktop and allow it to act as their phone
  Unified e-mail, voicemail, fax
    All messaging can be sent to a user's e-mail inbox
    This allows users to get all messages in one place and easily reply, forward, or archive messages

## Slide 8: VOIP Advantages
  Open, compatible standards
    In the same way that you can network Apple, Dell, and IBM PCs together, you can now connect devices from different telephony vendors together. Although this benefit has yet to be fully realized, this will allow businesses to choose the best equipment for their network, regardless of the manufacturer

## Slide 9: VOIP Problem Areas
How you choose to migrate from your conventional telephone system to VOIP is important
The quality and reliability of the VOIP system is tied directly to the underlying data network
Poor perceived call quality is the leading cause of failed VOIP implementation

## Slide 10: VOIP Problem Areas
VOIP is more than just call management and voice conversations
It is also a comprehensive set of methods to deal with quality of service
Lack of attention to these aspects of VOIP will doom even the most well-intentioned implementer

## Slide 11: Messages
In networks that use TCP/IP at the software layers a conversational approach to data exchange is used
Messages are communicated using datagrams or when they are fragmented packets
Voice delivered over these networks as packets is the essence of VOIP

## Slide 12: VOIP or IP Telephony
Two similar terms are often seen in the literature referring to VOIP or IP Telephony
In one view
  IP telephony is an IP-based voice offering
  Whereas VOIP refers to the specific act of transmitting digitized sound data on an IP network

## Slide 13: VOIP or IP Telephony
In another view
  VOIP refers to the overall technology family
  Whereas IP telephony is the act of mimicking traditional telephony applications
In general VOIP and IP telephony can be used interchangeably with VOIP the preferred term

## Slide 14: Network Convergence
A single converged network means there is only one network to manage
A single network also means that a failure can bring down both the data and phone systems

## Slide 15: The Layers of a VOIP Network
Recall that there are two hardware based layers
  The Physical Layer
    The layer that provides for the electrical, mechanical, radiant, or optical signaling pathways
  The Data Link Layer
    The layer that provides a medium for detecting errors
    It works link by link
    The data is carried by a frame

## Slide 16: The Layers of a VOIP Network
And there are several software based layers
  The Network Layer
    It provides a scheme for data routing across wide area links
    It provides an addressing scheme, so that disparate physical connections can be referenced by higher-layer services and by each other
    Provides a definition for connection-oriented and connectionless datagram structures

## Slide 17: The Layers of a VOIP Network
  The Transport Layer
    This layer provides error control across the entire network – from sender to receiver – regardless of the number of physical links between them
    It provides for two kinds of service
      High reliability using TCP that is complex with high overhead
      Less reliability using UDP that is less complex with low overhead
    VOIP generates 30 to 50 datagrams per second, therefore UDP is used
    Call setup and signaling may use TCP

## Slide 18: The Layers of a VOIP Network
The Application Layer
  The Application Layer provides the services needed by the application sending and receiving the VOIP call as signaling and traffic management

## Slide 19: The Layer of a VOIP Network

## Slide 20: VOIP Servers
VOIP servers are software-based devices that direct or participate in VOIP conversations in order to facilitate calling and other VOIP applications, such as
  Call switching and management like a traditional PBX
  Call recording and autoattendant functions like a voice mail system
  Call conferencing

## Slide 21: VOIP Servers
VOIP servers and voice endpoints in the same network make a SoftPBX system

## Slide 22: VOIP Endpoints
Endpoints are valid hosts on the IP network
Phones that connect directly into the network are IP Phones
Voice applications that run on an IP phone allow it to act like a traditional phone
Traditional analog phones can be connected to the network using a ATA - Analog Telephone Adapter

## Slide 23: VOIP Endpoints
Being IP hosts means that IP Phones must have a compatible IP address

## Slide 24: Type of Phone
Using existing traditional phones mean less capital investment
IP phones tend to have greater feature sets and programmability
IP phones can be completely software-based, so they can run as an application on a PC, Mac or Linux box

## Slide 25: Type of Phone
Wireless IP Phones can solve the wiring challenge but can introduce some problems of their own, such as a lack of QoS
100BaseT Ethernet and Cat 5e are the minimum for connecting IP phones

## Slide 26: Network Convergence
When you support only one transport type for all networked applications, including telecommunications, you’ve achieved complete convergence
Convergence increases administrator productivity
Costs drop the more voice and data networks are converged

## Slide 27: Pure IP or IP Enabled
Pure IP voice switches can’t make direct use of traditional circuit-switched telephones and trunks
Switches are totally packet-based
Connections to outside non-IP systems, like PSTN require outboard hardware

## Slide 28: Pure IP or IP Enabled

## Slide 29: Pure IP or IP Enabled
The media interfacing required to use traditional telephony devices with an IP-enabled switch is all contained within the switch chassis
IP-enabled switches are sometimes called hybrid switches

## Slide 30: Pure IP or IP Enabled