## Slide 1: Cisco CCNA Exploration CCNA 2 Routing Protocols and Concepts BGP Last Update 2012.04.03 1.1.0

## Slide 2: Objectives
Learn about using BGP to route between autonomous systems

## Slide 3: BGP
BGP – Border Gateway Protocol is a path vector routing protocol that is used to connect autonomous systems to each other
It is an interdomain routing protocol
It is a standard

## Slide 4: Why BGP is Used
BGP is an exterior or interdomian routing protocol
This means it is used to route between autonomous systems
What is an autonomous system or AS
RFC 4271 defines it this way

## Slide 5: AS
  The classic definition of an Autonomous System is a set of routers under a single technical administration, using an interior gateway protocol (IGP) and common metrics to determine how to route packets within the AS, and using an inter-AS routing protocol to determine how to route packets to other ASes

## Slide 6: AS
  Since this classic definition was developed, it has become common for a single AS to use several IGPs and, sometimes, several sets of metrics within an AS

## Slide 7: AS
  The use of the term Autonomous System stresses the fact that, even when multiple IGPs and metrics are used, the administration of an AS appears to other ASes to have a single coherent interior routing plan, and presents a consistent picture of the destinations that are reachable through it

## Slide 8: Autonomous Systems in Use
In practice some autonomous systems are quite large and some much smaller
Here is a table of the largest ones from a presentation by Mike Smith of Anglia Ruskin University to the Cisco Networking Academy community
The following slides are also from this same presentation from March 2012

## Slide 9: Autonomous Systems in Use
Notes: A list of top 10 ASs by CIDR block
SPRINT which is the largest has access to 272K networks containing over 7 Million /24 equivalent networks
SPRINT has connectivity to over 28000 over ASs

## Slide 10: Autonomous Systems in Use
This table says that Sprint in the US, AS number 1239, can see 28,451 other ASs
It advertises 272,256 network prefixes
That is a lot of networks
As you can see the other backbone providers are not far behind

## Slide 11: BGP Routing Table Growth
This means the number of routes a router running BGP must deal with is growing and growing and growing as seen here

## Slide 12: BGP Routing Table Growth

## Slide 13: BGP Routing Table Growth
Growth in the number of ASs
Growth rate = 3500 new AS per year

## Slide 14: IPXs
How do all of these ASs talk to each other
They interconnect through peering points called IXP – Internet Exchange Points
There are hundreds of these managed by many different organizations
For example, here are the ones offered by Equinox as of March 2012

## Slide 15: IPXs

## Slide 16: IPXs

## Slide 17: IPXs
Inside of these IPXs those that subscribe to them exchange traffic
This is called peering
As Mike Smith further points out there are two types of peering
  Public peering is accomplished using a shared fabric which is usually a Layer 2 switch technology

## Slide 18: IPXs
  Multiple carriers interconnect with one or more other carriers across a single physical port
  Private peering is the direct connection between two networks across a Layer 1 or Layer 2 medium that provides dedicated network capacity and is not shared
  Private peering is commonly used between very large networks

## Slide 19: IPXs
  Peering is a voluntary interconnection of Autonomous Systems for the purpose of exchanging traffic
  The pure definition of peering is settlement free – peers exchange traffic on the basis that I will forward your traffic if you will forward mine

## Slide 20: BGP
Mike Smith explains the use of BGP this way
  The key features of BGP are
    Policy based routing
    Uses TCP for connectivity
    Incremental updates
    Rich metrics
  It is designed to scale to huge internetworks, such as the Internet

## Slide 21: Why Use BGP
BGP is an appropriate routing protocol to use when
  An AS allows packets to transit through to reach other ASs
  An AS has multiple connections to other ASs as in multi-homing
  Routing policy and route selection for traffic entering and leaving the AS must be manipulated

## Slide 22: Why Not to Use BGP
Do not use BGP when
  There is a limited understanding of route filtering and BGP path-selection process among the technical staff
  There is a single connection to the Internet or another AS
  There is a lack of memory or processor power in the routers to handle constant updates on BGP routers

## Slide 23: BGP Message Types

## Slide 24: Update Messages
Update messages contain the following information
  Unfeasible Routes Length (2 bytes)
  Withdrawn Routes (variable)
  Total Path Attributes Length (2 bytes)
  Path Attributes (variable)
  Network Layer Reachability Information (variable)

## Slide 25: Update Messages
The Path Attributes field is of variable length and contains a sequence of attributes about a path
The Path Attributes field will be present in every Update message
The information contained in the Path Attribute field is used to track specific route information and is also used for routing decisions and filtering

## Slide 26: Update Messages
The Path Attribute field consists of
  Attribute type
  Attribute length
  Attribute value

## Slide 27: BGP Attributes

## Slide 28: BGP Attributes
Well known
  The attribute must be recognised by all implementations of BGP
Optional
  The attribute not recognised by an implementation of BGP

## Slide 29: BGP Attributes
Mandatory
  The attribute must be present in an Update message
Discretionary
  The attribute does not need to be present in an UPDATE message

## Slide 30: BGP Attributes
Transitive
  The attribute forwarded to another BGP peer that may not be recognised by this peer
Non-transitive
  The attribute not forwarded to another BGP peer

## Slide 31: BGP Attributes
Type Code | Name | Category | Description
1 | ORIGIN | Well-known mandatory | The AS that originated the routing information
2 | AS_PATH | Well-known mandatory | A list of all ASs the routing information has transited
3 | NEXT_HOP | Well-known mandatory | Specified the IP address of the next-hop router to the specified destination
4 | MULTI_EXIT_DISC | Optional non-transitive | Used to determine the best exit/entry point to the same AS if multiple points exist
5 | LOCAL_PREF | Well-known discretionary | Is used to set a preference of a route to a iBGP peer
6 | ATOMIC_AGGREGATE | Well-known discretionary | Used to choose a less specific (shorter mask) route rather than a more specific (longer mask) when receiving overlapping routes from a BGP speaker
7 | AGGREGATOR | Optional transitive | When a BGP peer perform route aggregation, it will include in the AGGREGATOR attribute its AS number and BGP Id
8 | COMMUNITY | Option transitive | Specifies the communities a route belongs to. A community is a group of destinations that have a common attribute
9 | ORIGINATOR_ID | Optional non-transitive | A BGP speaker that has the role of Route reflector creates this attribute. A route reflector can advertise iBGP learned routes to other iBGP peers. This is not normally allowed
10 | CLUSTER_LIST | Optional non-transitive | Used by a route reflector to specify the BGP peers that a part of its clients.

## Slide 32: Local Preference Attribute
The local pref attribute is used to force the selection of one path over another
For example

## Slide 33: Local Preference Attribute

## Slide 34: Multi Exit Attribute
This attribute is used to select a faster path to the same place such as a T3 over a T1

## Slide 35: Multi Exit Attribute

## Slide 36: BGP Routing Process

## Slide 37: BGP Routing Process

## Slide 38: BGP Routing Process

## Slide 39: BGP Routing Process

## Slide 40: Example BGP Configuration

## Slide 41: Example BGP Configuration
BORDER
router bgp 100
neighbor 200.200.200.2 remote-as 200
network 192.168.1.0
ISP
router bgp 200
neighbor 200.200.200.1 remote-as 100
network 194.82.46.0
Specifies the AS this router belongs to
Specifies the IP address of the remote AS and its AS number
Specifies the network to be advertised
Notes: BGP acts classfully unless you specify a mask.
There is no need to add the network address of the link between the two ASs – this is implicit in the neighbor statement

## Slide 42: Sample BGP Network

## Slide 43: BGP Configuration
enable
config t
int s0/0/0
ip address 192.168.2.1 255.255.255.0
no shutdown
exit

## Slide 44: BGP Configuration
router bgp 100
neighbor 192.168.2.2 remote-as 200
end

## Slide 45: BGP Configuration
enable
config t
int s0/0/0
ip address 192.168.2.2 255.255.255.0
no shutdown
exit

## Slide 46: BGP Configuration
router bgp 200
neighbor 192.168.2.1 remote-as 100
end

## Slide 47: BGP Commands
What do these various commands do
Let’s see what the Cisco BSCI book says about these

## Slide 48: BGP Commands
router bgp autonomous-system
Router(config)#
This command just enters router configuration mode; subcommands must be entered in order to activate BGP.
Only one instance of BGP can be configured on the router at a single time.
The autonomous system number identifies the autonomous system to which the router belongs.
The autonomous system number in this command is compared to the autonomous system numbers listed in neighbor statements to determine if the neighbor is an internal or external neighbor.
Notes: The syntax of basic BGP configuration commands is similar to the syntax for configuring internal routing protocols. However, there are significant differences in how BGP functions.
Use the router bgp autonomous-system command to identify to the router that any subsequent subcommands belong to this routing process. This command also identifies the local autonomous system in which this router belongs. The router needs to be informed of the autonomous system so it can determine if the BGP neighbors to be configured next are either Internal Border Gateway Protocol (IBGP) or External Border Gateway Protocol (EBGP) neighbors. The following table describes the router bgp command parameter:
The router bgp Command Parameter
autonomous-system Identifies the local autonomous system number. The route bgp command alone cannot activate BGP on a router. You must enter at least one subcommand under the router bgp command to activate the BGP process on the router.
If you place your router in autonomous system “A” and then try to configure a new router bgp “B” command, the router informs you that you are currently configured for autonomous system A. You must insert the autonomous system number in the router bgp command so that the router can properly identify the relationship between the neighboring router and itself.

## Slide 49: BGP Commands
neighbor {ip-address | peer-group-name}
remote-as autonomous-system
Router(config-router)#
The neighbor command activates a BGP session with this neighbor.
The IP address that is specified is the destination address of BGP packets going to this neighbor.
This router must have an IP path to reach this neighbor before it can set up a BGP relationship.
The remote-as shows what AS this neighbor is in. This AS number is used to determine if the neighbor is internal or external.
This command is used for both external and internal neighbors.
Notes: You use the neighbor ip-address remote-as autonomous-system command to activate a BGP session for external and internal neighboring routers.
This command identifies a peer router with which the local router will establish a session. The following table describes the neighbor remote-as command parameters:
Parameter Descriptions
ip-address Identifies the peer router.
peer-group-name Identifies the name of a BGP peer group.
autonomous-system Identifies the autonomous system of the peer router. A peer group is a group of BGP neighbors of the router being configured that all have the same update policies. Peer groups are described later in this lesson.
This command is mandatory for the establishment of each neighboring router relationship.
The address that is used in this command is the destination address for all BGP packets going to this neighboring router. In order for BGP to pass BGP routing information, this address must be reachable, because BGP attempts to establish a TCP session and exchange BGP updates with the device at this IP address.
The autonomous system number that is a part of this command is used to identify if this neighbor is an EBGP neighbor or an IBGP neighbor. If the autonomous system number is the same as the autonomous system number for this router, that neighbor is an IBGP neighbor and the IP address listed in this neighbor command does not have to be directly connected. If the autonomous system number is different from the autonomous system number for this router, this neighbor is an EBGP neighbor and the address in this neighbor command must be directly connected by default.