## Slide 1: Introduction to Routing and Packet Forwarding
Last Update 2014.01.30
1.9.0

## Slide 2: Objectives
Learn what routers do and how they do it

## Slide 3: A Computer as a Router
A router is just a special purpose computer
Indeed the first router called an IMP – Interface Message Processor was a minicomputer
This first router was used in the first non-proprietary network of networks called APRANET

## Slide 4: Development of Routers
To see how the need for a device such as a router developed we must look at how ARPANET developed into the Internet
The original concept of the ARPANET was for a relatively few computers to be connected to a single network
This slowly changed as it grew into a collection of multiple, independent networks joined together

## Slide 5: Development of Routers
This produced the question of how to ensure that computers attached to different networks, and running on different platforms, would be able to communicate with each other
The main protocol originally used was NCP - Network Control Protocol
This protocol did not have the ability to handle this function

## Slide 6: Development of Routers
One option was to modify the NCP
The design of NCP as more of a device driver than a true protocol made this difficult
So, it was decided to develop a new protocol stack, TCP/IP
It was also seen that additional functionality outside of just software would be needed

## Slide 7: Development of Routers
Four ground rules for these functions were specified
  Any network should be able to connect to the Internet without making internal changes
  If a packet fails to reach its destination, it will be retransmitted by the source
  No global control should exist at the operational level
  The independent networks will be connected by black boxes

## Slide 8: Development of Routers
These black boxes became routers

## Slide 9
What Does a Router Look Like

## Slide 10: This is a Router

## Slide 11: What Does a Router Look Like
You may be thinking, this is not a router, this is an old telephone switchboard
Well it is, but it illustrates exactly what a router does
So, what does a router do

## Slide 12: What Does a Router Do
A router is a simple device
It does exactly what a telephone switchboard operator does
  Path Determination
  and
  Switching
For example

## Slide 13: Doing Path Determination

## Slide 14: Doing Path Determination
The preceding is a perfect picture of path determination
You can see it in the look on the router’s face – I mean the telephone operator’s face
Someone has called in and said, “Get me New York” or some such place
The router I mean operator is thinking, ok to connect this call I need to take the cable in my right hand and plug it into …

## Slide 15: Doing Switching

## Slide 16: Doing Switching
How does a router do switching, in other words complete the call
By plugging the wire into the correct hole or by sending the packet out the correct interface
Just like the preceding photograph showed

## Slide 17: What Does a Router Do
These photographs showing a switchboard operator at an old style telephone switchboard illustrate the operation of a router perfectly
What is the person doing
A call has come in
The person talking to the operator has asked to speak to someone

## Slide 18: What Does a Router Do
The operator is the intermediary in this transaction
Based on who the person making the call wants to talk to the operator makes a determination as to which plug on the switchboard the connector must go into to make the connection - path determination

## Slide 19: What Does a Router Do
Then the operator completes the circuit by plugging the connector into the switchboard - switching
This is all there is to it
This is all a router does
What complicates the picture, just as what complicates the human operator above, is how the routing table is built and maintained, which we will discuss later

## Slide 20: Routers and Intersections
How about another way of looking at what a router does
A router is like an intersection
Just as an intersection allows you to get from one street to another, a router allows you to get from one network to another
Lets look at an example

## Slide 21: Routers and Intersections
INTERSECTION
DEVRY BUILDING AT 4800 REGENT
REGENT
FREEPORT

## Slide 22: Routers and Intersections
In this example the building we are in is located at 4800 Regent
This means the street is Regent and the building number on that street is 4800
In the city of Irving there can only be one street named Regent
But there could be many buildings with the 4800 number

## Slide 23: Routers and Intersections
ROUTER
192.168.1.0 NETWORK
10.1.1.0 NETWORK
WORKSTATIONON ONE NETWORK AT BUILDING NUMBER 23
SERVER ON ANOTHER NETWORK AT BUILDING NUMBER 3

## Slide 24: Routers and Intersections
The same is true of networks and routers
In this example the workstation is on the street named 192.168.1.0 at house number 23
The server is one the street named 10.1.1.0 at house number 3

## Slide 25: Routers and Intersections
When the workstation wants something from the server the router passes the request from the workstation to the server
And then sends the answer back from the server to the workstation
When you are in the building on Regent and need something from a building on Freeport, you would go through the intersection of Regent and Freeport

## Slide 26: Router Operation by Layer
Recall that the OSI model is made-up of seven layers and the commonly used TCP/IP routed protocol is made-up of four layers
In both cases the bottom layers are the same
These layers are

## Slide 27: Router Operation by Layer

## Slide 28: Router Operation by Layer
A router operates at the bottom layers as it does its two functions of
  Path Determination
  Switching
The first step in router operation occurs at layer 3 in the OSI model called the Internet or Network Layer in the TCP/IP model
This is where the router determines in which network a packet belongs

## Slide 29: Router Operation by Layer
Based on this determination at layer 2 in the OSI model the Data Link layer the packet is changed to a frame in whatever format is required for the type of connection that is used at the Physical layer
At the Physical layer or layer 1 in the OSI model the frame is switched out of the router onto a link for it to exit the router

## Slide 30: Cisco Routers
Let’s now look at the physical aspects of some typical routers
We will start with a Cisco 2501 router
The 2501 is part of the 2500 series
This is an older router that has been used in small to medium size sites
Current routers have the same characteristics

## Slide 31: Cisco 2501 Tour
The 2501 has a single AUI Ethernet port and two serial interfaces
It is powered by a 25Mhz Motorola CPU
On the front of the router is – nothing
How boring
I would think Cisco could at least put a light on the front to blink and keep us amused

## Slide 32: Cisco 2501 Front

## Slide 33: Cisco 2501 Tour
At least the back is a little more interesting

## Slide 34: Cisco 2501 Back

## Slide 35: Cisco 2501 Back
On the back of the router, in the case of the 2501 we have
  Ethernet AUI port
  Serial port number 0
  Serial port number 1
  Console port
  Auxiliary port
  Power switch
  Plug for the power cord

## Slide 36: Cisco 2501 Back
Ethernet Port
Serial Port
Serial Port
Activity Light
Activity Light
Activity Light

## Slide 37: Cisco 2501 Back
Hardware Failure Light
Auxiliary Port
Power Switch
Power Cord Plug
Console Port

## Slide 38: Cisco 2501 Back
On the back we have at least a few lights
Next to the Ethernet and serial ports is an activity light for each one
Next to the Auxiliary Port is a hardware failure light
If this light does not come on when the router is powered up, the router has a bad memory card or chip most likely

## Slide 39: Cisco 2501 Back
The Ethernet port is an AUI style
This was designed for a 10Base5 network
No one has used such a network in twenty years
Why Cisco has used this port for so long is beyond me

## Slide 40: Cisco 2501 Back
To actually use this port a transceiver will have to be attached to it to convert the port to an RJ-45 connector as is used in the real world
This is the device shown next

## Slide 41: Transceiver

## Slide 42: Transceiver
You must be very careful with an AUI connector
The transceiver will just plug straight onto the port, but you must lock it in place
This is done by sliding the locking tab over the knobs on the transceiver
If you do not do this the transceiver, which is heavy, may come loose

## Slide 43: AUI Interface Locking Tab
Locking tab

## Slide 44: Transceiver
Fortunately the newer routers use a standard RJ-45 connector

## Slide 45: Serial Ports
The next two ports over are used for the serial – WAN connections
In the case of a 2501 router these are high-density 60-pin connectors
This is where the V.35 cable attaches as it comes over from the CSU/DSU
These connectors are called fixed interface connectors because they are attached directly to the router motherboard

## Slide 46: Serial Ports
In the newer style routers these are modular interfaces
These plug into a bus on the motherboard
As such they may be changed for others
For example

## Slide 47: T Carrier Modular Interface

## Slide 48: ISDN Modular Interface

## Slide 49: Cisco Modular Interface

## Slide 50: 2600 Module Cover

## Slide 51: 2600 Module Slot Open

## Slide 52: 2600 External Connections

## Slide 53: External Router Connections

## Slide 54: More Serial Ports
When two serial ports are not enough a larger router is called for
In this case a Cisco 7000 is shown
The serial ports are on a slide-in board called a blade
As more ports are needed, another blade is put into the 7000’s chassis

## Slide 55: Cisco 7000

## Slide 56: Cisco 7000 Multiple Ports

## Slide 57: Cisco 7000 Multiple Ports

## Slide 58: Router Interfaces
When buying a router be sure to specify the correct interface based on the type of access line that will be used
In other words, an ISDN line cannot connect to an interface designed for a T Carrier line
Although a Frame Relay line can use the T Carrier interface, since Frame Relay is provided over a T Carrier line usually

## Slide 59: Router Interfaces
This is easier to do with the newer model routers that use the modular interfaces
These newer model routers just have slots as shown above
Any access line interface – that the manufacturer makes – can be plugged in
If the line is changed, there is no need to change the entire router

## Slide 60: Router Interfaces
The point is to be sure everything will connect properly to everything else being used

## Slide 61: Lab
Start Packet Tracer
Do Packet Tracer Activity 1.1.5.3

## Slide 62: Lab
Start Packet Tracer
Do Packet Tracer Activity 1.1.5.4

## Slide 63: Inside the Box
The only thing inside the router is a single circuit board
The only thing that can be done here is to add or change the memory or ROM chips

## Slide 64: Inside the Box

## Slide 65: Router Internal Components

## Slide 66: Router Internal Components

## Slide 67: 2600 Internal Components

## Slide 68: The Cisco IOS
The Cisco IOS in all its forms is the main asset of Cisco
The hardware upon which the various IOSs run are fairly unremarkable
What makes Cisco the market leader in many segments of the market is the quality and scope of the IOS

## Slide 69: Forms of the Cisco IOS
The Cisco IOS is used in
  Switches
  Routers
  Firewalls
  Wireless Access Points
  and so on
Each version is specific to its use

## Slide 70: Forms of the Cisco IOS
One of the problems with this is as Cisco buys companies, which they often do to expand market share, the operating system it comes with is different from those developed by Cisco
An example is the menu driven switch IOS
Over time it has been migrated to the more common Cisco command line style

## Slide 71: IOS Versions
There are many versions of the Cisco IOS
I will let Wendell Odom explain the simplified version of this
It is more complicated than this, but here are the basics

## Slide 72: IOS Versions
  Cisco produces a legion of IOS images, although over time, they've been reducing the number of different images
  For instance, each model series has a different IOS image
  In fact, inside one model series, they may be more than one image for different subsets of the model series

## Slide 73: IOS Versions
  To make bug fixes, Cisco fixes the code, compiles the IOS into an image file, gives it a new release number, and posts it
  For every model series that has a different IOS image, and every subset in that series that has a different IOS, Cisco then has to create a new IOS image for that next minor bug fix release

## Slide 74: IOS Versions
  On top of that, Cisco maintains different major versions of software, as you would expect, so a single bug fix may need to roll out into multiple major versions - all of which means different IOS images are recompiled
  Cisco also produces different trains of IOS, using a suffix on the main version number to identify the train

## Slide 75: IOS Versions
  A train is a series of IOS images that Cisco updates either with an eye towards safety, adding new features (which isn't as safe), or some compromise between the two
  Some trains are build to reduce risk, at the expense of adding less features; some have more features, but at the risk that those features cause other problems
  For example, 12.2, with no suffix, is the core train, called "mainline“

## Slide 76: IOS Versions
  It is the most stable train, with no new features added
  The T-train, named 12.2T, has the same bug fixes as 12.2 mainline, plus some new features when Cisco completes them, so it's potentially less stable, but it may give you a feature you need

## Slide 77: IOS Versions
  Other suffixes identify other trains, sometimes with newer features that are riskier, sometimes with newer features meant for a particular market
Here is a chart on this

## Slide 78: IOS Versions

## Slide 79: IOS Versions
In addition to the version numbers each one has one or more feature sets

## Slide 80: IOS Versions
Jessie Pagan in a presentation from the 2011 Cisco Academy Conference titled Cisco Tools, Online Resources and IOS Fundamentals expands on this
He says

## Slide 81: IOS Versions

## Slide 82: IOS Versions
A Cisco IOS image is a binary executable file of a feature set for a specific platform
Multiple different images exist of any one release
The Cisco IOS software image name represents the hardware, feature set, format, and other information about the image file

## Slide 83: IOS Versions
The figure below shows the image name of a 12.4(6)T Release with the Enterprise Base feature set for the Cisco 3725

## Slide 84: IOS Versions

## Slide 85: IOS Version 15
Although you will use the 12 version of the Cisco IOS for a long time you need to also know that Cisco has moved on to version 15
It has several major differences
Kevin Hamilton and Dwight Hughes discussed version 15 at the 2011 Cisco Academy conference
They say the first change is

## Slide 86: IOS Version 15
  There is only a single universal IOS image that contains all Cisco IOS features
  A single universal IOS image is shipped with the devices
  The IOS functionality is determined by licenses applied to the devices

## Slide 87: IOS Version 15
  There are only two IOS images for each release
    universalk9
      This universal image offers all the Cisco IOS features including strong crypto features such as VPN payload, Secure UC, and so on
    universalk9_npe
      With no payload encryption as is required to meet export restrictions
      It does not support any strong payload encryption, such as VPN payload

## Slide 88: IOS Version 15
For example for the 2901 router
  c2900-universalk9-mz.SPA.151-4.M.bin
  c2900-universalk9_npe-mz.SPA.151.4-M.bin

## Slide 89: IOS Version 15
Within each of these images are multiple feature sets
For example for the 2901 router the feature sets or technology packages are
  IP Base
  Security
  UC
  Data

## Slide 90: IOS Version 15
The IP Base Technology Package is enabled by default
Security, UC and Data Technology Package licenses activate more features

## Slide 91: IOS Version 15

## Slide 92: IOS Version 15
Here is the naming scheme for 15

## Slide 93: IOS Version 15

## Slide 94: IOS Version 15
To allow some stability between releases there will be about 20 months between mainline M releases
So if the new technology added in a T release is not needed, then these Ts can be ignored

## Slide 95: IOS Version 15

## Slide 96: IOS 15 Licensing
Now let’s look at the new licensing method
Here are the main licenses
  Permanent Licenses
  Temporary Licenses
  Features Licenses
    Software Activation Feature Licenses
    Right to Use Feature Licenses

## Slide 97: Permanent License
A Permanent License never expires
Once a permanent license is installed on a router, it is good for that particular feature set for the life of the router even across IOS versions
A permanent license is the most common license type used when a feature set is purchased for a device

## Slide 98: Temporary License
A Temporary License is good for a limited amount of time
For example an ISR G2 includes a full set of 60 day Temporary Licenses for the Data, UC and Security feature sets
These can be activated and deactivated at any time to evaluate a feature set before making the decision to convert to a Permanent License

## Slide 99: Temporary License
Once a Temporary License expires, it cannot be extended

## Slide 100: Feature License
A Feature License typically upgrades to one or more Technology Package licenses
This can be delivered with new router or upgraded at a later time
Licenses are enforced through Cisco Software Licensing framework

## Slide 101: License Management
There are several ways to manage these licenses including commands and web based tools on the Cisco site

## Slide 102: Versions 12 and 15
So the mainstream versions are currently 12 and 15
What happened to 13 and 14
Cisco is superstitious or at least they think their customers are
What are they afraid of
Todd Lammle explains it this way in an article from his website
Part of which is below

## Slide 103: Versions 13 and 14
  Cisco®’s 12.x code has definitely proven to be a very stable operating system
  But since change is a given, Cisco has gone through a lot of revisions, and it’s finally time to morph into the 13.x code
  But no… wait
  13 is bad

## Slide 104: Versions 13 and 14
  Buildings don’t have a 13th floor, and even if they do, elevators don’t go there!13 is a superstitiously cursed, unlucky number here in the U.S.
  Friday the 13th has been cursed since the 16th Century because that’s the day that the King of France attacked and attempted to jail all of the members of the secretive society, the Knights Templar

## Slide 105: Versions 13 and 14
  Cisco appears to feel a bit superstitious too… they skipped the 13.x code and went to… 14.x code
  Nope
  Not 14 either, because 14 happens to be a really nasty number in parts of Asia
  So to keep anyone from getting the willies, Cisco jumped to the new 15.x code

## Slide 106: Versions 13 and 14
  The actual reason for skipping versions 13 and 14 code is of course, nothing but a rumor, but it it’s a fun way to start to this blog

## Slide 107: Cisco Router Boot Process
When the router is first powered on the boot process starts
The first step is the POST – Power On Self Test
This is a test routine that checks the CPU, memory, and interfaces to make sure there are no hardware problems

## Slide 108: Cisco Router Boot Process
After the POST, the router will begin the boot sequence
The boot sequence steps are
  The Bootstrap Program, which is stored in ROM, runs
  The bootfield is read to find out the proper Operating System source
  The Operating System Image is loaded into RAM from Flash, TFTP, or ROM

## Slide 109: Cisco Router Boot Process
  The Startup Configuration File is read from NVRAM or TFTP server and then loaded into the RAM
  The Configuration File is then executed one line at a time and starts the processes to run the router according to that file
  If no Configuration File is found in NVRAM, the Cisco IOS will offer the chance to use the Initial Configuration Dialog

## Slide 110: Cisco Router Boot Process
  If the Initial Configuration Dialog is refused, then the router must be configured by hand from the command line

## Slide 111: Steps in Router Initialization

## Slide 112: Lab
Let’s see this in action
Start Packet Tracer
Bring a router into the workspace
Double click the router
Select the Config tab
Turn off the router, then turn it back on
Click on the CLI tab to watch the bootup
Select another router and do this again

## Slide 113: Initial Router Output
The process of doing the overhead work to make the computer ready to use is called booting, or the boot process, or rebooting the computer
When booting, the router generates messages about the boot process and sends them out the console port

## Slide 114: Initial Router Output
Router output during the boot process
  The version of IOS being loaded
  The number of interfaces
  The types of interfaces
  The amount of NVRAM
  The amount of flash memory

## Slide 115: Initial Router Output

## Slide 116: Router Operation Layers
A router does its work at layers 1, 2, and 3
For the path determination function the work is on layer 3
For the switching function the frames move on layers 1 and 2

## Slide 117: Routers at Layers 1 2 3
Routers make decisions at layer 3
But they also carry out functions at layers 1 and 2
At layer 2 the router must create a frame appropriate for the connection type attached to the interface, such as Ethernet or PPP
At layer 1 the frame is encoded onto the media

## Slide 118: Routers at Layers 1 2 3

## Slide 119: Command Line Interface
The router’s user interface is called the command-line
It is not a GUI as Cisco believes the use of the command line is superior to a GUI
The command line is accessed through a terminal emulator
There are three main methods to reach the command line

## Slide 120: Command Line Access
Console Port
  Uses the rollover or USB cable to make a local connection
SSH or Telnet
  Use a data line to make a remote connection
Auxiliary Port
  Uses a modem to make a remote connection

## Slide 121: Command Line Access

## Slide 122: Console Port
Some hardware and software is required to configure a Cisco router through the console port
You must also have direct physical access to the device
There is an old style and a new style console port

## Slide 123: Serial Console Port
Hardware Failure Light
Auxiliary Port
Power Switch
Power Cord Plug
Console Port

## Slide 124: Serial Console Port
For the serial console port the hardware required includes
  Rollover cable
    There are three types of these
  USB to serial port adaptor
    If the computer does not have a serial port as is very common these days a USB must be used

## Slide 125: Serial Console Port
A Rollover Cable has the wires on one end reversed in order at the other end
The newest version is a single cable with the adaptor built as part of it
The older version of this cable must be used with an adaptor that changes the connection for the serial port from a 9 pin D connector to a RJ-45 jack

## Slide 126: Serial Console Port
The are also adaptors that will turn a standard patch cable into a rollover cable
The cable is then attached to this connector with the other end in the Console Port on the back of the router
Cisco provides the cable with the router

## Slide 127: Rollover Cable

## Slide 128: Serial Port Adaptor

## Slide 129: Rollover Cable and Adaptor

## Slide 130: Rollover Cable

## Slide 131: Rollover Cable Adaptor

## Slide 132: USB Console Port
Starting with the G2 hardware version of the ISR – Integrated Services Routers which includes the 1941, 2901, and 2911 routers the console port is now a USB port
For example

## Slide 133: USB Console Port

## Slide 134: USB Console Port

## Slide 135: USB Console Port
You need the USB console driver from Cisco as well
It only took Cisco about as long as it did to replace the AUI port on the routers to do this
USB has only been the dominate port on PCs for years

## Slide 136: Terminal Program
A terminal program is needed to enter commands through
HyperTerminal as is included in Windows is commonly used, but it is not very suitable
The older version named Terminal that came with Windows 3.1 is much better
There are also many third party programs that do this, such as Putty

## Slide 137: Terminal Program
Set the communications parameters to
  9600 baud
  8 data bits
  No parity
  1 stop bits
  No flow control

## Slide 138: SSH Connection
SSH is used for remote connection to the router over the network
SSH will not work on all routers with basic IOS feature sets
First, install the required image on your router
SSH requires you to have an IPSec DES or 3DES encryption software image from Cisco IOS Release 12.1(1)

## Slide 139: SSH Connection
To configure SSH
  Router(config)# hostname hostname
  Router(config)# ip domain-name domainname
  Router(config)# crypto key generate rsa
To disable telnet
  Router(config)# line vty 0 4
  Router(config)# transport input ssh

## Slide 140: Auxiliary Port Connection
A connection to a router through the auxiliary port using a modem attached to it is less common these days
More used is a separate management network of some sort that allows secure remote access

## Slide 141: Auxiliary Port Connection
But of course if this network as well as the main network are both down, the onsite access through the console port or remote access through the auxiliary port must be used

## Slide 142: Auxiliary Port Connection
To make this type of connection a modem is attached at one end to the auxiliary port and at the other end to a standard PSTN line

## Slide 143: Auxiliary Port Connection
Hardware Failure Light
Auxiliary Port
Power Switch
Power Cord Plug
Console Port

## Slide 144: Modem Attached

## Slide 145: Auxiliary Port Connection
The configuration on the router is
  Router(config)#line 1
  Router(config−line)#modem in
  Router(config−line)#speed 115200
  Router(config−line)#transport input all
  Router(config−line)#flowcontrol hardware
  Router(config−line)#login
  Router(config−line)#password cisco

## Slide 146: Lab
Let’s make a console port connection to a router

## Slide 147: Lab
Let’s make a telnet connection to a router
  Enable telnet by entering
    Router(config)#line vty 0 4
    Router(config-line)#login
    Router(config-line)#password letmein
  Configure the directly connected interfaces
  From a remote router enter
    telnet 192.168.1.2
  or whatever the IP address is of the remote router

## Slide 148: Initial Configuration
There are three ways to do the initial configuration of a new router or one that has had its configuration wiped out
  AutoInstall
  System Configuration Dialog
  Configuration Mode

## Slide 149: Auto Install
The first method of configuring a Cisco router is the Auto Install method
This process will automatically configure the router after it is connected to the WAN
This requires that a host on the network be setup to provide the required configuration files

## Slide 150: Auto Install
The procedure at the router end is
  Attach the WAN cable
  Turn on the router
  The router will load the IOS from Flash memory
  The AutoInstall process will begin
  After the AutoInstall process completes, the administrator must copy the configuration to NVRAM

## Slide 151: Auto Install
With many bootstrap versions if a cable is detected on a WAN port it will attempt the AutoInstall procedure
The system will spend several minutes determining that no AutoInstall is available
To avoid this leave the cables unhooked until the IOS load finishes

## Slide 152: System Configuration Dialog
At bootup when no configuration is found in NVRAM and there is no Auto Install file waiting on some host, the system will ask if it should start the Initial Configuration Dialog, which is also called the System Configuration Dialog
This is a set of information required by the router for it to function at just a basic level

## Slide 153: System Configuration Dialog
In this approach a series of questions are asked by the system
The user need only supply the answers
When the router is first turned on it displays the following

## Slide 154: System Configuration Dialog

## Slide 155: System Configuration Dialog

## Slide 156: System Configuration Dialog

## Slide 157: System Configuration Dialog

## Slide 158: System Configuration Dialog

## Slide 159: System Configuration Dialog

## Slide 160: System Configuration Dialog

## Slide 161: System Configuration Dialog
This is all there is for basic configuration when it is done using the System Configuration Dialog

## Slide 162: System Configuration Dialog

## Slide 163: Command Line Configuration
The last and most basic method of setting up a Cisco router is to configure it from the command line
In this method all configuration is done manually from the keyboard
The keyboard is called the terminal in Cisco talk, just to confuse you

## Slide 164: Command Line Configuration
Enter
  config t
To begin the configuration from the keyboard

## Slide 165: Router Modes
When the router boots and the IOS loads the IOS stops at a prompt
At this prompt the router expects the human to do something
There are two main modes
These are

## Slide 166: Router Modes

## Slide 167: Router Modes

## Slide 168: Router Levels

## Slide 169: Privilege Levels
At the EXEC level the IOS provides 16 privilege levels ranging from 0 to 15
Two of these are predefined
User EXEC mode runs at privilege level 1 and enabled mode privileged EXEC mode runs at level 15
Every IOS command is pre-assigned to either level 1 or level 15
This assignment can be changed

## Slide 170: Moving Between Levels

## Slide 171: Basic Router Configuration
Basic router configuration is very simple
  Plan first
    Decide on the IP addressing scheme to use for the networks that will be connected
    Decide which interfaces will need to be activated to connect those networks
  Next setup the router
    Move from user to privileged level
    Move to global configuration level
    Move to interface configuration level

## Slide 172: Basic Router Configuration
    Activate the interfaces for the directly connected networks
    Move back to global configuration level
    Populate the routing table
    Tell the router to put all of this to use

## Slide 173: Basic Router Configuration

## Slide 174: Basic Router Configuration

## Slide 175: Lab
Start Packet Tracer
Do Packet Tracer Activity 1.2.2.4

## Slide 176: The Do Command
If you are running version 12.2(8) or later of the IOS the do command can be used to run privileged level commands in global configuration mode
For example show run can be issued while entering configuration commands
Just add do in front of the command
For example
  switch(config-if)#do show run

## Slide 177: Planes
Conceptually, a router operates on three distinct domains or planes
The management plane handles administration, configuration, and generally the persistent state of the router
The control plane covers monitoring, route table updates, and generally the dynamic operation of the router

## Slide 178: Planes
The data or forwarding plane handles the packets transiting the router among the networks it serves

## Slide 179: Planes

## Slide 180: Planes
When traffic is being forwarded from one network to another, it usually does not touch the CPU
The packets travel across the routing fabric from the incoming interface to the appropriate destination interface
Only management and control traffic for the router travel to or from the CPU

## Slide 181: IP Datagram
The thing that IP uses to carry stuff is the IP datagram
Like all such devices it has a header and a data area
HEADER | DATA

## Slide 182: IP Datagram Header
VERS
HLEN
SERVICE TYPE
TOTAL LENGTH
IDENTIFICATION
FLAG
FRAGMENT OFFSET
TTL
PROTOCOL
HEADER CHECKSUM
SOURCE IP ADDRESS
DESTINATION IP ADDRESS
IP OPTIONS

## Slide 183: IP Datagram Header
VERS
HLEN
SERVICE TYPE
TOTAL LENGTH
IDENTIFICATION
FLAG
FRAGMENT OFFSET
TTL
PROTOCOL
HEADER CHECKSUM
SOURCE IP ADDRESS
DESTINATION IP ADDRESS
IP OPTIONS

## Slide 184: IP Datagram Header
VERS or Version
  4 bits
  The version of IP
  Always 4 right now
  Shows as binary 0100
  To ensure everyone agrees on the format of the datagram

## Slide 185: IP Datagram Header
VERS
HLEN
SERVICE TYPE
TOTAL LENGTH
IDENTIFICATION
FLAG
FRAGMENT OFFSET
TTL
PROTOCOL
HEADER CHECKSUM
SOURCE IP ADDRESS
DESTINATION IP ADDRESS
IP OPTIONS

## Slide 186: IP Datagram Header
HLEN or Header Length
  4 bits
  Datagram header length in 32 bit words
  Used to indicate whether IP OPTIONS and PADDING fields are being used

## Slide 187: IP Datagram Header
VERS
HLEN
SERVICE TYPE
TOTAL LENGTH
IDENTIFICATION
FLAG
FRAGMENT OFFSET
TTL
PROTOCOL
HEADER CHECKSUM
SOURCE IP ADDRESS
DESTINATION IP ADDRESS
IP OPTIONS

## Slide 188: IP Datagram Header
SERVICE TYPE
  8 bits
  Specifies how the datagram should be handled
  QoS mechanism

## Slide 189: IP Datagram Header
VERS
HLEN
SERVICE TYPE
TOTAL LENGTH
IDENTIFICATION
FLAG
FRAGMENT OFFSET
TTL
PROTOCOL
HEADER CHECKSUM
SOURCE IP ADDRESS
DESTINATION IP ADDRESS
IP OPTIONS

## Slide 190: IP Datagram Header
TOTAL LENGTH
  16 bits
  The length of the datagram in octets including the header and data

## Slide 191: IP Datagram Header
VERS
HLEN
SERVICE TYPE
TOTAL LENGTH
IDENTIFICATION
FLAG
FRAGMENT OFFSET
TTL
PROTOCOL
HEADER CHECKSUM
SOURCE IP ADDRESS
DESTINATION IP ADDRESS
IP OPTIONS

## Slide 192: IP Datagram Header
IDENTIFICATION or Fragment Identifier
  16 bits
  Holds a unique integer that identifies which datagram a fragment belongs to if the packet has been fragmented, which most are

## Slide 193: IP Datagram Size
Minimum datagram size is 576 bytes
  With at least 552 bytes of data
Maximum size for an IP datagram is 65,535 bytes
  With at most 65,515 bytes of data
But Ethernet only handles 1500 bytes of data
So how is a 65,535 byte datagram to go into a 1500 byte data area
By fragmentation

## Slide 194: IP Datagram Size
It is then reassembled as seen above using the Fragment Offset part of the datagram header

## Slide 195: IP Datagram Header
VERS
HLEN
SERVICE TYPE
TOTAL LENGTH
IDENTIFICATION
FLAG
FRAGMENT OFFSET
TTL
PROTOCOL
HEADER CHECKSUM
SOURCE IP ADDRESS
DESTINATION IP ADDRESS
IP OPTIONS

## Slide 196: IP Datagram Header
FLAG or Fragmentation Flag
  3 bits, but part of the FRAGMENT OFFSET field
  Indicating that the datagram has been fragmented
  Bit 1 is not currently used
  Bit 2 is turned on to tell routers to not fragment a packet
    If the router must, but cannot, the packet is dropped and a message is sent to the receiver

## Slide 197: IP Datagram Header
  Bit 3 when on indicates more fragments are coming
    When set to 0 it indicates this is the last fragment
  All of this information is used to reassemble everything

## Slide 198: IP Datagram Header
VERS
HLEN
SERVICE TYPE
TOTAL LENGTH
IDENTIFICATION
FLAG
FRAGMENT OFFSET
TTL
PROTOCOL
HEADER CHECKSUM
SOURCE IP ADDRESS
DESTINATION IP ADDRESS
IP OPTIONS

## Slide 199: IP Datagram Header
FRAGMENT OFFSET
  13 bits
  This tells the receiver what piece of a datagram this packet is of a datagram that has been cut up due to the MTU of the underlying method being used to carry the datagram from point-to-point

## Slide 200: IP Datagram Header
  To distinguish fragments, each has its offset field set to the distance, measured in 8 byte units, between the beginning of the original datagram and the beginning of that particular fragment
  So the first fragment has an offset of 0, the second fragment has an offset value of the payload size of the first fragment, and so on

## Slide 201: IP Datagram Header
VERS
HLEN
SERVICE TYPE
TOTAL LENGTH
IDENTIFICATION
FLAG
FRAGMENT OFFSET
TTL
PROTOCOL
HEADER CHECKSUM
SOURCE IP ADDRESS
DESTINATION IP ADDRESS
IP OPTIONS

## Slide 202: IP Datagram Header
TTL or Time to Live
  8 bits
  Supposed to be in seconds, but things run so fast today it is normally hops
  Each router decrements the value by 1

## Slide 203: IP Datagram Header
VERS
HLEN
SERVICE TYPE
TOTAL LENGTH
IDENTIFICATION
FLAG
FRAGMENT OFFSET
TTL
PROTOCOL
HEADER CHECKSUM
SOURCE IP ADDRESS
DESTINATION IP ADDRESS
IP OPTIONS

## Slide 204: IP Datagram Header
PROTOCOL
  8 bits
  Indicates the higher level protocol used to create the datagram

## Slide 205: IP Datagram Header
VERS
HLEN
SERVICE TYPE
TOTAL LENGTH
IDENTIFICATION
FLAG
FRAGMENT OFFSET
TTL
PROTOCOL
HEADER CHECKSUM
SOURCE IP ADDRESS
DESTINATION IP ADDRESS
IP OPTIONS

## Slide 206: IP Datagram Header
HEADER CHECKSUM
  16 bits
  Checks the integrity of the header itself
  Not the data, the header

## Slide 207: IP Datagram Header
VERS
HLEN
SERVICE TYPE
TOTAL LENGTH
IDENTIFICATION
FLAG
FRAGMENT OFFSET
TTL
PROTOCOL
HEADER CHECKSUM
SOURCE IP ADDRESS
DESTINATION IP ADDRESS
IP OPTIONS

## Slide 208: IP Datagram Header
SOURCE IP ADDRESS
  32 bits
  Where it came from

## Slide 209: IP Datagram Header
VERS
HLEN
SERVICE TYPE
TOTAL LENGTH
IDENTIFICATION
FLAG
FRAGMENT OFFSET
TTL
PROTOCOL
HEADER CHECKSUM
SOURCE IP ADDRESS
DESTINATION IP ADDRESS
IP OPTIONS

## Slide 210: IP Datagram Header
DESTINATION IP ADDRESS
  32 bits
  Where its going

## Slide 211: IP Datagram Header
VERS
HLEN
SERVICE TYPE
TOTAL LENGTH
IDENTIFICATION
FLAG
FRAGMENT OFFSET
TTL
PROTOCOL
HEADER CHECKSUM
SOURCE IP ADDRESS
DESTINATION IP ADDRESS
IP OPTIONS

## Slide 212: IP Datagram Header
IP OPTIONS
  24 bits
  Not used except in testing

## Slide 213: IP Datagram Header
PADDING
  8 bits
  To bring the datagram up to a minimum size

## Slide 214: IP Datagram Header
DATA
  Size varies
  The important stuff

## Slide 215: Ethernet II Frame Format
Field | Bytes
Preamble | 8
Destination Address | 6
Source Address | 6
Type | 2
Data | 46-1500
Frame Check Sequence | 4

## Slide 216: Ethernet II Frame Format
Preamble
  This is a sequence of 7 bytes or 56 bits of alternating ones and zeros
  It is used for synchronization
  It gives components time to detect the signal, and be ready before the frame arrives
  It was set at this length because it originally took the equipment this long to sync up
  A preamble is not required for speeds above 10 Mbps

## Slide 217: Ethernet II Frame Format
SFD - Start Frame Delimiter
  Also part of the preamble is a sequence of 1 byte or 8 bits having the bit configuration 10101011 that indicates the start of the frame
Note the similarity of the bit pattern between the Preamble and the SFD
The only difference is that the last two bits of the SFD are both 1’s
Many people do not separate the Preamble and Start Frame Delimiter

## Slide 218: Ethernet II Frame Format
They consider it to all be the preamble
Because it takes a station an unknowable amount of time to lock on, it does not know how many bits of the Preamble have gone by
For this reason, it is said that the Preamble is lost in the synching up process

## Slide 219: Ethernet II Frame Format
As such no part of the Preamble ever enters the NIC’s buffer
This is why the size of the Preamble/SFD is excluded when the minimum and maximum Ethernet frame sizes are discussed

## Slide 220: Ethernet II Frame Format
Destination Address
  This is the MAC address of the station the message is for
  This address may specify either an individual address destined for a single station, a multicast address destined for a group of stations, or an address of all 1s bits that refers to all stations on the LAN and is called a broadcast address

## Slide 221: Ethernet II Frame Format
Source Address
  This is the MAC address of the sending station
Type
  Type indicates the protocol type that the frame is for at the network layer, such as
    0800 for TCP/IP
    8137 for IPX
  These are hexadecimal numbers

## Slide 222: Ethernet II Frame Format
Data
  This is the important stuff and has a maximum size of 1500 bytes
  If the size is less than 46 bytes, then bytes are placed in the Pad field to bring the frame length up to at least 64 bytes
  What goes into this data area is the original message and the headers placed in front of that message at each of those layers

## Slide 223: Ethernet II Frame Format
CRC - Frame Check Sequence
  This is used for error checking
  When the source station assembles a MAC frame, it performs a CRC calculation on all the bits in the frame from the Destination MAC Address through the Pad fields
  The source station stores the value in this field and transmits it as part of the frame
  When the frame is received by the destination station, it performs an identical check

## Slide 224: Ethernet II Frame Format
  If the calculated value does not match the value in this field, the destination station assumes an error has occurred during transmission and discards the frame

## Slide 225: Lab
Start Wireshark
Capture a few frames
Examine the IP header
Examine the Ethernet header