## Slide 1: Link State Routing Protocols
Last Update 2010.09.08
1.1.0

## Slide 2: Objectives
Learn about the characteristics of link state routing protocols

## Slide 3: Link State Routing Protocols
A link state routing protocol is one that uses the Dijkstra shortest path first algorithm
The shortest path is not the one with the fewest hops in all cases

## Slide 4: Link State Protocol Operation
In general link state routing protocols operate in this manner
  Each routers records its own directly connected networks
  Each router exchanges a hello packet with its directly connected neighbors
  Each router creates a Link State Packet that contains what it knows about its neighbors such as identification, link type, and bandwidth

## Slide 5: Link State Protocol Operation
  This Link State Packet is sent to all its neighbors who then store the information, after that they forward it until all routers have the same information
  Once all the routers have the same information each one constructs a topological map of the network from which the best routes to a destination are computed

## Slide 6: Link State Routing Protocols
There are only two link state routing protocols
  OSPF
  IS-IS

## Slide 7: Link State Routing Protocols
Routing protocol | Builds Topological map | Router can independently determine the shortest path to every network. | Convergence | A periodic/ event driven routing updates | Use of LSP
Distance vector | No | No | Slow | Generally No | No
Link State | Yes | Yes | Fast | Generally Yes | Yes