## Slide 1: OSPF
Last Update 2011.06.06
1.4.0

## Slide 2: Objectives
Learn about OSPF

## Slide 3: History of OSPF
OSPF was developed to replace RIP
Unfortunately being a committee project it took quite a while to be developed
Begun in 1987 OSPFv1 was not released until 1989 as RFC 1131
However, this version was experimental and never used

## Slide 4: History of OSPF
Only in 1991 was the first useable version - OSPFv2 - released as RFC 1247
RFC 2328 from 1998 updated 1247
In 1999 OSPFv3 was published as RFC 2740 to support IP Version 6

## Slide 5: Metric
OSPF uses cost as the metric for determining the best route
The best route will have the lowest cost
Cost is an arbitrary value according to the RFCs
Cisco uses the bandwidth of the interface
This form of the cost is calculated using the formula 108 / bandwidth

## Slide 6: Metric
It defaults to 100Mbps
This can be modified using the auto-cost reference-bandwidth command

## Slide 7: Shortest Path Algorithm
The algorithm that OSPF uses to create the routing table is the SPF algorithm
Using this algorithm the preferred path is the shortest path
The shortest path being the fastest connection
This may or may not be the one with the fewest hops

## Slide 8: Steps in OSPF Operation
There are five steps in basic OSPF operation
  Establish router adjacencies
  Elect a DR and BDR, if needed
  Discover routes
  Select the routes to use
  Maintain the routing table

## Slide 9: Multiaccess Networks
In a multiaccess network such as Ethernet or Frame Relay a designated router is needed
This election does not take place in a point to point network
The DR and BDR are selected based on the highest OSPF interface priority

## Slide 10: Multiaccess Networks
The election occurs as soon as the first router has its interface enabled on a multiaccess network
When a DR is elected it remains as the DR until one of the following occurs
    The DR fails
    The OSPF process on the DR fails
    The multiaccess interface on the DR fails

## Slide 11: Multiaccess Networks
The winner can be manipulated
  To do this
    Boot up the DR first, followed by the BDR, and then boot all other routers
    Shut down the interface on all routers, followed by a no shutdown on the DR, then the BDR, and then all other routers
    Use the ip ospf priority interface command
      Router(config-if)#ip ospf priority {0 - 255}
        Priority number range 0 to 255
        0 means the router cannot become the DR or BDR
        1 is the default priority value

## Slide 12: OSPF Relationships
There are seven states in the relationship between two OSPF conversant routers
  Down
  Init
  Two Way
  ExStart
  Exchange
  Loading
  Full Adjacency

## Slide 13: Down
This is the initial interface state
In this state, the lower-level protocols have indicated that the interface is unusable
No protocol traffic at all will be sent or received on such a interface
In this state, interface parameters should be set to their initial values

## Slide 14: Down
All interface timers should be disabled, and there should be no adjacencies associated with the interface

## Slide 15: Init
In this state, an Hello packet has recently been seen from the neighbor
However, bidirectional communication has not yet been established with the neighbor
The router itself did not appear in the neighbor's Hello packet
All neighbors in this state or higher are listed in the Hello packets sent from the associated interface

## Slide 16: Two Way
In this state, communication between the two routers is bidirectional
This has been assured by the operation of the Hello Protocol
This is the most advanced state short of beginning adjacency establishment
The Designated Router is selected from the set of neighbors in state 2-Way or greater

## Slide 17: ExStart
This is the first step in creating an adjacency between the two neighboring routers
The goal of this step is to decide which router is the master, and to decide upon the initial DD sequence number
Neighbor conversations in this state or greater are called adjacencies

## Slide 18: Exchange
In this state the router is describing its entire link state database by sending Database Description packets to the neighbor
Each Database Description Packet has a DD sequence number, and is explicitly acknowledged
Only one Database Description Packet is allowed outstanding at any one time

## Slide 19: Exchange
In this state, Link State Request Packets may also be sent asking for the neighbor's more recent LSAs
All adjacencies in Exchange state or greater are used by the flooding procedure
In fact, these adjacencies are fully capable of transmitting and receiving all types of OSPF routing protocol packets

## Slide 20: Loading
In this state, Link State Request packets are sent to the neighbor asking for the more recent LSAs that have been discovered, but not yet received in the Exchange state

## Slide 21: Full Adjacency
In this state, the neighboring routers are fully adjacent
These adjacencies will now appear in router-LSAs and network-LSAs

## Slide 22: OSPF Packet Types
To exchange information OSPF uses five packets types
  Type 1 - Hello
  Type 2 – Database Description Packet - DBD
  Type 3 – Link State Request
  Type 4 – Link State Update - LSU
  Type 5 – Link State Acknowledgement - LSACK

## Slide 23: Hello
Establishes and maintains adjacency information with neighbors

## Slide 24: Database Description Packet
Describes the contents of an OSPF router’s link state database

## Slide 25: Link State Request
Requests specific pieces of a router’s link state database

## Slide 26: Link State Update
Transports link state advertisements

## Slide 27: Link State Acknowledgment
Acknowledges receipt of a neighbor’s LSA

## Slide 28: OSPF Network Types
OSPF can operate in three type of networks
  Broadcast Multiaccess
  NBMA – Nonbroadcast multiaccess
  Point to Point

## Slide 29: Broadcast Multiaccess
Ethernet or Token Ring segment would be a multiaccess link

## Slide 30: NBMA
A Frame Relay or X.25 cloud would be classified as non-broadcast multiaccess

## Slide 31: Point to Point
A serial link connecting two routers together would be a point-to-point link

## Slide 32: OSPF Hello Protocol
What a router is running the OSPF routing process on an interface it sends Hello packets at regular intervals addressed to the multicast address 224.0.0.5
These are sent every 10 seconds for Broadcast Multiaccess and Point to Point networks
Every 30 seconds for NBMA – Nonbroadcast multiaccess networks

## Slide 33: OSPF Capture File
Let’s look at some of the OSPF activities just described in some frames from an OSPF network
Download this file
  HDLC with OSPF.cap
Double-click on it to open it in Wireshark
Go to frame 2
Expand all of the OSPF layer

## Slide 34: OSPF Capture File

## Slide 35: OSPF Capture File

## Slide 36: OSPF Capture File
This is a Hello packet from 192.168.2.1
As layer 3 shows it is being sent to the OSPF multicast address of 224.0.05
OSPF version 2 is being used
Hellos are sent every 10 seconds
There is no Designated Router

## Slide 37: OSPF Capture File
In frame 9 we see the other side of the link wake-up as it sends a Hello packet as well

## Slide 38: OSPF Capture File

## Slide 39: OSPF Capture File
In frames 11 to 23 the OSPF routes start exchanging information
Frame 11 is a Database Description packet from 192.168.2.2
In frame 13 the other side provides their information
Both sides have the same view of the network so they will use the information

## Slide 40: OSPF Capture File

## Slide 41: OSPF Capture File

## Slide 42: OSPF Capture File

## Slide 43: OSPF Capture File
In this Database Description packet this router says it is in area 0
The mtu is 1500 bytes

## Slide 44: OSPF Capture File

## Slide 45: OSPF Capture File

## Slide 46: OSPF Capture File
Frame 18 is a Link State Request from 192.168.2.2
Followed by a LSR from the other side in Frame 19

## Slide 47: OSPF Capture File

## Slide 48: OSPF Capture File

## Slide 49: OSPF Capture File
In frame 21 the 192.168.2.2 router sends a Link State Update saying hey wait a minute I just discovered another network hooked to me
In this case the 192.168.3.0 network
This is reported to be a stub network

## Slide 50: OSPF Capture File

## Slide 51: OSPF Capture File
In frame 23 we see all of the networks being reported by 192.168.2.1

## Slide 52: OSPF Capture File

## Slide 53: OSPF Capture File
In frame 26 and 27 we see a Link State Acknowledgement from each side

## Slide 54: OSPF Capture File

## Slide 55: OSPF Capture File

## Slide 56: OSPF Loopback
When the OSPF process starts on a router the IOS uses the local IP address as its OSPF router ID
If a loopback address is configured, it is used regardless of its value
A loopback address ensures stability as the loopback interface is not affected by links going up and down

## Slide 57: OSPF Loopback
Set the loopback address before enabling OSPF on an interface
To avoid routing problems use a 32 bit subnet mask for the loopback address

## Slide 58: Loopback Addressing
It is considered best practice, in configuring Cisco routers, to define one loopback interface, and designate it as the source interface for most traffic generated by the router itself

## Slide 59: Loopback Addressing
Adopting this practice yields several benefits for the overall stability and security management of a network, because the address of the loopback interface is fixed

## Slide 60: Loopback Addressing
When a router is configured to use the loopback interface for services, it is possible to configure the security of other devices in the network more tightly
When a service is configured to use the loopback interface as its source, we say that the service is bound to that interface

## Slide 61: Loopback Addressing
It means that IP packets generated by the router will have the loopback interface’s address as their source address
Also, the loopback interface’s address does not appear in any route-based network maps; hiding administrative aspects of your network from potential attackers is usually good practice

## Slide 62: Loopback Addressing
To create a loopback interface, simply assign it an IP address
For a border router, the loopback’s address usually should be in the range of the internal or DMZ network, not the external network

## Slide 63: Loopback Addressing
Note that the loopback address cannot be the same as the address of any other interface, nor can it be part of the same network as any other interface

## Slide 64: Loopback Addressing
For example
  Central# config t
  Central(config)# interface loopback0
  Central(config-if)# description Main Loopback Interface
  Central(config-if)# ip address 14.2.11.250 255.255.255.255

## Slide 65: Loopback Addressing
In general, router network services that can be bound to the loopback interface should be

## Slide 66: OSPF Authentication
Routers trust the routing information they receive from other routers
To ensure this is from a router that should be trusted, authentication can be set

## Slide 67: OSPF Authentication

## Slide 68: Configuring OSPF Timers
To speed link state failure notifications the OSPF timers can be adjusted

## Slide 69: Configuring OSPF Timers

## Slide 70: Configuration is Simple
In the vast majority of networks there is nothing needed other than enabling OSPF or any other routing protocol
It just works
This is true up to 30 routers or so talking to each other
Above that some tuning will be required

## Slide 71: Configuring OSPF
router ospf 1
  The process id from 1 to 65535 is a locally significant number that does not have to be the same on all routers
  It just links to a OSPF database held by the router
network 192.168.1.0 0.0.0.255 area 0
network 192.168.2.0 0.0.0 255 area 0

## Slide 72: Router ID
The router id is an IP address used to identify a router
Three criteria are applied to derive this
  The IP address configured with the OSPF router-id command
    This takes precedence over loopback and physical interface addresses

## Slide 73: Router ID
  If the router-id command is not used, then the router chooses highest IP address of any loopback interface
  If no loopback interfaces are configured then the highest IP address on any active interface is used

## Slide 74: Verifying OSPF Configuration
show ip protocol
show ip route
show ip ospf interface
shop ip ospf
show ip ospf neighbor detail
show ip ospf database

## Slide 75: Lab
Start Packet Tracer
Do activity 11.2.6.2.pka

## Slide 76: Lab
Lab 11-1