## Slide 1: Distance Vector Routing Protocols
Last Update 2008.05.02
1.0.0

## Slide 2: Objectives
Learn about the details of distance vector routing protocols

## Slide 3: Distance Vector Protocols
In the previous module the concept of distance vector routing protocols was introduced
In this module the details on this type of routing protocol will be discussed
A distance vector routing protocols only knows about two things
  Distance to final destination
  Vector or direction to that destination

## Slide 4: Distance Vector Protocols
These protocols have the following characteristics
  Whether changes have taken place or not periodic updates are sent out
  Direct knowledge is of their neighbors only
  The entire routing table is included with each routing update

## Slide 5: Distance Vector Protocols

## Slide 6: Routing Loops
Routing loops can occur when inconsistent routing tables are not updated due to slow convergence in a changing network

## Slide 7: Routing Loop Problem Example
For example let's say the following network had converged
That is all routers have the same, consistent knowledge and all routing tables in all routers are correct
This diagram assumes that Router C's preferred path to Network 1 is by way of Router B, and Router C has a distance of three hops to Network 1 in its routing table

## Slide 8: Routing Loop Problem Example

## Slide 9: Routing Loop Problem Example
The link to Network 1 fails
Router E sends an update to Router A telling Router A that it can no longer get to Network 1
Router A stops sending stuff to Network 1, But Routers B, C, and D keep on sending packets to Network 1 because they have not been informed of the change
Router A then sends out its update

## Slide 10: Routing Loop Problem Example
This tells Routers B and D to stop and they do
Router C still has not been informed
Router C stills thinks Network 1 is reachable through Router B
Router C now sends its regular update to Router D

## Slide 11: Routing Loop Problem Example
This update tells Router D that Network 1 is reachable through Router B
Router D says great
It updates its table and sends the good news on to Router A
Router A then tells Router E the news
Of course none of this is correct

## Slide 12: Routing Loop Problem Example
So packets for Network 1 just loop around the network from C to B to A to D and back to C

## Slide 13: Counting to Infinity Problem
This brings in the second problem, which is the count to infinity
The bad data will continue around the network unless there is a metric in it that says enough is enough
The common metric for this is the distance metric

## Slide 14: Counting to Infinity Problem
For example after 15 trips through a router a RIP packet will be discarded based on the assumption that the network is unreachable
This takes care of the problem, but it took a bunch of bandwidth wasting traffic to figure this out

## Slide 15: Split Horizon
Split horizon is a method of preventing a routing loop in a network
With split horizon information about routing for a packet is never sent back in the direction from which it was received

## Slide 16: Route Poisoning
The route poisoning rule says once a route is learned through an interface, advertise it as unreachable back through the same interface
Route poisoning is implemented by setting the hop count to one more than the maximum

## Slide 17: Triggered Updates
With triggered updates a change in the routing table is sent immediately rather than waiting for the scheduled update

## Slide 18: Holddown Timers
Count to infinity can be avoided by using holddown timers
When a router receives an update from a neighbor indicating that a previously unreachable network is now accessible
The router marks the route as inaccessible
Then it starts a holddown timer

## Slide 19: Holddown Timers
If an update is received from the same neighbor before the holddown timer expires indicating the network is accessible, the timer is released and the network is marked as reachable

## Slide 20: Holddown Timers
If an update arrives from a different neighboring router with a better metric than the one originally recorded for the network, the router marks the network as accessible and removes the timer

## Slide 21: Holddown Timers
If an update is received from a different neighbor router with a poorer metric, the update is ignored

## Slide 22: Techniques In Combination
When route poisoning is used with triggered updates, it speeds up the convergence time since neighboring routers do not have to wait 30 seconds before sending out information on the poisoned route
The combination of split horizon with poison reverse is called route poisoning

## Slide 23: Summary of Techniques

## Slide 24: Comparing RIP V1 to V2

## Slide 25: RIP Communication
RIP version 2 communicates with other routers through the 224.0.0.9 multicast address

## Slide 26: RIP Configuration
RIP configuration requires three configuration commands
  router rip
  version 2
  network

## Slide 27: Basic RIP Configuration
In this example, each router’s network command tells the router to start using RIP
  R1 looks for any interfaces whose IP address is in Class B network 172.16.0.0
  R1 sees that both its FA0/0 and S0/0 interfaces have IP addresses in network 172.16.0.0, so R1 starts sending RIP updates on both interfaces
  Similarly, R2 finds that both of its interfaces match the network 172.16.0.0 command as well, because both interfaces are in network 172.16.0.0 so, R2 also begins sending RIP updates on both interfaces
  As a result, R1 and R2 begin to learn routes from each other using RIP

## Slide 28: Basic RIP Configuration

## Slide 29: Basic RIP Configuration
When a RIP network command matches an interface IP address, the IOS enables RIP on that interface
When RIP is enabled on an interface, three actions related to that interface are carried out

## Slide 30: Basic RIP Configuration
It starts sending RIP updates out the interface
It starts listening for RIP updates coming in that interface from some other router
It starts advertising a route to reach the subnet attached to the interface

## Slide 31: Configuring RIP

## Slide 32: Preventing Routing Updates
The command passive-interface is used to prevent routers from sending routing updates thorough an interface
This is to prevent devices from learning about routes you would prefer they not know about
This disables the sending out of RIP updates from that interface, but the router still receives updates through it

## Slide 33: Load Balancing with RIP
RIP can do simple load balancing using up to six equal cost paths
It uses the round robin method

## Slide 34: Troubleshooting RIP Update
Common RIP troubleshooting commands include
  show ip rip database
  show ip protocols
  show ip route
  show ip interface brief
  debug ip rip