## Slide 1: RIP Version 2
Last Update 2011.06.06
1.2.0

## Slide 2: Objectives
Learn about RIP Version 2

## Slide 3: Characteristics of RIP
A distance vector routing protocol
Hop count is the only metric

## Slide 4: Comparing RIP V1 to V2

## Slide 5: RIP Communication
RIP communicates with other routers through the 224.0.0.9 multicast address

## Slide 6: RIP Configuration
RIP configuration requires two configuration commands
  router rip
  network
Cisco insists on defaulting to version 1 so the basic RIP configuration is actually
  router rip
  version 2
  network

## Slide 7: Basic RIP Configuration
In this example, each router’s network command tells the router to start using RIP
  R1 looks for any interfaces whose IP address is in Class B network 172.16.0.0
  R1 sees that both its FA0/0 and S0/0 interfaces have IP addresses in network 172.16.0.0, so R1 starts sending RIP updates on both interfaces
  Similarly, R2 finds that both of its interfaces match the network 172.16.0.0 command as well, because both interfaces are in network 172.16.0.0 so, R2 also begins sending RIP updates on both interfaces
  As a result, R1 and R2 begin to learn routes from each other using RIP

## Slide 8: Basic RIP Configuration

## Slide 9: Configuring RIP

## Slide 10: Basic RIP Configuration
When a RIP network command matches an interface IP address, the IOS enables RIP on that interface
When RIP is enabled on an interface, three actions related to that interface are carried out

## Slide 11: Basic RIP Configuration
It starts sending RIP updates out the interface
It starts listening for RIP updates coming in that interface from some other router
It starts advertising a route to reach the subnet attached to the interface

## Slide 12: Preventing Routing Updates
The command passive-interface is used to prevent routers from sending routing updates thorough an interface
This is to prevent devices from learning about routes you would prefer they not know about
This disables the sending out of RIP updates from that interface, but the router still receives updates through it

## Slide 13: Preventing Routing Updates

## Slide 14: Load Balancing with RIP
RIP can do simple load balancing using up to six equal cost paths
It uses the round robin method

## Slide 15: RIP Capture File
Let’s look at a capture file showing the RIP process
Download this file
  HDLC with RIP.cap
Open it in Wireshark by double-clicking it

## Slide 16: RIP Capture File
Select frame 1
Looking at the frame list we can see that in frames 2, 3, and 4 the router at 192.168.2.1 has had RIP enabled on it
We know this as it sends out two RIP Requests to the multicast RIP address of 224.0.0.9

## Slide 17: RIP Capture File

## Slide 18: RIP Capture File
What it is saying is
  Is there anyone at the other end of this link that is alive and speaks RIP Version 2
A short time later it says
  Well in any event I speak RIP
  Besides the network I am on, the 192.168.2.0 network, I also know where the 192.168.10 network lives
Let’s look at these three frames

## Slide 19: RIP Capture File

## Slide 20: RIP Capture File

## Slide 21: RIP Capture File

## Slide 22: RIP Capture File
Select frames 10 and 11
The router at the other end of the link, 192.168.2.2, wakes up and does the same thing
However, in between the two RIP Requests and its RIP Response, its neighbor at 192.168.2.1, says in frames 12 and 13

## Slide 23: RIP Capture File
Great, a friend let me tell you about the networks I know about

## Slide 24: RIP Capture File

## Slide 25: RIP Capture File

## Slide 26: RIP Capture File

## Slide 27: RIP Capture File

## Slide 28: RIP Capture File
In frame 14 192.168.2.2 says
  Here is who I know about
  Which is the 192.168.2.0 and 192.168.3.0 networks

## Slide 29: RIP Capture File

## Slide 30: RIP Capture File
RIP quiets down until frames 22, 23, 24, and 25 where 192.168.2.1 says to anybody listening on 224.0.0.9
  What’s going on
192.168.2.2 answers
  I am still here
  Nothing changed, see

## Slide 31: RIP Capture File

## Slide 32: RIP Capture File

## Slide 33: RIP Capture File
In frames 41, 44, 49, and 53 we see RIP sending it’s routing table every 30 seconds even though nothing has changed

## Slide 34: RIP Capture File

## Slide 35: RIP Capture File

## Slide 36: RIP Capture File
Thus it goes over and over like this for the rest of the capture file
Notice that RIP uses the Well Known port number 520

## Slide 37: Troubleshooting RIP Update
Common RIP troubleshooting commands include
  show ip rip database
  show ip protocols
  show ip route
  show ip interface brief
  debug ip rip

## Slide 38: Show IP Protocols Command

## Slide 39: Show IP Route Command

## Slide 40: Lab
Let’s look at some RIP traffic
Start Wireshark
Open RIP_v1.pcap
Examine the back and forth

## Slide 41: Lab
Lab 7-1