## Slide 1: The Routing Table
Last Update 2011.01.20
1.1.0

## Slide 2: Objectives
Learn how a routing table operates

## Slide 3: The Routing Table
To do its job of path determination and switching the router uses its routing table
The routing table is a database held in RAM
This database stores information on the directly connected routes as well as routes to other networks learned by the network administrator informing the router about a route or by talking to other routers

## Slide 4: The Routing Table
A directly connected network is one that has a cable directly attached to the router
For local area networks these appear on activation in the IOS
The others are advertised one after another using a network command of one sort or the other
These networks then appear in the table

## Slide 5: The Routing Table
Also in the routing table are networks learned from other routers
These remote networks are not directly connected to the router
They may only be reached by sending a packet through at least one more router
These routes are learned by the router through a static route or from a dynamic routing protocol

## Slide 6: How a Router Handles Frames
To understand what goes on in building, maintaining, and using a routing table let's first look at what a router does when a frame arrives at one of its interfaces
Recall that a router looks like this in its basic form

## Slide 7: How a Router Handles Frames
This is the front of a medium sized router

## Slide 8: How a Router Handles Frames
This is the back of a medium sized router

## Slide 9: How a Router Handles Frames
These are the interfaces of interest
AUI Ethernet LAN Interface
Serial WAN Interface
Serial WAN Interface

## Slide 10: How a Router Handles Frames
Typically a packet will come in one of the serial interfaces
The router must then decide whether it goes to the LAN interface - the AUI port in this case - goes back out the other serial interface because it belongs somewhere else, or should be dropped because the router does not know what to do with it
In detail this process proceeds this way

## Slide 11: How a Router Handles Frames
The data-link level identifier in the frame's destination address is examined
If it contains either the identifier of the router's interface or a broadcast identifier, the router removes the packet from the frame and passes the packet to the network layer
At the network layer the destination of the packet is examined

## Slide 12: How a Router Handles Frames
If the destination address is either the IP address of the router's interface or an all hosts broadcast address, the protocol field of the packet is examined and the data is switched to the appropriate local network
However, if none of this applies to a frame, then the frame does not belong here

## Slide 13: How a Router Handles Frames
It should be somewhere else
So, routing is required
If routing is required, the router will look in the routing table for the correct route
A route table entry must contain at least two things
  A destination address
  A pointer to the destination

## Slide 14: How a Router Handles Frames
The destination address is an address of a network the router can reach
The pointer will indicate the way to this point is through a directly attached interface or the address of another router on a directly connected network
That router is the next hop router since it is one hop closer to the destination

## Slide 15: How a Router Handles Frames
If nothing can be found in the routing table, the packet is dropped and a Destination Unreachable message is sent back

## Slide 16: Remote Networks
When a network is not directly connected to one of the router’s interfaces an entry must be made into the routing table to tell the router how to reach this remote network
This entry can be done manually for each remote network using a static route or automatically by a dynamic routing protocol

## Slide 17: Static Routes
A static route is added to the routing table by an administrator typing on a keyboard
Likewise this route can only be changed by an administrator typing on a keyboard
Therefore these routes are only used for
  Very stable connections
  Connections where there is only one way out
An S means a static route

## Slide 18: Static Route

## Slide 19: Lab
Start Packet Tracer
Do Packet Tracer Activity 1.3.2.2

## Slide 20: Lab
Start Packet Tracer
Do Packet Tracer Activity 1.3.3.2

## Slide 21: Dynamic Routes
A dynamic route is a route learned by talking to other routers
These routes come and go automatically without the administrator having to do anything

## Slide 22: Dynamic Routes

## Slide 23: Using the Routing Table
As Cisco points out in their lecture material for this course there are three basic principles that will help you understand, configure, and troubleshoot routing issues
  These principles are from Alex Zinin's book, Cisco IP Routing

## Slide 24: Using the Routing Table
  Every router makes its decision alone, based on the information it has in its own routing table
  The fact that one router has certain information in its routing table does not mean that other routers have the same information
  Routing information about a path from one network to another does not provide routing information about the reverse, or return, path

## Slide 25: Lab
Start Packet Tracer
Do Packet Tracer Activity 1.3.3.4

## Slide 26: Asymmetric Routing
A route is one way
The ability of a packet to go from point A to point B says nothing about the ability of a packet to go from point B to point A
As such routing may be asymmetrical where a packet may take one route from point A to point
Then it may take an entirely different route from point B back to point A

## Slide 27: Load Balancing
If two equal cost paths exist in a routing table the router can make use of both by performing load balancing

## Slide 28: Routing Table Structure
As mentioned a routing table can contain any of three different type of routes
  Directly connected
  Static
  Dynamic

## Slide 29: The Routing Table
Let’s look at a routing table
Here is the network

## Slide 30: The Routing Table

## Slide 31: The Routing Table
Let’s examine the routing table for Router 3
As you can see on the diagram Router 3 knows about networks 2 and 3 as these are directly connected to it
Network 2 exists between Router 3 and Router 2
Network 3 exists between Router 3 and Router 4

## Slide 32: The Routing Table
Router 3 has no knowledge of networks 1, 4, 5, 6, and 7 as they are all on the other side of one or more other routers
Here is the routing table for Router 3

## Slide 33: The Routing Table

## Slide 34: The Routing Table
As the routing table shows networks 1 and 2 are reached by going out of port serial 0/0/1
While networks 3, 4, 5, 6, and 7 are reached by going out of the serial 0/0/0 port
In this case each of these is reached by use of a static route as the S shows

## Slide 35: The Routing Table
With the C indicating the directly connected networks
What if the remote networks were learned from a dynamic routing protocol
Let’s see what the routing table would look like if RIP was the routing protocol used
This view is from Router 6

## Slide 36: The Routing Table

## Slide 37: The Routing Table
The R in the table indicating those routes learned through the RIP dynamic routing protocol

## Slide 38: Routing Table Structure
A route in a Cisco routing table can be one of two types
  Level 1
    These have a subnet mask equal to or less than the classful mask of the network address
  Level 2

## Slide 39: Level 1 Routes
A level 1 route can function as
  Default route
  Supernet route
  Network route
A level 1 ultimate route is one that includes either
  A next hop address
  An exit interface

## Slide 40: Parent and Child Routes
A level 1 route can also be a parent route
  A parent route does not contain either a next hop IP address or exit interface information
A parent route is created any time a subnet is added to the routing table
Child routes are level 2 routes
Child routes are a subnet of a classful network address

## Slide 41: Level 2 Routes
Level 2 child routes contain the route source and the network address of the route
Level 2 child routes are also considered ultimate routes as they contain the next hop address or exit interface or both

## Slide 42: Parent and Child Routes

## Slide 43: Route Lookup Process
The route lookup process proceeds this way
  Examine the level 1 routes
    If the best match is a level 1 ultimate route and is not a parent route this route is used to forward packet
  Examine the level 2 child routes
    If there is a match with a level 2 child route then that subnet is used to forward the packet

## Slide 44: Route Lookup Process
  If no match is made then the routing behavior type must be determined
The router determines if it should use classful or classless routing behavior
  If classful, then the packet is dropped
  If classless, then router searches the level one supernet and default routes
    If there is a level 1 supernet or default route match, then the packet is forwarded
    If not, the packet is dropped

## Slide 45: Route Lookup Process
The default routing behavior is ip classless
Classless routing behavior works for
  Discontiguous networks
  CIDR supernets
Level 1 routes are searched
  Supernet routes are checked first
    If a match exists then forward packet
  Default routes are checked second
    If no match or default route then drop packet

## Slide 46: Route Lookup Process
If no match is found, then a match with fewer bits is attempted

## Slide 47: The Best Match
The best match is also known as the longest match
The best match is the one that matches the most bits from the left to the right when matching the destination address to the routing table

## Slide 48: The Best Match