## Slide 1: EIGRP
Last Update 2014.06.13
1.4.0

## Slide 2: Objectives
Learn what EIGRP is and how it operates

## Slide 3: What is EIGRP
EIGRP is a distance vector routing protocol
Cisco finally quit calling it a hybrid routing protocol I am pleased to see
This is a Cisco only protocol
It was first released as a replacement for RIP and a follow-on to IGRP in 1992 to support classless addressing

## Slide 4: EIGRP Metric
EIGRP is still and will remain in wide use
The metric for EIGRP is theoretically made up of
  Bandwidth
  Delay
  Reliability
  Load
  MTU
  Hop Count

## Slide 5: EIGRP Metrics
Despite being in the list MTU and Hop Count are not used
In practice only bandwidth and delay are used
Despite it appearing that these metrics can be adjusted, in practice they are constants
The only one that can be successfully manipulated is delay, but there is really no reason to alter it either

## Slide 6: EIGRP Metrics
Just leave them all at their default values
MTU is listed as a metric, but it was never implemented in EIGRP
Much of this metric confusion is due to the need to make IGRP backward compatible with IGRP as well as confusion in the early days of all of this
The maximum hop count is 224

## Slide 7: EIGRP Multicast Address
EIGRP uses the multicast address 224.0.0.10

## Slide 8: EIGRP Benefits
EIGRP has the following benefits
  Rapid convergence
  Efficient use of bandwidth as only partial bounded updates are sent as needed only to the routers affected
  Supports CIDR
  Supports VLSM
  Supports IP, IPX, and AppleTalk

## Slide 9: EIGRP Concepts
The following three tables are maintained by EIGRP
  Neighbor table
  Topology table
  Routing table

## Slide 10: Neighbor Table
The most important table
It lists adjacent routers
There is one table per routed protocol in use
When a hello packet is not received within the hold time the topology change is recomputed due to the change in the neighbor table

## Slide 11: Neighbor Table Elements
Neighbor Address
  The network layer address of the neighbor router
Smooth Round Trip Timer
  The average time it takes to send and receive packets from a neighbor
Queue Count
  The number of packets waiting to be sent
Sequence Number
  The last packet received

## Slide 12: Topology Table
This is a table made up of all of the EIGRP routing tables of the routers that are talking to each other
It is more properly called a list of all the networks known table
EIGRP takes this and the information in the neighbor table to compute the lowest cost path to each destination, which it places in the routing table

## Slide 13: Topology Table Elements
Feasible Distance
  FD is xxxxxxxx
  The lowest calculated metric to each destination
Route Source
  via xxx.xxx.xxx.xxx
  The source of the route is the identification number of the router that originally advertised the route

## Slide 14: Topology Table Elements
Reported Distance
  xxxxxxx/xxxxxx
  The distance that an adjacent neighbor reports to a specific destination
Interface Information
  The interface through which the destination is reached

## Slide 15: Topology Table Elements
Router Status
  P – Passive
    The route is stable and ready for use
  A – Active
    Route is being recomputed

## Slide 16: Topology Table Organization
The organization of the topology table is
  Successor routes at the top
  Feasible successors next
  Possible loops at the bottom

## Slide 17: Successor
The successor is the primary router or the next router in the path
This route is identified by the DUAL algorithm from the information in the neighbor and topology tables
This route is placed in the routing table
There can be up to four of these for each route

## Slide 18: Feasible Successor
The feasible successor is a backup router
These are identified at the same time as the successors
They are only kept in the topology table
These are not required
In general they are not used
When the route goes away generally the whole thing is just recomputed

## Slide 19: Route Selection Rules
Let’s see how this all happens

## Slide 20: Route Selection Rules

## Slide 21: Route Selection Rules
RTA has a route to Z via RTB
For RTA RTB is the current successor for Z
RTA sends packets for Z to RTB
RTC also claims to have a route to Z with same metric
RTA installs RTC as a successor as well
Any of RTA’s neighbors that advertise a loop free route to Z, but with a worse metric than what is already in the table are added as feasible successors
For RTA this is RTX in this example

## Slide 22: Route Selection Rules

## Slide 23: Route Recomputation
If a route becomes unavailable and a feasible successor does not exist, then the router must ask its neighbors for a route
The neighbors must reply

## Slide 24: Routing Table
These best routes are placed in the routing table

## Slide 25: Null0
The Null0 interface is not a physical interface
  It is only used to advertise routes when
    At least one subnet is learned via EIGRP
    Automatic summarization is enabled
  The Null0 interface is used to discard any packets that match the parent route, but do not match any of the child routes

## Slide 26: Null0

## Slide 27: Null0

## Slide 28: Configuration
Basic configuration of EIGRP consists of
  router eigrp commonrouteinformationnumber
  network networknumber
and
  eigrp log-neighbor-changes
    Recommended by Cisco to monitor stability

## Slide 29: Configuration

## Slide 30: Configuration
The common route information number is a common source of confusion since Cisco insists on calling it an autonomous system number, it is not
This number has absolutely nothing to do with the concept of an autonomous system
It just represents a common number for each of the routers talking to each other to use

## Slide 31: Configuration
It is most similar to a process number
Even though the number can be anything from 1 to 65535 just use 1 all the time

## Slide 32: Configuration
The same sort of confusion is seen in the network command
In general you can use just the command
  network 192.168.1.0
for example
To use the network command to advertise just specific subnets the wildcard mask can be used

## Slide 33: Configuration
Now why not the subnet mask
Because as usual all the Cisco engineers were drunk as skunks on a beach in Cancun
They thought is would be so funny to use a wildcard mask, which is the opposite of the subnet mask, just to make all of this harder to learn

## Slide 34: Configuration
Consider that the router does not care as all it sees are ones and zeros
Even worse in some versions of the IOS you can enter a subnet mask, which the IOS then converts to a wildcard
Engineers are such a pain in the rear

## Slide 35: Configuration
Use the bandwidth command to adjust the speed to match the actual speed of the data line

## Slide 36: EIGRP Capture File
Let’s examine the frames used by EIGRP as it goes about its work
Download this file
  HDLC with EIGRP.cap
To open it in Wireshark double-click on it
Select frame 3
Expand all of the fields in the Cisco EIGRP layer

## Slide 37: EIGRP Capture File

## Slide 38: EIGRP Capture File
What can we learn
The router named 192.168.2.1 says in this Hello frame
  Hi, I speak EIGRP
  Is there anyone that speaks the same routing protocol at the other end of this link
Notice it sends this to the EIGRP multicast address of 224.0.0.10

## Slide 39: EIGRP Capture File
What else do we see
This is Version 2 of EIGRP
The AS is 1
The metrics are K1 to K5 with only K1 and K3 being used
These represent bandwidth and delay which are the default metrics
The router is running IOS version 12.3

## Slide 40: EIGRP Capture File
This is EIGRP version 1.2
192.168.2.1 does this again in frames 6, 8, and 10
Then in frame 12 192.168.2.2 sys hi there I am alive and I speak EIGRP
192.168.2.1 says great in frame 13
Here is a network I know about that you do not, the 192.168.1.0 network

## Slide 41: EIGRP Capture File

## Slide 42: EIGRP Capture File

## Slide 43: EIGRP Capture File
As we see in frame 13 the network is
  192.168.1.0/24
  The delay value is 2560
  The bandwidth is 25600
  The mtu is 1500
  The reliability is high at 255
Notice the network name and prefix length in the bottom two fields

## Slide 44: EIGRP Capture File
In frame 21 we have an Update from 192.168.2.2 where it reports on the 192.168.3.0 network

## Slide 45: EIGRP Capture File

## Slide 46: EIGRP Capture File
There are a few more updates in the next few frames
Then at frame 31 we see a EIGRP ACK frame from 192.168.2.1 to 192.168.2.2
In frame 35 the same thing from 192.168.2.2 to 192.168.2.1

## Slide 47: EIGRP Capture File

## Slide 48: EIGRP Capture File

## Slide 49: EIGRP Capture File
At this point everybody knows about everybody else
At frame 37 they start the Hello process to see if there is anyone else out there and whether their current partner is still alive
Notice that nothing else happens for the rest of the capture file, except for this Hello process
Other wise EIGRP is quiet

## Slide 50: EIGRP Capture File

## Slide 51: Verifying EIGRP
These commands are used to check the operation of EIGRP
  show ip eigrp neighbors
    Used to view the neighbor table
  show ip eigrp topology
    Used to show the topolgy table
  show ip route
    Used to show the routing table
  show ip protocols
    Used to see if EIGRP is enabled

## Slide 52: Verifying EIGRP

## Slide 53: Verifying EIGRP

## Slide 54: Lab
Start Packet Tracer
Do activity 9.9.2.6.pka

## Slide 55: Lab
Lab 9-1