## Slide 1: IS-IS
Last Update 2012.02.16
1.1.0

## Slide 2: Objectives
Learn about IS-IS

## Slide 3: What is IS-IS
IS-IS Intermediate System to Intermediate System pronounced as I-S I-S is a link state interior domain routing protocol
It is used mostly by ISPs as it scales better than OSPF in very large networks
It has seen increasing use in non-ISP networks with the deployment of IPV6 since it had stable support for IPV6 before OSPFv3 was ready

## Slide 4: What is IS-IS
For example in February 2012 it was reported on the NANOG list that the following used it as their IGP
  University of Pennsylvania
  Nokia
  Zynga

## Slide 5: What is IS-IS
In addition to using IS-IS for IPV6 deployment a message on the NANOG list gave these reasons as well
  I would say a place like a college or industrial campus that might do some MPLS on the campus or across the organization would be a good candidate to find ISIS being used

## Slide 6: What is IS-IS
  For example a virtual LAN that interconnect several offices of a given department that are in different physical locations and uses MPLS to do that would likely use ISIS
  So the "engineering department" of the entire organization might appear to be on one virtual net even though the various offices are in different buildings/cities

## Slide 7: What is IS-IS
IS-IS was developed in the 1990s
IS-IS uses the Dijkstra's algorithm just as does OSPF

## Slide 8: What is IS-IS
IS-IS uses the area concept seen in OSPF, but in a slightly different way
When the network is subdivided into areas using IS-IS the areas are called levels using a two-level hierarchy instead
A router only exists in one area

## Slide 9: What is IS-IS
The routers are then classified as
  Level 1 to route entirely within an area
  Level 2 to route between areas
  Level 1-2 to do both

## Slide 10: What is IS-IS
When a packet needs to go to another area, a Level 1 router sends the packet to the nearest Level 2 router in its own area
The packet travels via Level 2 routing to the destination area, then by Level 1 routing to the destination
Level 2 routers are inter area routers
They can only form relationships with other Level 2 routers

## Slide 11: What is IS-IS
Routing information is exchanged between Level 1 routers and other Level 1 routers
Level 2 routers only exchange information with other Level 2 routers
Level 1-2 routers exchange information with both levels
They are used to connect the inter area routers with the intra area routers

## Slide 12: What is IS-IS
In OSPF a border router is in two or more areas at once
In IS-IS area borders are in between routers, designated as Level 2 or Level 1-2
Thus an IS-IS router is only part of a single area
Unlike OSPF IS-IS also does not require an Area 0 to be a backbone area through which all inter-area traffic passes

## Slide 13: What is IS-IS
The popularity of IS-IS among ISPs is due both its ability to scale into larger networks and it being less talkative
Thus the links see less overhead on them

## Slide 14: Configuration of IS-IS
interface ethernet0
ip address 172.16.12.2 255.255.255.0
no shutdown
ip router isis
  To turn on the interface
  Then enable IS-IS for IP on the interface

## Slide 15: Configuration of IS-IS
interface Serial0
ip address 172.16.23.1 255.255.255.252
no shutdown
ip router isis
  To turn on the interface
  Then enable IS-IS for IP on the interface

## Slide 16: Configuration of IS-IS
router isis
net 49.0001.1720.1600.2002.00
  To enable IS-IS on the router
  Then assign an area and system ID to the router