## Slide 1: SDN Last Update 2014.09.19 2.0.1

## Slide 2: Objectives
Learn what Software Defined Networking is and whether it matters

## Slide 3: Sources
Most of this is copied with minor edits from
  An article by William Stallings in the March 2013 issue of the Internet Protocol Journal
  Software Defined Networking with OpenFlow by Siamak Azodolmolky
  SDN and OpenFlow for Beginners by Vivek Tiwari
  A presentation to NANOG 57 by Steven Wallace and Chris Small

## Slide 4: Sources
SDN: Software Defined Networks by Thomas D. Nadeau and Ken Gray

## Slide 5: What is SDN
In traditional networks a layer 2 switch and other network devices combine the hardware and software to control the operation of the device as it moves frames in and out of its ports in a single physical device
Each device in the network operates on its own

## Slide 6: What is SDN
How does SDN differ from this
This definition with a few modifications is copied from Azodolmolky
  The concept of programmable networks has been proposed as a way to facilitate network evolution
  In particular, SDN is a new networking paradigm, in which the forwarding hardware is decoupled from the control decisions

## Slide 7: What is SDN
  This involves the migration of control logic, which currently is tightly integrated in the networking devices, such as Ethernet switches, into accessible and logically centralized controllers
  This allows the underlying networking infrastructure to be abstracted
  This separation provides a more flexible, programmable, vendor-agnostic, cost efficient, and innovative network architecture

## Slide 8: What is SDN
  Besides the network abstraction, the SDN architecture provides a set of API - Application Programing Interfaces that simplifies the implementation of common network services
  Examples being routing, security, traffic engineering, QoS, and the like

## Slide 9: What is SDN
  In SDN, the network intelligence is logically centralized in software-based controllers at the control plane, and network devices become the simple packet forwarding devices at the data plane that can be programmed via an open interface
  One of the early implementations of this open interface is called OpenFlow

## Slide 10: How Does SDN Work
Azodolmolky tells us that SDN decentralizes and abstracts the network thusly
  Instead of enforcing policies and running protocols on a convolution of scattered devices, the network is reduced to simple forwarding hardware and the decision-making network controller

## Slide 11: How Does SDN Work
  The forwarding hardware consists of the following
    A flow table containing flow entries consisting of match rules and actions to take
    A transport layer protocol that securely communicates with a controller about new entries that are not currently in the flow table

## Slide 12: How Does SDN Work
Stallings adds that
  SDN – Software Defined Networking is a method to abstract or virtualize network creation and management by separating the data and control planes
  The main point is to move from a distributed device management method to a centralized management format

## Slide 13: How Does SDN Work
  This is similar to the way the servers in local area networks were once managed individually, and then moved to a directory system where all servers are now managed from a central point

## Slide 14: Why Use SDN
Stallings suggests the main reason one would want to move to SDN is the expanding use of server virtualization
As Stallings explains
  But it creates problems with traditional network architectures
  One problem is configuring VLANs

## Slide 15: Why Use SDN
  Network managers need to make sure the VLAN used by the virtual machine is assigned to the same switch port as the physical server running the virtual machine
  But with the virtual machine being movable, it is necessary to reconfigure the VLAN every time that a virtual server is moved

## Slide 16: Why Use SDN
  In general terms, to match the flexibility of server virtualization, the network manager needs to be able to dynamically add, drop, and change network resources and profiles
  This process is difficult to do with conventional network switches, in which the control logic for each switch is co-located with the switching logic

## Slide 17: Will SDN Amount to Anything
Will SDN be successful in the market
The trade press certainly thinks so
Here are some graphics from a SDN market report by IDC from April 2013
Keep in mind that the trade press often overhypes new ideas

## Slide 18: Will SDN Amount to Anything

## Slide 19: Will SDN Amount to Anything

## Slide 20: Will SDN Amount to Anything

## Slide 21: Will SDN Amount to Anything

## Slide 22: Will SDN Amount to Anything
According to Tiwari SDN became mainstream in 2012 when VMware purchased Nicira for 1.25 billion dollars in order for VMware to do for network virtualization what it had done for server virtualization
That amount for a new technology focused everyone’s attention on this concept

## Slide 23: Will SDN Amount to Anything
Tiwari also points out that everything inside a data center has been abstracted from the hardware except for the network
It is logical that this will be the next step

## Slide 24: Parts of a SDN
A SDN based network looks like this

## Slide 25
Controller
Switch
Switch
Switch
Host
Host
Host
Host
Host
Host
Network Management Programs
Northbound Interface
Southbound Interface
Using OpenFlow to Control the Switches Through a TCP TLS Connection
Control Plane
Control Plane
Data Plane
Data Plane
End Devices

## Slide 26: SDN Controller
Let’s see what these parts do
  On the northbound interface the controller provides a programmatic interface to the network, where applications can be written to perform control and management tasks, and offer new functionalities
  This view assumes that the control is centralized and applications are written as if the network is a single system

## Slide 27: SDN Controller
  While this simplifies policy enforcement and management tasks, the bindings must be closely maintained between the control and the network forwarding elements
  A controller that strives to act as a network operating system must implement at least two interfaces

## Slide 28: SDN Controller
  Northbound Interface
    A northbound interface that presents a programmable API to network control and high-level policy applications and services
  Southbound Interface
    A southbound interface that allows switches to communicate with the controller

## Slide 29: Northbound Interface
External management systems or network applications may wish to extract information about the underlying network or control an aspect of the network behavior or policy
Additionally, controllers may find it necessary to communicate with each other for a variety of reasons

## Slide 30: Northbound Interface
For instance, an internal control application may need to reserve resources across multiple domains of control, or a primary controller may need to share policy information with a backup controller

## Slide 31: Northbound Interface
Unlike controller-switch communication, that is the southbound interface, there is no currently accepted standard for the northbound interface and they are more likely to be implemented on an ad-hoc basis for particular applications

## Slide 32: Southbound Interface
The southbound interface is well defined
It functions as a de facto standard for switch control

## Slide 33: SDN Switch
An OpenFlow switch consists of a flow table, which performs packet lookup and forwarding
Each flow table in the switch holds a set of flow entries that consists of
  Header fields or match fields, with information found in the packet header, ingress port, and metadata, used to match incoming packets

## Slide 34: SDN Switch
  Counters, used to collect statistics for the particular flow, such as number of received packets, number of bytes, and duration of the flow
  A set of instructions or actions to be applied after a match that dictates how to handle matching packets, such as forwarding a packet out to a specified port
A flow table looks like this

## Slide 35: SDN Switch

## Slide 36: SDN Switch

## Slide 37: SDN Switch

## Slide 38: SDN Switch
Each flow entry is associated with zero or more actions that instruct the OpenFlow switch how to handle matching packets
If no forward actions are present, the packet is dropped
Action lists must be processed in the specified order

## Slide 39: SDN Switch
However, there is no guaranteed packet output ordering within an individual port
For instance, two packets which are generated and destined to a single output port as part of the action processing, may be arbitrarily re-ordered

## Slide 40: SDN Switch
Stallings says that an SDN switch encapsulates and forwards the first packet of a flow to an SDN controller
The controller decides what to do with a flow of packets
If the packets are to be handled, a flow table is created for them

## Slide 41: SDN Switch
The switch forwards incoming packets that are part of this flow out the appropriate port based on the flow table
The flow table can define a priority for the flow
The switch can drop packets on a particular flow, temporarily or permanently, as dictated by the controller

## Slide 42: SDN Switch
SDN switches differ from the current layer 2 and 3 switches in that they perform these functions
  Encapsulate and forward the first packet of a flow to an SDN controller so that the controller can determine if a flow should be added to the switch flow table

## Slide 43: SDN Switch
  Once a flow is established the switch forwards incoming packets for that, and each other flow, out of the appropriate port based on the flow table

## Slide 44: SDN Switch
Upon a packet arrival at the OpenFlow switch, the packet header fields are extracted and matched against the matching fields' portion of the flow table entries
This matching starts at the first flow table entry and continues through subsequent flow table entries

## Slide 45: SDN Switch
If a matching entry is found, the switch applies the appropriate set of instructions associated with the matched flow entry
For each packet that matches a flow entry, the associated counters for that entry are updated

## Slide 46: SDN Switch
If the flow table look-up procedure does not result in a match, the action taken by the switch will depend on the instructions defined at the table-miss flow entry
The flow table must contain a table-miss entry in order to handle table misses
This particular entry specifies a set of actions to be performed when no match is found for an incoming packet

## Slide 47: SDN Switch
These actions include dropping the packet, sending the packet out on all interfaces, or forwarding the packet to the controller over the secure OpenFlow channel

## Slide 48: SDN Switch
If a switch loses contact with the controller, as a result of an echo request timeout, TLS session timeout, or other disconnection, it will attempt to contact one or more backup controllers
If some number of attempts to contact a controller fail, the switch must enter emergency mode and immediately reset the current TCP connection

## Slide 49: SDN Controller Operation
The controller configures and manages the switch, receives events from the switch, and sends packets out to the switch through this interface
Using the OpenFlow protocol, a controller can add, update, or delete flow entries from the switch's flow table
That can happen reactively - in response to a packet arrival - or proactively

## Slide 50: SDN Controller Operation
With a reactive control model, the OpenFlow switches must consult an OpenFlow controller each time a decision must be made, such as when a new packet flow reaches an OpenFlow switch

## Slide 51: SDN Controller Operation
There will be a small performance delay as the first packet of each new flow is forwarded to the controller for a decision after which future traffic within that flow will be forwarded at line rate within the switching hardware

## Slide 52: SDN Controller Operation
While the first-packet delay is negligible in many cases, it may be a concern if the central OpenFlow controller is geographically remote or if most flows are short-lived, such as a single-packet flow
An alternative proactive approach is also possible in OpenFlow to push policy rules out from the controller to the switches

## Slide 53: SDN Controller Operation
The OpenFlow protocol can be viewed as one possible implementation of controller switch interactions – the southbound interface - as it defines the communication between the switching hardware and a network controller
Controller to switch messages are initiated by the controller

## Slide 54: SDN Implementation
Here is the diagram Stallings uses to illustrate how SDN is implemented

## Slide 55: SDN Implementation

## Slide 56: SDN Implementation
In this type of system a controller performs all of the functions, such as routing, policy implementation, and security
This is the SDN control plane
It is deployed in one or more SDN servers which are the controllers

## Slide 57: SDN Implementation
This controller defines and controls the data flows that occur in the SDN data plane
As Stallings says
  Each flow through the network must first get permission from the controller, which verifies that the communication is permissible by the network policy

## Slide 58: SDN Implementation
  If the controller allows a flow, it computes a route for the flow to take, and adds an entry for that flow in each of the switches along the path
  With all complex functions subsumed by the controller, switches simply manage flow tables whose entries can be populated only by the controller

## Slide 59: SDN Implementation
  Communication between the controller and the switches uses a standardized protocol and API
SDN devices can be implemented for Ethernet switches at layer 2, routers at layer 3, transport layer switching at layer 4, or application layer switching and routing

## Slide 60: SDN Protocols
For all of this to work one or more protocols are used
Some of these will be proprietary and some open source
It remains to be seen which approach wins out

## Slide 61: SDN Protocols
OpenFlow is the open source protocol
Most major networking equipment manufacturers have a proprietary protocol as well

## Slide 62: What is OpenFlow
The OpenFlow protocol is often misunderstood to be equivalent to SDN, but it is not
OpenFlow is just one method

## Slide 63: What is OpenFlow
Here is the basic history of OpenFlow according to Tiwari
  The concept of separating the control plane and data plane is not new; this has been used in the telephone industry and has been kicked around since the 90’s for networking

## Slide 64: Before OpenFlow
  Here are a few interesting facts for you
    Ipsilon networks proposed GSMP - RFC 1987 - General switch management protocol in 1996
    This had a controller and was a flow based model for ATM switches
    This company was not very successful and eventually bought by Nokia
    In the year 2000, ForCES - forwarding and control element separation - was there and you can find a couple of RFC’s on this

## Slide 65: Before OpenFlow
    In 2004 RCP - Routing control platform - was proposed to overcome the fully meshed nature of iBGP
    The proposal was to have a centralized platform separate from the forwarding plane that can collect information and performs route selection on behalf of the routers and presents to them the best routes
    Ethane came in 2007 which coupled simple flow based switches managed by a central controller which controlled the flows

## Slide 66: What is OpenFlow
Tiwari also writes that OpenFlow is an open source project that was the result of a six-year research collaboration project between Stanford University and the University of California at Berkeley
  Developed at Stanford OpenFlow Version 1.0 was announced in December 2009
  March 2011 ONF - Open Network Foundation was launched

## Slide 67: What is OpenFlow
  October 2011 Stanford University hosts the first Open Networking Summit
  February 2011 OpenFlow Version 1.1.0
  October 2011 First Open Networking Summit
  February 2012 OpenFlow Version 1.2
  April 2012 Second Open Networking Summit
  June 2012 OpenFlow Version 1.3
  April 2013 Third Open Networking Summit

## Slide 68: What is OpenFlow
Nadeau and Gray provide this as the main driver for the current interest in SDN
  Early proponents of SDN saw that network device vendors were not meeting their needs, particularly in the feature development and innovation spaces
  High-end routing and switching equipment was also viewed as being highly overpriced for at least the control plane components of their devices

## Slide 69: What is OpenFlow
  At the same time, they saw the cost of raw, elastic computing power diminishing rapidly to the point where having thousands of processors at one’s disposal was a reality
  It was then that they realized that this processing power could possibly be harnessed to run a logically centralized control plane and potentially even use inexpensive, commodity-priced switching hardware

## Slide 70: What is OpenFlow
  A few engineers from Stanford University created a protocol called OpenFlow that could be implemented in just such a configuration
  OpenFlow was architected for a number of devices containing only data planes to respond to commands sent to them from a logically centralized controller that housed the single control plane for that network

## Slide 71: What is OpenFlow
  The controller was responsible for maintaining all of the network paths, as well as programming each of the network devices it controlled

## Slide 72: What is OpenFlow
Commonly used versions are 1.0 and the current 1.3
According to Tiwari the versions have been
  OpenFlow Switch Specification 1.0.0 December 31 2009 along with the Errata 1.0.1
  OpenFlow Switch Specification 1.1.0 February 28 2011

## Slide 73: What is OpenFlow
  OpenFlow Switch Specification 1.2 December 2011
  OpenFlow Switch Specification 1.3.0 June 25 2012
  OpenFlow Switch Specification 1.3.1 September 6 2012
  OpenFlow Switch Specification 1.3.2 April 25 2013

## Slide 74: What is OpenFlow
Just to give you an idea, the latest versions of OpenFlow now has support for IPv6
It also supports three types of ports - logical, physical and reserved
There is provision for tunneling which can be used in datacenter deployments or VPN deployments

## Slide 75: What is OpenFlow
Features like bandwidth management, QoS and per flow metering have been added
The default behavior in OpenFlow 1.0 is to send all unknown packets to the controller
This has been changed to drop the packet unless specific rules are there to send the packet to the controller

## Slide 76: What is OpenFlow
ONF has decided to freeze the major version at 1.3 right now so that industry can catch up to it
It wants to give the industry a stable target that the manufacturers can aim for

## Slide 77: What is OpenFlow
OpenFlow is an open interface for remotely controlling the forwarding tables in network switches, routers, and access points used to create software defined networks

## Slide 78: OpenFlow
Stallings discusses the purpose of a protocol such as OpenFlow when he writes
  To turn the concept of SDN into practical implementation, two requirements must be met
  First, there must be a common logical architecture in all switches, routers, and other network devices to be managed by an SDN controller

## Slide 79: OpenFlow
  This logical architecture may be implemented in different ways on different vendor equipment and in different types of network devices, so long as the SDN controller sees a uniform logical switch function

## Slide 80: OpenFlow
  Second, a standard, secure protocol is needed between the SDN controller and the network device
Both of these requirements are addressed by OpenFlow, which is both a protocol between SDN controllers and network devices, as well as a specification of the logical structure of the network switch functions

## Slide 81: OpenFlow
OpenFlow is defined in the OpenFlow Switch Specification, published by the ONF - Open Networking Foundation
ONF is a consortium of software providers, content delivery networks, and networking equipment vendors whose purpose is to promote software-defined networking

## Slide 82: OpenFlow
In the OpenFlow environment an SDN controller communicates with OpenFlow compatible switches using the OpenFlow protocol running over the SSL
Each switch connects to other OpenFlow switches and, possibly, to end-user devices that are the sources and destinations of packet flows

## Slide 83: OpenFlow
Within each switch, a series of tables typically implemented in hardware or firmware are used to manage the flows of packets through the switch

## Slide 84: OpenFlow

## Slide 85: What is a Flow
A flow is defined as a sequence of packets that share common header values
Stallings points this out as well
  We can now offer a more precise definition of the term flow
  From the point of view of an individual switch, a flow is a sequence of packets that matches a specific entry in a flow table

## Slide 86: What is a Flow
  The definition is packet oriented, in the sense that it is a function of the values of header fields of the packets that constitute the flow, and not a function of the path they follow through the network
  A combination of flow entries on multiple switches defines a flow that is bound to a specific path

## Slide 87: What is a Flow
Tiwari adds that
  The key here is that you now have much greater control over traffic as it is seen as flows
  As a result you can treat the flow of video, voice, email, IM, and a screen being shared from the same computer differently from one point to the other on your network in a dynamic and secure fashion

## Slide 88: Tables Used by OpenFlow
OpenFlow uses three types of tables in the logical switch
  Flow Table
    This table directs incoming packets to the proper flow that then specifies the functions that are to be performed on the packets
    There may be multiple flow tables that process in pipeline fashion

## Slide 89: Tables Used by OpenFlow
  Group Table
    This table may trigger a variety of actions that affect one or more flows
  Meter Table
    The metering table controls any performance adjustments that may apply

## Slide 90: Flow Table
The main table used is the flow table
Every packet that comes into a switch goes through at least one flow table, and perhaps several
The flow table has six parts
Stallings defines them this way
  Match Fields
    Used to select packets that match the values in the fields

## Slide 91: Flow Table
  Priority
    Relative priority of table entries
  Counters
    Updated for matching packets
    The OpenFlow specification defines a variety of timers
    Examples include the number of received bytes and packets per port, per flow table, and per flowtable entry; number of dropped packets; and duration of a flow

## Slide 92: Flow Table
  Instructions
    Actions to be taken if a match occurs
  Timeouts
    Maximum amount of idle time before a flow is expired by the switch
  Cookie
    Opaque data value chosen by the controller
    May be used by the controller to filter flow statistics, flow modification, and flow deletion; not used when processing packets

## Slide 93: Flow Instructions
Stallings explains the details of the flow instructions this way
  The instructions component of a table entry consists of a set of instructions that are executed if the packet matches the entry

## Slide 94: Actions
  Before describing the types of instructions, we need to define the terms Action and Action Set
  Actions describe packet forwarding, packet modification, and group table processing operations
  The OpenFlow specification includes the following actions

## Slide 95: Actions
    Output
      Forward packet to specified port
    Set-Queue
      Sets the queue ID for a packet
      When the packet is forwarded to a port using the output action, the queue id determines which queue attached to this port is used for scheduling and forwarding the packet
      Forwarding behavior is dictated by the configuration of the queue and is used to provide basic QoS support
    Group
      Process packet through specified group

## Slide 96: Actions
    Push-Tag/Pop-Tag
      Push or pop a tag field for a VLAN or MPLS packet
    Set-Field
      The various Set-Field actions are identified by their field type; they modify the values of respective header fields in the packet
    Change-TTL
      The various Change-TTL actions modify the values of the IPv4 Time To Live (TTL), IPv6 Hop Limit, or MPLS TTL in the packet

## Slide 97: Action Sets
An Action Set is a list of actions associated with a packet that are accumulated while the packet is processed by each table and executed when the packet exits the processing pipeline

## Slide 98: Instructions
Instructions are of four types
  Direct packet through pipeline
    The Goto-Table instruction directs the packet to a table farther along in the pipeline
    The Meter instruction directs the packet to a specified meter
  Perform action on packet
    Actions may be performed on the packet when it is matched to a table entry

## Slide 99: Instructions
  Update action set
    Merge specified actions into the current action set for this packet on this flow, or clear all the actions in the action set
  Update metadata
    A metadata value can be associated with a packet
    It is used to carry information from one table to the next

## Slide 100: Flow Tables
Recall that there can be more than one flow table
If there is they interact in this way as Stallings shows

## Slide 101: Flow Tables

## Slide 102: OpenFlow Protocol
Stallings then goes over the main protocols used by OpenFlow
  The OpenFlow protocol describes message exchanges that take place between an OpenFlow controller and an OpenFlow switch
  Typically the protocol is implemented on top of SSL – Secure Sockets Layer or TLS - Transport Layer Security providing a secure OpenFlow channel

## Slide 103: OpenFlow Protocol
  The OpenFlow protocol enables the controller to perform add, update, and delete actions to the flow entries in the flow tables
  It supports three types of messages
    Controller-to-Switch
      These messages are initiated by the controller and, in some cases, require a response from the switch
      This class of messages enables the controller to manage the logical state of the switch, including its configuration and details of flow- and group-table entries

## Slide 104: OpenFlow Protocol
      Also included in this class is the Packet-out message
      This message is used when a switch sends a packet to the controller and the controller decides not to drop the packet but to direct it to a switch output port
    Asynchronous
      These types of messages are sent without solicitation from the controller
      This class includes various status messages to the controller
      Also included is the Packet-in message, which may be used by the switch to send a packet to the controller when there is no flow-table match

## Slide 105: OpenFlow Protocol
    Symmetric
      These messages are sent without solicitation from either the controller or the switch
      They are simple yet helpful
      Hello messages are typically sent back and forth between the controller and switch when the connection is first established
      Echo request and reply messages can be used by either the switch or controller to measure the latency or bandwidth of a controller switch connection or just verify that the device is operating
      The Experimenter message is used to stage features to be built into future versions of OpenFlow

## Slide 106: OpenFlow Protocol

## Slide 107: OpenFlow Protocol
The OpenFlow protocol enables the controller to manage the logical structure of a switch, without regard to the details of how the switch implements the OpenFlow logical architecture

## Slide 108: OpenFlow Only or Enabled
With OpenFlow equipment the devices can be OpenFlow only or they can be just OpenFlow enabled
With OpenFlow enabled equipment both OpenFlow and a proprietary protocol will work on the devices
Most of the traditional device manufacturers have gone this way

## Slide 109: Cisco Protocol
Equipment manufacturers are naturedly reluctant to support commodity hardware and open source protocols as there is little profit there
To both combat this move as well as to extend it they have created their own control protocols
For example Cisco’s is called onePK – Cisco ONE platform kit

## Slide 110: Cisco Protocol
This allows Cisco to support OpenFlow but also expand on it while protecting its installed base and future hardware sales

## Slide 111: Scaling a SDN
Will SDN work in large distributed networks
Centralization of the control function does not mean one has to use a single controller
As Tiwari points out this can be a logically centralized controller that physically exists in multiple data centers with the redundancy that this implies

## Slide 112: Scaling a SDN
The authors suggest that to do so the placement and reliability of the controllers are the central concerns
A study conducted on a large emulated network with 100,000 hosts and up to 256 switches, revealed that all OpenFlow controllers were able to handle at least 50,000 new flow requests per second in each of the experimental scenarios

## Slide 113: Scaling a SDN
Multiple controllers may be used to reduce the latency or increase the scalability and fault tolerance of an OpenFlow SDN deployment
OpenFlow allows the connection of multiple controllers to a switch, which would allow backup controllers to take over in the event of a failure

## Slide 114: SDN Domains
Stallings notes that in a large enterprise network, the deployment of a single controller to manage all network devices would prove unwieldy or undesirable
A more likely scenario is that the operator of a large enterprise or carrier network divides the whole network into numerous nonoverlapping SDN domains

## Slide 115: SDN Domains

## Slide 116: SDN Domains
He goes on to state that the reasons for using SDN domains include the following
Scalability
  The number of devices an SDN controller can feasibly manage is limited
  Thus, a reasonably large network may need to deploy multiple SDN controllers

## Slide 117: SDN Domains
Privacy
  A carrier may choose to implement different privacy policies in different SDN domains
Incremental deployment
  A carrier’s network may consist of portions of traditional and newer infrastructure
  Dividing the network into multiple, individually manageable SDN domains allows for flexible incremental deployment

## Slide 118: An Alternate View
Nadeau and Gray argue that the concept behind SDN is neither new or original
Further they believe there are significant issues surrounding the concept as well
For example

## Slide 119: An Alternate View
  One of the tenets expressed early in the introduction of SDN is the potential advantage in the separation of a network device’s control and data planes
  This separation affords a network operator certain advantages in terms of centralized or semi-centralized programmatic control

## Slide 120: An Alternate View
  It also has a potential economic advantage based on the ability to consolidate in one or a few places what is often a considerably complex piece of software to configure and control onto less expensive, so-called commodity hardware

## Slide 121: An Alternate View
In their view OpenFlow is just one of a number of network virtualization methods
As they note
  There are a few variations on the SDN theme and some oft spoken components to be considered
  OpenFlow is one, which architecturally separates the control and management planes from the data plane on the networking device

## Slide 122: An Alternate View
  This allows for a centralized controller to manage the flows in the forwarding nodes
  However, OpenFlow is only one protocol and one element of SDN
  There are many other protocols now
  Some examples include I2RS, PCE-P, BGP-LS, FORCES, OMI, and NetConf/Yang
  All of these are also open standards

## Slide 123: An Alternate View
  What’s important to remember is that SDN is not a protocol; it’s an operational and programming architecture

## Slide 124: An Alternate View
Whereas as the other sources support and promote the concept of and suggested method of implementation as laid out by the work at Stanford, Nadeau and Gray suggest that the pure approach suggested by the Stanford work will never be deployed since no organization will replace all of their equipment
Here is their continuum of SDN

## Slide 125: An Alternate View

## Slide 126: An Alternate View
Will SDN be revolutionary or evolutionary
Nadeau and Gray argue that
  At one end of the spectrum of answers to the question of where to put the control plane lies the revolutionary proponents, who propose a clean slate approach in which the control plane of a network is completely centralized

## Slide 127: An Alternate View
  In most cases, this extreme approach has been tempered to be, in reality, a logically centralized approach due to either scale or high availability requirements that make a strictly centralized approach difficult
  In this model, no control plane functions effectively exist at a device; instead, a device is a dumb - albeit fast - switching device under the total control of the remotely located, centralized control plane

## Slide 128: An Alternate View
  Toward the middle of the spectrum, the evolutionary proponents see domains within the general definition of networks in which a centralized control paradigm provides some new capabilities, but does not replace every capability nor does it completely remove the control plane from the device

## Slide 129: An Alternate View
It should be kept in mind that Nadeau and Gray work for Juniper
One of the forwards for the book was written by the CTO of Cisco

## Slide 130: Another View
In a blog post from 16 September 2014 Ivan Pepelnjak summaries the state of SDN as follows
  After the initial onslaught of SDN washing, four distinct approaches to SDN have started to emerge, from centralized control plane architectures to smart reuse of existing protocols

## Slide 131: Another View
    Control-Data Plane Separation
      The “original” (or shall I say orthodox) SDN definition comes from Open Networking Foundation and calls for a strict separation of control- and data planes, with a single control plane being responsible for multiple data planes
      That definition, while serving the goals of some ONF founding members, is at the moment mostly irrelevant for most enterprise or service provider organizations, who cannot afford to become a router manufacturer to build a few dozens of WAN edge routers

## Slide 132: Another View
      … and based on the amount of resources NEC invested in ProgrammableFlow over the last years, it’s not realistic to expect that we’ll be able to use OpenDaylight in production environments any time soon (assuming you’d want to use an architecture with a single central failure point in the first place)
      I am positive there will be people building OpenFlow controllers controlling forwarding fabrics, but they might eventually realize what a monumental task they undertook when they’ll have to reinvent all the wheels networking industry invented in the last 30 years including:

## Slide 133: Another View
        Topology discovery;
        Fast failure detection (including detection of bad links, not just lost links);
        Fast reroute around failures;
        Path-based forwarding and prefix-independent convergence;
        Scalable linecard protocols (LACP, LLDP, STP, BFD …)

## Slide 134: Another View
    Overlay virtual networks
      The proponents of overlay virtual networking solutions use the same architectural approach that worked well with Telnet (replacing X.25 PAD), VoIP (replacing telephone exchanges) or iSCSI, not to mention the global Internet – reduce the complexity of the problem by decoupling transport fabric from edge functionality (a more cynical mind might be tempted to quote RFC 1925 section 2.6a)

## Slide 135: Another View
      The decoupling approach works well assuming there are no leaky abstractions (in other words, the overlay can ignore the transport network – which wasn’t exactly the case in Frame Relay or ATM networks). Overlay virtual networks work well over fabrics with equidistant endpoints, and fail as miserably as any other technology when being misused for long-distance VLAN extensions

## Slide 136: Another View
    Vendor-specific APIs
      After the initial magical dust of SDN-washing settled down, only a few vendors remained standing (I’m skipping those that allow you to send configuration commands in XML envelope and call that programmability)
      Arista has eAPI (access to EOS command line through JSON-formatted REST calls) as well as the capability to install any Linux component on their switches, and use programmatic access to EOS data structures (sysdb)
      Cisco’s OnePK gives you extensive access to inner working of Cisco IOS and IOS XE

## Slide 137: Another View
      NX-API does the same for Nexus 9K (it's so refreshing to get consistently incompatible APIs from the same vendor) and is supposed to become available on other Nexus platforms
      Juniper has some SDK that’s safely tucked behind a partner-only regwall
      Just the right thing to do in 2014

## Slide 138: Another View
    Reuse of existing protocol
      While the vendors and the marketers were fighting the positioning battles, experienced engineers did what they do best – they found a solution to a problem with the tools at hand
      Many scalable real-life SDN implementations (as opposed to works great in PowerPoint ones) use BGP to modify forwarding information in the network (or even filter traffic with BGP FlowSpec), and implement programmatic access to BGP with something like ExaBGP

## Slide 139: Another View
Which one should I use?
  You know the answer: it depends (and I'll got into more details in my SDN Deployment Considerations webinar)
  If you’re planning to implement novel ideas in the data center, overlay virtual networks might be the way to go (more so as you can change the edge functionality without touching the physical networking infrastructure)

## Slide 140: Another View
  Do you need flexible dynamic ACLs or PBR? Use OpenFlow (or even better, DirectFlow if you have Arista switches)
  Looking for a large-scale solution that controls the traffic in LAN or WAN fabric? BGP might be exactly what you need
  Finally, you can do things you cannot do with anything else with some vendor APIs (but do remember the price you’re paying)

## Slide 141: Summary
What will happen with SDN
Good question