## Slide 1: DAS Last Update 2012.03.19
1.9.0

## Slide 2: Objectives of This Section
Learn how to
  Recognize what DAS is
  Know when to use DAS
  Use RAID and the levels of RAID

## Slide 3: What is DAS
DAS – Directly Attached Storage is just another way of talking about hard drives contained inside a server or in a separate box directly attached to the server
This distinction is made and the term DAS is used only in relation to the other forms of storage that will be discussed in the next few presentations
In other words NAS, SAN, and SSP

## Slide 4: What is DAS
So when you think of DAS, just think of a file server
DAS can be one or more drives inside the server using SCSI, SAS – Serial Attached SCSI, SATA, or IDE or in a box directly attached to the server using SCSI, SAS – Serial Attached SCSI, or eSATA
In this case these drives can be in one of two configurations

## Slide 5: What is DAS
The first is JBOD – Just a Bunch of Disks
  This is a collection of drives of the same or different size that contain the applications and data
  This information can be contained on a single drive or it can span drives
This method does nothing for fault tolerance, which is the ability to not loose data when a drive dies

## Slide 6: What is DAS
The second way to configure a DAS is to use RAID – Redundant Array of Inexpensive Disks
In this case capacity, fault tolerance, or both are increased
RAID has been used since 1989

## Slide 7: RAID
RAID can be done in software or hardware
Use the hardware version as discussed below
Many server operating systems support software RAID, but using it is a bad idea
  First is its reliance on the host CPU
  Since software RAID runs on the host processor and uses system memory resources, there is a performance penalty

## Slide 8: RAID
  Every compute cycle used to run software RAID drains bandwidth from the system's host processor and limits it from performing other tasks
  Software RAID is also not bootable
  Since the RAID functionality is contained within the operating system, it cannot mirror the operating system itself
  Software RAID offers no protection from errors within the operating system

## Slide 9: RAID
  Therefore, it cannot provide as high a level of reliability as RAID implemented outside the operating system
To provide faster performance and greater fault tolerance drives can be linked together in a RAID array

## Slide 10: RAID
Simple RAID subsystems are just a collection of disk drives in a cabinet that are all connected to a single controller board
The RAID controller orchestrates read and write activities in the same way a controller for a single disk drive does, and treats the array as if it were in fact a single drive

## Slide 11: RAID
RAID management software that resides in the host system provides the means to manage data to be stored on the RAID subsystem
RAID can be optimized for performance, the highest capacity, fault tolerance or a combination of two or three of the above

## Slide 12: RAID
Several RAID levels have been defined and standardized in accordance with those general optimization parameters

## Slide 13: RAID 0
An array configured as RAID Level 0 is an array optimized for performance, but at the expense of fault tolerance
RAID Level 0 is achieved through a method known as striping
The collection of drives in a RAID Level 0 array has data laid down in such a way that it is organized in stripes across all the drives

## Slide 14: RAID 0
A typical array can contain any number of stripes, usually in multiples of the number of drives present in the array
As an example, imagine a four-drive array configured with 12 stripes - four stripes of designated space per drive
Stripes 0, 1, 2 and 3 would be located on corresponding hard drives 0, 1, 2 and 3

## Slide 15: RAID 0
Stripe 4, however, appears on a segment of drive 0 in a different location than Stripe 0; stripes 5 through 7 appear accordingly on drives 1, 2 and 3
The remaining four stripes are allocated in the same even fashion across the same drives

## Slide 16: RAID 0
The reason RAID 0 is a performance-enhancing configuration is that striping enables the array to access data from multiple drives at the same time
In other words, since the data is spread out across a number of drives in the array, it can be accessed faster because it's not bottled up on a single drive

## Slide 17: RAID 0
This is especially beneficial for retrieving very large files, since they can be spread out effectively across multiple drives and accessed as if it were the size of any of the fragments it is organized into on the data stripes

## Slide 18: RAID 0
The downside to RAID Level 0 configurations is that it sacrifices fault tolerance, raising the risk of data loss because no room is made available to store redundant data
If one of the drives in the RAID 0 fails for any reason, there is no way of retrieving the lost data

## Slide 19: RAID 1
The RAID Level 1 configuration employs what is known as disk mirroring, and is done to ensure data reliability or a high degree of fault tolerance
RAID 1 also enhances read performance, but the improved performance and fault tolerance come at the expense of available capacity in the drives used

## Slide 20: RAID 1
In a RAID Level 1 configuration, the RAID management software instructs the controller to store data redundantly across a number of the drives in the array
In other words, the same data is copied and stored on different disks or mirrored to ensure that, should a drive fail, the data is available somewhere else within the array

## Slide 21: RAID 1
In fact, all but one of the drives in a mirrored set could fail and the data would remain intact
A read performance gain can be realized if the redundant data is distributed evenly on all of the drives of a mirrored set within the subsystem

## Slide 22: RAID 1
The number of read requests and total wait times both drop significantly
Inversely proportional to the number of hard drives in the RAID
For example, three read requests could be made

## Slide 23: RAID 1
The first request looks for data in the first block of the virtual drive, the second request goes to block 0, and the third seeks from block 2
Each request is then sent to the various drives
The RAID management software can assign each read request to an individual drive

## Slide 24: RAID 1
So that rather than having to handle the flow of each data stream one at a time the controller can send three data streams almost simultaneously, which in turn reduces system overhead

## Slide 25: RAID 5
This is the last of the most common RAID levels in use, and is probably the most frequently implemented
RAID Level 5 provides redundancy by interleaving parity check data with user data throughout the drive array
This allows the system to recover any lost data should a single drive fail

## Slide 26: RAID 5
This is done by using the parity data to recreate any data lost by failure of a single drive
Since all drives can be read simultaneously read performance is maximized

## Slide 27: RAID 5
Writing can be slower because of the need to also write parity information in addition to the
data
There is loss of storage space due to the need to store the parity information
For example in a set of five 18GB hard drives, which totals 90GB of space, only 72GB of actual data can be stored

## Slide 28: Parity
Here is what EMC says about parity from their book titled Information Storage and Management
  Parity information can be stored on separate, dedicated HDDs or distributed across all the drives in a RAID set
  Figure 3-4 shows a parity RAID

## Slide 29: Parity

## Slide 30: Parity
  The first four disks, labeled D, contain the data
  The fifth disk, labeled P, stores the parity information, which in this case is the sum of the elements in each row
  Now, if one of the Ds fails, the missing value can be calculated by subtracting the sum of the rest of the elements from the parity value

## Slide 31: Other RAID Levels
Some other RAID levels have been developed as custom solutions by independent vendors
These are not established standards
They have the usual risks of any proprietary solution

## Slide 32: Other RAID Levels
RAID Level 6, which emphasizes ultra-high data integrity
RAID Level 0 + 1 - also known as RAID Level 10 - which focuses on high I/O performance and very high data integrity
In this method the data is striped, then mirrored

## Slide 33: Forms of RAID
Here is a nice table from Storage magazine from May 2010 that shows all of the different types of RAID

## Slide 34: Forms of RAID

## Slide 35: Forms of RAID

## Slide 36: Other RAID Factors
RAID Level 53, which combines RAID Level 0 and 3 for uniform read and write performance
The final factor in a RAID system is the amount of cache - memory - on the RAID controller card
The more memory the better since this speeds performance

## Slide 37: Problems with DAS
DAS has limitations
Primarily it does not scale easily
It also cannot be separated very far from the server itself
This is why the other methods have been developed

## Slide 38: Problems with DAS
When the needs of the organization outgrow the size of the drive in the server, either a new server must be purchased, a bigger drive must be put in the server, or more drives must be added to the attached box
All of this produces downtime and management problems

## Slide 39: Problems with DAS
In particular you must manage the data on each server by its self
Each server will require that
  Volumes be setup
  Rights assigned to files and directories
  Data be backup
  And so on

## Slide 40: Lab
Let’s find a hot swappable RAID box