## Slide 1: Disk Interfaces Last Update 2011.04.14
1.9.0

## Slide 2: Objectives of This Section
Learn
  What disk interfaces are used in servers now and will be used in the future

## Slide 3: Types of Disk Interfaces
There are three types of disk interfaces that may be encountered in servers
Currently in wide use
  IDE ATA
  SCSI
  Fibre Channel

## Slide 4: IDE ATA
IDE – Integrated Drive Electronics also called ATA – Advanced Technology Attachment is the most widely used disk interface
It was designed to be offered in workstations so as to lower their cost
Over the last few years it is seeing more and more use in servers

## Slide 5: IDE ATA
The correct name for this interface is ATA, but everyone calls it IDE
This standard was developed in the late 1980s by the SFF – Small Form Factor Committee, a group made up of engineers from major drive manufacturers
At its basic level this is a 16-bit parallel path method

## Slide 6: IDE ATA
It connects the devices using a 40 pin unshielded ribbon cable
The cable length is limited to 18 inches
This interface is designed for data storage devices only
This is used in workstations and small servers

## Slide 7: IDE ATA
The current IDE standards include
  Ultra DMA/33, which transfers data at 33 MBps
  Ultra DMA/66 at 66 MBps
    It uses an 80-pin shielded cable
    So the old and new will diverge
  ATA/100 at 100 MBps also uses the 80-pin cable
  ATA/133 at 133 MBps

## Slide 8: IDE ATA
  Serial ATA with speeds from 150 to 600 MBps is the latest version

## Slide 9: Serial ATA
Interest in SATA - Serial ATA arose as the standard parallel ATA schemes run out of speed
Besides the speed increase another nice aspect is the cable used
It is smaller, as well as allowing for a longer distance of 1 meter

## Slide 10: Serial ATA
In this scheme all devices are seen as masters, this simplifies configuration
Serial ATA allows for hot swapping of drives, which means the computer does not have to be turned off first

## Slide 11: SCSI
SCSI – Small Computer Systems Interface is the dominate disk interface seen in servers
This is another parallel path interface
It uses unshielded ribbon cables with a varying number of pins depending on the type of SCSI it is

## Slide 12: SCSI
Maximum cable length is 3 meters for normal SCSI and 25 meters for Differential SCSI
The SCSI chain must be terminated at each end
Termination in this case is a resistor
Many newer devices figure out they are on the end and self terminate

## Slide 13: SCSI
This is particularly true of controller boards
But you must be sure the chain is properly terminated or errors in data will occur
Each device in the SCSI chain has a number to identify it
This is the device number
  For 8 bit SCSI it ranges from 0 to 7
  For 16 bit SCSI it ranges from 0 to 15

## Slide 14: SCSI
SCSI naming is quite confused
In general it proceeds this way
There are three major parameters that define a SCSI connection and distinguish the various versions
  Bus width
  Bus speed
  Type of electrical signaling

## Slide 15: SCSI-1
SCSI-1 is the original version of SCSI
It uses an 8-bit-wide data bus running at 5 MHz
The transfer rate of up to 5 MBps

## Slide 16: SCSI-2
SCSI-2 introduced two major changes
The first, called Fast SCSI, doubled the bus speed to 10 MHz, which doubled the maximum transfer rate of the 8-bit bus to 10 MBps
It also introduced a 16-bit bus, known as Wide SCSI, which again doubled throughput

## Slide 17: SCSI-2
Combine the two new features and you get Fast/Wide SCSI, capable of up to 20-MBps throughput

## Slide 18: SCSI-3
SCSI-3, also known as UltraSCSI, doubled the bus speed to 20 MHz
This gave 8-bit UltraSCSI a 20 MBps transfer rate and Wide UltraSCSI a 40 MBps rate

## Slide 19: SCSI Signaling
The original SCSI specification called for single-ended signaling
That is each bit is sent as a signal over an individual wire
With this system, SCSI-1 cables could stretch up to 6 meters
SCSI-2 was limited to just 3 meters

## Slide 20: SCSI Signaling
UltraSCSI and Wide UltraSCSI could handle 3-meter runs, but not with more than four devices
Eight devices limited the cable to 1.5 meters
Differential signaling, which uses two wires for each bit, changed this

## Slide 21: SCSI Signaling
The extra circuitry used for differential signaling is more expensive and requires more power
The big advantage is that differential SCSI buses can be as long as 25 meters

## Slide 22: SCSI
The LUN is the Logical Unit Number from 1 to 7
This number only applies to multifunction devices
Of which I have never seen an example
So in most cases the SCSI device has a device number and a LUN of 0

## Slide 23: SCSI
Type | MBps | Cable Single | Cable Differential | Devices
SCSI-1 | 5 | 6 | 25 | 8
Fast SCSI | 10 | 3 | 25 | 8
Fast/WideSCSI | 20 | 3 | 25 | 16
UltraSCSI | 20 | 1.5 |  | 8
Wide Ultra SCSI | 40 | 1.5 | 25 | 8 or 16
Ultra2 SCSI | 40 |  | 25 | 8
Wide Ultra 2 SCSI | 80 |  | 25 | 16
Ultra 160 SCSI | 160 |  |  | 16
Ultra 320 SCSI | 320 |  |  | 16
Ultra 640 SCSI | 640 |  |  | 16

## Slide 24: Serial Attached SCSI
A new version of SCSI that abandons the parallel interface for a serial interface is Serially Attached SCSI
This solution is being positioned as faster than SATA and less costly than Fibre Channel

## Slide 25: Serially Attached SCSI

## Slide 26: Fibre Channel
Fibre Channel is called Fibre Channel instead of Fiber Channel because it was first designed for fiber optic cable, but later copper was used as well
So to remove the association with fiber cable the spelling was changed to fibre
Seems a little silly to me

## Slide 27: Fibre Channel
Fibre Channel takes the best part of SCSI the command set and adds higher data transfer rates and longer distances
In contrast to the other two types of disk interfaces this is a serial interface
It uses copper or fiber in half and full duplex modes

## Slide 28: Fibre Channel
When used to connect storage devices it uses an arbitrated loop called FC-AL implemented as a hub; similar in function to an Ethernet hub or a switched fabric; similar to an Ethernet switch
In the arbitrated loop approach bandwidth is shared among all the devices on the network

## Slide 29: Fibre Channel
In the switched fabric a port is dedicated to each device
Fibre Channel functions like a group of networked devices
The basic setup is a loop of media with connections for up to 126 devices
In practice only 30 devices are practical at present, but this is quite a few more than the typical fifteen drives in SCSI

## Slide 30: Fibre Channel
A second controller can be used to create a second connection to each device
One path can be dedicated to reads and the other to writes to reduce losses in speed due the overhead produced by the arbitration activity
In its original form Fibre Channel was used to connect the LAN to the SAN

## Slide 31: Fibre Channel
The SAN still used SCSI for the storage devices themselves
Manufacturers are now starting to use Fibre Channel for all of the connections including the drives
Why not use SCSI for SANs
SCSI does have the required high transfer rate

## Slide 32: Fibre Channel
It is also limited to a 25-meter cable length at best
SCSI has higher overhead in that it requires a handshake and an acknowledgement for each byte transferred
Fibre Channel uses a 2048 byte packet to transfer data

## Slide 33: Fibre Channel
This larger packet is more efficient in that it sends more data before an acknowledgement is required
Fibre Channel is not a standard, therefore Interconnection can be a problem
The cost of Fibre Channel is higher compared to SCSI

## Slide 34: Fibre Channel
Some vendors think Ethernet will overtake both SCSI and Fibre Channel as Fibre Channel can also be carried over Ethernet links

## Slide 35: iSCSI
With iSCSI native SCSI commands are carried using TCP/IP protocols
This approach is gaining in popularity as it runs over normal cabling rather than the special purpose Fibre Channel cables

## Slide 36: Who Use What
Here is a graph from the April 2011 issue of Storage magazine showing what is most commonly used

## Slide 37: Who Use What