## Slide 1: LAN Design Evolution
Last Update 2011.07.05
1.2.0

## Slide 2: Objectives
Learn about basic LAN design

## Slide 3: Organization Size
Books and articles in the trade press would make you think that every organization in the country is huge
That each one of these has a highly complex network with layer after layer of equipment
In reality most organizations are fairly small

## Slide 4: Network Size
The network needed by most organizations is therefore also fairly small
Keep in mind that a single broadcast domain can work just fine with anywhere from 200 to 1,000 active users depending on the nature of the network traffic

## Slide 5: Organization Size
Let’s see how many firms and the dependent establishments there are at various sizes
Here is data from 2004 from the Census Bureau

## Slide 6: Organization Size

## Slide 7: SOHO
Let’s look first at the small firms
Those with 1 to 19 employees
As this table shows there are 4,453,810 of those
Clearly none of these need more than a single local area network consisting of a single switch or hub, a Server or NAS box, and a printer

## Slide 8: SMB
Small and Medium sized businesses are defined as those with 500 or fewer employees
There are 612,893 of those
No doubt an organization with up to 500 staff in a single location could also work well with a single local area network, a set of switches, a server, maybe separate storage, and a number of printers

## Slide 9: SMB
This too is not a very complicated setup

## Slide 10: Large
This leaves just 37,629 organizations with more than 500 employees out of over 5 million total firms

## Slide 11: Do Not Over Complicate
What is the point to this discussion
To point out to you to not over complicate this
A basic, simple, single layer network design will work for over 99 percent of all firms

## Slide 12: Hierarchical Network Design
The best method to use when designing a network is the top down network design methodology detailed in Top Down Network Design by Priscilla Oppenheimer
The methodology Cisco suggests in this chapter is an abbreviated version of the top down approach

## Slide 13: Hierarchical Network Design
This discussion will provide you with a solid basis for further study of this preferred design methodology
As the book points out this model divides the network into three distinct layers
  Access
  Distribution
  Core

## Slide 14: Hierarchical Network Design
In practice most organizations only use the first two layers, with the smallest organizations collapsing even these two layers into one
Only the largest entities need all three layers
A judicious use of these layers will create a network design that can be grown in size indefinitely

## Slide 15: Hierarchical Network Design
Let’s look at each of these three layers of a hierarchical network design

## Slide 16: Access Layer
The access layer is where all end devices connect to the network
End devices range from PCs to printers to wireless access points, and even routers
Any device that connects using a NIC typically
No redundancy exists at the access layer

## Slide 17: Distribution Layer
The distribution layer aggregates the data from the access layer
This layer also controls the flow of traffic using policies
Broadcast domains are defined at the access layer edge of this layer
High availability through redundant devices is required at this layer

## Slide 18: Core Layer
The core layer is designed to move data at high speed
This layer moves data as fast as possible between the various distribution layer devices
High availability and redundancy are critical to this layer

## Slide 19: Hierarchical Network Model

## Slide 20: Hierarchical Network Design
Several benefits are listed for this design model including
  Scalability
  Redundancy
  Performance
  Security
  Manageability
  Maintainability

## Slide 21: Scalability
Scalability refers to what is needed today as well as the future
The ability to grow, for example
  Cabling is meant to last for 10 years
  Switches and routers are meant to last for 2 to 5 years, since it is easier to change these

## Slide 22: Redundancy
Redundancy is how a network maintains high availability
Availability is uptime
It is expressed as a percent and is related to the time period
Such as

## Slide 23: Availability Downtime Allowed Per Week in Minutes Based on a 24 Hour Day 99.7% at 30 minutes looks ok, what if all at one time 95% sounds good, but 504 minutes doesn’t
99.999 | .10 |  | 99 | 101
99.95 | 5 |  | 98 | 202
99.9 | 10 |  | 97 | 302
99.7 | 30 |  | 96 | 403
99.5 | 50 |  | 95 | 504

## Slide 24: Performance
Performance is a key indicator for most projects
In some cases it is only that
  “No one complains”
In most cases it is more definitive

## Slide 25: Performance
Common performance measures include
  Capacity v Throughput
  Bandwidth Utilization
  Offered Load
  Accuracy
  Efficiency
  Latency
  Response
  Device CPU Utilization

## Slide 26: Performance
Capacity
  This is the data carrying capacity of a circuit
    Usually measured in bits per second
Throughput
  This is the quantity of error free data transmitted per unit of time
  This is normally the packets per second
Bandwidth Utilization
  The percent of total available capacity in use

## Slide 27: Performance
Offered Load
  This is the sum of all the data all network devices have ready to send at a particular time
Accuracy
  Exactly what goes out gets to the other end
  To check accuracy use a network analyzer to check the CRC on received frames

## Slide 28: Performance
  Track the number of frames received with a bad CRC every hour for one or two days
  It is normal for errors to increase as network utilization goes up
  So check the number of errors against the network load
  The error rate is acceptable if there are not more than one error per megabyte of data

## Slide 29: Performance
Efficiency
  How much overhead is required to deliver an amount of data
  How large a packet can be used
    Larger better
    Too large means too much data is lost if a packet is damaged
    How many packets can be sent in one bunch without an acknowledgment

## Slide 30: Performance
Latency
  This is the delay in transmission
  or
  The time that passes from when a user expects something to appear, to when it does appear
  Instantaneous response is the only goal

## Slide 31: Performance
Response
  Related to latency, but also a function of the application and the equipment the application is running on
  Most users expect to see something on the screen in 100 to 200 milliseconds

## Slide 32: Performance
Device CPU Utilization
  High utilization on a device may create a bottleneck as the device will be unable to handle the offered load regardless of the bandwidth coming in or going out of the device
  In other words, the device becomes the bottleneck

## Slide 33: Security
In assessing the amount of security, balance the risks against the cost
There is no point in locking things down so tight, nothing can be used
Common risks include
  Use of resources
  Loss of data
  Alteration of data
  Denial of service

## Slide 34: Manageability
Manageability refers to how easy will it be to monitor the network
To check for
  Performance problems
  Errors
  Security problems
  Configuration
  Accounting, if chargeback used

## Slide 35: Maintainability
How difficult will it be for the network management team to run the network you will be leaving
How difficult will it be for the network team to change the network by themselves

## Slide 36: Network Design Considerations
When designing the network the layout and subsequently the devices used are dictated by
  Location of network users
  Location of the data stores
  QoS requirements

## Slide 37: Network Design Considerations
To design a network some basic information is required
The first thing to determine is where the users of the data are located
Users are not by level or job function
Rather they are determined by what use they are making of the network
For example

## Slide 38: Network Design Considerations
In a law firm the users are not
  Lawyers
  Paralegals
  Secretaries
The network does not care how much they are paid or what their function is
Rather the users are
  Word processing users
  Internet users

## Slide 39: Network Design Considerations
Once the users are located the next step is to decide where their data is stored
This data is for example
  Hard drives in one form or the other
  Internet access
With the ends points in hand the next question is how large of a pipe is needed to connect these two points

## Slide 40: Network Design Considerations
The amount of traffic can be determined by measurement or estimation
With this information in hand a topology map is created
Such as

## Slide 41: Network Topology

## Slide 42: Lab
Let’s build a hierarchical network design
Start Packet Tracer
Open file e3-1243.pka

## Slide 43: Network Diameter
Other things to consider include the diameter of the network
This is the number of devices that a frame most cross from one end device to another
The smaller the diameter the less latency
Proper use of the three layers in the hierarchical model will prevent network diameter from being a problem

## Slide 44: Network Diameter

## Slide 45: Types of Traffic
In current large networks in addition to data, voice and video traffic is carried over the same set of wires
This requires the traffic be prioritized
QoS – Quality of Service places the time sensitive traffic in front of the traffic that can wait

## Slide 46: Devices Used in LANs
At all three layers switches are commonly used as the connection point
As such their selection requires careful consideration at each level of the hierarchy
Common features include the following

## Slide 47: Switch Features
Form Factor
Performance
Link aggregation
PoE
Layer 3

## Slide 48: Form Factor
The switch may be
  Fixed
  Stackable
  Modular

## Slide 49: Fixed Configuration
A fixed configuration switch cannot be physically altered or added to

## Slide 50: Fixed Configuration

## Slide 51: Stackable
A stackable switch cannot be altered, but it can be added to by attaching other switches in such a way that several switches appear as one

## Slide 52: Stacking
If the network runs out of ports more can be added by stacking another switch on top of the existing one
Switches use proprietary cables for this
There will be a limit on the number of switches that can be stacked
In the Cisco StackWise method the limit is nine

## Slide 53: Stacking
Stacking Cables

## Slide 54: Modular
A modular switch allows blades to be added to a single chassis when additional capacity is required
Up to the capacity of the chassis, ports can be added by just inserting more blades

## Slide 55: Modular

## Slide 56: Modular

## Slide 57: Performance
Main performance measures include
  Port Density
  Forwarding rate

## Slide 58: Port Density
The port density is the number of ports on a single switch
Typically this is four to 96 although some switches can support many more

## Slide 59: Forwarding Rate
The forwarding rate is how quickly the switch can process frames
This is in frames per second
The desired performance is wirespeed where the switch can process any frame presented
For a 24 port Gigabit switch this would be 24 Gbps

## Slide 60: Forwarding Rate
Wirespeed switches are seen at the distribution and core layers

## Slide 61: Link Aggregation
In link aggregation up to eight ports are bound together to move the traffic from one switch to another one
Etherchannel is the Cisco method for this

## Slide 62: PoE
To power devices such as access points and IP phones a switch needs to be able to generate electrical power as well as send and receive data
PoE – Power Over Ethernet does this
Not all switches support PoE

## Slide 63: Layer 3 Functions
To interconnect the various broadcast domains in the hierarchical network a layer 3 device is needed
To avoid having to use a router for this layer 3 switches were developed

## Slide 64: Development of Switches
Let’s also look at the development and use of switches over the years
The development of switches has progressed over the years as new technologies appear
Let’s look at the various designs that have been used to create networks to see why switches were developed and how they are used

## Slide 65: Point-to-Point Backbone
In the first example a LAN that originally covered only a single floor has been extended to cover two floors using a point-to-point backbone design

## Slide 66: Point-to-Point Backbone

## Slide 67: Collapsed Backbone
In the next design we see the single LAN extended to even more floors
All of the servers are now centralized in a single location to ease management
In this collapsed backbone design all of the devices are still in a single collision domain and a single broadcast domain, since hubs at layer 1 are used
This is called a flat design

## Slide 68: Collapsed Backbone

## Slide 69: Hierarchical Backbone Design
A flat design does not scale well
As more and more devices are added to the shared domains – collision and broadcast – things start to slow down
The solution is to introduce hierarchy to the design so as to divide up these domains

## Slide 70: Bridged Backbone
In this first example of a hierarchical design a layer 2 device, in this case a bridge, is used to divide the collision domain

## Slide 71: Bridged Backbone

## Slide 72: Routed Backbone
Bridges worked well for isolating collisions, but did nothing for the broadcast domain
In the next example a single router was introduced, as a layer 3 device, to isolate the broadcast domains

## Slide 73: Routed Backbone

## Slide 74: Switched Backbone
Routers were not the best device for this so layer 3 switches were created to handle this function
Further hubs are now replaced with layer 2 switches on each floor so as to divide up the shared collision domain that still existed on each floor when hubs are used there

## Slide 75: Switched Backbone

## Slide 76: Switched Backbone
In this example the PCs and servers are connected to the layer 2 switches using UTP
These are the ports across the bottom

## Slide 77: Switched Backbone
The backbone connections are fiber optic cable
A fiber module is inserted in the top part of the layer 2 switch for connection to the layer 3 switch on the bottom floor

## Slide 78: Switched Backbone

## Slide 79: Switched Backbone
On the bottom floor, where all of the layer 2 switches connect together, a layer 3 switch is placed
There must be a module for each layer 2 switch

## Slide 80: Switched Backbone
And close up

## Slide 81: Backbone
Fiber Optic Cable backbone connection

## Slide 82: Switches by Layer
Next we will look at the desirable characteristics of switches at each layer of the hierarchical model

## Slide 83: Access Layer Switches
An access layer switch needs to support
  VLAN creation
  Link aggregation
  QoS
and perhaps
  Port security
  PoE
Cost per port is a significant consideration at this layer

## Slide 84: Distribution Layer Switches
This is the layer where all the work is done
These multilayer switches – layers 2 and 3 – must be able to interconnect the VLANs created at the access layer
Processing power is the main consideration here, not cost
Layer 3 functions are also used at this layer to implement Access Control Lists

## Slide 85: Distribution Layer Switches
These ACLs are used to control the flow of traffic
Link aggregation and QoS as at the access layer are also needed here

## Slide 86: Core Layer Switches
Speed is the major consideration at the core layer
Of course these must also support the same QoS and link aggregation of the other layers