## Slide 1: VLANs
Last Update 2015.05.12
1.9.0

## Slide 2: Objective
Learn what a VLAN is and how to configure one

## Slide 3: What is a VLAN
Another way to separate a LAN that gets too large, besides a physical basis, is to divide it logically using a VLAN
A VLAN is a collection of nodes grouped together in a broadcast domain without necessarily being physically near each other

## Slide 4: What is a VLAN
A VLAN is a single or stack of switches that instead of connecting to a single network can be divided port by port into distinct networks merely by configuring the switch
The standard for VLANs is 802.1Q

## Slide 5: When to Use a VLAN
The main reasons to divide a network are
  Maintain security
  Traffic management
  Control broadcast traffic

## Slide 6: Security
Security is another concern these days as we find more and more security holes on the inside of the network
When a group of users belongs to the same broadcast domain, all of the network traffic generated within that broadcast domain is accessible by each user

## Slide 7: Security
Thus, if a user is running a network analyzer, they can see every frame that crosses the network
Security issues arise when programs send data that needs to be protected, such as payroll data

## Slide 8: Security
For example, if all human resource computers are assigned to a VLAN, access to that virtual network could be limited to only those computers that are part of the HR department
This is done by restricting which MAC addresses are allowed access to any VLAN

## Slide 9: Security
Keeping track of which MAC address is assigned to a particular VLAN and switch port can be a difficult task of course

## Slide 10: Traffic Management
One can also look at a VLAN in terms of the use, such as
  Data
  Voice
  Video
  Management
This use might be for ease of network management or for QoS reasons

## Slide 11: Control of Broadcast Traffic
Layer 3 devices block broadcasts from traveling between network segments
However, in a flat, switched – using layer 2 switches - network, broadcasts travel throughout the entire network and are seen by every PC connected to the wire
In a large LAN, broadcasts can overwhelm the network and eventually lead to network failure

## Slide 12: Control of Broadcast Traffic
By dividing switch ports into VLANs, separate broadcast domains are created without using layer 3 devices
For example, a single switch, that supports this function, with say 24 ports
Ports 1 through 12 would be on one VLAN and users on ports 13 through 24 would be on another VLAN

## Slide 13: Control of Broadcast Traffic
Using this scenario, if all groups were generating the same amount of broadcast traffic, you would cut the broadcasts seen by each switch port in half, without having to buy any additional switches

## Slide 14: VLANs

## Slide 15: VLAN ID Ranges
Basic VLAN IDs are 1 to 1005
VLAN 1 is the default VLAN which always exists
IDs 1002 through 1005 are reserved for Token Ring and FDDI VLANs, which of course no longer exist
IDs 1 and 1002 to 1005 are automatically created and cannot be removed

## Slide 16: VLAN ID Ranges
There are also extended range VLANs
These are identified by a VLAN ID between 1006 and 4094
These support fewer VLAN features than normal range VLANs
VTP as explained later cannot deal with extended range VLANs

## Slide 17: VLAN Database File
Configurations are stored in a database file named vlan.dat
This file is stored in the flash memory of the switch
Erasing the startup config will not delete the vlans

## Slide 18: VLAN Database File
If you are brave, this is done by issuing the command
  delete flash:vlan.dat
It is better is to just go to global configuration mode, display the vlan database, and then remove each one by preceding the command that created each one with no in front

## Slide 19: VLAN Database File
For example
  enable
  show vlan brief
  config t
  no vlan 2
  no vlan 3
  end

## Slide 20: Types of VLANs
The only type of VLAN used today is a static port based VLAN where each port is assigned to a VLAN
By default all ports are assigned to VLAN 1, which is also the default native or management VLAN
VLAN 1 cannot be used for any other purpose

## Slide 21: Management VLAN
By default the management VLAN is VLAN 1
This can be changed
Cisco says to do this for security reasons
However, Cisco recommends changing to 99
Of course, everyone knows this, so what is the point, leave it at 1

## Slide 22: Native VLAN
The native VLAN is how a switch identifies frames that should be forwarded as normal frames
In other words, these are not VLAN frames
They are not modified when they are sent over the trunk links

## Slide 23: Management VLAN
If you change the management VLAN on one switch, but not on another switch, a common error will display on the CLI
This is Native VLAN Mismatch
This means the native or management VLAN on one or more switches differs from the other switches

## Slide 24: VLAN Trunk
A VLAN trunk is a point-to-point link between a switch port on one switch and a port on another device, such as a switch or router
The trunk carries the traffic of multiple VLANs over this single link
This allows VLANs to be extended across an entire network

## Slide 25: VLAN Trunk
802.1Q defines trunk formation on Fast Ethernet and Gigabit Ethernet ports

## Slide 26: Tagging Frames
As the standard Ethernet II frame format does not include a facility to indicate which if any VLAN a frame belongs to this marking is done using tags
The 802.1Q form of the tag is inserted into the frame as opposed to being placed at the beginning of the frame as the older Cisco ISL method used
Here is the 802.1Q tag format as shown in a graphic from Fluke Networks

## Slide 27: Tagging Frames

## Slide 28: Tagging Frames
The 802.1Q method inserts 4 bytes of information between the Source MAC Address and Type Fields
These fields are
  Type Code
  Priority
  CFI
  VLAN ID

## Slide 29: Tagging Frames
Let’s look at an example
Here one computer with an IP address of 10.0.0.1 is pinging another computer at IP address 10.0.0.2
In this display from Wireshark the VLAN tags look like a layer between the Data Link and Network layers

## Slide 30: Tagging Frames

## Slide 31: Tagging Frames
They are not
Wikipedia provides us with a nice graphic that shows where these extra fields go in the Ethernet II frame

## Slide 32: Tagging Frames

## Slide 33: Tagging Frames
Notice below in this display of an actual capture using Wireshark that the Type code has a hex number code of 8100 to indicate that the next protocol to be encountered is the VLAN protocol
Wireshark very nicely explains to use that this is telling us that 802.1Q Virtual LAN information will appear next

## Slide 34: Tagging Frames

## Slide 35: Tagging Frames
Sure enough there it is
The three fields that carry the information needed are
  Priority
  CFI
  ID
as summarized for us in the first line of the VLAN tag display

## Slide 36: Tagging Frames
In this case the
  Priority is 0
  CFI is 0
  VLAN is 20
What does all of this mean
Just below the summary line we see that
  The priority value in this example is Best Effort

## Slide 37: Tagging Frames
This priority refers to the 802.1p defined priorities of
  0 and 1 Best Effort
  2 Excellent Effort
  3 Critical Application
  4 Video
  5 Voice
  6 Internetwork Control
  7 Network Control

## Slide 38: Tagging Frames
Here is a frame with a higher priority
In this case 7 as STP is used for Network Control

## Slide 39: Tagging Frames

## Slide 40: Tagging Frames
The next field or tag is CFI
  This is the Canonical Format Indicator
  These days it is always 0
  The values are
    0 where the MAC address is in canonical format
    1 where the MAC address is in non-canonical format

## Slide 41: Tagging Frames
  In the old days this code was used for compatibility between Ethernet and Token Ring networks
Since Token Ring is dead, so is the code
The last field carries the number of the VLAN
In this case VLAN 20

## Slide 42: Tagging Frames
In the format that Wireshark uses to show us these tags the normal Type code field appears next
In this example the protocol to which the Data Link layer will hand the data to at the Network layer is the Internet Protocol or IP
Its code is 0800 in hex

## Slide 43: Frame Tags
Let’s look at some example frames where on the same setup we can see the native or management VLAN which is VLAN 1
The VLAN on the first switch which is VLAN 2
And the VLAN on the second switch which is VLAN 3
In this case the VLANs talk to each other through a Router on a Stick

## Slide 44: VLAN 1

## Slide 45: VLAN 2

## Slide 46: VLAN 3

## Slide 47: VLANs and Subnets
A VLAN should entirely encompass a single IP address subnet
There should be a one to one correspondence between VLANs and subnets
A VLAN should never cross a subnet boundary
A subnet should never be used on more than one VLAN

## Slide 48: VLAN Configuration
The basic VLAN configuration steps are
  Add the VLANs
  Assign the ports to the VLANs

## Slide 49: Add a VLAN

## Slide 50: Where Are the Ports

## Slide 51: Assign Ports to VLANs

## Slide 52: Verifying VLAN Configuration

## Slide 53: Changing a VLAN Assignment

## Slide 54: Deleting a VLAN

## Slide 55: Configuring VLAN Trunks

## Slide 56: Configuring VLAN Trunks
You can also restrict which VLANs may be sent over a trunk

## Slide 57: Configuring VLAN Trunks

## Slide 58: Lab
Let’s make some VLANs
Start Packet Tracer
Open file e3-3344.pka

## Slide 59: Remove a Trunk

## Slide 60: Voice VLAN
A single switch port can be carry the traffic for two VLANs even while set to access mode if the second VLAN is for voice traffic

## Slide 61: Verifying Trunk Configuration

## Slide 62: Common VLAN Problems

## Slide 63: VLAN Problem Isolation

## Slide 64: VLAN Problem Isolation

## Slide 65: Sources
The information on the frame alterations for VLANs was copied word for word from a paper on VLANs from Fluke Networks

## Slide 66: Lab
Let’s make some VLANs
Lab 3-1