## Slide 1: InterVLAN Routing
Last Update 2009.03.08
1.1.0

## Slide 2: Objectives
Learn about routing between VLANs

## Slide 3: Routing Between VLANs
All of these VLANs we have been talking about usually need to talk to each other
Since they are separate broadcast domains using separate subnets this requires they talk through a layer 3 device
Cisco explains how to do this in this chapter in a strange way

## Slide 4: Routing Between VLANs
They state that there are three theoretical ways to route between VLANs, then they proceed to say that the best way, a layer 3 switch, will not be discussed as it is beyond the scope of the book
Then what was the point in bringing up the topic if they did not intend to explain it totally

## Slide 5: Layer 3 Switch Routing
Even more the configuration of a layer 3 switch as a router for interVLAN routing is fairly simple
So we will cover it anyway
Of the other two methods they mention the first one where a separate port on the layer 3 device is used for each VLAN is a dim bulb idea so we will not cover it at all
The third method is a router on a stick

## Slide 6: Layer 3 Switch Routing
We will cover this method
So of the three Cisco mentions we will talk about
  Router on a Stick
  Layer 3 Switch Routing

## Slide 7: Router on a Stick
In a router on a stick configuration a router without any WAN interfaces is used
It has a single LAN interface that carries all of the traffic for the various VLANs using subinterfaces
This single port is configured as a trunk link between the switch and the router
A subinterface is a virtual interface created on the single physical interface

## Slide 8: Router on a Stick
Each VLAN gets its own subinterface

## Slide 9: Router on a Stick Configuration
  configure terminal
  interface f0/0.10
  encapsulation dot1q 10
  ip address 192.168.10.1 255.255.255.0
  interface f0/0.30
  encapsulation dot1q 30
  ip address 192.168.30.1 255.255.255.0
  interface f0/0
  no shutdown

## Slide 10: Lab
Let’s do a little Router on a Stick
Start Packet Tracer
Open file e3-6225.pka

## Slide 11: Layer 3 Switch Routing
To route VLANs on a layer 3 switch a SVI – Switch Virtual Interface is created
Here is a configuration from a paper on the Cisco web site
In this example a Cisco 3550 switch will be used
This is the sample network they used

## Slide 12: Sample Network Layout

## Slide 13: Configuration
Enabling routing
  Switch(config)#ip routing
Create the VLANs
  Switch#vlan database
  Switch(vlan)#vlan 2
  Switch(vlan)#vlan 3
  Switch(vlan)#vlan 10
  Switch(vlan)#exit

## Slide 14: Configuration
Assign an IP address to each VLAN
  Switch(config)#interface vlan2
  Switch(config-if)#ip address 192.168.2.1 255.255.255.0
  Switch(config)#no shutdown

## Slide 15: Configuration
Assign an IP address to each VLAN
  Switch(config)#interface vlan3
  Switch(config-if)#ip address 192.168.3.1 255.255.255.0
  Switch(config)#no shutdown

## Slide 16: Configuration
Assign an IP address to each VLAN
  Switch(config)#interface vlan10
  Switch(config-if)#ip address 192.168.10.1 255.255.255.0
  Switch(config)#no shutdown

## Slide 17: Configuration
Configure the interface to the default router
  Switch(config)#interface FastEthernet 0/1
  Switch(config-if)#no switchport
    To make the interface layer 3 capable
  Switch(config)#ip address 192.168.1.1 255.255.255.0
  Switch(config)#no shutdown

## Slide 18: Configuration
Setup the default route
  Switch(config)#ip route 0.0.0.0 0.0.0.0 192.168.100.1

## Slide 19: Layer 3 Switch Routing
That is all there is to it

## Slide 20: Lab
Let’s configure a Layer 3 Switch to do InterVLAN Routing
Start Packet Tracer
Open the file Configuring InterVLAN Routing.pka

## Slide 21: Lab
Let’s configure interVLAN routing
Lab 6-1