## Slide 1: Access Control Lists Last Update 2015.06.09 1.4.1

## Slide 2: Objectives
Learn what access control lists are and how to construct them

## Slide 3: Access Control Lists
An access control list is list of conditions that categorize packets
It takes the form of a collection of permit and deny statements that can
  Apply to just addresses
  or
  Upper layer information as well
It tells the router what types of packets to accept or deny

## Slide 4: How ACLs Work
Regardless of use how the access list is configured is the same
The difference is how it is applied
  Such as to a routing protocol instead of an interface

## Slide 5: How ACLs Work

## Slide 6: Form
ACLs are lists of instructions that are applied to a router’s interface in the form of a series of if-then statements
  If the condition is meet, then the action is taken
  If the condition is not meet, then the next statement is evaluated
ACLs are defined for each protocol enabled for an interface

## Slide 7: Reasons for Use
Access lists are used for the following
  Restrict access to a network
  Restrict access to the VTY ports
  Categorize packets for QoS
  Control which networks will or will not be advertised by dynamic routing protocols
  Provide traffic flow control
  Limit routing updates

## Slide 8: Process
This is a two part process
  Create the access list
  Apply the access list to the interface

## Slide 9: Creating an ACL
Order matters
  Each packet is compared to each statement until a match is found
  At that point comparison stops and action is taken
  Place the most restrictive statements at the top
  Place the least restrictive statements at the bottom

## Slide 10: What Do ACLs Look Like

## Slide 11: Creation Mode
ACLs are created at the global configuration level
For example
  Router(config)#

## Slide 12: Application Mode
ACLs are applied at the interface or subinterface level
For example
  Router(config-if)#

## Slide 13: Types of ACLs
There are two types of ACLs
  Standard
  Extended

## Slide 14: Creating a Standard ACL
No one uses a standard ACL as they are quite limited
They can only read the source IP address
But we will cover them anyway

## Slide 15: Creating a Standard ACL
Creating an ACL is a process of filling in the blanks
  Command to initiate an access list
  Number of the access list
  Action to take
  Source IP address to watch for
  Source wildcard mask

## Slide 16: Command
The command is always
  access-list

## Slide 17: Number of the Access List
The number of the access list indicates the protocol of interest
About the only numbers used are
  1-99
  1300-1999

## Slide 18: Action to Take
The actions that can be taken include
  deny
  permit

## Slide 19: Source IP Address
There are several ways the source IP address can be listed
  A specific IP address when one is of interest
  A network address when a range is of interest
  The word host then the IP address
    Which can take one of two forms
      host 192.168.1.23
      or just
      192.168.1.23

## Slide 20: Source IP Address
  The word any
    Any source IP address will match
      any = 0.0.0.0 255.255.255.255

## Slide 21: Source Wildcard Mask
To specify a network rather than just a host a wild card mask is needed
The word any
  Any source IP address will match
    any = 255.255.255.255

## Slide 22: Ending a Standard ACL
Must include as the last line
  permit any

## Slide 23: Standard ACL Creation
Here is an example of the whole process
  Router(config)# access-list 1 permit 192.168.1.1
  Router(config)# access-list 1 deny 192.168.1.2
  Router(config)# access-list 1 permit 192.168.1.0 0.0.0.0.255
  Router(config)# access-list 1 deny any
  Router(config)# interface s0
  Router(config-if)# ip access-group 1 in

## Slide 24: Extended ACLs
An extended access list is better
It can check
  Source IP address
  Destination IP address
  Protocol
  Port
This is basically a fill in the blanks process

## Slide 25: Creating an Extended ACL
Fill in the blanks
  Command to initiate an access list
  Number of the access list
  Action to take
  Protocol to restrict the action to
  Source IP address to watch for
  Source wildcard mask
  Destination IP address to watch for
  Destination wildcard mask
  Action to take
  Port or service name to watch for
  Log results

## Slide 26: Command
The command is always
  access-list

## Slide 27: Number of the Access List
The number of the access list indicates the protocol of interest
About the only numbers used are
  100-199
  2000-2699

## Slide 28: Action to Take
The actions that can be taken include
  deny
  permit
  dynamic

## Slide 29: Layer 3 or 4 Protocol
The protocol from layer 3 or 4 that will be acted upon is listed by number or by name
If a layer 3 protocol is listed, then nothing is specified at the application layer
If a layer 4 protocol is listed, then later an application layer protocol can be defined
The layer 4 protocol must match the application layer protocol

## Slide 30: Layer 3 or 4 Protocol
In other words, tcp goes with ftp, whereas utp goes with tftp and so on
  Protocol number
    0 to 255
  Protocol number by name
    Layer 3
      ip
      ipinip
      igrp
      eigrp
      ospf

## Slide 31: Layer 3 or 4 Protocol
      icmp
      igmp
      gre
      nos
    Layer 4
      tcp
      udp

## Slide 32: Source IP Address
There are several ways the source IP address can be listed
  A specific IP address when one is of interest
  A network address when a range is of interest
  The word host then an IP address which can take one of two forms
      host 192.168.1.23
      or just
      192.168.1.23

## Slide 33: Source IP Address
  The word any
    Then any source IP address will match
      any = 0.0.0.0 255.255.255.255

## Slide 34: Source Wildcard Mask
A wildcard mask as discussed below
The word any
  Any source IP address will match
    any = 255.255.255.255

## Slide 35: Destination IP Address
There are several ways the destination IP address can be listed
  A specific IP address when one is of interest
  A network address when a range is of interest
  The word host then an IP address
  The word any
    Any source IP address will match
      any = 0.0.0.0 255.255.255.255

## Slide 36: Destination Wildcard Mask
A wildcard mask as discussed below
The word any
  Any destination IP address will match
    any = 255.255.255.255

## Slide 37: Action to Take
The action in this case is
  eq
    Equal the port number of service
  gt
    Be greater than the port number
  lt
    Be less than the port number
  neq
    Do not match a port number

## Slide 38: Action to Take
  range
    Match a range of port numbers
  established
    Match on established tcp connections
  fragments
    Check fragments
  precedence
    Match on a precedence value
  tos
    Match on a tos value

## Slide 39: Port or Service Name
Specify the port by number or by service name
  Port number
    0-65535
  Port by name, such as the common ones
    telnet - 23
    ftp control - 21
    ftp data - 20
    www - 80

## Slide 40: Log the Hits by the Access List
log
log-input

## Slide 41: How ACLs Work
An ACL is a group of statements that define how packets do the following
  Enter inbound router interfaces
  Relay through a router
  Exit outbound router interfaces

## Slide 42: Entering an Interface
The router checks to see if the packet is routable
Checks if the inbound interface has an ACL
Tests packets against the ACL
If a packet is allowed in, checks the packet against the routing table to determine the destination interface

## Slide 43: Entering an Interface
Checks if the outbound interface has an ACL
Tests packets against the ACL

## Slide 44: Packets That Are Checked
ACLs filter not packets that originate in the router itself, but packets from other sources

## Slide 45: Implicit Deny
Packets are checked against each statement in order
If it does not match any statement, then it is denied access, as there is an implicit deny at the end of every ACL
Therefore every access list must have at least one permit statement

## Slide 46: Placing ACLs
Standard ACLs should be placed close to the destination
Extended ACLs should be placed close to the source

## Slide 47: Placing ACLs
If you place a standard ACL that denies access by a network or device IP address at the port where the network or device connects to the router nothing will be allowed out of the local network
This is why standard lists are suggested for placement near the destination
To me this is a silly rule

## Slide 48: Placing ACLs
As the diagram above shows this sends a bunch of unnecessary traffic through the router and out on the network
In my view place it where is does the job, but does not restrict access to things the network or device needs to access

## Slide 49: Applying ACLs
When assigning an ACL to an interface inbound or outbound placement should be specified
The filter direction can be set to check packets that travel into or out of an interface
When determining if the ACL is addressing inbound or outbound traffic, look at the interface from inside the router

## Slide 50: Applying ACLs
Traffic coming in from an interface is filtered by an inbound access list
Traffic going out an interface is filtered by an outbound access list
Apply the ACL with the access-group command from interface configuration mode such as
  ip access-group 10 in

## Slide 51: Inbound v Outbound
Outbound ACLs are generally more efficient
Therefore they are preferred
A router must check every incoming packet against the ACL before checking the routing table, where it may not even be routable

## Slide 52: Wildcard Mask
A wildcard mask is used to specify a range of addresses for the access list to impact
It is like an inverted subnet mask
For example
  A subnet mask of 255.255.0.0
    11111111.11111111.00000000.00000000
  Is a wildcard mask of 0.0.255.255
    00000000.00000000.11111111.11111111

## Slide 53: Wildcard Mask
The 0s mean match this part of the address
The 1s mean ignore

## Slide 54: Wildcard Mask
255.255.0.0 is easy
What about 255.255.240.0
Convert to binary
  11111111.11111111.1111.0000.00000000
Reverse the bit position values
  00000000.00000000.00001111.11111111
Convert the reversed to decimal
  0.0.15.255

## Slide 55: Wildcard Mask Shortcut
Another way is to take the subnet mask value in decimal, then subtract that number from 255
For example
  255-255=0
  255-255=0
  255-240=15
  255-0=255

## Slide 56: Wildcard Mask Block Size
Block sizes can also be used to explain wildcard masks
Block sizes are used to specify a range of addresses
Common block sizes are
  64 32 16 8 4
When you need to specify a range of addresses, you select the next largest block size

## Slide 57: Wildcard Mask Block Size
For example
  To specify 34 networks, use a block size of 64
  To specify 18 networks, use a block size of 32
  To specify 2 networks, use a block size of 4
In other words, select the next largest block size

## Slide 58: Wildcard Mask Block Size
In practice all that you have to remember is the wildcard number is always one number less than the block size
If the block size is 8, the wildcard number is 7

## Slide 59: Form of a Wildcard Mask
Let’s look at an example
  What wildcard mask is used to permit all packets from any host in the 172.30.16.0 to 172.30.31.0 subnets
  The answer is 0.0.15.255
  Why
    0.0 because these two octets are checked and passed
    255 because this is the decimal equivalent of all 1s in the last octet
      We will pass anything in the last octet

## Slide 60: Form of a Wildcard Mask
    To see the 15 we must think in binary
    Decimal 15 in binary is 00001111
    The 16 in this third octet is 00010000
    The first four 0s in the mask for this octet tell to match the first four bits in the IP address
    The last four bits in the IP address are ignored as the wildcard mask values are 1s
    Therefore everything from 16 to 31 will be passed as each of these numbers in binary begins with 0001

## Slide 61: Wildcard Any
Using any is the same as using 255.255.255.255
Keep in mind 255.255.255.255 is the same as 11111111.11111111.11111111.11111111
in binary
Recall that a 1 means do not check this bit value
In other words, pass it through

## Slide 62: Wildcard Host
To match an exact host address
For example
  172.30.16.29 0.0.0.0
Is the same as
  172.30.16.29 any
0 means check this bit value
In other words, everything must match

## Slide 63: Extended ACLs

## Slide 64: Named ACLs
Named ACLs allow you to both create and apply standard or extended access lists
The only difference is some changes to the syntax
  ip access-list
    Instead of
  access-list
    Also
  ip access-list standard nameofthelist
    Instead of
  access-list 10

## Slide 65: Named ACLs

## Slide 66: Restricting VTY Access
Create an access list that permits only the host or hosts that should be able to telnet
Then deny all others
For example
  access-list 50 permit 172.16.10.3
  line vty 0 4
  access-class 50 in
Recall that there is an implied deny at the end, so every other host is denied access

## Slide 67: Restricting VTY Access

## Slide 68: Restricting VTY Access

## Slide 69: Verifying ACLs
Show commands are used to check access lists
  show access-lists
  show ip interface
  show running-config

## Slide 70: Verifying ACLs
log command
  The log command can be added at the end of an access list beginning with IOS 12.0
  This causes any match of the statement to be printed to the console
  They do not appear on telnet connections unless the command
    terminal monitor
  is issued

## Slide 71: To Change an Access List
To change an access list execute the show run command
Copy the access list commands to Notepad
Edit the commands
Remove the old access list from the interface using
  no ip access-group whateverthenumberis in/out

## Slide 72: To Change an Access List
Remove the access list itself using
  no access-list whateverthenumberis
Select and copy the revised access list commands back to the router
Apply the access list

## Slide 73: To Remove an ACL
To remove an access list
Remove the access list from the interface using
no ip access-group whateverthenumberis in/out
Remove the access list itself using
no access-list whateverthenumberis

## Slide 74: Automatic Creation of ACLs
The protocol analyzer Wireshark can be used to create some ACLs based on a packet that exhibits the problem the ACL is intended to solve
Here is the procedure as explained by Laura Chappell

## Slide 75: Automatic Creation of ACLs

## Slide 76: Automatic Creation of ACLs
Here is an example using the sick-client.pcap file opened in Wireshark

## Slide 77: Automatic Creation of ACLs

## Slide 78: Automatic Creation of ACLs
Select a packet

## Slide 79: Automatic Creation of ACLs

## Slide 80: Automatic Creation of ACLs
Select Tools then adjust the values placed there if needed

## Slide 81: Automatic Creation of ACLs

## Slide 82: Automatic Creation of ACLs

## Slide 83: Automatic Creation of ACLs

## Slide 84: Automatic Creation of ACLs
Select Copy and place the data where needed