## Slide 1: Analog Modem
Last Update 2007.06.07
1.1.0

## Slide 2: Objectives of This Section
Learn
  What an analog modem is
  How an analog modem works

## Slide 3: What is a Modem
A modem is a modulator and demodulator in that it converts, in this case, analog phone signals into digital signals and back
This device is required as computer equipment generates a digital signal, whereas the PSTN can only deal with an analog signal

## Slide 4: What is a Modem

## Slide 5: Modem
The modem used in the workstation or at the central site if only a few remote sites are supported can attach to the computer using
  Adaptor Card plugged into the bus
  External connection through a serial port
  PCMCIA card in a PC Card or Cardbus slot
  External connection through a USB port

## Slide 6: Modem

## Slide 7: Modem

## Slide 8: USB Modem

## Slide 9: Modem Standards
When modems were first introduced the old Bell System defined the standards, today the ITU does
ITU modem standards are denoted by a V
The standards of interest include
  Compression
  Data Transfer Rate
  Error Correction

## Slide 10: Compression
Compression is a method required for a modem to be useable as an access device
Without compression of the data, the actual speed of the line would be only 600 bps
In compression, familiar, repeating character sets are replaced with symbols or strings

## Slide 11: Compression
These symbols or strings require fewer bits to send the information
The current standards for compression are V.44, the slightly older V.42bis, and the even older MNP5

## Slide 12: Data Transfer Rate
V.90 and V.92 define two data transfer rates that are widely used
These, however, or only useful when the central site is connecting to the PSTN through a digital, rather than an analog, data line
When these standards are used the speed from the central site back to the remote site is 53 Kbps

## Slide 13: Data Transfer Rate
But since the remote site is connecting using an analog line, the speed from that site to the central site is 33.6 Kbps for V.90 and 48 Kbps for V.92

## Slide 14: Error Correction
Because of the noise on regular phone lines error correction is required
The most commonly used standards for compression are V.42 and MNP4