## Slide 1: FDDI
Last Update 2007.05.27
1.1.0

## Slide 2: Objectives of This Section
Learn
  What FDDI is
  Where FDDI is used

## Slide 3: Context
Layer | 1
Network Type | LAN CAN

## Slide 4: What is FDDI
FDDI - Fiber Distributed Data Interface was pronounced dead on 13 December 1999 by Network World magazine
They based their assessment on the announcement by the companies that make FDDI chips that their last shipments would be made in early 2000

## Slide 5: What is FDDI
FDDI was killed by faster methods such as Gigabit Ethernet and ATM and cheaper 100 Mbps technologies such as Fast Ethernet

## Slide 6: What is FDDI
FDDI was used in three ways
  To link devices such as routers so that they can talk to each other
  To create LAN backbones because of its support for high bandwidth and greater distances than copper at one time
  To create CANs

## Slide 7: FDDI Connecting Routers
FDDI connector on a router

## Slide 8: FDDI Connector

## Slide 9: Operation
The FDDI specification describes a 100 Mbps token passing, dual-ring connection using fiber-optic cables
In FDDI’s dual-ring architecture traffic on each ring flows in opposite directions called counter-rotating rings
The dual-rings consist of a primary and a secondary ring

## Slide 10: Operation
During normal operation, the primary ring is used for data transmission, and the secondary ring remains idle
FDDI can use either type of optical fiber: single-mode or multi-mode
FDDI allows two kilometers between stations using multi-mode fiber, and even longer distances using a single mode

## Slide 11: Operation
FDDI only specifies the physical and media-access portions of the OSI reference model, layers 1 and 2
In this way it is similar to Ethernet and Token Ring
FDDI's primary fault-tolerant feature is the dual ring

## Slide 12: Operation
If a station on the dual ring fails or is powered down, or if the cable is damaged, the dual ring is automatically wrapped - doubled back onto itself - into a single ring
When the ring is wrapped, the dual-ring topology becomes a single-ring topology