## Slide 1: HDLC
Last Update 2012.04.30
1.5.0

## Slide 2: Objectives of This Section
Learn
  What HDLC is
  Where HDLC is used
  How HDLC operates

## Slide 3: Context
Layer | 2
Network Type | WAN

## Slide 4: Layers
As a layer 2 technology HDLC must have something below it at layer 1 to ride on, as well as something at layers 3 through 7 in order to operate
Typically this is
  Layer 1
    T Carrier
  Layer 3 through 7
    TCP/IP

## Slide 5: What is HDLC
HDLC – High Level Data Link Control Protocol is a layer 2 encapsulation method used to send data over a point-to-point serial link, such as a T1 line
This is a bit oriented protocol that was developed by the ISO
It is based on IBM’s SDLC – Synchronous Data Link Control protocol
HDLC was released as a standard in 1979

## Slide 6: Operation
Even though HDLC is a standard of sorts, every vendor’s implementation of HDLC is slightly different
This means one vendor’s router at one end of a line cannot talk HDLC to another vendor’s router at the other end of the line

## Slide 7: Operation
Unlike most proprietary solutions, vendors will allow any other vendor to support their implementation of HDLC if the other vendor wants to
For example the Cisco version of HDLC, often called cHDLC, is also supported by Juniper Networks on some of their systems

## Slide 8: Operation
An ancillary protocol used by HDLC is SLARP – Serial Line Address Resolution Protocol
SLARP is used for configuration and management of the link
For configuration it can be used to assign an IP address to the other end of the link, at least in the Cisco version of HDLC

## Slide 9: Operation
For management it is responsible for sending out keepalives to ensure the other end of the connection is still talking

## Slide 10: HDLC Frame Format
HDLC specifies three different frame formats
The only difference is what is in the control field
The types are
  I – Information frame
  S – Supervisory frame
  U – Unnumbered frame

## Slide 11: HDLC Frame Format
The I frame is used to carry data
The S frame is used for flow control
The U frame handles link initialization and disconnection

## Slide 12: HDLC Frame Format
Flag
Address
Control
Data
FCS
Flag

## Slide 13: HDLC Frame Format
These fields do the following
  Flag
    1 byte
    This field marks the start of the frame
    The value is always 0x7E, the 0x means the number is a hexadecimal number

## Slide 14: HDLC Frame Format
  Address
    1 byte
    This field serves no real purpose, as HDLC does not really use addressing
    The address is always 0F or 8F, for either unicast or multicast
    0F is used when the end point is known, such as data transfer
    8F is used for keep alive frames

## Slide 15: HDLC Frame Format
  Control
    1 byte
    This field is used, as described above, to indicate the use of the data area
  Data Field
    Variable size
    This field contains the important stuff

## Slide 16: HDLC Frame Format
  FCS
    2 bytes, but can be 4 bytes
    The FCS – Frame Check Sequence is the CRC used to ensure everything arrived intact
  Flag
    1 byte
    This field marks the end of the frame
    The value is always 0x7E

## Slide 17: Cisco HDLC Frame Format
Flag
Address
Control
Type Code
Data
FCS
Flag

## Slide 18: Cisco HDLC Frame Format
Cisco adds one additional field
  Type Code
    2 bytes
    This is used as a protocol field to indicate the protocol at the next level
    The EtherType codes are used in most cases, unless Ethernet does not have a corresponding function
    For example, 0x800 means IP and 0x8137 means IPX

## Slide 19: HDLC Capture File
Let’s look at some real HDLC frames
Download this file
  HDLC with RIP.cap
Open it in Wireshark by double-clicking it

## Slide 20: HDLC Capture File
Select frame 5
First we see some keep alive frames
Expand all of the fields
As mentioned above SLARP is used by Cisco for these keep alive frames

## Slide 21: HDLC Capture File

## Slide 22: HDLC Capture File
Down in frame 29 a ping packet is sent
Notice the address field changes from the multicast used for the keep alive frames to a unicast address as the ping goes to a specific end point
The protocol field holds the code for IP at the next layer

## Slide 23: HDLC Capture File

## Slide 24: SLARP
A SLARP – Serial Line Address Resolution Protocol frame is often seen along with cHDLC frames as these are used as keep alive messages for the link
SLARP is also used like a reverse ARP to receive an IP address over a serial line similar to receiving a address via DHCP on a LAN or to learn the IP address of the neighboring router

## Slide 25: Troubleshooting HDLC
The first thing to do when a problem arises on a link that uses HDLC is to check the physical connection
Also check the configuration of physical layer devices, such as the CSU/DSU
This is by far the most common source of the trouble
There is little troubleshooting for HDLC

## Slide 26: Troubleshooting HDLC
About the only thing to examine are the sequence numbers in the keepalive packets as discussed in Oppenheimer and Bardwell

## Slide 27: For More Information
T1: A Survival Guide
  Matthew S. Gast
  ISBN 0-596-00127-4
Troubleshooting Campus Networks
  Priscilla Oppenheimer and Joseph Bardwell
  ISBN 0471210137