## Slide 1: IPv6
Last Update 2012.10.29
1.9.0

## Slide 2: Objectives of This Section
Learn about IPv6

## Slide 3: IPv6
Soon we will move to IPv6
Why you might ask
Well because

## Slide 4: Why 32 Bits
How did we get here
Why were 32 bits used in the first place
Why not 64 or 128 or some other number of bits for the address space
Let’s here from the person who decided on 32 bits in the first place
Here is an email message sent to the NANOG mailing list in 2010 on this

## Slide 5: Why 32 Bits
  Hi,
  Vint Cerf kindly sent through some more explanation
  Regards,
  Mark

## Slide 6: Why 32 Bits
  Begin forwarded message:
  Date: Sat, 3 Apr 2010 08:17:28 -0400
  From: Vint Cerf vint at google.com
  To: Mark Smith nanog at 5d5b20a518b8f6864949bd940457dc124746ddc.nosense.org
  c: Andrew Gray <3356 at blargh.com
  NANOG List nanog at nanog.org
  Subject: Re: legacy /8

## Slide 7: Why 32 Bits
  When the Internet design work began, there were only a few fairly large networks around
  ARPANET was one
  The Packet Radio and Packet Satellite networks were still largely nascent
  Ethernet had been implemented in one place: Xerox PARC
  We had no way to know whether the Internet idea was going to work

## Slide 8: Why 32 Bits
  We knew that the NCP protocol was inadequate for lossy network operation (think: PRNET and Ethernet in particular)
  This was a RESEARCH project
  We assumed that national scale networks were expensive so there would not be too many of them
  And we certainly did not think there would be many built for a proof of concept

## Slide 9: Why 32 Bits
  So 8 bits seemed reasonable
  Later, with local networks becoming popular, we shifted to the class A-D address structure and when class B was near exhaustion, the NSFNET team (I think specifically Hans-Werner Braun but perhaps others also) came up with CIDR and the use of masks to indicate the size of the "network" part of the 32 bit address structure

## Slide 10: Why 32 Bits
  By 1990 (7 years after the operational start of the Internet and 17 years since its basic design), it seemed clear that the 32 bit space would be exhausted and the long debate about IPng that became IPv6 began
  CIDR slowed the rate of consumption through more efficient allocation of network addresses but now, in 2010, we face imminent exhaustion of the 32 bit structure and must move to IPv6

## Slide 11: Why 32 Bits
  Part of the reason for not changing to a larger address space sooner had to do with the fact that there were a fairly large number of operating systems in use and every one of them would have had to be modified to run a new TCP and IP protocol
  So the "hacks" seemed the more convenient alternative

## Slide 12: Why 32 Bits
  There had been debates during the 1976 year about address size and proposals ranged from 32 to 128 bit to variable length address structures
  No convergence appeared and, as the program manager at DARPA, I felt it necessary to simply declare a choice

## Slide 13: Why 32 Bits
  At the time (1977), it seemed to me wasteful to select 128 bits and variable length address structures led to a lot of processing overhead per packet to find the various fields of the IP packet format
  So I chose 32 bits
  vint

## Slide 14: IPv6
Larger address space
  IPv6 addresses are 128 bits, compared to IPv4's 32 bits
  It has been said that if each IPv6 address was represented by a grain of sand, then the entire address space would generate enough sand to build 300 million earth size planets
  However, not all of these individual grains of sand will be able to be used as single addresses

## Slide 15: IPv6
  So like IPv4, the useable number of addresses is less at about the number of grains of sand in the world
  The exact total number being
      340,282,366,920,938,463,374,607,431,768,211,456
  That’s about
      56,713,727,820,156,300,000,000,00
  addresses for each person on the planet

## Slide 16: IPv6
  This larger addressing space allows more support for addressing hierarchy levels, a much greater number of addressable nodes, and simpler autoconfiguration of addresses
Globally unique IP addresses
  Every node can have a unique global IPv6 address, which eliminates the need for NAT
  However, I expect everyone will still use NAT

## Slide 17: IPv5
Now if we are currently using IPv4 and moving to IPv6, what happened to IPv5
Let’s let Geoff Huston in an article from the Internet Protocol Journal for March 2011 Volume 14 Number 1 explain
He writes

## Slide 18: IPv5
  It would be reasonable to expect the successor protocol of IP Version 4 to be called IP Version 5, but as it turned out Version 5 of the Internet Protocol Family was already taken
  In the late 1980s the Internet Protocol itself was the topic of a considerable level of research, as researchers experimented with different forms of network behavior

## Slide 19: IPv5
  Version 5 of the Internet Protocol was reserved for use with an experimental IP protocol, the Internet Stream Protocol, Version 2 (ST-II), written up as RFC 1190 in 1990
  When it came time to assign a protocol number of the “next generation” of IPv4, the next available version number was 6, hence IPv6

## Slide 20: IPv5
Since this is the same story I have heard before, I assume this is definitive

## Slide 21: IPv7
There is no IPv7 or any other reasonable replacement for IPv6 at least not yet
So how long will IPv6 be useful
In the same issue of the Internet Protocol Journal Geoff Huston offers this view

## Slide 22: IPv7
  The design intent of IPv6 is a usable lifetime of more than 50 years, as compared with a “mainstream” deployment lifetime of IPv4 of 15 years, assuming that you are prepared to draw a line at around 1995 and claim that at that time the protocol moved from an interesting academic and research project to a mainstream pillar of the global communications industry

## Slide 23: IPv6 Address Types
There are three main types of IPv6 addresses
They are

## Slide 24: IPv6

## Slide 25: IPv6

## Slide 26: IPv6

## Slide 27: IPv6

## Slide 28: IPv6 Address Parts
Each IPv6 address is 128 bits
In practice these 128 bits are divided into two 64 bit parts
  The first 64 bits from the left are for the networks of various sorts
  The last 64 bits are for the host’s interface
  As in

## Slide 29: IPv6 Address Parts

## Slide 30: IPv6 Address Parts
The last 64 bits are straight forward, they belong to the end device’s NIC
As the first 64 bits are designated for networks these bits are further subdivided
Since most distribution plans assume that each end user will be given a /48 address this means the remaining 16 bits of the first 64 are available to the end user for networks at their premises

## Slide 31: IPv6 Address Parts
The first 48 bits are then used by those networks above the end user premises
The first three are reserved by the IANA
The next 45 are for use by various Regional Registries and upstream ISPs
As in

## Slide 32: IPv6 Address Parts

## Slide 33: IPv6 Distribution From IANA
The hierarchy of address distribution will be as follows
  Each RIR receives a /12 to /23
  Large ISPs each receive a /32
  They are expected to give each customer a /48 although some are thinking a /56 may work as well
  Each network a customer has regardless of size or type will use a /64

## Slide 34: IPv6

## Slide 35: IPv6

## Slide 36: IPv6

## Slide 37: IPv6 Address Types
There are two basic types of IPv6 addresses
  Global Unicast Address or GUA
  Unique Local Address or ULA
In each case the form is eight groups, always eight groups
So if you see a set of :: where the zeros have been replaced just expand this section so that there are eight altogether

## Slide 38: GUA
For a GUA the first four groups will come from an ISP
It constitutes the network and subnet they use
The last four groups are yours to use as you wish
For example 2001:0db8:1234:1234::

## Slide 39: GUA Address Planning
Lets examine the most commonly suggested IPv6 addressing plan
Recall that a IPv6 address is 128 bits long
Each digit in the hexadecimal numbering system is a nibble or half a byte
This is equivalent to four bits so an IPv6 address can be represented by 32 hexadecimal numbers

## Slide 40: GUA Address Planning
These 32 hex numbers are the ones we will use for the addressing plan
Prefixes in a slash number form are used to group IPv6 addresses
These prefixes define all of the addresses that start with the same series of bits from the leftmost

## Slide 41: GUA Address Planning
For example
  2001:0db8::/32
  This would indicate all of the addresses from
    2001:0db8:0000:0000:0000:0000:0000:0000
    to
    2001:0db8:ffff:ffff:ffff:ffff:ffff:ffff
You will often see the 0db8 part of the address written as just db8 as the rules allow prepended zeros to be omitted

## Slide 42: GUA Address Planning
Why did they do this, just to confuse you
They love to do these sorts of things to students
Back to the point
To see why this is so lets see how the 128 bits fit into this
Consider that each group of hex numbers separated by a colon represents 4 binary places

## Slide 43: GUA Address Planning
As there are 32 of these hex numbers, 32 times 4 equals 128 bits
Likewise each group of four hex numbers represents 16 bits
So if the first two groups of hex numbers are already set for you, then you have a prefix of /32 as 16 plus 16 equals 32

## Slide 44: GUA Address Planning
Doing all of this by groups of four makes deciphering the address easier
Therefore, common prefixes seen are /48, /52, /56, /60, /64, and so on
Using this by fours division address blocks are typically assigned this way
Here is a table from RIPE NCC the European regional Internet registry in a December 2010 white paper

## Slide 45: GUA Address Planning

## Slide 46: GUA Address Planning
As seen in the table a large ISP will receive a /32 from their regional registry, such as ARIN for the US
They will then assign smaller blocks of addresses to their customers
The general assumption is that all organizations will receive a very large address space from their upstream provider

## Slide 47: GUA Address Planning
In this example it is a /48
Now giving everyone a /48 may seem like a waste of address space, and it is, but this is where we are today
In no case should a home user be provided with only a single address as would be the case with a /128 as was common with IPv4

## Slide 48: GUA Address Planning
It is further expected that each network – LAN, CAN, MAN, and WAN link will be assigned a /64
So we have 16 bits to use to create these /64 networks from the /48 address space provided to us since the difference between 48 and 64 is 16

## Slide 49: GUA Address Planning
This means we can create 65,536 networks with 18,446,744,073,709,551,616 hosts on each one of these networks
  This is eighteen quintillion, four hundred forty-six quadrillion, seven hundred forty-four trillion, seventy-three billion, seven hundred nine million, five hundred fifty one thousand, six hundred and 16 or just 18,446 quintillion hosts

## Slide 50: GUA Address Planning
These 65,536 network names would range from
  2001:0db8:1234:1234:0000/64
  to
  2001:0db8:1234:1234:ffff/64
If a /56 is provided, then 256 networks can be created instead of 65,536

## Slide 51: GUA Address Planning
What you do with these addresses is up to you
You may just assign these 65,536 one by one
The RIPE white paper suggests three ways to do this in a more organized way based on location, use type, or both
There are advantages and disadvantages to each approach

## Slide 52: GUA Address Planning
The white paper suggests this layout
  2001:0db8:1234:1234:LLLL:GGGG:BBBB:BBBB
    16 bits are assigned to a location L and 16 bits are assigned to a use type G
    As a result, there are 32 bits remaining Bs
    Following this addressing plan, 65,536 locations can be addressed, with each location having 65,536 use types
    Each of these networks could have 4,294,967,296 end devices

## Slide 53: GUA Address Planning
The location and use types could be reversed to provide
  2001:0db8:1234:1234:GGGG:LLLL:BBBB:BBBB
16 bits are assigned to a use type G and 16 bites to locations L yielding 65,536 use types with each one in 65,536 possible locations
Placing use types first can make it easier to apply security policies such as ACLs

## Slide 54: ULA
The ULA is similar to the RFC1918 private address space
These addresses begin with fd
This address is in three parts
  Network Address
  Subnet Address
  Device Address

## Slide 55: ULA Network Address
After the fd the next ten hex numbers – the first 48 of the 128 bits - define the network address
This is the first three hex number groups
This can be anything after the fd

## Slide 56: ULA
For simplicity this form can be used
  fd00:0000:0000
or any of the 72 trillion network and subnet possibilities

## Slide 57: IPv6
Site multihoming
  IPv6 allows hosts to have multiple IPv6 addresses and allows networks to have multiple IPv6 prefixes
  Consequently, sites can have connections to multiple ISPs without breaking the global routing table

## Slide 58: IPv6
Header format efficiency
  A simplified header with a fixed header size makes processing more efficient

## Slide 59: IPv6
Improved privacy and security
  IPsec is the IETF standard for IP network security, available for both IPv4 and IPv6
  Although the functions are essentially identical in both environments, IPsec is mandatory in IPv6
  IPv6 also has optional security headers

## Slide 60: IPv6
Flow labeling capability
  A new capability enables the labeling of packets belonging to particular traffic flows for which the sender requests special handling, such as nondefault quality of service (QoS) or real-time service

## Slide 61: IPv6
Increased mobility and multicast capabilities
  Mobile IPv6 allows an IPv6 node to change its location on an IPv6 network and still maintain its existing connections
  With Mobile IPv6, the mobile node is always reachable through one permanent address

## Slide 62: IPv6 Traffic Types
In IPv6 there are still three types of traffic
However the functions are somewhat different
  Unicast
    One to one
  Anycast
    One to nearest
      Examples of when anycast addresses could be used are load balancing, content delivery services, and service location

## Slide 63: IPv6 Traffic Types
      For example, an anycast address could be assigned to a set of replicated FTP servers
      A user in China who wants to retrieve a file would be directed to the Chinese server, whereas a user in the Europe would be directed to the European server
  Multicast
    One to many
    This is also the broadcast format

## Slide 64: IPv6 Host Address
The host address in IPv6 is referred to as an interface identifier
Its form is
  OUI – FFFE – Serial Number
  In other words the hex numbers FFFE are placed between the two parts of the MAC address
  This makes it a 64 bit address

## Slide 65: IPv6

## Slide 66: Implementing IPv6
The question now is how best to make the move from 4 to 6
Transition ideas include
  Dual stacks
  Tunneling
  Translation
The suggested approach is to dual stack where possible, otherwise tunnel

## Slide 67: Implementing IPv6
Consult the Internet Protocol Journal for March 2011 Volume 14 Number 1 for a detailed discussion of the possible ways to implement this transition
In particular consult Transitioning Protocols by Geoff Huston

## Slide 68: Implementing IPv6
Dual stacking is basically what occurred when the move from other routed protocols such as IPX, Decnet, and so forth to TCP/IP occurred
I ran multiple routed protocols on each end device, then tunneled the non TCP/IP traffic across the WAN

## Slide 69: Implementing IPv6
Keep in mind that all the devices out there will have to be upgraded or replaced during this implementation process
Many devices cannot and will not ever support IPv6 in any form
Various models suggest anywhere from 80 years to 2 years to make this transition
Huston in the article above guesses 5 years

## Slide 70: Implementing IPv6
Why not just NAT forever
Huston says this
  But address sharing has its limitations
  When a single household shares a single address, nothing unusual happens
  But If I were to try to do the same address-sharing trick of using a single IP address to share across, say 2,000 customers, I would cross over into a world of pain

## Slide 71: Implementing IPv6
  Many applications today gain speed through parallelism, and they support parallelism through consuming port addresses
  Each IP address can support the parallel operation of 65,535 sessions, using a 16-bit port identifier as the distinguishing identifier
  But when address sharing is used, these ports are shared across the number of devices that are all sharing this common address

## Slide 72: Implementing IPv6
  When 2,000 customers are sharing a single address and each customer has some 20 or so devices, then the average number of port addresses per device is 1.5
  Common applications that exploit parallel operation include such favorites as Gmail, Google Maps, and iTunes

## Slide 73: Implementing IPv6
  With a sufficiently constrained number of available ports to use, these applications would cease to work
  Indeed, many network applications would fail, and at a level of a single address shared across 2,000 households, I would guess that up to half of these 2,000 customers would not have a working Internet at any single point in time

## Slide 74: Dual Stacks
A dual stack is just what it says
Both IPv4 and IPv6 are run at the same time
For example

## Slide 75: Dual Stacks

## Slide 76: Dual Stacks

## Slide 77: Tunneling
There are several tunneling methods
  Manual 6 over 4 tunneling
  Dynamic 6 over 4 tunneling
  Intrasite Automatic Tunnel Addressing Protocol
  Teredo Tunneling
At this point which one to use is undecided

## Slide 78: Translation
A form of NAT can be used on some Cisco routers to translate 6 to 4 and back
Translation is not a preferred method

## Slide 79: Sources
The slides with the blue line on top are from a presentation by Byju Pularikkal to the Nanog meeting 51 in January 2011