## Slide 1: ISDN Last Update 2011.05.06 1.3.0

## Slide 2: Objective
Learn what ISDN is and how it is used

## Slide 3: What is ISDN
ISDN – Integrated Services Digital Network was meant to be the way to use the existing PSTN, copper, analog phone system to deliver voice, video, data, and music to any location over a single physical line as a digital instead of an analog circuit
It was the first attempt at convergence
Before ISDN a separate interface was required for each of those services

## Slide 4: What is ISDN
ISDN was first deployed in the late 1980s
ISDN was defined by the ITU-T in 1984
Although it is still widely available and somewhat widely used, it never took off
The main problems were
  Poor marketing by the phone companies
  Poor implementation by the phone companies
  Priced too high by the phone companies

## Slide 5: What is ISDN
  Too little bandwidth was defined by the BRI interface for the amount of information to be sent, as BRI was meant as the main deployment method for ISDN

## Slide 6: Current Use
Currently ISBN is used to link a small office to the main office
It is also commonly used as a backup line for higher speed circuits
ISDN can be deployed as a switched circuit or an always on circuit

## Slide 7: Speeds
ISDN is offered at two basic speeds
  BRI – Basic Rate Interface or 2B+D
    B Channel - 64 Kbps - Data
    B Channel - 64 Kbps - Data
    D Channel - 16 Kbps – Control
    128 Kbps data rate
  PRI – Primary Rate Interface or 24B+D
    23 B Channels
    1 D Channel
    1.544 Mbps data rate

## Slide 8: ISDN Access Options

## Slide 9: Setup
The most difficult part of ISDN circuit setup is getting the service provider and the ISDN box talking the same language
In general there are six basic ways a service provider can setup an ISDN line
Try to find out what method they use and set the ISDN box on your end to match

## Slide 10: Setup
As Eicon – a maker of ISDN equipment - says these are
  EZ-ISDN 1 or IOC: U
    Offers voice and data on both ISDN channels and supports advanced calling features such as call conference, call transfer, and caller ID on the first ISDN number
  EZ-ISDN 1A or IOC: V
    Same as EZ-ISDN 1, but adds voice mail

## Slide 11: Setup
  IOC: “S”
    Offers voice and data on both ISDN channels, but without any advanced calling features
      If you select this package, make sure to get Additional Call Offering (ACO), which is required for call bumping and call waiting to work correctly
  EZ-ISDN 3 or 3A
    Same as EZ-ISDN 1 (1A), plus adds support for Always On/Dynamic ISDN (AO/DI)

## Slide 12: Setup
  Capability Package AB
    Same as IOC U, but with advanced calling support on both channels and support for AO/DI
  Capability Package AC
    Same as IOC V, but with advanced calling support on both channels and support for AO/DI

## Slide 13: Setup
You will also need to find out the following from the service provider
  At least the SPID
    This is the line identification number
  And maybe the ISDN switch type they use, which could be
    National ISDN-1
    AT&T 5ESS
    AT&T 5ESS Point-to-Point

## Slide 14: ISDN Switch Types

## Slide 15: ISDN Standards

## Slide 16: Cisco ISDN BRI Interfaces

## Slide 17: ISDN Interfaces
S/T ISDN Interface
U ISDN Interface

## Slide 18: Reference Points
As seen in the literature and occasionally discussed during implementation of an ISDN circuit, there are reference points defined in an ISDN network
Each of these points is indicated by a letter
As in

## Slide 19: Reference Points
CUSTOMER SITE |  |  |  |  |  |  | SERVICE PROVIDER |  |  |  | 
ISDN | TE1 |  |  | S | NT2 | T | NT1 | U | LT | V | ET
NON ISDN | TE2 | R | TA | S | NT2 | T | NT1 | U | LT | V | ET

## Slide 20: ISDN Reference Points
R: the connection between a non-ISDN Terminal Equipment (TE2) and a Terminal Adapter (TA), e.g. an RS-232 serial interface
S: references the points that connect into the customer switching device Network Termination type 2 (NT2) and enables calls between the various types of customer premises equipment
T: electrically identical to the S interface, it references the outbound connection from the NT2 to the ISDN network or Network Termination type 1 (NT1)
U: the connection between the NT1 and the ISDN network owned by the telephone company

## Slide 21: ISDN Functions

## Slide 22: BRI Reference Points

## Slide 23: Reference Points
In the diagram ISDN means equipment designed to connect to an ISDN network
  TE1 is the ISDN designed equipment
By non ISDN is meant standard equipment
  TE2 is the non ISDN equipment
The S and T points are one in most locations so this is referred to as the S/T reference point

## Slide 24: Reference Points
It is the customer part of the network
U and V are the service provider reference points

## Slide 25: ISDN and the OSI Model layers
ISDN uses two channels, one for the control information on the D channel and one for the useful data on the B channels
This means that different things happen on the same circuit depending on whether the transmission is control or data related
Let’s look at what happens on each channel in relation to the OSI model layers
BRI will be used for this purpose

## Slide 26: ISDN 3-Layer Model

## Slide 27: ISDN at Layer 1
ISDN uses two different frame formats at layer 1 for the B channel
One is used for incoming data and one for outgoing
These frames are 48 bits long, with 36 bits of that being data
On both the D and B channels the I.430 protocol is used
Which channel is active is determined by TDM – Time Division Multiplexing

## Slide 28: ISDN at Layer 2
At layer 2 the channels differ
On the D channel the protocol is LAPD – Link Access Procedure - D Channel for BRI
As the acronym indicates layer 2 is used on the D channel to ensure that the control and signaling information is sent and received properly
LAPD is similar to HDLC

## Slide 29: LAPD Frame
FLAG
ADDRESS
CONTROL
DATA
FCS
FLAG

## Slide 30: LAPD Frame
The flags mark the start and finish of the frame
The address tells us where it is going and where it has come from
  There are two identifiers here
    The SAPI – Service Access Point Identifier indicates what higher level protocol is being carried in the data field
    The TE1 identifier points to the equipment on a multipoint line at the customer site

## Slide 31: LAPD Frame
Control identifies the
frame type
The data is the important stuff
FCS is the error checking

## Slide 32: ISDN at Layer 2
On the B channel at layer 2 the data is carried by PPP

## Slide 33: ISDN Data Link Layer

## Slide 34: ISDN at Layer 3
ISDN layer 3 specifications are used for ISDN signaling on the D channel
Q.931 is commonly used here
On the B channel the data uses TCP/IP these days
Let’s look at an example of a B channel ISDN frame

## Slide 35: ISDN at Layer 3

## Slide 36: Q.931 Messaging-Call Setup

## Slide 37: Call Processing
The D channel is used to send the called number to the local ISDN switch
The local switch uses the SS7 signaling protocol to set up a path and pass the called number to the remote ISDN switch
The remote ISDN switch signals the destination over the D channel
The destination ISDN NT-1 device sends the remote ISDN switch a call-connect message
The remote ISDN switch uses SS7 to send a call-connect message to the local switch
The local ISDN switch connects one B channel end-to-end, leaving the other B channel available for a new conversation or data transfer. Both B channels can be used simultaneously

## Slide 38: Configuring ISDN BRI

## Slide 39: Configuring ISDN BRI

## Slide 40: Configuring ISDN PRI

## Slide 41: ISDN PRI Examples

## Slide 42: Verifying ISDN Configuration

## Slide 43: Verifying ISDN Configuration

## Slide 44: Troubleshooting ISDN

## Slide 45: DDR Operation

## Slide 46: Configuring Legacy DDR

## Slide 47: Defining Static Routes for DDR

## Slide 48: Static Route Considerations
When configuring static routes, consider the following
  By default, a static route will take precedence over a dynamic route because of its lower administrative distance
  Without additional configuration, a dynamic route to a network will be ignored if a static route is present in the routing table for the same network.
  To reduce the number of static route entries, define a summarized or default static route

## Slide 49: Specifying Interesting Traffic

## Slide 50: Configuring Dialer Information

## Slide 51: dialer-group

## Slide 52: dialer-map

## Slide 53: dialer idle-timeout

## Slide 54: Dialer Profiles Overview
Define encapsulation and access control lists
Determine minimum or maximum calls
Turn features on or off

## Slide 55: Dialer Profiles Overview

## Slide 56: Dialer Profile Elements

## Slide 57: Configuring Dialer Interfaces

## Slide 58: Configuring Physical Interfaces

## Slide 59: Verifying DDR
show dialer
show dialer interface [BRI]
show isdn active
show isdn status

## Slide 60: Troubleshooting DDR
debug isdn q921
debug isdn q931
debug dialer [events|packets]
isdn call interface
clear interface bri