## Slide 1: Optical Interfaces
Last Update 2014.07.10
1.3.0

## Slide 2: Objectives of This Section
Learn
  What optical interfaces are
  How to install and connect to them

## Slide 3: Optical Interfaces
There are several types of optical interfaces
  Modules that plug into an opening with an electrical connector at the back
    Fast and Gigabit Ethernet
      GBIC – Gigabit Interface Convertor
      SFP – Small Form Factor Pluggable
    10G Ethernet
      XENPAK
      XFP
      SFP+

## Slide 4: Optical Interfaces
  Boards that go in a slot to connect to a backplane
    Modular interface boards

## Slide 5: GBIC and SFP
The older and slower types are the GBIC and the SFP
The SFP was designed to replace the GBIC in order to save front panel space
The SFP is close to the size of an RJ-45 port

## Slide 6: GBIC and SFP

## Slide 7: GBIC

## Slide 8: GBIC Types
We will look at some Cisco GBIC models to illustrate the types that are commonly used
  1000BASE-T GBIC WS-G5483
    Connects a GBIC port to Category 5 UTP cable using a standard RJ-45 interface
    The maximum distance is 328 feet or 100 meters

## Slide 9: GBIC Types
  1000BASE-SX GBIC WS-G5484
    For a multimode fiber link up to 1815 feet or 550 m and on laser-optimized multimode fiber OM3 up to 3281 feet or 1 km
  1000BASE-LX/LH WS-G5486
    IEEE 802.3z 1000BASE-LX10 standard for up to 6.2 miles or 10 km over single-mode fiber and up to 550 meters over multimode fiber

## Slide 10: GBIC Types
  1000BASE-ZX GBIC WS-G5487
    For single mode fiber optic link spans up to 43.4 miles or 70 km
Here is a summary table from Cisco

## Slide 11: GBIC Types

## Slide 12: GBIC Slot

## Slide 13: SFP

## Slide 14: SFP Types
There are several types of SFPs
They differ based on the type of fiber optic cable they will connect to and the distance over which they will drive a single
For example

## Slide 15: SFP Types
  For 850 nm multimode fiber optic cable over Ethernet SX distances up to 550 m at 1.25 Gbps
  For 850 nm multimode fiber optic cable over Ethernet SX distances up to 150 m at 4.25 Gbps
  These have a black or beige extractor lever
  For 1310 nm single mode fiber optic cable over Ethernet LX distances up to 10 km
  These typically have a blue extraction lever

## Slide 16: SFP Types
  We will look at some Cisco SFP models to illustrate the types that are commonly used
    1000BASE-T SFP GLC-T
      Connects to standard UTP Category 5 up to 328 feet or 100m
    1000BASE-SX SFP GLC-SX-MM
      Connects to multimode fiber optic cable either 50 or 62.5 at distances up to 550 m and 220 m respectively
      It can support up to 1km over laser-optimized 50 μm multimode fiber cable

## Slide 17: SFP Types
    1000BASE-LX/LH SFP GLC-LH-SM
      Operates on standard single mode fiber-optic links up to 10 km and up to 550 m on any type of multimode fiber optic cable
      A mode conditioning cable may be needed
    1000BASE-EX SFP GLC-EX-SM
      For standard single-mode fiber-optic link spans of up to 40 km in length
      A 5 dB inline optical attenuator should be inserted between the fiber-optic cable and the receiving port on the SFP at each end of the link for back-to-back connectivity

## Slide 18: SFP Types
    1000BASE-ZX SFP GLC-ZX-SM
      For standard single mode fiber optic links of approximately 70 km
      The SFP provides an optical link budget of 21 dB, but the precise link span length depends on multiple factors such as fiber quality, number of splices, and connectors
      When used over shorter distances with single mode fiber optic cable it might be necessary to insert an inline optical attenuator in the link to avoid overloading the receiver
      A 10-dB inline optical attenuator should be inserted between the fiber-optic cable plant and the receiving port on the SFP at each end of the link whenever the fiber-optic cable span loss is less than 8 dB

## Slide 19: SFP Types
Here is a summary table from Cisco

## Slide 20: SFP Types

## Slide 21: SFP Slot

## Slide 22: SFP Slot

## Slide 23: XENPAK
With the development of 10G Ethernet new interfaces were developed
It first appeared in 2001

## Slide 24: XENPAK

## Slide 25: XFP
Announced in 2002 the XFP is another 10G plug in transceiver

## Slide 26: XFP

## Slide 27: SFP+
The SFP+ is an enhanced version of the SFP designed for higher speeds such as 10G Ethernet

## Slide 28: SFP+

## Slide 29: Modular Board Based
Modular routers have a slot at the base of which is a connector to the device’s circuit board that allows the interfaces of the device to be changed without the need for an entirely new device
These modular connectors look like this

## Slide 30: Modular Connector Slot Cover

## Slide 31: Modular Connector Slot

## Slide 32: Modular Interface Board

## Slide 33: Modular Interface Board

## Slide 34: Media Converter
Some times to save money fiber optic cable will be run from one point to another, but the devices at the ends, such as a switch, will have copper ports, since copper based boxes are cheaper than ones with fiber interfaces
To convert the copper port to the fiber optic cable a media converter is required
Such as

## Slide 35: Media Converter

## Slide 36: Connecting to Fiber Ports
To connect to a fiber optic cable port the correct type of fiber optic cable must be used
In addition the ends of the cable and the ports must be clean
Only an inspection scope can determine whether these ports and cable ends are clean enough

## Slide 37: Handling Fiber Optic Media
Anytime you work with fiber optic cable it is important to keep everything clean
It is also important to protect yourself from injury from small pieces of fiber
These fiber pieces that are produced as a normal part of the termination process can get in your eyes or stick in your skin
They are difficult to remove

## Slide 38: Keeping the Media Clean
It is critical that the ends of fiber optic cable be kept clean
Dirty connections are a common cause of link failures
According to Fluke 85% of link failures are due to contaminated ends

## Slide 39: Inspection
The best way to check for dirt is an inspection scope
For multimode fiber 200 times magnification is used
For single mode cable 400 time is required

## Slide 40: Inspection Scope

## Slide 41: Inspection Scope

## Slide 42: Inspection Scope

## Slide 43: Inspection Process

## Slide 44: Sources of Problems
The are two main sources of problems on fiber ends
  Contamination
    Dirt and Dust
    Finger Prints
    Cleaning Method Used
    Skin Oils and Cable Gels
  Damage
    Pitting
    Scratches

## Slide 45: Contamination
There are many sources of contamination that leads to dirt particles on connections
  Airborne dust and dirt
  Improper or insufficient cleaning of tools and materials
  Debris from poor quality components
  Dirt from the technicians hands
Here are some examples of common problems from Fluke and others

## Slide 46: Contamination
Even touching the end of a fiber will deposit excessive oil
Gel from used to pull cable will do the same thing
Dust caps do not necessarily help as they may transfer contamination

## Slide 47: Dust

## Slide 48: Dirt

## Slide 49: Finger Print

## Slide 50: Dirt

## Slide 51: Dust and Skin

## Slide 52: Dust and Skin

## Slide 53: Dust and Skin

## Slide 54: Dry Cleaned

## Slide 55: Too Much Solvent Cleaner

## Slide 56: Pitting
In some cases the amount of dirt is so great that scratches, pits, and chips can be seen in the fiber ends

## Slide 57: Scratches

## Slide 58: Scope Resolution
In general scopes have one of three resolutions
  Low – 60X
    This does not show much detail, but it has a wide field of view
  Medium – 200X
    This will show dirt, oils, dust, and lint
  High – 400X
    This level will show pits and scratches as well

## Slide 59: Scope Resolution
In the field the 200X is the most widely used

## Slide 60: Cleaning
The solution to this problem is proper cleaning
This means the use of optical grade materials to do the cleaning
Cleaning can be done using dry or wet methods

## Slide 61: Best Practice When Cleaning
As discussed below there are many suggested methods for cleaning fiber
To cut to the chase here is what Fluke says is the best way to do this regardless of whether it is a plug or jack

## Slide 62: Best Practice When Cleaning
  Dab the contaminated end-face with a solvent-dampened wipe or swab
  The solvent dissolves and removes contaminants that have dried and firmly affixed to the end-face without producing a static charge that can attract dust from the air
  It also evaporates quickly, making it preferable to isopropyl alcohol which takes much longer to disappear and can leave a staining residue in the process

## Slide 63: Best Practice When Cleaning
  Rub the fiber end-face perpendicularly against a dry wipe several times
  Re-inspect the fiber end-face with an optical microscope to ensure that all the debris has been removed

## Slide 64: Dry Cleaning
Dry cleaning is very common
However it can lead to static charges on the ends of the connectors
These charges then attract dust

## Slide 65: Wet Cleaning
Although an extra step, wet cleaning is more effective
Isopropyl alcohol at 99 percent is commonly used for this purpose
While effective alcohol must be allowed time to dry, since alcohol will absorb water from the air
There are solutions designed for fiber optic cable that are a better choice

## Slide 66: Cleaning Cable Ends
Let’s look at some common methods used to clean fiber optic media as provided by Fluke
Using Fluke Networks Fiber Optic Cleaning Card
  Peel cover from an unused “N”– shaped cleaning zone
  Apply a minimal amount of solvent from the Solvent Pen to the first corner of the “N”

## Slide 67: Cleaning Cable Ends
  Avoid isopropyl alcohol
  Place the end-face perpendicular to the card in the first corner of the unused “N”
  Swipe through the “N” shape using gentle pressure moving from wet to dry
  Always check the end-face with a fiber microscope before insertion
  If necessary, repeat the cleaning process from step #1 using another unused “N”
  Never swipe over the same area twice

## Slide 68: Cleaning Cards

## Slide 69: Cleaning Cable Ends
Using Fluke Networks’ Fiber Optic Cleaning Cube
  Pull out a clean wipe and lay it over the foam platen
  For best results, apply a minimal amount of solvent from the Solvent Pen
  A 1 cm diameter spot is sufficient
  Avoid isopropyl alcohol

## Slide 70: Cleaning Cable Ends
  Place the end-face perpendicular to the cube in the wet spot
  Swipe the end-face from the wet spot into a dry area using gentle pressure
  Always check the end-face with a fiber microscope before insertion
  If necessary, repeat the cleaning process on a clean portion of the wipe
  Each wipe can clean up to four end-faces. Never swipe over the same area twice

## Slide 71: Cleaning Cube

## Slide 72: Cleaning Cable Ends
Using Fluke Networks’ Fiber Optic Swabs
  Select the swab with the correct diameter to fit inside the port to be cleaned. 2.5 mm Fiber Optic Swabs fit SC, ST, and all other 2.5 mm diameter ports. 1.25 mm Fiber Optic Swabs fit LC and MU ports
  Using the Fiber Optic Cleaning Cube or Card, apply some solvent from the Solvent Pen to a wipe
  Avoid isopropyl alcohol

## Slide 73: Cleaning Cable Ends
  Touch the swab to the wet spot on the wipe for 3 seconds to draw a minimal amount of solvent
  Touching the swab directly to the Solvent Pen will likely result in excess solvent
  Insert the damp swab into the port and turn several times, applying gentle pressure

## Slide 74: Cleaning Cable Ends
  Follow the damp swab with a dry one, using the same procedure to remove any remaining solvent from the end-face and alignment sleeve
  Always check the end-face with a fiber microscope before insertion
  If necessary, repeat the cleaning process with fresh swabs

## Slide 75: Cleaning Swabs

## Slide 76: Cleaning Swabs

## Slide 77: Area to Clean
It is important to clean not only the core area of the fiber end, but also the cladding area
In this photograph the core is the white dot the cladding is the dark circle

## Slide 78: Area to Clean

## Slide 79: Area to Clean
Failing to clean the cladding area as well as inside the connector itself will allow the debris there to migrate to the core, thus blocking the light based signal
Clean both the patch cord ends as well as the bulkhead connectors such as these

## Slide 80: Area to Clean

## Slide 81: Attenuators
Sometimes an optical interface generates too much, rather than too little power
In this case the interface can be replaced or an attenuator can be added
Let’s look at an excellent real world example of this from a blog post at the Tekcert website posted on 9 July 2014
Here is what it says

## Slide 82: Attenuators
Once in a while I find myself doing some awesome work over long distances
In today's case, I've been working on some core and data center interconnects that span 5-35 miles (8-56km) using dark fiber
One of the connections was causing a warning message in the logs

## Slide 83: Attenuators
  %SFF8472-5-THRESHOLD_VIOLATION: Te1/1: Rx power high warning; Operating value: 0.3 dBm, Threshold value: -1.0 dBm
If you see a simple warning message like this, don't panic, it's a pretty easy fix
Start by doing some research on the connection
The show transceiver detail command says

## Slide 84: Attenuators

## Slide 85: Attenuators
From this you can see the Rx power is over the warning threshold of -1.0
The low warning threshold is -15.8 dBm, so we want to attenuate the signal enough to land between -15.8 and -1.0
Once you've identified how much signal to attenuate, purchase an attenuator that matches your connection type

## Slide 86: Attenuators
In my case, I have LC connections because I'm using SFP-10G-ER optics and I also needed at least 1.4 dB of attenuation
Since we had a 7dB attenuator on hand, that's what I used

## Slide 87: Attenuators
If you don't have one on hand, a quick search turned up this Fiber Attenuator Singlemode Simplex LC/UPC Fixed 7db at Amazon

## Slide 88: Attenuators

## Slide 89: Attenuators
To install the attenuator, you need to place it on the fiber connecting to the receive side of the optic
If you aren't sure which side is receive, there is a Cisco doc with a diagram showing you which side is receive (it's the right side)

## Slide 90: Attenuators
Here's a link to that doc
  http://www.cisco.com/c/en/us/td/docs/interfaces_modules/transceiver_modules/installation/note/78_15160.html
After installing the attenuator, here's the results

## Slide 91: Attenuators

## Slide 92: Attenuators
As you can see the Optical Receive Power is -6.7 dBm, or exactly 7 dBm lower
Isn't this stuff totally awesome
Ok, maybe not that much, but still pretty cool when things work
Hope this helps someone out there faced with long dark fiber runs and overpowering optics