## Slide 1: PPP Last Update 2011.06.01 1.4.0

## Slide 2: Objective
Learn what PPP is

## Slide 3: What is PPP
PPP – Point-to-Point protocol is a layer 2 protocol that is used on either asynchronous, in other words dialup, or synchronous data lines as a simple way to transport packets between two peers
Its purpose is to get layer 3 packets across a serial point-to-point link that is full duplex
PPP was developed to replace SLIP – Serial Line Internet Protocol

## Slide 4: What is PPP
SLIP does not
  Support any layer 3 protocol but TCP/IP
  Allow dynamic IP address assignment
  Support authentication or encryption
  Operate at high speeds
PPP also extends on HDLC as described elsewhere, but part of which is used in PPP itself
The main extension is the use of NCP

## Slide 5: Operation
It is often said that PPP defines activity at both the physical and data link layers of the OSI model
In practice the only definition that PPP does concerning the physical layer is to say that there must be one, which is somewhat obvious, and to say that it must be a serial point-to-point link

## Slide 6: Operation
This makes PPP primarily a layer 2 protocol
At layer 2, PPP defines three sublayers

## Slide 7: PPP Layers
Layer 3
NCP
LCP
HDLC
Layer 1

## Slide 8: PPP Layered Architecture

## Slide 9: PPP at Layer 1
As stated, the physical layer for PPP is specified to be a serial communication method including
  EIA/TIA-232
  EIA/TIA-422
  V.35
The only requirement for this serial link is that circuit must be full duplex and asynchronous

## Slide 10: PPP at Layer 2
At layer 2 PPP begins to do its work
To do this work of carrying data from one end of a point-to-point serial link to the other, PPP must transition between several states

## Slide 11: PPP at Layer 2
Idle
Establishing
Authenticating
Networking
Terminating

## Slide 12: Establishing a PPP Session

## Slide 13: PPP Configuration Options

## Slide 14: PPP Operation

## Slide 15: Transition States
In the idle state the link is not being used
There is no active carrier on the line
In the establishing state the two end points have started communication
If any of the PPP options are to be used, they are negotiated here
During authentication, which is optional, the end points exchange information to establish they are who they say they are

## Slide 16: Transition States
When the networking state is reached the real transfer of data begins
The connection remains in this state until communication is terminated
In the termination state one side closes the link

## Slide 17: PPP Frame Format
To do its work PPP uses several different frames
The major PPP frame looks like this

## Slide 18: PPP Frame Format
Flag
Address
Control
Protocol
Data and Padding
FCS
Flag

## Slide 19: PPP Frame Format
These fields do the following
  Flag
    1 byte
    This field marks the start of the frame
    The value is always 0111110
  Address
    1 byte
    No purpose as PPP does not support addressing
    The address is always 11111111, which is the HDLC broadcast address

## Slide 20: PPP Frame Format
Control
  1 byte
  This is used to indicate that transmission of the data will not be sequenced and is to be sent over a connectionless link
  The value is always 00000011
Protocol
  2 bytes
  This field is used to direct whatever is in the data field to its proper location
  It identifies the encapsulated protocol

## Slide 21: PPP Frame Format
Data Field
  Variable size, but 1500 bytes is the default
  Larger sizes can be used, if both sides agree
  This field contains the important stuff
FCS
  2 bytes, but can be 4 bytes
  The FCS – Frame Check Sequence is the CRC used to ensure everything arrived intact

## Slide 22: PPP Frame Format
  Flag
    1 byte
    This field marks the end of the frame
    The value is always 0111110

## Slide 23: Protocol Field
The value in the protocol field is typically expressed as a hexadecimal number
Common codes include
  IP – 0021
  IPX – 002b

## Slide 24: HDLC in PPP
Although HDLC is discussed elsewhere as an alternative to PPP as a way to send data over a serial link, a form of HDLC is used to encapsulate the datagrams to be sent over the serial link

## Slide 25: Link Control Protocol
The LCP - Link Control Protocol is a part of the PPP specification
LCP is used to establish, configure, maintain, and terminate links
LCP information is carried in the data field of the PPP frame

## Slide 26: Link Control Protocol
The way a the device knows this data relates to LCP instead of data to be passed up the stack is by looking in the protocol field
LCP data is indicated by C021, a hexadecimal number, in that field
The LCP looks like this

## Slide 27: Link Control Protocol Format
Code
Identifier
Length
Information

## Slide 28: Link Control Protocol Format
The fields in this packet do the following
  Code
    1 byte
    The code defines the type of LCP packet this is
  Identifier
    1 byte
    This field is used to match a request to a reply
    One end point places a value in this field
    This value will be copied to the reply

## Slide 29: Link Control Protocol Format
  Length
    2 bytes
  Information
    Variable in length
    This field holds the extra information that is required by some types of LCP packets, such as whether authentication will be required

## Slide 30: PPP Capture File
Let’s look at some PPP frames
Download
  PPP with RIP.cap
Open it in Wireshark by double-clicking it
Select frame 1
This is a LCP PPP frame
In frame 13 we see a PPP ACK

## Slide 31: PPP Capture File

## Slide 32: PPP Capture File
In frame 15 some IP traffic appears
Then in frame 16 some CDP traffic
Notice in frame 15 that an IP address appears as the links begin to come up

## Slide 33: PPP Capture File

## Slide 34: PPP Capture File

## Slide 35: PPP Capture File
In frames 23 and 28 RIP begins to talk at both ends of the link

## Slide 36: PPP Capture File

## Slide 37: PPP Capture File
The RIP responses are in frames 31 and 35

## Slide 38: PPP Capture File

## Slide 39: PPP Capture File
Beginning with frame 50 a series of ping requests and responses go back and forth all carried at layer 2 by PPP

## Slide 40: PPP Capture File

## Slide 41: PPP Capture File
So we see here PPP hard at work carrying all types of information

## Slide 42: Authentication
Authentication was an important addition to PPP compared to SLIP
Authentication is not needed in a point-to-point link over a T1 line, but it is needed for a dialup connection
You want to know who you are talking to whenever you cannot control both ends of the connection

## Slide 43: Authentication
PPP can use either of two protocols for authentication
  PAP
  CHAP

## Slide 44: PPP Authentication Protocols

## Slide 45: PAP

## Slide 46: PAP
PAP – Password Authentication Protocol is very simple and basically useless
It works this way
  The user wanting access to an end point sends an authentication request that includes the username and password
  The end point either accepts or rejects the request

## Slide 47: PAP
The problem is the password is sent in clear text
PAP packets can be identified by the code C023 in the protocol field

## Slide 48: PPP Authentication Protocols

## Slide 49: CHAP
CHAP provides protection against playback attack through the use of a variable challenge value that is unique and unpredictable

## Slide 50: CHAP
CHAP – Challenge Handshake Authentication Protocol improves on PAP by keeping the password secret
CHAP will also recheck the authentication on a periodic basis
CHAP is indicated by C223 in the protocol field

## Slide 51: Encapsulation Authentication

## Slide 52: CHAP Authentication Process

## Slide 53: Configuring PPP Authentication

## Slide 54: PAP Configuration

## Slide 55: CHAP Configuration

## Slide 56: Compression
In addition to authentication, compression is another optional service offered by PPP
Compression does not have to be used, but it is very useful for dial-up connections

## Slide 57: PPP from Layer 2 to 3
At the top of PPP is the NCP – Network Control Protocol
NCP is used once LCP has established the connection and any authentication has taken place
At this stage NCP connects PPP to the higher level protocols that begin their work at layer 3

## Slide 58: PPP from Layer 2 to 3
More specifically it encapsulates the IP, IPX, or whatever other traffic comes down into a form PPP can deal with at layer 2
For example, IPCP – Internetwork Protocol Control Protocol is used by NCP to create and then terminate a connection that will send TCP/IP packets
The protocol field 8021 indicates this

## Slide 59: Network Control Protocol

## Slide 60: Using PPP
Using PPP is quite easy on most devices
For example to use PPP encapsulation on a Cisco router, just type
  encapsulation ppp
At the configure interface level

## Slide 61: Configuring PPP

## Slide 62: PPP Configuration Commands

## Slide 63: Verifying PPP

## Slide 64: Troubleshooting PPP
The first thing to do when a problem arises on a link that uses PPP is to check the physical connection
Also check the configuration of physical layer devices, such as the CSU/DSU
This is by far the most common source of the trouble

## Slide 65: Troubleshooting PPP
The next thing to check is the configuration of PPP in the router for a direct link or access server if a dial-up connection is being made
The most common error is when authentication is being used for the link
The username setting causes the most errors in this case

## Slide 66: Troubleshooting PPP
When configuring the username on a router, it is the hostname of the router at the other end of the connection
Consult the Oppenheimer and Bardwell text for more details on this issue

## Slide 67: Debug PPP Authentication

## Slide 68: For More Information
T1: A Survival Guide
  Matthew S. Gast
  ISBN 0-596-00127-4
Troubleshooting Campus Networks
  Priscilla Oppenheimer and Joseph Bardwell
  ISBN 0471210137