## Slide 1: PPPoE
Last Update 2011.07.21
1.4.0

## Slide 2: Objectives Of This Section
Learn
  What is PPPoE
  What layer PPPoE operates in
  Who is using PPPoE
  Why are they using PPPoE
  How PPPoE works

## Slide 3: What is PPPoE
PPPoE is Point-to-Point Protocol over Ethernet
PPPoE relies on two widely accepted standards
  PPP
  Ethernet

## Slide 4: What is PPPoE
PPPoE is a specification for connecting the users on an Ethernet network to the Internet through a common broadband medium, such as a single DSL line, wireless device, or cable modem
PPPoE uses tunneling to do this
  Tunneling involves the embedding of messages in one format within the packets of another format

## Slide 5: What is PPPoE
PPPoE functions similarly to virtual private networking tunneling protocols like PPTP - Point-to-Point Tunneling Protocol that are also derived from PPP
PPPoE operates at layer 2
Many home users do not even know if their connection to the Internet uses PPPoE

## Slide 6: What is PPPoE
If one's cable or DSL setup requires logging in to the Internet, most likely this setup involves PPPoE

## Slide 7: Why Are They Using PPPoE
PPPoE is used to allow Internet Service Providers to use their existing Radius authentication systems from their Dial-Up service over a broadband based connection
  Dial-Up uses PPP, most broadband connections use Ethernet, hence Point to Point Protocol over Ethernet

## Slide 8: Why Are They Using PPPoE
PPPoE mainly benefits the service provider
ISPs can manage IP addresses and track users in much the same way they manage their traditional dial-up service
  Each customer receives one IP address and network usage can easily be tracked to individual user accounts

## Slide 9: Why Are They Using PPPoE
PPPoE also theoretically benefits the home customer through ease of use
  Internet users accustomed to traditional dial-up will already be familiar with the PPPoE connection model
  Customers might be more comfortable entering their password each time they want to connect and having the ability to disconnect than they would with always on

## Slide 10: Why Are They Using PPPoE
  PPPoE offers better security and control for the home user than alternatives

## Slide 11: How PPPoE Works
PPPoE has two distinct stages
There is a Discovery stage and a PPP Session stage
When a host wishes to initiate a PPPoE session, it must first perform Discovery to identify the Ethernet MAC address of the peer and establish a PPPoE Session_ID

## Slide 12: How PPPoE Works
PPP defines a peer-to-peer relationship, Discovery is inherently a client-server relationship

## Slide 13: How PPPoE Works
The PPPoE Discovery Stage is made up of four steps
  Initiation
  Offer
  Request
  Session Confirmation

## Slide 14: PPPoE Frame Format
PPPoE uses a standard Ethernet II frame to carry its information
Let us recall when it looks like

## Slide 15: Ethernet II Frame Format

## Slide 16: Ethernet II Frame Format
Field | Bytes
Preamble | 8
Destination Address | 6
Source Address | 6
Type | 2
Data | 46-1500
Frame Check Sequence | 4

## Slide 17: PPPoE Frame Format
A PPPoE frame is made-up of three parts
  A PPP frame which is carried
  Inside a PPPoE frame
  Which is carried inside an Ethernet frame
As this nice graphics from www.h3c.com shows us

## Slide 18: PPPoE Frame Format

## Slide 19: PPPoE Frame Format
The PPPoE frame is placed in the Data field of the Ethernet frame
When this is done the Type code field contain one of these hexadecimal codes depending on which of two PPPoE messages are being sent
  8863 for the Discovery Stage
  8864 for the normal traffic flow stage

## Slide 20: PPPoE Frame Format
According to RFC 2516 the PPPoE frame itself looks like this

## Slide 21: PPPoE Frame Format

## Slide 22: PPPoE Frame Format
The fields in this frame do the following
  VER
    This four bits field must be set to 0x1 for this version of the PPPoE specification
  TYPE
    This field is four bits and must be set to 0x1 for this version of the PPPoE specification

## Slide 23: PPPoE Frame Format
  CODE
    An eight bit field
    Code value 0x00 indicates session data; 0x09 indicates PADI packets; 0x07 indicates PADO or PADT packets; 0x19 indicates PADR packets; 0x65 indicates PADS packets

## Slide 24: PPPoE Frame Format
  SESSION_ID
    This field is sixteen bits long
    The value is fixed for a given PPP session and, in fact, defines a PPP session along with the Ethernet SOURCE_ADDR and DESTINATION_ADDR

## Slide 25: PPPoE Frame Format
  LENGTH
    This field is sixteen bits long
    The value, in network byte order, indicates the length of the PPPoE payload
    It does not include the length of the Ethernet or PPPoE headers

## Slide 26: Capture File for PPPoE
Let’s look at a capture file of some PPPoE traffic
Download this file
  PPPoE.cap
Examine it using Wireshark by double-clicking on it
Frame 1 shows PPPoE looking for someone to talk to

## Slide 27: Capture File for PPPoE
The fields should match those we just discussed
Let’s see if they do

## Slide 28: Capture File for PPPoE

## Slide 29: Capture File for PPPoE
The device on the other end says hi, I will talk to you, who are you

## Slide 30: Capture File for PPPoE

## Slide 31: Capture File for PPPoE
The next few frames continue the session establishment process

## Slide 32: Capture File for PPPoE

## Slide 33: Capture File for PPPoE

## Slide 34: Capture File for PPPoE

## Slide 35: Capture File for PPPoE
Here is a are you there, yes I am, process similar to pinging

## Slide 36: Capture File for PPPoE

## Slide 37: Capture File for PPPoE

## Slide 38: Capture File for PPPoE
As you can see the PPPoE layer of the frames do not change much no matter what the higher layer protocols are up to

## Slide 39: PPPoE in Operation
Here is an example of the setup for a ADSL circuit that uses PPPoE

## Slide 40: PPPoE Operation

## Slide 41: PPPoE Operation

## Slide 42: Source
Some of this was copied from Newton’s Telecom Dictionary and RFC 2515