## Slide 1: Packet Over SONET
Last Update 2010.01.17
1.2.0

## Slide 2: Objectives of This Section
Learn
  What Packet over SONET is
  Where Packet over SONET is used

## Slide 3: Context
Layer | 1
Network Type | MAN WAN

## Slide 4: Layers
As a layer 1 technology Packet over SONET requires something at layers 2 through 7 in order to operate
Typically this is
  Layer 2
    PPP
  Layer 3 through 7
    TCP/IP

## Slide 5: What is PoS
Overhead on a data line always wastes expensive space
Some is of course necessary, but constant attention has gone into trying to reduce it as much as possible
PoS - Packet over SONET is one way to eliminate the overhead introduced by ATM, which is typically used at layer 2 when SONET is used at layer 1

## Slide 6: What is PoS
PoS attempts to place data as directly onto the physical SONET layer as possible
Cisco estimates that putting IP traffic directly onto SONET by using PoS instead of ATM produces a 25 to 30 percent increase in efficiency

## Slide 7: Operation
Recall that SONET is a high speed TDM based transport technology that was developed to carry voice traffic
PoS is used to place data into SONET frames by encapsulating it through a series of PPP like layer 2 frames
The sequence is

## Slide 8: Framing
PPP RFC 1661 Format
PPP in HDLC Like Framing RFC 1662 Format
Mapping and Scrambling
PPP Over SONET RFC 2615 Format

## Slide 9: Framing
At the top of this stack is the standard PPP frame format
Then some small alterations are made as it is transformed into the RFC 1662 version of PPP

## Slide 10: RFC 1662 PPP Frame Format
Flag
Address
Control
Protocol
Data and Padding
FCS
Flag

## Slide 11: RFC 1662 PPP Frame Format
These fields do the following
  Flag
    1 byte
    This field marks the start of the frame
    The value is always 0111110
  Address
    1 byte
    No purpose as PPP does not support addressing
    The address is always 11111111, which is the HDLC broadcast address

## Slide 12: RFC 1662 PPP Frame Format
Control
  1 byte
  This is used to indicate that transmission of the data will not be sequenced and is to be sent over a connectionless link
  The value is always 00000011
Protocol
  2 bytes
  This field is used to direct whatever is in the data field to its proper location
Data Field
  Variable size, but 1500 bytes is the default
  Larger sizes can be used, if both sides agree
  This field contains the important stuff

## Slide 13: RFC 1662 PPP Frame Format
  FCS
    2 bytes, but can be 4 bytes
    The FCS – Frame Check Sequence is the CRC used to ensure everything arrived intact
  Flag
    1 byte
    This field marks the end of the frame
    The value is always 0111110
As you can see, this is the standard PPP frame format

## Slide 14: Mapping and Scrambling
At the bottom of this collection of protocols are the alterations specified by RFC 2615 in order to place the data directly onto a SONET frame without the added overhead of something like ATM
The primary change is the need to add encryption to the data, as is typically done in ATM

## Slide 15: Current Use
PoS is typically deployed by the end user as a point-to-point link between two sites in a MAN

## Slide 16: Speeds
Common speeds range from OC-3 to OC-48
That is 155 Mbps to 2,488 Mbps

## Slide 17: For More Information
RFC 1662
RFC 2615