## Slide 1: X.25
Last Update 2011.06.05
1.6.0

## Slide 2: Objectives of This Section
Learn
  What X.25 is
  Where X.25 is used

## Slide 3: Context
Layer | 1 2 3
Network Type | WAN

## Slide 4: Layers
X.25 is from the old days
It was designed to handle all bottom three layers of the OSI model
It does not need any other protocols to work

## Slide 5: What is X.25
X.25 is a set of protocols defined by the ITU – International Telecommunications Union
It is widely used for low speed circuits because it is available world wide
In many cases it is the only reliable network service available
In the US it in generally no longer offered

## Slide 6: What is X.25
As the only document on the AT&T web site says

## Slide 7: What is X.25

## Slide 8: Current Usage
X.25 is commonly used for small size transactions such as
  Airline reservation systems
  Credit card authorizations
  ATMs
  POS terminals
  Short messaging services and text messages
This is because the maximum speed is about 200 kbps

## Slide 9: Current Usage
It has been estimated by Sangoma technologies, who still makes X.25 equipment that there is $10 billion invested worldwide in X.25 hardware
Some examples of networks using X.25 are
  A lottery system Spain
  The SITA system, used to communicate information among carriers and between the carriers, airlines, and other institutions

## Slide 10: Current Usage
  A cell phone system in India, where the gathering of billing data is X.25-based
  Many legacy systems are used by such large institutions as banks and phone companies

## Slide 11: Operation
X.25 is a packet switched network
To switch the packets from one place to another X.25 uses three devices
  DTE - Data Terminal Equipment
    These are the things that communicate across the network, such as terminals and PCs at the customer site
  DCE - Data Circuit Terminating Equipment
    These are the devices that create the X.25 network, such as modems and packet switches at the carrier’s site

## Slide 12: Operation
  PSE - Packet Switching Exchange Equipment
    These are the packet switches in the X.25 network
It all works like this

## Slide 13: Operation
The DTEs generate the data to be sent
The DCEs prepare the data
The PSEs operate inside the carriers network to carry the data from end to end
Either as a separate box or as software inside the DTE a PAD – Packet Assembler/Dissembler is used to format the data

## Slide 14: Operation
Local Office |  | Edge of Carrier’s Network | Carrier’s Network |  |  | Edge of Carrier’s Network | Remote Office | 
DTE | PAD | DCE | PSE | PSE | PSE | DCE | PAD | DTE

## Slide 15: Operation

## Slide 16: Operation
X.25 assumes the underlying circuit is very unreliable
An X.25 session starts when a DTE device contacts another DTE device to request a conversation
The session requires creation of a virtual circuit
If the request is accepted, the two systems begin full duplex transfer

## Slide 17: Operation
Data is sent serially from the DTE to the PAD
The PAD breaks the data into smaller pieces and adds the transmission overhead
The PAD then sends the packet to the first PSE
The PSE checks the CRC
If the CRC is ok, the PSE sends an acknowledgement back

## Slide 18: Operation
Then the PSE sends the packet to the next PSE
The first PSE holds the packet until the next PSE acknowledges receiving the packet
Finally, the receiving station receives the packet

## Slide 19: Operation
To move the packets through the network, X.25 defines protocols at all three bottom layers of the OSI model
At the network layer
  PLP – Packet Layer Protocol
At the data link layer
  LAPB – Link Access Procedure, Balanced
At the physical layer
  X.21

## Slide 20: Operation
The PLP protocol at the network layer manages the packet exchanges between the DTE devices
It does this in five phases
  Call setup
  Data transfer
  Idle
  Call clearing
  Restarting

## Slide 21: Operation
LAPB at the data link layer manages packet framing and communication between DTE and DCE devices
At the physical layer X.21 defines the physical medium

## Slide 22: Problems with X.25
Note the large amount of processing and the holds at each step
This is a slow process, but very reliable
The sequence of events is designed for a network that is prone to errors

## Slide 23: Carrier’s Network
Also keep in mind that the exact network that the carrier uses may or may not work as just described
The carrier is free to transmit data as it wishes, as long as it accepts and delivers data defined by X.25

## Slide 24: Carrier’s Network
X.25 as currently defined is only concerned with the portion of the route from the customer’s equipment to the carrier’s network, not what goes on inside the carrier’s network itself

## Slide 25: Speeds
The theoretical speed range is 2.4 Kbps to 2 Mbps
200 Kbps is about the practical maximum
Common speeds are 9.6 Kbps and 64 Kbps
There are not many high speed X.25 circuits