## Slide 1: 802.11 Equipment
Last Update 2008.12.09
1.2.0

## Slide 2: The Basic 802.11 Equipment
Only two parts are needed to create a 802.11b network
The parts are
  Access Point
  NIC
Such a network looks like this

## Slide 3: The Basic 802.11 Equipment

## Slide 4: What is an Access Point
An access point or AP provides a means to connect a wireless device to a wired network
It is the intermediary in the connection between the wired and wireless networks

## Slide 5: Access Point Operating Modes
An AP can operate in one of three modes
  Root Mode
  Repeater Mode
  Bridge Mode

## Slide 6: Root Mode
In root mode the AP is connected directly to the wired network by attaching a cable to the Ethernet port in the AP and to a hub or switch on the wired network
This is the default configuration for most access points
In root mode one access point can talk to another one by going through the wires they both share

## Slide 7: Root Mode
This type of conversation is required when a device communicating with one AP needs to talk to a device that is attached to another AP on the same wired network
APs also use this connection to coordinate roaming among access points similarly configured
In this mode an AP is operating as a bridge at layer 2 of the OSI model

## Slide 8: Communication in Root Mode

## Slide 9: Bridge Mode
In this mode the AP operates like a bridge
A bridge is a way to connect two physical parts of the same network together
Devices do not connect to bridges

## Slide 10: Bridge Mode

## Slide 11: Repeater Mode
In repeater mode an additional access point is used to wirelessly extend the range of an existing access point
This is done by having the clients at the extended distance connect wirelessly to the AP that is located away from the main access point
This extended access point then connects wirelessly back to the main AP

## Slide 12: Repeater Mode
The cell of the extended AP must overlap the cell of the main AP by 50 percent for this to work effectively
The throughput of the wireless LAN – Local Area Network is cut significantly as the repeater must receive and retransmit each frame on the channel
This basically doubles the traffic on the wireless media

## Slide 13: Repeater Mode
In general, to setup an AP for this role all that is required is to switch the AP to repeater mode, then set the SSID, which is the name of the wireless network, to match the SSID of the root mode AP
Not all APs have a repeater mode

## Slide 14: Repeater Mode

## Slide 15: Access Point Management
There is an ongoing argument concerning the way to manage an increasing number of access points
As organizations add more and more access points there is a need to limit the amount of time required to manage these
The suggested method is to use limited access points and wireless switches

## Slide 16: Access Point Management
The term wireless switch is an unfortunate marketing term for taking all of the intelligence out of the access points, which is fine, and placing it in a single box at the junction point between the wireless and wired networks

## Slide 17: Access Point Management
Here is a discussion on this from Ortronics
  Centralized wireless LANs use a wireless controller to manage, process, and configure your radio frequency (RF) environment
  The access points, sometimes called "thin APs", communicate directly with the central controller located at the edge of the wired network

## Slide 18: Access Point Management
  Unlike a traditional more costly access point, all the functionality and intelligence is offloaded to the controller
  This provides a single point of administration for various policies relating to security, intrusion detection, user roles, and software upgrade

## Slide 19: Access Point Management
  A traditional wireless LAN uses decentralized "fat" access points that perform all the network processing and functionality in each unit
  Manual configuration of each access point consumes valuable network administrator time to manually set power levels, channel, security, and many other configurable parameters

## Slide 20: Access Point Management
  In larger deployments, this could lead to configuration mistakes that go unnoticed causing performance problems or network security risks
  Firmware upgrades, to fix or add functionality, can be a painstaking process with as few as six access points
  Each AP will most likely have to be individually updated and touched by the administrator if remote upgrade tools are not available

## Slide 21: Access Point Management
  New standards, such as 802.11i for robust security, may require hardware replacement due to a lack of processing power or incompatibility with your existing access points
  Centralized deployment lowers total cost of ownership and solves many of the problems associated with older architectures

## Slide 22: Access Point Management
  Enhanced integrated functionality i.e. VPN, Secure VoIP fast roaming support, intrusion detection, stateful firewall, and auto calibration redundancy, are typically unsupported by distributed access points

## Slide 23: Access Point Management
  Wireless controllers inspect all wireless traffic prior to being sent to the wired network. Ortronics wireless controllers are able to automatically download minimal configuration parameters and are aware of surrounding access points so that calibration of power and channel settings occur

## Slide 24: Antenna Types
Most APs come with either a single dipole antenna or diversity antennas
A diversity antenna is simply multiple antennas connected to a single receiver
This helps to overcome multipath reception problems

## Slide 25: Access Point Options
Depending on price and manufacturer an access point may have some of the following options available
  Detachable Antenna
  Filtering
  Radio Cards
  Variable Power Output
  Wired Network Connection

## Slide 26: Detachable Antenna
With a detachable antenna it is possible to
  Mount the AP away from the antenna, such as the antenna outside and the AP inside
  Allow a higher gain antenna to be exchanged for the standard dipole

## Slide 27: Filtering
Filtering that is possible on an AP is usually
  MAC filtering
  Protocol filtering
In MAC filtering a table of those devices that are allowed on the network is kept based on the MAC address of each device

## Slide 28: Filtering
Protocol filtering allows the restriction of what type of network access is allowed through the wireless portion of the network

## Slide 29: Radio Cards
Most APs have a radio that is fixed in place
To change the radio requires a fork lift upgrade
In other words, throw out the existing AP and buy another one
Radio cards, added through PCMCIA slots, allow the radio portion of the AP to be upgraded

## Slide 30: Radio Cards
Another use of a radio card slot is to allow a single AP to perform two functions, such as standard access point and bridge in a single unit
A last use is to use the slot to add capacity without buying another AP

## Slide 31: Variable Power Output
Variable power output allows the power, in milliwatts, can be adjusted
Normally this is used to control the cell size the AP serves

## Slide 32: Wired Network Connection
The standard way of connecting an access point to the wired network is either a 10BaseT or 100BaseT connection
But this limits the distance the AP can be from the wired network to 100 meters
A fiber port, such as 100BaseFX, allows a more distant connection

## Slide 33: Example Access Point
Let’s look at an example of a typical access point
In this case a DLink DWL-900AP+
On the front of the unit are three lights
  Power
  LAN activity
  WAN activity

## Slide 34: Example Access Point
On the back
  Reset button
  Wired LAN connection
  Power supply connection

## Slide 35: DLink DWL-900AP+ Front
Power Wired LAN Activity Wireless LAN Activity

## Slide 36: DLink DWL-900AP+ Back
LAN Connection
Reset
Power Supply

## Slide 37: Setup
Once the physical connections are made the access point must be configured
In this example the DLink DWL-900AP+ is setup using the built-in setup program as seen in the pages that follow
In the first few screenshots the setup wizard is being used

## Slide 38: Setup
Then the normal method is shown where the individual setup pages are selected
Typical configuration steps include
  Login
  Set a password
  Select the SSID and channel

## Slide 39: Setup
  Enable WEP
  Set an IP address and subnet mask for the AP
  Setup the built-in DHCP server
  Set the operating mode
  Adjust the performance
  Setup MAC filtering

## Slide 40: Setup
After the AP is in operation the status of the network can be checked through the AP’s management program

## Slide 41: Login

## Slide 42: Setup Opening Menu

## Slide 43: Setup Wizard

## Slide 44: Password Setup

## Slide 45: SSID and Channel Setup

## Slide 46: WEP Setup

## Slide 47: Setup Wizard Finish

## Slide 48: Setup Wizard Finish

## Slide 49: WEP Setup

## Slide 50: IP Address Setup

## Slide 51: DHCP Server Setup

## Slide 52: Mode Setup

## Slide 53: Performance Adjustment

## Slide 54: MAC Filtering Setup

## Slide 55: Setup Saving and Recovery

## Slide 56: Password Setup

## Slide 57: Firmware Upgrade

## Slide 58: Activity

## Slide 59: Activity

## Slide 60: Activity

## Slide 61: Wireless Status

## Slide 62: Help Topics

## Slide 63: Wireless NIC
The next piece of equipment needed when creating a wireless network based on the 802.11 standards is a NIC – Network Interface Card
Recall that as in a wired network the NIC is used to allow a device to connect to the network
This is the link between a device and the network

## Slide 64: Wireless NIC
It puts information onto the network
It takes information off of the network

## Slide 65: NIC Forms
Wireless NICs come in several forms including these typical ones
  PCMCIA
  Adaptor Card
  USB Port Adaptor
  Compact Flash
  Wired to Wireless Bridge

## Slide 66: PCMCIA Form
PCMCIA is the format designed for laptop computers
As in

## Slide 67: PCMCIA NIC

## Slide 68: PCMCIA NIC

## Slide 69: PCMCIA NIC

## Slide 70: PCMCIA NIC

## Slide 71: CardBus v PC Card
There are two types of PCMCIA interfaces used in laptops
PC Card
  This is a 16 bit 3.3 or 5 volt interface
CardBus
  This is a 32 bit 3.3 volt interface
PC Card is the older one
It has not been used much since 1999

## Slide 72: CardBus v PC Card
This style of NIC an also be used in a desktop system by using an adaptor

## Slide 73: Desktop Wireless NIC
The PCMCIA form is sometimes used to make a NIC for use in a desktop computer
When used this way the PCMCIA card is inserted into a carrier that will attach to the bus in a desktop computer, such as the PCI bus
For example

## Slide 74: Wireless NIC – PCI

## Slide 75: Compact Flash Form
The CF - Compact Flash form of the NIC is used for PDAs and other handheld devices smaller than a laptop computer
These look like

## Slide 76: CF NIC

## Slide 77: CF NIC
CF NIC

## Slide 78: USB Port Form
A new form for a NIC is using the USB port to attach the NIC to the computer
As in

## Slide 79: USB Port Form

## Slide 80: Wired to Wireless Adaptor
Another new form for a NIC of sorts is the wired to wireless adaptor, also called a wireless bridge
This device functions like a bridge to allow a device with a built in wired NIC to attach to a wireless network without altering the built in NIC
As in

## Slide 81: Wired to Wireless Adaptor

## Slide 82: Wireless NIC Setup
The setup for a wireless NIC mirrors that of the access point for the most part
In this example, after the two opening screens the following is seen
  System parameters
  Radio frequency setup
  Performance setup
  Security setup

## Slide 83: NIC Utility Program

## Slide 84: NIC Setup Screen

## Slide 85: NIC System Parameters

## Slide 86: NIC RF Setup

## Slide 87: NIC Performance Setup

## Slide 88: NIC Security Setup

## Slide 89: Review
What are the major parts of a wireless LAN