## Slide 1: Wireless CAN
Last Update 2011.02.02
1.2.0

## Slide 2: Use of Wireless
Wireless links can be used to create a CAN where the use of a cable connection is too costly or the ground between points does not allow it, such as not controlling the right of way
We will see an example of each

## Slide 3: Useable Frequencies
For use in a CAN the frequencies that are useable are
  Unlicensed
    900 MHz
    2.4 GHz
    5 GHZ
    24 GHz
    60 GHz
  Semi-Licensed
    3.65 GHz

## Slide 4: Useable Frequencies
  Licensed
    6 GHz
    11 GHz
    18 GHz
    23 GHz

## Slide 5: Which Frequency to Use
The lowest cost way to create a short range point-to-point link such as is used in a CAN is to use a 5 GHz link
There is less interference in this band than there is in the 2.4 GHz band
900 MHz does not have enough bandwidth for it to be useable
Higher in cost are 24 GHz unlicensed links

## Slide 6: Which Frequency to Use
These are short range, low speed solutions right now
A semi-licensed solution when 5 GHz is too busy in an area is the 3.5 GHz band
The license cost is lower than the traditional licensed frequencies
The protection from interference is less than licensed frequencies

## Slide 7: Which Frequency to Use
The licensed solutions typically connect at 800 mbps to 1 Gig
Companies that offer these solutions include
  Dragonwave
  Nera
  Motorola Canopy
  Ligowave
  Ubiquiti

## Slide 8: Deployment
The actual deployment of this equipment, such as how to mount it outside or design the network to use it, are covered in separate presentations
It does not matter what frequency is deployed, the techniques concerning installation and management are the same

## Slide 9: Example Connection
In this first example a tower is located over 400 feet from the network operations center
The right of way between the two is accessible
However for this application the cost of running a cable is prohibitive
Here is the path

## Slide 10: Relationship of Facilities

## Slide 11: Obstructions
Notice that the line of sight between the two points is obstructed by trees as the antennas are mounted at the height of the middle of the trees
This was done to avoid the need to hire a tower climber
Normally this would be a problem

## Slide 12: Obstructions
In this case the short distance along with the high gain of the antennas allows this connection to be made

## Slide 13: Obstructions

## Slide 14: Obstructions

## Slide 15: Tower

## Slide 16: Network Operations Center

## Slide 17: Method of Connection

## Slide 18: Method of Connection

## Slide 19: Example Connection
The system illustrated here is used by the City of Joshua Texas to interconnect several of their facilities that are separated by a road and a railroad
In this case the right of way is not accessible
Here is the overhead view of the area

## Slide 20: Relationship of Facilities

## Slide 21: City Administration

## Slide 22: Public Works

## Slide 23: Fire Station

## Slide 24: Animal Control

## Slide 25: Typical Distance

## Slide 26: Method of Connection