## Slide 1: Modeling Networks Last Update 2011.08.01 121.0

## Slide 2: Objectives
To see how networks can be modeling and tested before deployment

## Slide 3: Modeling Networks
It is often useful to model a network before it is deployed into the real world
There are different types of modeling tools from simple to complex that can be used
We will look at four types of tools
  Application Testing Tool
  Simulator
  Emulator
  Network Modeling Tool

## Slide 4: Application Testing Tool
One type of application testing tool is one used to determine what hardware is needed to run an application
It is also good practice to test a new application before deploying it on the network to see how it will respond to common network problems
To do this a software based tool can be used to stand in for the network

## Slide 5: Application Testing Tool
This allows a real workstation to access a real server with the traffic going through the software based tool

## Slide 6: Simulator
A simulator is a program that is designed to present an environment that looks as near as possible to the real equipment it is simulating
The simulator used here is Packet Tracer

## Slide 7: Emulator
An emulator is a program designed to run programs on a computer that would normally be run on a separate piece of equipment
Virtualization programs such as VMWare are emulators
The emulator used here is GNS3

## Slide 8: Network Modeling Tool
Network modeling tools are designed to present as realistically as possible a complex real world network
The network modeling tool that will be used in this example is Opnet

## Slide 9: Application Testing Tool
Let’s look at an example of a sizing tool used before deploying an application

## Slide 10: Application Testing Tool
Now let’s see how application performance is tested using WANem as an example of this type of tool
WANem works by attaching three computers to a network
Typically one computer is used as a workstation such as an end user would use to access the application

## Slide 11: Application Testing Tool
Another is used to run the application on a server such as would be used in the actual deployment of the application
The last runs WANem to serve as the network
As the WANem documentation points out it looks like this

## Slide 12: Application Testing Tool

## Slide 13: Application Testing Tool
Once the network is created as shown above one or more problems are introduced into the network while the application is being accessed by the end user
The impact of this can then be seen at both the end user and server ends

## Slide 14: Sample Network Simulation
Let’s create a sample network to see how Packet Tracer simulates a network

## Slide 15: Sample Network Simulation
Start creating the network by loading a background grid using the Set Tiled Background button
Select the
  grid_25x25.png
for this example

## Slide 16: Sample Network Simulation

## Slide 17: Sample Network Simulation
Select the Generic PC under End Devices and drag it as the first PC onto the workspace

## Slide 18: Sample Network Simulation

## Slide 19: Sample Network Simulation
Always remember to close windows after you're done viewing them, otherwise, they will clutter the workspace
Open the PC's configuration window and change its settings by going to the Config tab

## Slide 20: Sample Network Simulation

## Slide 21: Sample Network Simulation
Change the PC's name to Tokyo
Under Interface, click on FastEthernet and set the IP address as 192.168.1.1

## Slide 22: Sample Network Simulation
It will assume other settings for you
Make sure that the Port Status is on
Note for future reference that you could modify other Ethernet interface settings, such as bandwidth, duplex, MAC address, and subnet mask in this window
Drag another PC to the workspace, name it Paris and set its IP address as 192.168.1.2

## Slide 23: Sample Network Simulation
Make sure that the Port Status is on
Under Connections, select the Copper Straight-through cable, the solid black line, and make a connection between the devices with it
The red lights on the link indicate that the connection is not working
The point is the simulator will do what you tell it, whether that is right ort wrong

## Slide 24: Sample Network Simulation
Now, using the Delete tool, remove the Copper Straight-through cable, and use a Copper Cross-over cable instead

## Slide 25: Sample Network Simulation

## Slide 26: Sample Network Simulation
The lights should turn green at this point, and if you mouse over or hover over either PC, you'll see the link status indicated as up

## Slide 27: Sample Network Simulation
Your network should look similar to this

## Slide 28: Sample Network Simulation

## Slide 29: Sample Network Simulation
Reposition your network devices by dragging them
Add an overall network description by using the i button on the upper right corner of Packet Tracer
Then add some text labels on the logical workspace by using the Place Note tool

## Slide 30: Sample Network Simulation

## Slide 31: Sample Network Simulation
Single click on the Tokyo PC
Turn the PC on and off and on again, while paying attention to the link lights
Do the same step for the Paris PC
Turning devices off will result in red link lights meaning that the link is down
Save your work by using the File -> Save As option

## Slide 32: Sample Network Simulation
Start with your original saved file open
Notice you are in Realtime Mode
Use the Add Simple PDU tool to send a simple 1-time ping message called an echo request, to the other PC, which responds with an echo reply because you have properly configured their IP address settings

## Slide 33: Sample Network Simulation

## Slide 34: Sample Network Simulation
To use the Add Simple PDU tool
  Click on it
  Click on the first PC
  Click on the second PC
Then look down in the bottom right corner to see if the ping was successful

## Slide 35: Sample Network Simulation

## Slide 36: Sample Network Simulation
Scroll around in the User Created Packet Window to see the different aspects of this ping message, including an indication that the ping was successful
Alternatively, toggle the PDU List Window to see a larger display of this message

## Slide 37: Sample Network Simulation

## Slide 38: Sample Network Simulation
You can save one or more of these messages as a scenario
When you start, you are in Scenario 0
Label this first scenario with an i note
Different scenarios allow you to use the same topology for experiments with different groupings of user created packets
Click on New to create a new scenario

## Slide 39: Sample Network Simulation
New scenarios will always initially be blank
Add two packets by using the Simple PDU tool, perhaps a PDU from Paris to Tokyo and a different PDU from Tokyo to Paris
Then add a little i note describing the scenario, to complete Scenario 1
An example is shown next

## Slide 40: Sample Network Simulation

## Slide 41: Sample Network Simulation
Go back and forth between Scenario 0 and 1
Several different scenarios can be saved for a single network
Now delete Scenario 1 using the Delete button
You are back at Scenario 0

## Slide 42: Sample Network Simulation
If you want to remove the PDU, you could scroll across in the User Created Packet Window and click on delete on the last column
Do so
Delete the whole scenario

## Slide 43: Sample Network Simulation
Start with your original saved file open
In Realtime Mode, send a simple PDU from Tokyo to Paris
Delete the PDU by using the method learned in the previous section
Switch to Simulation Mode

## Slide 44: Sample Network Simulation
In this mode, time freezes, therefore you can watch your network run at a slower pace, observing the paths that packets take and inspecting them in detail packet tracing
Under the Event List Filters, click on All/None to uncheck all fields, and then click on ICMP to only view ICMP packets in the animation

## Slide 45: Sample Network Simulation
Add a simple PDU from Tokyo to Paris
The eye icon at the left of the Event List indicates that this packet is currently displayed as an envelope
Click on Capture/Forward button once
This acts like a network sniffing program, capturing the next event that occurs on the network

## Slide 46: Sample Network Simulation
Note that after clicking on Capture/Forward, the packet in the workspace moves from one device to another - this is the ICMP echo request message from Tokyo to Paris
Another event is also added in the Event List this reflects the change that happened in the workspace

## Slide 47: Sample Network Simulation
The first time through an animation, the meaning of the Capture/Forward is Capture; after resetting the simulation, the meaning would be Forward
Adjust the speed of the animation by dragging the Play Speed slider to the right
Click on Capture/Forward button a second time

## Slide 48: Sample Network Simulation
This captures the next network event - this is the echo reply from Paris to Tokyo, shown as successful with a green check mark on the envelope, and the animation plays faster this time
Dragging the speed slider to the opposite direction - to the left - would have slowed the animation
Click on Capture/Forward button again

## Slide 49: Sample Network Simulation
At this point, Paris has already sent an echo reply to Tokyo therefore, there are no more ICMP events left to capture
A No More Events window will appear notifying you of this, as shown in the screenshot below
Click OK

## Slide 50: Sample Network Simulation

## Slide 51: Sample Network Simulation
Continuing from the last activity, click on Reset Simulation
This clears the entries in the Event List except for the original packet
Click on the packet envelope on the workspace to bring up the PDU Information window like the one shown in the screenshot below

## Slide 52: Sample Network Simulation
This window contains the OSI model tab which shows how the packet is processed at each layer of the OSI model by the current device
Close this window, and note that this packet is indicated in the Event List by the eye icon
The whole row in the Event List is also highlighted

## Slide 53: Sample Network Simulation
For this row, clicking on the color square in the Info column is equivalent to clicking directly on the packet envelope

## Slide 54: Sample Network Simulation

## Slide 55: Sample Network Simulation
Use the Next Layer and Previous Layer buttons to see details of the packet processing at the relevant OSI Layers
Note that only the Out Layers can be viewed in the case of this original echo request message

## Slide 56: Sample Network Simulation
Click on the Outbound PDU Details tab
This shows exactly what is in the PDU headers, broken up into header type and the individual fields in each header
Close the PDU Information window
Click on Capture/Forward button once

## Slide 57: Sample Network Simulation
Click again on the packet in the workspace to open the PDU Information window
Notice that this time, information regarding the In Layers and Out Layers can both be viewed
Click on the Inbound PDU Details tab

## Slide 58: Sample Network Simulation
In this case this shows the details of the inbound echo request packet from Tokyo to Paris
Click on the Outbound PDU Details tab, which shows similar information, but in this case for the echo reply packet from Paris to Tokyo

## Slide 59: Sample Network Simulation
Click on Reset Simulation again
This time click on Auto Capture/Play
The echo request and echo reply will be automatically captured, and the No More Events message will occur automatically

## Slide 60: Sample Network Simulation
Click on the Back Button twice to rewind the animation one step at a time
Now click on the Capture/Forward button twice to forward the packet through the animation
Also note the change in which packet is highlighted in the Event List

## Slide 61: Sample Network Simulation
Remember that at any time, you can either click on the packet envelope directly, or click on the Info column in the Event List, to open up the PDU Information window
Click on the Back Button twice to rewind the animation
This time click Auto Capture/Play and the packet animation will automatically occur

## Slide 62: Sample Network Simulation
Start by closing the existing workspace and reopening your original saved file
Open the ARP Tables for both PCs by clicking on each PC using the Inspect tool
The ARP tables always appear on the same spot
Reposition one of them to make them both visible

## Slide 63: Sample Network Simulation
You can also resize the tables for better viewing
In Realtime Mode, send a simple PDU from Tokyo to Paris
Notice that the ARP tables are filled in automatically as shown here

## Slide 64: Sample Network Simulation

## Slide 65: Sample Network Simulation
Delete the PDU using the method learned in the previous sections
Notice that the entries in the ARP tables are not cleared
This is so because the ARP entries for both devices have already been learned
Deleting the user created PDUs does not reset what already occurred in the network

## Slide 66: Sample Network Simulation
Click Reset Network
Notice that the ARP tables are cleared
The Reset Network button power cycles devices by turning them off and then on
By doing so, they lose temporary information like the tables they learned
Go to Simulation Mode

## Slide 67: Sample Network Simulation
In the Event List Filters, make sure that ICMP and ARP are checked so that you can view ICMP and ARP packets in the animation
Create a new simple PDU from Tokyo to Paris
Notice that since you reset the network earlier, the ARP tables are empty

## Slide 68: Sample Network Simulation
ARP request packets need to be issued before the ICMP ping packets, so that the devices in the network can learn about each other
Click on Auto Capture/Play to watch the animation
Click on Reset Simulation

## Slide 69: Sample Network Simulation
Notice that even though the Event List is cleared - except for the user created PDU, the ARP tables still remain full
Click on Capture/Play
This time, since the ARP tables are full, there are no new ARP packets issued
Click on Reset Network
Doing so will empty the tables

## Slide 70: Sample Network Simulation
Notice that a new ARP request packet appears automatically on the Event List
Single-clicking on the Delete button removes the entire scenario including all the PDUs associated with it
Double-clicking on (delete) in the far right column in the PDU List window deletes individual PDUs

## Slide 71: Sample Network Simulation
The Reset Simulation button clears all entries in the Event List, except for User Created PDUs, and allows you to restart the animation
This, however, does not reset the device tables
The Reset Network button allows you to power-cycle all of the devices in your network

## Slide 72: Sample Network Simulation
It turns all devices off and then turns them back on so the tables that the devices built are lost along with configurations and other information not automatically saved
Saving your work periodically prevents you from losing configurations and changes in the network that you want to keep

## Slide 73: Sample Network Emulation
Let’s switch to emulating instead of simulating the network design
In this example using GNS3 we will be running not a simulation of the Cisco IOS, but the real Cisco IOS
This brings the experience nearer to what you would see in the actual network

## Slide 74: Sample Network Emulation
To see how GNS3 works we will create a simple topology
  The GNS3 window is divided into four panes by default
    The left-most pane lists the types of nodes available
      You will see router icons for the various platforms, a PIX firewall, Ethernet switch, ATM bridge, ATM switch, Frame Relay switch, and Cloud
      Other node types may be added as explained later

## Slide 75: Sample Network Emulation
    The right-most pane will provide a topology summary that will be better understood when we built more complex topologies
      For now, just know that the pane exists
    The middle section contains two panes
      The top pane is your work area where a topology may be graphically built
      The bottom pane, called the Console, shows Dynagen at work
        Click on a router icon under Nodes Types corresponding to the IOS platform you are using
        In our example, we are using a 7200 platform

## Slide 76: Sample Network Emulation
        Drag an appropriate router node type over to the workplace pane in the middle and let go
        We now have a router ready to configure
        Right-click the router and choose Configure
        Click the Slots tab to see what is already there if anything
        If there are none, select some
        Click
          Ok

## Slide 77: Sample Network Emulation

## Slide 78: Sample Network Emulation

## Slide 79: Sample Network Emulation

## Slide 80: Sample Network Emulation

## Slide 81: Sample Network Emulation
Start the router by right clicking on the router and selecting
  Start

## Slide 82: Sample Network Emulation

## Slide 83: Sample Network Emulation

## Slide 84: Sample Network Emulation
Now access the command line of the IOS by right clicking on the router and selecting
  Console

## Slide 85: Sample Network Emulation

## Slide 86: Sample Network Emulation
Look around as you would do on any Cisco router

## Slide 87: Adjust the Balance
Another digression
When the first lab is done a setting needs to be adjusted so that Dynamips does not use up all of the resources of the computer it is running on
This should be done with just one router in place

## Slide 88: Adjust the Balance
To do this
  Right-click the router and choose Idle PC
    GNS3 will spend a moment calculating an Idle PC value before presenting the screen to the right
    If you click the drop-down arrow, you see a list of possible idlepc values
    Potentially better idlepc values are marked with an asterisk
    Choose one of the values with an asterisk and click OK

## Slide 89: Adjust the Balance
    You’ll receive a confirmation that the idlepc value has been applied

## Slide 90: Adjust the Balance

## Slide 91: Adjust the Balance

## Slide 92: Adjust the Balance
If you choose IOS images and hypervisors on the Edit menu, and doubleclick on the image under the IOS Images tab, you’ll see the new idlepc value displayed under Settings
You may repeat this process to find the value that reduces CPU usage the most

## Slide 93: Adjust the Balance
To observe CPU usage in Windows, press Ctrl+ALT+DEL and choose Task Manager
Click on the Performance tab to view CPU usage
You will observe that without an idlepc value, CPU usage will be at or near 100%, but with an idlepc value, CPU usage will drop to a very low value

## Slide 94: Sample Network Emulation
You may now return to your client window to use your router
You are actually running the Cisco IOS that you found
All commands supported by the IOS are available
Remember earlier we chose a FastEthernet adapter and a four-port serial adapter

## Slide 95: Sample Network Emulation
If you issue the show ip interface brief command, you’ll see the designations for these ports on the router
Exit GNS3

## Slide 96: Sample Network Emulation
Although a single router is useful to get familiar with commands, it would be nice to build more complex topologies
With GNS3 very complex topologies may be built
Let’s build a topology with three routers

## Slide 97: Name the Project
The next time GNS3 is started it will ask for a project name
Start GNS3
You can name a project if you wish or click Cancel

## Slide 98: Name the Project

## Slide 99: Sample Network Emulation
Drag three routers running an IOS you have configured into the workspace
Right-click each router and choose Configure under the Slots tab, include a FastEthernet adapter and PA-4T serial adapter
Now we’re ready to connect the routers together

## Slide 100: Sample Network Emulation
Click the Add a link button on the toolbar at the top

## Slide 101: Sample Network Emulation

## Slide 102: Sample Network Emulation
Choose Manual from the drop-down menu
Your cursor will change to a cross
Click on R1 and select s1/0 – then click on R1 and select s1/0
Click on R2 again and select s1/1 – then click on R3 and select s1/1

## Slide 103: Sample Network Emulation
Now click the Add a link button again, it looks like a red stop sign with an X
After clicking on it, the icon will change back to a connector look
Notice the right-pane call Topology Summary
Your connections are now available for viewing by clicking beside each router

## Slide 104: Sample Network Emulation
Configure the routers
Then test the connectivity

## Slide 105: Sample Network Model
Application testing, simulation, and emulation work well for basic network designs
For more complex ones a network modeling tool such as Opnet is needed to validate the design before deployment
Let’s see how Opnet works

## Slide 106: Sample Network Model
To illustrate how to use IT Guru let’s create a Sample Network Model with one scenario
Select
  File
  New

## Slide 107: Sample Network Model

## Slide 108: Sample Network Model
The Project screen appears
Although there are other options in the drop down box, Project is the only one commonly used
Click
  OK

## Slide 109: Sample Network Model

## Slide 110: Sample Network Model
On this screen you may name the project
You may also name the scenario
Spaces are not allowed
Click
  OK

## Slide 111: Sample Network Model

## Slide 112: Sample Network Model
On the next screen, Startup Wizard: Initial Topology, commonly the default Create Empty Scenario is used
Click
  Next

## Slide 113: Sample Network Model

## Slide 114: Startup Wizard
The Startup Wizard is used to create the basic layout of the network
The elements it uses are
  Define the network’s scale such as the world or an office
  Define the size of the area in which the network will function, such as the US or a certain size office
  Select a palette that will provide the objects

## Slide 115: Sample Network Model
On this screen select the scale of the network
For this example use the Office
Click
  Next

## Slide 116: Sample Network Model

## Slide 117: Sample Network Model
Set the size of the network just specified
For this example use 100 by 100 meters
Click
  Next

## Slide 118: Sample Network Model

## Slide 119: Sample Network Model
Select the Palette contents
The Palette holds the icons for the elements that can be dragged and dropped onto the network space just created
There are a large number of these
It is best to add the ones you think might be useful based on the name of the Palette

## Slide 120: Sample Network Model
Then experience will tell you which ones are most useful to your situation
The basic ones are

## Slide 121: Cisco

## Slide 122: Client Server

## Slide 123: Ethernet

## Slide 124: Ethernet Advanced

## Slide 125: Frame Relay

## Slide 126: Frame Relay Advanced

## Slide 127: Internet Toolbox

## Slide 128: LANs

## Slide 129: Links

## Slide 130: Links Advanced

## Slide 131: Wireless LAN

## Slide 132: Sample Network Model
Once the palette or palettes are selected click
  Next

## Slide 133: Palette List

## Slide 134: Sample Network Model
If you need additional devices other devices can be added to the palette by selecting
  Configure Palette
from the Palette window
This produces this list

## Slide 135: Sample Network Model

## Slide 136: Sample Network Model
Then the drop down list can be used to select one or more palettes
The existing palette can be removed by selecting
  Clear

## Slide 137: Sample Network Model

## Slide 138: Sample Network Model
In this example we will use the Ethernet palette to create a basic LAN

## Slide 139: Sample Network Model
The Startup Wizard: Review screen appears
If everything is as desired, then click
  OK
If not, click
  Back

## Slide 140: Sample Network Model

## Slide 141: Sample Network Model
The workspace with the palette appears

## Slide 142: Sample Network Model

## Slide 143: Sample Network Model
Notice that the palette often gets in the way of the workspace where the network elements are placed
To remove the palette from the screen click on the
  X box in the window
To return it to the screen click on the Palette button

## Slide 144: IT Guru Interface
Where is the palette button
Let’s look at the rest of the IT Guru interface

## Slide 145: IT Guru Interface

## Slide 146: Palette Button

## Slide 147: Palette Button
This button makes the palette appear, if you removed it from the screen

## Slide 148: Consistency Button

## Slide 149: Consistency Button
Check consistency of network links

## Slide 150: Failed Button

## Slide 151: Failed Button
Mark selected node or link as failed

## Slide 152: Restored Button

## Slide 153: Restored Button
Mark selected node or link as restored

## Slide 154: Level Button

## Slide 155: Level Button
Go to next higher level in network hierarchy

## Slide 156: Zoom In Button

## Slide 157: Zoom In Button
Zoom in for a closer look

## Slide 158: Zoom Out Button

## Slide 159: Zoom Out Button
Zoom out for a wider look

## Slide 160: Simulation Button

## Slide 161: Simulation Button
Configure, then run the simulation

## Slide 162: Results Button

## Slide 163: Results Button
View graphs and tables of collected statistics

## Slide 164: Graphs Button

## Slide 165: Graphs Button
Hide or show all graphs

## Slide 166: Sample Network Model
Back to the sample project
With the palette showing drag and drop the devices needed for the network of interest
These can be of two types
  Node
  Link

## Slide 167: Nodes
Nodes are devices that can send and receive information, such as
  Switch
  Workstation
  Printer
  Server

## Slide 168: Links
Links are media that connect nodes to each other

## Slide 169: Drag and Drop Behavior
Another oddity of IT Guru is the behavior of the drag and drop function
You left click on the object in the palette, then drag it over to the workspace
However, unless you deselect the object or go back to the palette, each subsequent click on the workspace will deposit another object of the same type

## Slide 170: Drag and Drop Behavior
To unselect an object, click the right mouse button
Then go back to the palette for the next object
The point to this behavior is to allow multiple copies of the same object to be placed one after the other
The object still looks like it is selected, but it is not

## Slide 171: Drag and Drop Behavior
Just click elsewhere on the workspace to make the circle around the object disappear

## Slide 172: Network Creation Methods
There are three ways to create a network
  Drag and Drop
  Rapid Configuration
  Importation

## Slide 173: Drag and Drop
In Drag and Drop nodes and links are selected on the palette, then dragged to the workspace

## Slide 174: Rapid Configuration
Rapid Configuration is faster than Drag and Drop for large networks
Select
  Topology
  Rapid Configuration
Then complete the options presented

## Slide 175: Rapid Configuration

## Slide 176: Rapid Configuration
Let’s create a basic LAN using this method
This step is done after the workspace is completed as discussed above
A basic LAN will require
  The Ethernet palette
  Star configuration
  A 16 port switch
  Links using 100 Mbps
  10 workstations

## Slide 177: Rapid Configuration

## Slide 178: Rapid Configuration

## Slide 179: Rapid Configuration

## Slide 180: Rapid Configuration
This only sets up the basic layout, such as what everything attaches to, the number of workstations, and the link speed between devices
This method will not bring in devices, such as servers
It also will not place the application or profile icons in the workspace

## Slide 181: Rapid Configuration
The palette is used to bring the rest of the objects in

## Slide 182: Importation
Go on to the next slide as this section has not been completed yet

## Slide 183: Sample Network Model
The link objects are used to connect the devices to each other
In this example the 100BaseT link will be used
It does not matter what order is used to connect the devices to each other
Just click on one, then the other
Again right click to deselect the link object

## Slide 184: Sample Network Model
For our sample project reduce the number of workstations to five by deleting nodes 5 through 9
To delete an object select it, then right click
We also need to and a server and a printer
From the Ethernet palette select and place these two objects

## Slide 185: Sample Network Model
Now we have a functioning network so the palette can be dismissed from the workspace
With the palette gone rearrange the devices so they are easier to see
This is the result for my sample network

## Slide 186: Sample Network Model

## Slide 187: Sample Network Model
We have the devices we need, but the devices can do nothing without two additional elements
These are the ones mentioned above
  Application Definition
    Applications that will run on the network
  Profile Definition
    Applications an object will use

## Slide 188: Sample Network Model
You drag and drop these two elements from the palette as well
These last two objects are used to set the overall behavior for the simulation
This makes the sample network look like this

## Slide 189: Sample Network Model

## Slide 190: Set Application Attributes
The Application Definition object defines what applications will run over the network
To select the applications right click on the Application Definition object
Don’t worry about the following diagram being different from our sample network, this is just an illustration of how to select the Application Definition object

## Slide 191: Set Object Attributes

## Slide 192: Set Object Attributes
Select
  Edit Attributes
To add applications click on the
  Applications Definitions
line
The click on the number to the right of
  Rows

## Slide 193: Set Application Attributes
Click on the
  0
to the right of Rows
Select the number of applications that will run on the network
That number of application rows will appear
The row numbering will start with 0

## Slide 194: Set Application Attributes
Click on the
  +
for the row
Then click on the
  +
beside the word Description
This produces a list of the common applications found on a network

## Slide 195: Set Application Attributes

## Slide 196: Set Application Attributes
To add an application click on the
  Off
to the right of the name of the application

## Slide 197: Set Application Attributes

## Slide 198: Set Application Attributes
After the applications that will run on the network are set click
  OK

## Slide 199: Set Application Usage
OPNET uses a probabilistic model to create the traffic
These values can be adjusted to match your network or the default values can be used
The exact name of the various objects may differ slightly from the examples shown next depending on the version of OPNET being used

## Slide 200: Set Application Usage
  Database Access (Light)
    50% database queries, 50% database entries
    Transactions arrive with inter-arrival times exponentially distributed with mean 30 seconds
    Each transaction is 16 bytes

## Slide 201: Set Application Usage
  Email (Light)
    Emails are sent with inter-arrival times exponentially distributed with mean 3600 seconds
    Each email is sent to a group of 3
    Emails are received with inter-arrival times exponentially distributed with mean 3600 seconds
    Each email is received by a group of 3
    Each email is 500 bytes.

## Slide 202: Set Application Usage
  File Transfer (Heavy)
    50% of file transfers from client to server (put), 50% from server to client (get)
    The time between each client’s file transfer requests, is exponentially distributed with mean 360 seconds
    All files are 50000 bytes

## Slide 203: Set Application Usage
  File Transfer (Light)
    50% of file transfers from client to server (put), 50% from server to client (get)
    The time between each client’s file transfer requests, is exponentially distributed with mean 360 seconds
    All files are 1000 bytes

## Slide 204: Set Application Usage
  File Print (Light)
    Print requests arrive with inter-arrival times exponentially distributed with mean 90 seconds
    Print requests are normally distributed with mean 3000 bytes, standard deviation of 300 bytes

## Slide 205: Set Application Usage
  Web Browsing (Heavy HTTP 1.1)
    Page inter-arrival times are exponentially distributed with mean 60 seconds
    Each Page has 1000 bytes of text 5 “medium images” each with size randomly picked with a uniform distribution on [500,2000] bytes

## Slide 206: Set Application Usage
  Web Browsing (Light HTTP 1.1)
    Page inter-arrival times are exponentially distributed with mean 720 seconds
    Each Page has 500 bytes of text 5 “small images” each with size randomly picked with a uniform distribution on [10,400] bytes

## Slide 207: Set Application Usage
  Telnet (Light)
    Inter Command time normally distributed with mean 120 seconds, variance 10
    Each command from terminal to telnet host consists of a normally distributed amount of bytes with mean 10, variance 4
    Each command from telnet host to terminal consists of a normally distributed amount of bytes with mean 5, variance 2.778

## Slide 208: Set Application Usage
A default set of applications can be used instead of defining each one individually
To use the default set
Right click on the Application Definition element
Select
  Edit Attributes
On the Application Definitions row click on the right side

## Slide 209: Set Application Usage
Select
  Default

## Slide 210: Set Application Usage

## Slide 211: Set Application Usage
This provides a common set of network applications such as
  HTTP
  FTP
  Email
  Database
  And so on

## Slide 212: Set Application Usage
The next task is to create profiles
These profiles are collections of applications, as just defined above, that individuals or groups using the network will use
This is the second step in placing activity on the network

## Slide 213: Set Application Usage
The last part of injecting traffic is to assign a profile to an object on the network, such as a server or a workstation
The Profile Definition element is used for this purpose
To configure the Profile Definition object right click on it
Then select
  Edit Attributes

## Slide 214: Set Application Usage

## Slide 215: Set Application Usage
  Profile Configuration
Click on the right side of the
  row
This will produce a drop down list
Select
  Edit

## Slide 216: Set Application Usage

## Slide 217: Set Application Usage
Another window will appear
Click on the 0 in the box top the left of Rows

## Slide 218: Set Application Usage

## Slide 219: Set Application Usage
Select
  1
row for this example

## Slide 220: Set Application Usage

## Slide 221: Set Application Usage
The row or rows will appear above

## Slide 222: Set Application Usage

## Slide 223: Set Application Usage
Change the profile name under the Profile Name column on the left by clicking on
  Enter Profile Name…
For this example enter
  Web User

## Slide 224: Set Application Usage

## Slide 225: Set Application Usage
Also for this example change the Repeatability to
  unlimited

## Slide 226: Set Application Usage

## Slide 227: Set Application Usage
Under the Applications column select
  Edit
Then select
  1
In the box to the left of Rows

## Slide 228: Set Application Usage

## Slide 229: Set Application Usage
Click under the Name column
Select
  Web Browsing (Heavy HTTP 1.1)
for this example
Then close all windows by clicking
  OK
  OK
  OK

## Slide 230: Set Application Usage

## Slide 231: Set Application Usage
The traffic profile has been created
Now it can be applied to the workstations

## Slide 232: Set Application Usage
Select one of the workstations by clicking on it
Right click on it
From the pop up menu select
  Select Similar Nodes

## Slide 233: Set Application Usage

## Slide 234: Set Application Usage
In general end devices, such as workstations generate traffic
Connection points, such as switches, do not
In this example, left click on the workstation

## Slide 235: Set Application Usage
While holding down the Crtl key click on the remaining workstations so all of then are selected
Right click and select
  Edit Attributes

## Slide 236: Set Application Usage

## Slide 237: Set Application Usage
On the Attributes window select
  Apply Changes to Selected Objects
In the bottom left corner of the window so the changes made in this window will apply to all the workstations

## Slide 238: Set Application Usage

## Slide 239: Set Application Usage
Click the
  +
beside Application Supported Profiles
And the
  0
To the right
Then select the number of profiles to be used

## Slide 240: Set Application Usage
In this case
  1
One row will appear
Select
  Web User
as defined above

## Slide 241: Set Application Usage

## Slide 242: Set Application Usage
Click
  OK
The workstations are ready to generate traffic
For this example the server must be configured as well so the web traffic has somewhere to go
Right click on the Server
Select Edit Attributes

## Slide 243: Set Application Usage
Select
  Edit
On the Application Supported Services row
A new window appears

## Slide 244: Set Application Usage

## Slide 245: Set Application Usage

## Slide 246: Set Application Usage
Select
  1
In the box to the left of Row

## Slide 247: Set Application Usage

## Slide 248: Set Application Usage
Select
  Web
By clicking on
  None
In the Name column
As above select
  Web Browsing (Heavy HTTP 1.1)
to create a generic HTTP server

## Slide 249: Set Application Usage
Then Click
  OK
  OK

## Slide 250: Set Application Usage

## Slide 251: Select Functions to Measure
The last configuration step is to select what to measure
There are two basic types of measures
  Individual
  Global
Individual measures apply to an object
Global measures apply to the network as a whole

## Slide 252: Select Individual Measures
To select individual measures right click the object, such as a server
The select
  Chose Individual Statistics
from the popup menu
This shows a list of things that can be measured

## Slide 253: Select Individual Measures

## Slide 254: Select Individual Measures
To select on expand the item of interest by clicking on the
  +
Then select the items to be measured
Such as
  Server Http
    Traffic Received (bytes/sec)
    Traffic Sent (bytes/sec)

## Slide 255: Select Individual Measures

## Slide 256: Select Individual Measures

## Slide 257: Select Global Measures
To select a global measure right click on the workspace away from the objects
The select
  Chose Individual Statistics
There will be a short delay as IT Guru initializes itself for this function

## Slide 258: Select Global Measures

## Slide 259: Select Global Measures

## Slide 260: Set Global Measures
The global statistics list appears
Expand
  Global Statistics

## Slide 261: Select Global Measures

## Slide 262: Set Global Measures
Select the measures
In this case
  Node Statistics
    TCP
      Connection Aborts
      Delay
      Retransmission Count

## Slide 263: Select Global Measures

## Slide 264: Select Global Measures

## Slide 265: Set Global Measures
Click
  OK

## Slide 266: Save the Simulation
If desired save the simulation by selecting
  File
    Save
Provide a name

## Slide 267: Run the Simulation
Everything is now completed
To run the simulation click on the
  configure/run simulation
Button
Usually the default values have to be changed

## Slide 268: Run the Simulation

## Slide 269: Run the Simulation
In this case the duration is set to 30 minutes

## Slide 270: Run the Simulation

## Slide 271: Run the Simulation
Click on
  Run
The next two screens appear one after the other
When the simulation is finished
Click on
  Close

## Slide 272: Run the Simulation

## Slide 273: Run the Simulation

## Slide 274: Examine the Results
To view the results of the simulation each individual measure must be selected, as well as any global measures
To examine an individual measure
Right click on the object of interest such as the server

## Slide 275: Examine the Results
Select
  View Results
Expand the hierarchy to show the measure
Click on the checkbox to select the measure
Click the
  Show
button

## Slide 276: Examine the Results
A graph of the results appears

## Slide 277: Examine the Results

## Slide 278: Examine the Results

## Slide 279: Examine the Results

## Slide 280: Examine the Results
To examine the global measure
Right click in the workspace
Select
  View Results
Click on the checkbox to select the measure
Click the
  Show
button

## Slide 281: Examine the Results
A graph of the results appears

## Slide 282: Compare Results
Once the first scenario is working a baseline for the network of interest has now been created
The effects of a change to the network can be assessed by creating a new scenario, then comparing the results of the two scenarios

## Slide 283: Compare Results
For example, a second floor might be added to the network
What impact will this have on the existing single floor network we just setup

## Slide 284: Create Second Scenario
To do this first create a new scenario by copying, then modify what was just done
Select
  Scenarios
  Duplicate Scenario
  Provide a name for the new scenario
Click
  OK

## Slide 285: Create Second Scenario
Setup the second scenario just as you did the first one
Just change what needs to changed or add any additional network segments or nodes
As before run the simulation

## Slide 286: Compare Results
To compare the affect of the added load on the original network select
  Compare Results
from the pop up menu that appears when right clicking on the object or on the workspace
Now two lines will appear in the results graph for the measure of interest

## Slide 287: Summary
As we can see when examining these four different types of tools the simulator and the emulators are very similar
The main difference being how close to the actual equipment the user experience is
The emulator produces the nearer to real experience, but it is but it is limited in what can be built

## Slide 288: Summary
The dedicated network modeling tool has much more detail that can be set so as to better represent the network that will be deployed
However, simulators and emulators range from free to very low cost, whereas a network modeling toll can be very costly
The type and complexity of the network being modeling will guide which tool to use