## Slide 1: Voice Design Last Update 2011.06.14 1.0.0

## Slide 2: Objectives
To see how the basic design principles should be adjusted to handle voice traffic

## Slide 3: Designing for Voice
Placing voice traffic on the data network creates a whole new class of network design issues such as concerns for
  Packet Delay
  Packet Loss

## Slide 4: Packet Delay
Delay causes voice quality to degrade
The limit for delay is 150 milliseconds one way

## Slide 5: Packet Delay

## Slide 6: Packet Delay
Delay can be classified as
  Fixed
  Variable

## Slide 7: Fixed Delay
Fixed delay has three parts
  Propagation delay
    This is the time required to travel from one endpoint to the other
    In general this is not an issue, except for satellite links
  Serialization delay
    This is the delay from sending a frame onto a network interface
    It is related to the link speed

## Slide 8: Fixed Delay
    The higher the speed, the less time it takes to place the bits on the circuit
    This is only a factor for links up to 1 Mbps
  Processing delay
    This is the time required to compress a block of PCM samples

## Slide 9: Fixed Delay

## Slide 10: Variable Delay
Variable delay is due to
  Queuing delay
    This delay comes from the queuing delays in the egress trunk buffers on the part that is connected to the WAN
  Dejitter buffer
    The variable delay between packets is jitter
    Dejitter buffers are used to smooth this delay out
  Variable packet sizes

## Slide 11: Variable Delay

## Slide 12: Packet Loss
Loss causes clipping and skips

## Slide 13: QoS
QoS is commonly required for networks that carry delay sensitive traffic such as voice
QoS used for voice includes the following
  Bandwidth reduction
    This is compression
  Bandwidth reservation
    The RSVP – Resource Reservation Protocol reserves bandwidth along a routing path to ensure a certain quality level for delay sensitive traffic

## Slide 14: QoS
  QoS classification
    Classification is done using ACLs or route maps
    Along with setting the IP precedence bit
      Voice is usually set to 5
  Congestion avoidance
    Traffic shaping and policy setting are used for this
    This adjusts the flows of traffic to reduce certain types in order to give voice less congestion
  Congestion management
    There are several methods that can be used to sort traffic to prioritize it at the outlet point

## Slide 15: Table 9-1

## Slide 16: Table 9-2

## Slide 17: Table 9-3

## Slide 18: Table 9-4

## Slide 19: Table 9-5

## Slide 20: Table 9-6