## Slide 1: WAN Design
Last Update 2007.06.06
1.1.0

## Slide 2: Objectives of This Section
Learn some aspects of network design that are specific to a WAN

## Slide 3: What is a WAN
A WAN is any network larger than a MAN
In addition many MANs are large enough or located in such a way that WAN connection methods must be used
A WAN type connection will always require a service provider’s service be used
Unlike a LAN or CAN where the entire network could be located on property you control

## Slide 4: What is a WAN
For a WAN it is unlikely you will be able to directly control all aspects of the network
The data lines and perhaps some of the equipment will be under the control of a service provider

## Slide 5: WAN Application Requirements

## Slide 6: Enterprise Services
In the Cisco design model the WAN connections are typically part of the distribution layer on small and medium sized organizations
In larger networks the connection is at the core layer
In all cases the WAN connections are part of the Enterprise Services section

## Slide 7: Enterprise Services
Enterprise Services are those common to all users in the organization
Such as, email, Internet access, or video conferencing
These services are placed within their own network near the backbone network that connects all of the organization’s networks
Traffic to and from these services must cross a layer 3 device

## Slide 8: Shared Block
Within the Enterprise Services section the WAN connections are part of a Shared Block
A Shared Block contains such things as
  A server farm
  Connection to the WAN
  Connection to the Internet

## Slide 9: Enterprise Composite Model

## Slide 10: Enterprise Edge

## Slide 11: Network Layouts
The size and the amount of redundancy required in the network will dictate the basic network design, as will the available funding
The common network layouts include

## Slide 12: Network Layouts
Point-to-Point
Hub and Spoke
Partial Mesh
Full Mesh

## Slide 13: Point-to-Point

## Slide 14: Hub and Spoke

## Slide 15: Partial Mesh

## Slide 16: Full Mesh

## Slide 17: Redundancy
Of course neither the Point-to-Point or the Hub and Spoke utilize any redundancy
Both the mesh network do
The design used today is dependent on the type of data line used
Let’s look at the progression of data line usage that has occurred over time

## Slide 18: Progression of Data Line Usage
In medium to large networks the trend has been from
  Private Lines
  to
  Frame Relay
  to
  MPLS

## Slide 19: Progression of Data Line Usage
In each case the desire has been to lower the costs
The way to do this has been to move to networks where the data travels over a shared network backbone

## Slide 20: Private Lines
The original design was to use private lines
Depending on speed this has been one or more of the following
  DDS
  T1
  T3

## Slide 21: Private Lines
To provide redundancy a private line was required between each location on the network

## Slide 22: Frame Relay
With a frame relay network a single data line connects each location to the service provider’s frame relay network
This lowered the cost as only a single data line was required at each location including the headquarters where all of the locations connect
PVCs then provide connectivity over the shared line to each location

## Slide 23: Frame Relay
A PVC is required to connect each redundant connection as well

## Slide 24: MPLS
In the current implementation using MPLS, tunnels are built from any site to any site through the service provider’s MPLS network

## Slide 25: Progression of Data Line Usage
In each case costs have dropped because of the shared nature of the network, while redundancy has been enhanced
The cost of private lines meant that little high speed redundancy was possible at a reasonable cost
Frame relay connections allowed more redundancy
MPLS allows a full mesh approach

## Slide 26: The Internet as the Network
Some see the next trend as being the use of the Internet as the WAN network to provide the ultimate in cost control
However, this is problematic at best due to
  Lack of SLA
  Lack of known latency
  No single point of contact
But lower cost

## Slide 27: What is a SLA
SLA stands for Service Level Agreement
In reality it is a prenuptial agreement
Something overpriced lawyers use as weapons both for you and against you
Something you never look at or use, until things start going wrong
More specifically it
  Details the level of service that is guaranteed
  Details the remedy, if that level is not met

## Slide 28: This is Why You Need One

## Slide 29: A SLA is Useless
Fundamentally a SLA is totally useless, but you must have one for any large contract for service
It is useless because as we will see below the only remedy is that the service provider will pay you some small amount of money or have a high ranking executive tell you how sorry they are
What you really need is for them to roll back time

## Slide 30: A SLA is Useless
What you need is that time lost to be given back
This is impossible
So a SLA is useless, but get one anyway

## Slide 31: Define in the SLA
There are two main elements to a SLA
  Performance
  Availability
For these two elements there are three things to include in the SLA
  Standard
    A measurable benchmark
  Measure
    Must be quantifiable

## Slide 32: Define in the SLA
  Remedy
    The penalty
Other things to include in the SLA are
  Clearly define responsibilities
    Each person responsible for seeing that a function is performed should be identified by position
  Cover corrective action
    Define who resolves each type of problem
  List all parties involved in the agreement
    Especially if there are multiple service providers

## Slide 33: Define in the SLA
  Specify the period of time the agreement covers
    Usually one or two years
  Identify and define each service covered
  Identify service level indicators
    Describe how the indicator is measured
    Define who is responsible for performing the measurement
      Common indicators include
        Bandwidth used or data throughput levels, such as bps
        Latency
        Availability, such as percent of uptime

## Slide 34: Define in the SLA
  Define nonperformance
    What constitutes nonperformance
    What is done if the indicators are not met
      These are often qualified
        Instead of saying all transactions will not have more than a 2 second response time
        Most will say 95% of all transactions will have a 2 second or less response time

## Slide 35: Define in the SLA
  Define the reports to be produced
    Frequency of reporting
    Who will have access to the reports
    Availability of real-time reports as well as periodically produced reports
The remedies themselves must be
  Simple to calculate
  Reasonable

## Slide 36: Define in the SLA
If they are to hold up in arbitration or court
The remedy is usually a percentage of the monthly fee
  It should be enough to remove the profit, but not so much as to put them out of business
  It should also escalate with repeated occurrences

## Slide 37: Other Remedies
As money in exchange for time is not very useful, some have suggested an additional remedy to use to help focus the service provider on actually solving problems
Craft a defined escalation policy that ensures that any issues receive immediate attention from the right people inside the service provider's organization

## Slide 38: Other Remedies
First, define what constitutes a service incident
Then create severity tiers that characterize the impact of a service weakness
For example, outright service cessation is obviously Tier 1
But you also should consider latency spikes, which can affect user response-time

## Slide 39: Other Remedies
Sustained latency of 250 msec or more for periods of longer than 1 minute may constitute a Tier 2 event
Once the tiers are defined, determine how quickly the carrier should inform you of an incident, how quickly it should respond to your notification, and how quickly you can expect restored service

## Slide 40: Other Remedies
After that, get the names, job descriptions, and phone numbers for the individuals who will be directly responsible for repairs
Get the contact information for the individuals to whom they report
Then, define explicitly when the service provider will escalate an incident

## Slide 41: Other Remedies
The service provider should agree to inform you directly every time an incident has been escalated
Now for the secret to this method
Explicitly specify that a senior member of management will address any issues that are not resolved in a timely fashion and to your complete satisfaction, at a time and date of your choosing

## Slide 42: Other Remedies
In other words, if you are sufficiently unhappy, an executive vice president will fly out to your site to explain why your service doesn't work
This works for a simple reason
Nobody wants to tell the vice president he has to exchange a Friday tee time for a room full of angry customers

## Slide 43: Other Remedies
The result is a more energetic effort to avoid the situation, which is exactly what you wanted in the first place
The forgoing excellent suggestion, assuming you are a large enough customer to talk them into thus, is from a column in Network World by Johna Till Johnson

## Slide 44: SLA Problems
Often an SLA means nothing in practice
For example
  “When SLA's are offered by Qwest, they apparently don't mean much.
  Our DSL has been down for nearly 3 days already- they promised a fix today, now they are saying Monday to even get a tech on it (apparently their remote dslam stinger has gone bad and I guess they don't stock a spare).

## Slide 45: SLA Problems
  Meanwhile we are half dead in the water. Very unimpressive service to say the least.”

## Slide 46: SLA Caution Areas
Be careful if performance is measured using averages
  If 90 out of 100 things are averaging 40 ms latency and the remaining 10 average 80 ms latency, then the overall average is 44 ms
  The average might then be within the tolerance
  However a delay of 80 ms for any one thing may be too high

## Slide 47: SLA Caution Areas
The definition of uptime is a slippery slope
Percentage is not as important as the time period over which it is measured
What is covered under the uptime is also important
  For example, in a circuit is it just part or the whole thing end-to-end
    If just one part has a 100% uptime guarantee, but another part has a 97% uptime guarantee, then the circuit uptime guarantee is 97%, not 100%

## Slide 48: SLA Caution Areas
    The part most likely to fail is the one that is always guaranteed at the lower level
Another uptime issue is related to the percentage of uptime guaranteed and over what period of time it is guaranteed
For example
  Let’s say the uptime guarantee is 99%
  That comes out to just 87.6 hours of downtime in an entire year

## Slide 49: SLA Caution Areas
  That sounds pretty good
  But what if you are an online flower shop
  What if all of those hours happen to span the 4 days just before Mother’s Day

## Slide 50: SLA Uptime Table
Uptime Percentage | 8 Hour Day Downtime | 24 Hour Day Downtime
90 | 291.2 hours | 876 hours
95 | 145.6 hours | 438 hours
99 | 29.12 hours | 87.6 hours
99.9 | 2.91 hours | 8.76 hours
99.99 | 17.47 minutes | 52.56 minutes
99.999 | 1.747 minutes | 5.246 minutes

## Slide 51: Monitoring the SLA
There are two ways to ensure the SLA is being adhered to
  Just trust the service provider
  or
  Watch it yourself
Monitoring can even be outsourced
  Companies monitor and argue for you
  In such a case, you have outsourced the outsourcing

## Slide 52: Putting It Into Practice
Let’s evaluate a sample SLA
Using the SLA handed out to you
Take a few minutes and look for the following

## Slide 53: Putting It Into Practice
Latency Guarantees
  Part of network covered
  Latency allowed
  Is it averaged
  What is Force Majeure
  Remedy

## Slide 54: Putting It Into Practice
Uptime levels
  Part of network covered
  Percent of uptime guaranteed
  Excluded events
  Remedy

## Slide 55: UUNET SLA

## Slide 56: UUNET SLA

## Slide 57: UUNET SLA

## Slide 58: AT&T DSL SLA
This summary page describes the Service Level Agreement (SLA) applicable to the AT&T Yahoo! High Speed Internet Business Edition family of services
A. Network Availability - 99.99%
  AT&T POPs on the IP/DSL Backbone Network shall be "Available" 99.99% of the time in delivering traffic to/from other AT&T POP locations on the IP/DSL Backbone measured over a calendar month

## Slide 59: AT&T DSL SLA
  Network Availability shall be calculated based on an aggregate monthly measurement average between AT&T MegaPOP and MiniPOP endpoints within the USA
  Customer shall be entitled to one (1) day's credit prorated from the Customer's Recurring Monthly Service Fees if AT&T fails to meet the aggregate Network Availability guarantee during any calendar month

## Slide 60: AT&T DSL SLA
  Any calculation of Network Availability shall not include any unavailability resulting from (a) scheduled Network maintenance; (b) the occurrence of a Force Majeure event, unavailability of an AT&T Virtual POP, or (c) the failure of non-service impacting equipment or systems responsible for network measurements

## Slide 61: AT&T DSL SLA
B. Installation Interval - 5 Calendar Days
  For completed, End User circuits on which billing has commenced, “Installation Interval” is calculated as the number of whole calendar days between the date AT&T received the customer order and the service activation date

## Slide 62: AT&T DSL SLA
  *Customer shall be entitled to 50% credit of the first whole month’s monthly recurring charge for that particular circuit if AT&T fails to meet the Installation Interval guarantee during the initial installation phase of the order
  This calculation excludes: (a) any customer that does not have an active voice line currently in service with AT&T (must add high-speed Internet service to existing line), (b) any requested due date that occurs after the first available install date,

## Slide 63: AT&T DSL SLA
  (c) lack of facilities within the AT&T network, (d) any orders which are changed by the customer after original date of submission, (e) orders must be placed before 12PM local time or the interval will not start until the following calendar day, (f) any customer with access provided by AT&T SPORT or (g) any delay resulting from Force Majeure events

## Slide 64: AT&T DSL SLA
C. Network Latency - 40ms:
  AT&T's aggregate monthly average, roundtrip POP-to-POP latency on the IP/DSL Backbone Network shall be 40.0 milliseconds or less between MegaPOP locations on the AT&T IP/DSL Backbone

## Slide 65: AT&T DSL SLA
  Aggregate monthly roundtrip latency shall be calculated based on the geometric mean of regular measurement samples between AT&T MegaPOP endpoints within the contiguous forty-eight (48) States of the USA
  Customer shall be entitled to one (1) day's credit pro-rated from the Customer's Recurring Monthly Service Fees if AT&T fails to meet the aggregate Network Latency Guarantee during any calendar month

## Slide 66: AT&T DSL SLA
  Any calculation of Network Latency shall not include any failure attributable to (a) scheduled Network maintenance; (b) the occurrence of a Force Majeure event, or (c) the failure of non-service impacting equipment or systems responsible for network measurements

## Slide 67: AT&T DSL SLA
D. Data Delivery (Packet Loss) - 99.9%:
  AT&T's aggregate monthly average packet loss between AT&T POPs on the IP/DSL Backbone shall not exceed 0.1%
  Packet Loss shall be calculated based on the arithmetic mean of aggregate monthly measurements between AT&T MegaPOP and MiniPOP endpoints within the USA

## Slide 68: AT&T DSL SLA
  *Customer shall be entitled to one (1) day‘s credit pro-rated from the Customer's Recurring Monthly Service Fees if AT&T fails to meet the aggregate Network Packet Loss SLA during any calendar month

## Slide 69: AT&T DSL SLA
  Any calculation of Network Packet Loss shall not include any failure attributable to (a) scheduled Network maintenance; (b) the occurrence of a Force Majeure event, or (c) the failure of non-service impacting equipment or systems responsible for network measurements

## Slide 70: AT&T DSL SLA
E. 24 Hour Service Restoration:
  Customer connectivity shall be restored in 24 hours or less from the time AT&T is notified of the outage
  *Customer shall be entitled to one (1) day's credit (based on 30 day calendar month) from the Customer's recurring monthly service fees if AT&T fails to meet the 24 Hour Service Restoration SLA

## Slide 71: AT&T DSL SLA
  Any calculation of 24 Hour Service Restoration shall not include any failure attributable to (a) scheduled Network maintenance; (b) the occurrence of a Force Majeure event; (c) the failure of non-service impacting equipment or systems responsible for network measurements; or (d) any CPE failures; (e) any outage involving access facilities; including Central Office (CO), Remote Terminal (RT), or Digital Subscriber Line Access Multiplexer (DSLAM) equipment

## Slide 72: AT&T DSL SLA
  (*) Credits are not automatically applied. Customer must apply via the Business DSL SLA website located at http://www.att.com/businessdslsla, or by calling our Customer Care at 1-877-722-3755

## Slide 73: AT&T DSL SLA
G. Scheduled Network Maintenance:
  Scheduled Network Maintenance refers to upgrades or modifications to network equipment software, network equipment hardware, or Network capacity
  Scheduled Network Maintenance may temporarily degrade the quality of AT&T’s Internet Service, including the possibility of short-duration outages

## Slide 74: AT&T DSL SLA
  Such effects related to Scheduled Network Maintenance shall not give rise to service credits under this SLA
  Scheduled Network Maintenance shall be undertaken only on Tuesday and Thursday mornings between the hours of 2:00AM and 5:00AM Central Time in the United States independent of the local time zone of each respective AT&T Point-of-Presence (POP)

## Slide 75: AT&T DSL SLA
  AT&T reserves the right to change Scheduled Network Maintenance dates & times upon 30 days notification via update to be posted at this site

## Slide 76: AT&T DSL SLA
H. Emergency Network Maintenance:
  Emergency Network Maintenance refers to efforts to correct network conditions that are likely to cause a material Service outage and that require immediate action. Emergency Network Maintenance may temporarily degrade the quality of AT&T’s Internet Service, including the possibility of short-duration outages

## Slide 77: AT&T DSL SLA
  Such effects related to Emergency Network Maintenance shall entitle Customer to service credits as set forth in this SLA if and only if service degradation or loss-of-service occurs outside of Scheduled Network Maintenance time windows identified in Section F

## Slide 78: AT&T DSL SLA
  AT&T may undertake Emergency Network Maintenance at any time deemed necessary and shall provide notice of Emergency Network Maintenance to Customer as soon as is commercially practicable under the circumstances

## Slide 79: AT&T DSL SLA
I. Force Majeure:
  Neither AT&T nor Customer shall be responsible for damages or for delays or failures in performance resulting from acts or occurrences beyond their reasonable control, including without limitation: fire, lightning, explosion, power surge or failure, water, acts of God, war, revolution, civil commotion or acts of civil or military authorities or public enemies; any law, order, regulation,

## Slide 80: AT&T DSL SLA
  ordinance, or requirement of any government or legal body or any representative of any such government or legal body; or labor unrest, including strikes, slowdowns, picketing or boycotts; inability to secure raw materials, transportation facilities, fuel or energy shortages, or acts or omissions of other common carriers

## Slide 81: AT&T DSL SLA

## Slide 82: AT&T T Carrier SLA
AT&T’s commitment on provisioning
  30 Days from Technical Interview
  Excludes any LEC facility issues
AT&T commitment on On-net Network Availability
  99.999% AT&T’s IP network has continually outperformed its major competitors for over a year

## Slide 83: AT&T T Carrier SLA
  Proof is readily available on the Internet
  AT&T’s IP network performance statistics are publicly available at www.att.com/ipnetwork

## Slide 84: AT&T T Carrier SLA

## Slide 85: AT&T T Carrier SLA

## Slide 86: AT&T T Carrier SLA

## Slide 87: AT&T T Carrier SLA
AT&T/SBC's commitment on Off-net Network Availability
  The monthly average full-page download time for the Keynote Business 40 websites, from within selected domestic MegaPOP locations, will not exceed 110% of the US25 Overall metric

## Slide 88: AT&T T Carrier SLA
  The Keynote Business 40 (KB40) Internet Performance Index measures the average download time for the home pages of 40 significant US-based business Web Sites
  These measurements are taken by automated agents attached to key points in the Internet backbone in the 25 largest metropolitan areas of the United States

## Slide 89: AT&T T Carrier SLA
AT&T's commitment on Maximum Time to Restore
  < 3 hours AT&T's commitment on Data Delivery
  99.9% Internet Service Availability
    SBC’s Dedicated Internet Access Service will be available to Customer 99.95% of the time in a calendar month

## Slide 90: AT&T T Carrier SLA
    Service Unavailability exists when the Internet connection is unable to transmit and receive IP Packets to/from On-Net Hosts and AT&T records such failure in the trouble ticketing system
    Service Unavailability is measured from the time SBC has actual knowledge of a service outage and a trouble ticket is opened, either in response to notification by the Customer or in response to alarms from internal network management systems, to the time Customer’s Impaired DIA Service is again able to transmit and receive IP Packets from SBC On-Net Hosts

## Slide 91: AT&T T Carrier SLA
AT&T's commitment on Maximum Latency
  39 ms Network Latency
    Average round-trip transmissions will be 40 milliseconds or less between selected MegaPOP endpoints within the IP Network, measured by averaging samples taken during a calendar month between these endpoints

## Slide 92: AT&T T Carrier SLA
AT&T's commitment on Maximum Packet Loss
  0.1% Network Packet Loss
    During any calendar month, packet loss will not exceed 0.1% based upon monthly averages, between MegaPOP and MiniPOP endpoints within the IP network

## Slide 93: AT&T T Carrier SLA
AT&T's commitment on Throughput
  There is a National Maintenance Windows for Tuesday and Thursday mornings at Eastern Time: 3:00 A.M. to 6:00 A.M.
  From the contract, "Customer understands and agrees that temporary interruptions may occur as normal and reasonable events in the provision of the Service
  All computer systems and networks need routine maintenance from time to time

## Slide 94: AT&T T Carrier SLA
  SBC generally schedules and performs such maintenance, on an as needed basis, during the times indicated on SBC’s website (located at http://dedicated.sbcis.sbc.com/NDWS/)
  Not all scheduled network/systems maintenance will affect Customer’s Service

## Slide 95: AT&T T Carrier SLA
  However, SBC will endeavor to provide Customer five (5) business days advance notice, or if not possible, reasonable advance notice if SBC believes that such routine scheduled maintenance will affect Customer’s Service

## Slide 96: AT&T T Carrier SLA
  In the event of a network/systems emergency requiring immediate attention, SBC reserves the right to perform emergency maintenance without notice or upon short notice, and shall use all reasonable efforts to minimize the effect of such work on Customer’s Service.“

## Slide 97: Optimization and Acceleration
Once the WAN line is selected and installed thought should be given to how to make the optimum use of the data line
Hardware and software is available that, through various methods, makes better use of the data line than can be achieved by just sending data down the line from the router

## Slide 98: Optimization and Acceleration
This is a new and developing field
As a Gartner research report says
  Optimization techniques for WANs can improve most organizations' application response times, particularly where network latency is high, which is often due to centralization of servers and IT resources

## Slide 99: Optimization and Acceleration
  Typically, WAN optimization controllers (WOCs) mitigate the sometimes severe impact of network latency on the performance of applications and the underlying protocols
  Through data reduction and prioritization techniques, WOCs can also help organizations avoid costly bandwidth upgrades

## Slide 100: Optimization and Acceleration
  The WOC market is rapidly maturing, but it is still dynamic with a high level of vendor innovation
  This has led to different vendors offering different combinations of features. So, before choosing a vendor, ensure you understand the applications and services running on the network, and the protocols that they use

## Slide 101: Optimization and Acceleration
  Also conduct a detailed analysis of your network traffic to identify specific problems — for example, excessive latency, bandwidth oversubscription or lack of prioritization for certain types of traffic
  Finally, insist on a real-life trial before committing to any purchase.

## Slide 102: Optimization and Acceleration

## Slide 103: For More Information
Top Down Network Design
  Priscilla Oppenheimer
  ISBN 1578700698

## Slide 104: Review
What is a WAN
What is an SLA
What is the major problem with SLAs