## Slide 1: Wireless Design
Last Update 2013.09.06
3.3.0

## Slide 2: Wireless Design Considerations
The design of a wireless network is science and art
Much is known and much is unknown, so guidelines based on experience are commonly used rather than exact formulas at this stage of development

## Slide 3: Wireless Design Considerations
There is an important consideration to keep in mind when designing a wireless network
In a wired network the signal is contained in a wire
When laying out or troubleshooting the network, the confines of the network are readily apparent

## Slide 4: Wireless Design Considerations
It is in the wires and the devices that connect to those wires
Whereas, in a wireless network the actual network is three dimensional and uncontained
Issues such as beamwidth, interference, atmosphere, and so on have a significant affect on the ability and consistency of the wireless network to do its work

## Slide 5: Wireless Design Considerations
To successfully design a wireless network you must learn to think and operate multidimensionally in a constantly changing environment

## Slide 6: Coverage
In this presentation the majority of the material will focus on wireless LAN design
The design of a CAN link uses the same basic principles as the wireless LAN design
The major difference being the types of obstacles encountered outside, such as trees
Otherwise the approach is the same

## Slide 7: Coverage
The design of a wireless MAN is very dependent on the type of network it is
A licensed cellular MAN is much different from an unlicensed SCADA network
There is little general design guidance that can be offered for these proprietary systems as the manufacturer of the equipment used will provide the design details

## Slide 8: Uses of a Wireless LAN
In addition to the usual uses for wireless local area networks new uses are being suggested as data rates increase
For example this slide from an Agilent webinar from January 2012 shows some of these new uses

## Slide 9: Uses of a Wireless LAN

## Slide 10: Designing a Wireless LAN
The way to start any network design is to apply a top down approach that relates the business needs of the organization to the technical implementation of the network
Based on this systematic design approach a physical network is laid out on paper
The discussion here is the changes to this network design brought about by the use of wireless devices

## Slide 11: Designing a Wireless LAN
In a network where the parts are connected with wires, in general, one need only decide where to place the parts and what capabilities each of these parts require to create an effective and efficient network

## Slide 12: Design Methods
A wireless network can be designed
  By hand using experience and guidelines
  or
  Using an automated design program

## Slide 13: Wireless LAN Network Design
To do this by hand acquire or create a drawing of the site of sufficient scale so that
  Device locations can be marked
  Radio signal coverage areas can be indicated
  Notes can be made

## Slide 14: Wireless LAN Network Design
Next, using experience from actual practice or based on guidelines discussed here, place the access points and their presumed coverage areas on the drawing, such as

## Slide 15: Wireless LAN Network Design
CELL 1
802.11b/g
CHANNEL 1
11 Mbps TO EDGE
CELL 3
802.11b/g
CHANNEL 11
11 Mbps TO EDGE
CELL 2
802.11b/g
CHANNEL 6
11 Mbps TO EDGE
CELL 4
802.11b/g
CHANNEL 6
11 Mbps TO EDGE
CELL 7
802.11b/g
CHANNEL 16
11 Mbps TO EDGE
CELL 5
802.11b/g
CHANNEL 11
11 Mbps TO EDGE
CELL 6
802.11b/g
CHANNEL 1
11 Mbps TO EDGE

## Slide 16: Wireless LAN Network Design
To crosscheck this, in some cases it will be necessary to perform some basic calculations to check for proper signal propagation
These calculations and the AP placement itself must take into account the physical characteristics of the site as well as the equipment being used, such as the type and directional nature of the antenna

## Slide 17: Wireless LAN Network Design
For example, an omnidirectional antenna will radiate the signal equally in all directions
If the AP is placed against the outside wall of the building, the radiation pattern and therefore the ability to intercept the signal may extend into a nearby street

## Slide 18: Wireless LAN Network Design
A directional antenna and more access points may be a better choice in this case, if relocation of the omnidirectional antenna is not possible

## Slide 19: The Goal
The goal of the network design is to propagate a signal that serves the needs of the network’s users
The two main considerations are
  Coverage
  Capacity

## Slide 20: Coverage
Coverage is designed to provide a low density of users with low throughput demands

## Slide 21: Capacity
Capacity is designed to support a large number of users using high bandwidth requirement applications such as voice and video
The focus for this type of design is a high density of access points, which can mean stacking access points physically on top of each other, to serve an area

## Slide 22: Capacity
Support for lower data rates must be disabled
Like a wired network each device should connect at the maximum rate or not connect at all
This calls for a large number of access points
In most cases this means moving to an all 802.11n 5GHz network

## Slide 23: Capacity
The 2.4GHz range and 802.11a/b/g devices must be abandoned
Next, the critical factor in maintaining connectivity for high capacity is the SNR – Signal to Noise Ratio
The higher the SNR the better the performance
The actual signal an noise levels are less important

## Slide 24: Signal to Noise Ratio Guidelines
40 dB or higher
  Excellent
  Always associated
  Very Fast
25 to 40 dB
  Very good
  Always associated
  Fast

## Slide 25: Signal to Noise Ratio Guidelines
15 to 25 dB
  Low
  Always associated
  Usually fast
10 to 15 dB
  Very low
  Mostly associated
  Usually slow

## Slide 26: Signal to Noise Ratio Guidelines
5 to 10 dB
  No signal
  Not associated
  Not useable

## Slide 27: Signal Levels
Some devices are more demanding of a strong signal than others
A suggested minimum is

## Slide 28: Signal Levels

## Slide 29: Receive Sensitivity
Next in importance in maintaining a high data rate connection is the receive sensitivity of the radio
Here are the sensitivities required for various data rates from a white paper from Juniper Network in 2011 and from Agilent from January 2012

## Slide 30: Receive Sensitivity

## Slide 31: Receive Sensitivity

## Slide 32: Access Point Spacing
Gast reports in his 802.11ac book that in general a single access point can provide coverage for about 3000 sf regardless of the 802.11 version used
According to a White Paper by Gigawave provided by Global Knowledge from 2009 access points should be between 40 and 70 feet from each other for good coverage

## Slide 33: Access Point Spacing
They should not be any closer to each other than 28 feet
Antennas should not be higher than 20 feet

## Slide 34: The Low Data Rate Problem
An additional problem with allowing the lower data rates on a network designed for high capacity is pointed out by Juniper in the same white paper
As they say

## Slide 35: The Low Data Rate Problem
  The shared media nature of 802.11n means that the problems related to a highly variable association rate are aggravated by Head-of-Line Blocking, because there is nothing to stop the transmission of larger, low priority packets ahead of smaller, high priority packets on ingress

## Slide 36: The Low Data Rate Problem
  Because more clients might be connected at the lower link rates, an access point’s aggregate throughput can plummet when it needs to allocate more airtime to those users transferring data at low rates

## Slide 37: The Low Data Rate Problem
  To make matters worse, the low rate users on the edge of the network also tie up a disproportionate amount of airtime—50% of all users might be consuming more than 70% of airtime, for example—degrading performance for everyone else sharing the same radio
  Transmission of a 1 MB file at the MCS0 rate takes 20 times longer than transmission at MCS15

## Slide 38: The Low Data Rate Problem
  Because 802.11n uses a shared media paradigm, only one client can transmit data at a time, which means that all other clients must wait their turn to transmit

## Slide 39: Reduce Power
The next point Juniper makes is the gains achieved by reducing the transmit power of the access points
  While turning down transmit power may seem counterintuitive, a reduction in transmit power levels is a valuable technique for maximizing throughput for both an access point and its neighbors

## Slide 40: Reduce Power
  Turning down the power slightly reduces the radius of the service area, but it also reduces interference by a much greater factor
  Turning down transmit power is a prudent and proven technique for maximizing throughput for an access point and its neighbors in a high-density deployment
  This makes it a best practice for a WLAN designer to streamline a wireless cell for optimal performance

## Slide 41: High Capacity Summary

## Slide 42: Next Steps to Higher Capacity
In the future as client devices are produced with better MIMO support this will increase throughput for these high capacity networks

## Slide 43: Other Considerations
In addition to the above the following needs to be considered in wireless network design

## Slide 44: Site Considerations
Things to consider when designing a network that will use wireless devices include
  Materials the site is made of
  Size of the network
  Existing networks
  Mounting points
  Electrical power for the access points
  Purpose of the network

## Slide 45: Site Considerations
  Bandwidth required
  Roaming required
  Security requirements

## Slide 46: Materials Effect on Signal Loss
The materials in the site have a major impact on the received signal strength and therefore on the coverage area
Different materials have different effects on the radio waves in order of most to least
  Metal in walls
  Tinted or coated windows
  Metal in ceilings or floors

## Slide 47: Materials Effect on Signal Loss
  Wood
  Glass
  Brick and concrete
The building’s construction has a major impact
Radio signal obstructions commonly found in buildings include
  Steel studs in walls
  Steel doors

## Slide 48: Materials Effect on Signal Loss
  Large structures inside the building
These large structures, such as elevator shafts and stairwells, have considerable metal in their structure
These areas will cast a radio signal shadow or area where the signal is entirely blocked
Steel reinforced floors have the same effect

## Slide 49: Materials Effect on Signal Loss
In an office environment the furniture itself may also have an effect, for example
  Metal filing cabinets
  Metal mesh furniture
In a warehouse environment other elements may come into play, such as
  Metal racks
  The products themselves as

## Slide 50: Materials Effect on Signal Loss
    Anything with a high water content will block the signal
    This is true of both the product and the packaging
    Paper and cardboard can have a high water content

## Slide 51: Materials Effect on Signal Loss
Obstruction | Additional Loss dB | Effective Range Feet
Open Space | 0 | Up to 100
Window – Glass | 3 | 70
Window – Metal Tint | 5-8 | 50
Drywall | 5-8 | 50
Woodwall | 10 | 30
6” Wall | 15-20 | 15
12” Wall | 20-25 | 10
Floor/Ceiling | 15-20 | 15
Floor/Ceiling – Thick | 20-25 | 10
Source: CWNA Study Guide Page 336

## Slide 52: Materials Effect on Signal Loss
Type of Building | Loss in dBs | Frequency in MHz
Grocery Store | 5.2 | 914
Retail Store | 8.7 | 914
Open Plan Factory | 7.9 | 1300
Open Plan Factory | 3.7 | 1300
Open Plan Factory | 4.0 | 1300
Open Plan Factory | 9.2 | 1300
Open Plan Factory | 9.7 | 1300
Open Plan Office Building | 9.6 | 915
Open Plan Office Building | 14.1 | 1900
Open Plan Office Building wit Partitions | 14.2 | 915
Open Plan Office Building with Partitions | 12.7 | 1900
These figures are from a study on cellular phone frequency penetration with frequencies in the 910 to 1900 MHz range. It is unclear from the text, but these appear to be average loss figures for the building as a whole.
Sarkar and others from IEEE Antennas and Propagation Magazine Vol.45 No.3 June 2003

## Slide 53: Materials Effect on Signal Loss
Location |  | Loss in dBs
Building 1 | 1 Floor | 12.9
 | 2 Floors | 18.7
 | 3 Floors | 24.4
 | 4 Floors | 27.0
Building 2 | 1 Floor | 16.2
 | 2 Floors | 27.5
 | 3 Floors | 31.6
These figures are from a study on cellular phone frequency penetration with frequencies in the 910 to 1900 MHz range. Sarkar and others from IEEE Antennas and Propagation Magazine Vol.45 No.3 June 2003

## Slide 54: 802.11bb/g Coverage
In general when using 802.11b/g equipment in a typical office environment it is safe to assume a 30 dB loss for every 100 feet
This translates into
  In a closed office
    50 to 60 feet
  In an office setup with cubicles
    90 feet

## Slide 55: 802.11b/g Coverage
  In hallways and large rooms
    150 feet
For the number of walls that can be penetrated
  Solid concrete
    One or two
  Concrete blocks
    Three to four
  Wood and drywall
    Five to six

## Slide 56: 802.11a Coverage
The coverage area for 802.11a is less than 802.11b/g
This is due to the use of a higher frequency
The same area can be covered as 802.11b/g, but the number of access points will have to be increased

## Slide 57: Attaching to the Wired Network
As part of the wireless design the attachment or attachments to the wired network must be considered as well
There are two ways to attach the AP to the wired network
  Use a separate switch for the wired network and another one for the wireless network
  Use one switch with VLANs used to divide ports between wired and wireless networks

## Slide 58: Isolation of the Network
In addition to using a separate switch or VLAN for the wireless network, further isolation of the wireless from the wired network can be provided by placing the wireless equipment in a DMZ area
This is an area that is isolated from the wired network by a firewall

## Slide 59: Isolation of the Network
Regardless of the method used to attach to the wired network and no matter how large the wireless network is, all access points should be in a single IP address subnet to provide isolation for the wireless network
A separate DHCP server should be used for the wireless clients

## Slide 60: 802.11b/g Channel Layout
One problem with increasing the coverage area of an 802.11b/g network is the limited number of channels
Although there are 11 channels, any channel used must be separated by at least 5 channels

## Slide 61: 802.11b/g Channel Layout
These then are the three channels that can be used
  1
  6
  11
These channels can be used to increase the coverage area
Three APs can also be used to serve a single area, thereby increasing throughput

## Slide 62: 802.11b/g Cell Channel Layout

## Slide 63: 802.11b/g Cell Channel Layout

## Slide 64: 802.11b/g Cell Channel Layout

## Slide 65: 802.11b/g Channel Layout
As a general rule the useable transmission radius of an access point should not overlap more than two other access points
In other words no single point anywhere on the plan should be touched by more than three circles
In practice it is often possible to use channels 1, 4, 8, and 11 in the same area at the same time

## Slide 66: 802.11b/g Channel Layout
There is minimal overlap among this set of channels

## Slide 67: Transmitting Power
As the amount of power that can be used by a transmitting device is regulated in most countries, this is not a variable that can be adjusted for the most part
Many people want to immediately amplify a signal to allow more devices to receive it
But as a wireless network must talk back and forth, amplification at one end is going to call for amplification at the other end as well

## Slide 68: Transmitting Power
The second problem with amplifying the desired signal is that it also amplifies the noise
Usually amplification is not as useful as it would seem at first
Higher gain antennas are a better choice

## Slide 69: Transmitting Power
Typical transmit power ratings seen in a wireless LAN include
  100 mW – 20 dBm
  50 mW – 17 dBm
  30 mW – 15 dBm
  20 mW – 13 dBm
  5 mW – 7 dBm

## Slide 70: Errors
Even though a readable signal at an acceptable data rate may be present, if too many errors occur, then the network will be unusable due to excessive traffic from retransmissions
Both the CRC error count and the packet retry count indicate the presence of bad packets on the wireless network

## Slide 71: An Error Metric
An error metric to use is the percentage of bad packets to good packets at the data rate of interest
Recall that on a wireless network the data rate can vary
The problem is finding a tool to provide this information

## Slide 72: Errors
If the network has less than 10 percent bad packets at the desired speed, it is operating properly
If the network has more than 30 percent bad packets at the desired speed, it needs attention
Keep the operating speed in mind
A network that has less than 10 percent bad frames, but is only working at 2 Mbps is not what is desired

## Slide 73: CRC Errors
Now for some details on the two types of errors mentioned above
Every frame ends with a FCS – Frame Check Sequence, more commonly called the CRC – Cyclic Redundancy Check
Whenever the bits in the frame have been corrupted the CRC calculated by the receiver will not match the CRC that was stored in the frame by the sender

## Slide 74: CRC Errors
In such a case the frame is discarded by the receiver

## Slide 75: Retry Packet Count
The second type of error occurs when a frame is not acknowledged, it is assumed to have not arrived and is resent
In this case the retry packet count will go up
This is seen in the Retry field of the 802.11 MAC Header
For a normal frame the bit is set to 0, on a retry it is set to 1

## Slide 76: Path Loss
What produces the variation in all of this, data rate and signal strength and error count, is the path loss that is always present in a wireless as opposed to a wired network
In some cases calculations based on the actual environment in which the network will be installed are called for, rather than just using estimates and guidelines

## Slide 77: Real World Path Loss
Formulas tend to reflect a lab environment
They must be adjusted for the much dirtier and RF obstructed real world
For example in a typical office, just the structure, such as wallboard, that makes the offices themselves will increase signal loss

## Slide 78: Real World Path Loss
If the environment has an unusual amount of metal objects, such as metal wall studs, shelving and so forth, or the environment has a high water content, such as plants, then the signal loss will be greater
This is especially if we are talking about an 802.11b/g network at 2.4 GHz

## Slide 79: Calculating Path Loss
Let’s do a calculation for a typical real world office environment
Assume
  100 mW access point transmitting at 20 dBm
    Most 802.11b/g APs have transmitter output power of 15 to 20 dBm’s
  Receiver 75 feet from the access point
  8 walls in between the AP and the receiver at 6 dB per wall

## Slide 80: Calculating Path Loss
Calculate total loss
  Free space loss
    30 dB per 100 feet
      30 dB X .75 = 22.5 dB
  Wall Loss
    6 dB per wall
      6 dB X 6 = 36 dB
  Fade margin
    30 dB

## Slide 81: Calculating Path Loss
  Total Loss
    22.5 dB + 36 dB + 30 dB = 88.5 dB
Free Space Loss
  Free space loss is the loss that would be experienced in a vacuum
  It is the natural spreading out of the signal much as water spreads out as it leaves the end of a hose
  As frequency increases, so does free space loss

## Slide 82: Calculating Path Loss
  As stated above it can be estimated as 30 dB per 100 feet for an 802.11b/g network
Wall Loss
  This is the added loss that occurs when the signal not only has to traverse free space, but also penetrate a wall
  Here six walls

## Slide 83: Calculating Path Loss
Fade Margin
  This is the way engineers try to account for the known but unmeasurable effects of things encountered in the environment, such as reflection, absorption, refraction, and diffraction of the RF signal
  This is basically a fudge factor
  20 to 30 dB is a common value for this in a wireless LAN

## Slide 84: Calculating Path Loss
For the industrious there is also the Barnett-Vignant reliability equation
    F = 30LOG10(D) + 10LOG10(6ABf) – 10LOG10(1 – R) – 70
    F = fade margin in dB
    D = distance in kilometers
    A = terrain roughness factor, where 4 is used for a smooth surface, 1 for average, and .25 for rough
    B = weather factor, where 1 is for the worst case, .5 for hot humid areas, .25 for inland areas, and .125 for dry or mountainous areas

## Slide 85: Calculating Path Loss
    f = frequency in GHz
    R = reliability expressed as a decimal, such as .9999

## Slide 86: Calculating Path Loss
The result would be at the receiver 75 feet from the AP with the eight walls in between
  20 dBm – 88.5 dB = -68.5 dBm
Based on the guideline given above of at least -65 dBm being required at the receiver, this location is too far away

## Slide 87: Calculating Path Loss
But a signal would still be receivable as the -68.5 figure is within the minimum range called for by the standard

## Slide 88: Calculating Path Loss
Either the
  Access point will have to be relocated
  The receiver will have to be relocated
  A directional antenna aimed toward the receiver will have to be installed
  Some of the obstructions to the RF signal will have to be removed, such as busting a large hole in a couple of the walls
  Well not really, but you get the idea

## Slide 89: Wiring for Access Points
The introduction of 802.11n will bring changes to the way cabling is provided to access points
Even though the theoretical 600 Mbps speeds discussed are unlikely, speeds of 75 to 150 Mbps are likely in a pure 802.11n environments

## Slide 90: Wiring for Access Points
This means each of these access points will need at least a 100 Mbps wired connection back to the MDF
In a large environment where multiple access points connect to an IDF with a single backbone cable to the MDF a Gigabit wired connection may be needed as the aggregate from the multiple access points will surely exceed 100 Mbps

## Slide 91: Wiring for Access Points
In an ideal 802.11n environment, you might even consider a 10G backbone

## Slide 92: Alternative to Rewiring
Motorola has an interesting access point that can be installed in place of an existing RJ-45 jack in a room
The existing wallplate is removed
A short cable connects the existing RJ-45 jack to the AP
The AP is mounted to the existing hole in the wall

## Slide 93: Alternative to Rewiring
This provides a tight signal for just one room, such as in a dormitory, classroom, patient room, or hotel
This can be standalone or centrally managed
Here is what it looks like

## Slide 94: Alternative to Rewiring

## Slide 95: Bandwidth Requirements
What type of bandwidth do you really need for common wireless network uses
A BICSI newsletter from June 2008 suggested these numbers

## Slide 96: Bandwidth Requirements

## Slide 97: Over Subscription
Of course you do not need to provide the maximum data rate to each user at every moment in time
Just like in a retail establishment queuing theory tells you that not everyone will do the same thing at the same time
The same BICSI newsletter suggested these over subscription rates

## Slide 98: Over Subscription

## Slide 99: Tools Used
At present there is no single, low cost tool that can be used to do a site survey for a LAN
To work around this most people do one or both of the following
  They rely on the guidelines discussed above
  They just use the tools that are supplied with the hardware they are installing

## Slide 100: Spectrum Analyzer
Let’s discuss some of these common tools
  Spectrum Analyzer
  Site Survey Tool
  Network Analyzer
A spectrum analyzer is used to look for and measure the strength of radio frequency signals within the band to be used

## Slide 101: Spectrum Analyzer
This device is expensive, from $2,000 to $10,000 depending on the features and frequencies included
It looks like this

## Slide 102: Spectrum Analyzer

## Slide 103: Spectrum Analyzer
Be sure to buy one with a peak hold function
There are low cost very basic spectrum analyzers that can be used for 802.11 networks
One of these is by Metageek
The hardware is a USB receiver

## Slide 104: Spectrum Analyzer

## Slide 105: Spectrum Analyzer

## Slide 106: Spectrum Analyzer

## Slide 107: Site Survey Tool
Once it has been determined that the site is free of any interference that might cause a problem for the frequencies to be used, measurements can be taken to determine if the placement of the devices is suitable
The tool for this is one that will measure at least
  Signal strength
  Noise level

## Slide 108: Site Survey Tool
As discussed above the best way to use these two measurements is to display a signal to noise ratio

## Slide 109: Site Survey Tool

## Slide 110: Site Survey Tool
As seen on this tool from Cisco’s the most important parameters
  Signal Strength
  Noise Level
  Signal to Noise Ratio
The screenshot above is from the tool running in passive mode
In active mode it gives an indication of the errors being seen on the network

## Slide 111: Site Survey Tool

## Slide 112: Site Survey Tool
In this case things look pretty good as no errors are showing right now
The way to use this tool is to set it up on a laptop
Then walk around the site to check the effect on signal and noise levels
By doing this the suitability of the original plan can be determined and devices rearranged as required

## Slide 113: Network Analyzer
A network analyzer, such as Sniffer Wireless from Network Associates or AiroPeek from Wild Packets, will show some information useful for a site survey
Sniffer Wireless will be used to illustrate this

## Slide 114: Network Analyzer
The opening display is the same as Sniffer has been for quite a while
The only apparent difference for a wireless network is in the title bar

## Slide 115: Network Analyzer

## Slide 116: Network Analyzer

## Slide 117: Network Analyzer
In the title bar we can see that
  This is a wireless network
  It is using 802.11b/g
  The modulation scheme is DSSS
  The current channel is 1
  The signal strength on channel 1 is 63%

## Slide 118: Gauge Dashboard View
To make the dashboard appear, click on the dashboard button on the toolbar

## Slide 119: Gauge Dashboard View

## Slide 120: Gauge Dashboard View
The dashboard is a set of gauges showing
  Utilization
  Packets per Second
  Errors per Second
  Throughput
Below this is a line chart
  Utilization is selected by default
  Other lines can be added by checking the boxes

## Slide 121: Gauge Dashboard View

## Slide 122: Detail Dashboard View
The information seen in the gauges can be expanded to show more detail by clicking the Detail tab

## Slide 123: Detail Dashboard View

## Slide 124: Detail Dashboard View

## Slide 125: Detail Dashboard View
Two items in this view relate specifically to wireless networks

## Slide 126: Detail Dashboard View

## Slide 127: Detail Dashboard View

## Slide 128: Detail Dashboard View
PLCP and WEP ICV are peculiar to a wireless network
PLCP is a physical layer sublayer
  What is shown here are the number of PLCP errors seen on the network
  PLCP errors occur when a wireless station receives a Physical Layer Convergence Protocol header with an invalid checksum

## Slide 129: Detail Dashboard View
WEP ICV refers to the security on a wireless network
  This is the number of packets sent indicating an invalid WEP ICV

## Slide 130: The Problem With the Tools
We will stop here as there is much more that a network analyzer can do that relates to a wireless network, but this is covered in detail in the How to use Sniffer Wireless presentation
As can be seen there is no single, low cost tool that gives us all of the parameters we need

## Slide 131: The Problem With the Tools
Specialized tools can be purchased for this purpose, but they can be expensive
AirMagnet is an example of this type of tool

## Slide 132: Automatic Design
Some companies are attempting automate more and more of the installation and management of wireless networks
For example Aruba Wireless Networks has a product called RF Director
When using the Aruba APs with this tool an AutoCAD drawing of a building can be imported

## Slide 133: Automatic Design
Based on this and standard parameters the Aruba tool places the APs on this diagram, as well as selecting the channels to use and the power settings
Once the APs are installed the tool is run again
It then adjusts the settings based on the actual affects of the building on the wireless signal

## Slide 134: Testing
If the calculations are not definitive or if the network is so critical that it must work right out of the box, then a test network may be called for
To check the data rate and the other factors, lay out a typical network, including workstations, in the actual environment

## Slide 135: Testing
Then transfer data between devices using some sort of automated operation, such as a batch file, a NIC utility program, or a program designed for this
Examples of this type of program include
  FTP transfers, although the requirement of FTP to read and write to disks may affect the result

## Slide 136: Testing
  Netperf, a free tool from www.netperf.org
  Two products from NetIQ, the free QCheck and the more powerful Chariot
Once the data is flowing, measure the data rate, signal strength, and errors at various parts of the network